## Slide 1: Sharing the Medium
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Introduction
Sharing a link (a wire a fibre with a station at each end)
  TDM, FDMSharing a network
  Circuit switching, packet switching
  Queuing strategies in routers
What about sharing the medium?
  Multiple stations of a wireless network
  Multiple stations on a single wire
Can we do it flexibly?
  Like a group of people conversing?
Notes: We have looked at sharing links either by FDM or TDM. Both of these divide the capacity of a link into fixed capacity sub-channels each of which may be used by a separate activity.
We have looked at sharing a network. The networks we have considered have looked roughly like the telephone network with switches connected by link. We have seen that we can share the network by switching circuits or packets. Packet switching is the preferred choice as it is a form of statistical multiplexing which is favoured by the bursty nature of computer traffic,
We now ask whether it is possible to eliminate the switches and share the medium directly. If we are to succeed we need a way of controlling access to the medium since it is dear that only one computer can be using it at any one time. Techniques for doing this are called "Medium Access Control" (MAC) algorithms.

## Slide 3: Aloha - simple contention
Packet radio - University of Hawaii - 1970s
"Contention-based" system - transmitters uncoordinated => collisions
Collision recovery - wait a random time and try again
How well will this work?
host
host
host
Notes: The ALOHA protocol was devised at the University of Hawaii in the 1970s. The protocol was first used on a packet radio network which was built to connect the various campuses of the University which were distributed amongst several islands, The transmitters were uncoordinated so it was quite possible for two or more to transmit simultaneously causing collisions. The ALOHA protocol attempts nothing to prevent this. It merely says "if a collision occurs wait a random time and try again". The random factor is necessary in order to prevent collisions occurring systematically on the re-transmissions. It is easy for a station to detect a collision; it just listens to the channel and detects whether the signal it transmitted has been altered in any way. Note that on a satellite network, as opposed to a packet radio network, there will be a considerable (propagation) delay before collisions can be detected. Geostationary satellites are 35,784 Km above the equator. At the speed of light the round-trip delay is about 240 ms - more if you are not on the equator. Protocols which allow these sort of conflicts between stations in order to solve the channel allocation problem are called "contention" systems. There are many variants.

## Slide 4: Aloha Throughput
Notes: The graph shows the theoretical throughput curve for Aloha. This is based on the assumption that all packets are of the same length and that the intervals between transmission attempts have a negative exponential distribution.
In the graph:
  S is the throughput – the combined rate for all stations at which packets are successfully delivered.
  G is the offered load – the combined rate for all stations at which packets are transmitted. G will be bigger than S since it includes colliding transmissions.
  Both S and G are normalised – they are measured in units of packets per packet time. Thus a perfectly utilised network would have a throughput of 1.
When G=1, i.e. the offered load exactly matches the network capacity, the throughput then is about 0.14. Thus 86% of our transmissions are actually retransmissions.
The best utilisation of 18.4% occurs at G= 0.5. Trying to achieve higher utilisation just makes matters worse. Eventually very little is happening except retransmissions colliding with each other and throughput approaches zero.
Does this mean that Aloha is hopeless? Not really but you have to ensure that the network has enough raw capacity so that G can be kept below 0.5.

## Slide 5: Slotted Aloha
Upper diagram – A and B would both collide with ongoing transmission
  Vulnerability period 2T (from t0 –T to t0 + T)
Lower diagram – transmissions start on “timeslot boundaries”
  A would collide but B is deferred - vulnerability period T
Utilisation is now 36.8%
  … but there is an extra ½T delay on average …
Time
t0
t0+T
t0-T
Time
t0
t0+T
t0-T
A
A
B
B
Notes: The upper diagram shows that, with standard ALOHA, a packet transmission beginning at t0 will be destroyed by another transmission beginning in the interval (t0 -T, t0+T) – a vulnerability period of 2T.
If we constrain transmissions to start on timeslot boundaries (so-called “slotted ALOHA”) then any transmission becoming available during the interval (t0, t0+T) will be deferred and will not collide. This reduces the vulnerable period to T.
Analysis shows that this results in a doubling of the maximum utilisation. The down-side is that packets must wait for a timeslot – an average of T/2 sec. additional delay.
There must be some mechanism for ensuring that all stations are synchronised to the same slot boundaries. In a satellite network this can be done by having the satellite transmit regular pulses indicating timeslot boundaries.
Note in this and other algorithms the difference between a collision (in which a transmission is lost and must be re-transmitted) and a deferral (in which a transmission is merely delayed).

## Slide 6: Carrier Sense Multiple Access
“Listen before speaking”
Avoids collisions?
Time
t0
t0+T
bit 1
bit F
time
A
B
D
p
t
bit 1
No!
  (but it helps)
Notes: If a station continuously monitors the network it can discover when another station is transmitting and can defer its own transmission until the network is silent. This avoids many collisions. The buzz phrase for this is "carrier sense".
Carrier sense does not avoid all collisions. The problem is that propagation delay ensures that another station's transmission may already have begun (legitimately) but has not yet reached us (see slide). The longer the propagation delay, the more likely this is to happen. In the extreme case of a satellite network, the propagation delay is about 240ms. Listening to the network may tell us that the network was silent 240ms ago but it does not help us to know what is happening now. Carrier sense cannot be used in such networks.
However, provided the propagation delay is low, CSMA gains a lot over Aloha. This is the situation for most LANs (both wired and wireless) where the maximum distance between stations is nearly always less than a few Km. For example, the propagation delay on a 2Km optical fibre is 20003x108 = 6.7s. At 10Mbps only 67 bits can be transmitted in this time - a very small portion of the size of the average packet. However, note that at 1Gbps 6700 bits or 837 bytes can be transmitted in 6.7s - a sizeable portion of a packet.

## Slide 7: Non-persistent CSMA
Suppose several stations are waiting:
  If stations transmit immediately the medium goes quiet there will be many collisions
Non persistent – “if medium is busy wait a random time and retry”
  Avoids systematic collisions on busy network
Data available
Transmit here
Persistent
Data available
Non-Persistent
Transmit here
Random time
Notes: As indicated in the previous slide, the naive CSMA strategy is for a station to monitor the medium continuously and, when it is silent, then transmission immediately. This is called persistent CSMA. The problem with this strategy is that if two or more stations are waiting, they will almost certainly collide when they begin transmission. (Here we should note that the diagram above omits a potentially important detail; namely that it takes some time for the fact that the network is silent to propagate to all stations). It should be clear that, when network load is heavy, persistent CSMA will generate very many collisions so that throughput will drop.
Several solutions to this problem have been studied. One approach is non-persistent CSMA. Here a station which finds the network busy backs off i.e. it waits a random time before listening again. Another approach is p-persistent CSMA. Here a station continues to listen to a busy network waiting for it to become silent. When it does so, the station transmits with a probability p, defers (i.e. waits a random time) with a probability (1-p). If p is 1 we have persistent CSMA, If p is (say) 0.5, then two stations both waiting for silence will collide with probability 0.25. The downside is that they will both defer with probability 0.25 leading to an unnecessary delay.
Note. We are considering here the strategy to be adopted when a station finds that the network is busy and defers its transmission. Do not confuse this with the strategy to be adopted when, despite our efforts, a collision does occur. In particular, note that CSMA-CD (see later) handles collisions in a way which resembles that used by non-persistent CSMA to handle deferrals.

## Slide 8: Throughput Comparison
Notes: The graph shows the theoretical throughput curves for two varieties of CSMA and ALOHA.
We can see that CSMA is always better than Aloha.
When the normalised load is low, persistent CSMA wins. This is because non-persistent is wasting time by deferring packets for a random time when these could, most likely, be transmitted immediately. However, as the load increases, persistent CSMA performance collapses as the network becomes dominated by collisions.
[The non-persistent graph is actually misleading. At high loads the probability of collisions becomes significant thus invalidating one of the assumptions made in the analysis. In reality the throughput would start to collapse as a result.]

## Slide 9: Collision detection
In CSMA, collisions last one frame time
  Why not stop once a collision is detected?
  How long does it take to detect a collision?
time
A
B
bit 1
p
bit 1
p
bit F
t
Answer: 2p
  E.g. 10Mbps Ethernet: tmax = 1.2ms, p = 10s
Notes: With both persistent and non-persistent CSMA a collision costs us one frame time. If we were to detect collisions as soon as we could and immediately stop transmission we would waste less time. Is this complication worthwhile?
The diagram shows the worst case in which B starts to transmit just before the first bit of A's transmission arrives. This takes one propagation delay p. However, at this point A is unaware of the collision and will not become aware until the first bit of B's transmission reaches A. This takes another time p. Thus, in the worst case it takes 2p to detect a collision where p is the maximum propagation delay between two stations. So, if we add collision detection, the time wasted in a collision reduces from t to 2p.
The original Ethernet (10Mbps) MAC protocol is CSMA with collision detection - CSMA-CD. The maximum size Ethernet packet is 1500 bytes and the transmission rate is 10Mbps. This means tmax = 1.2ms. The maximum distance between two stations is 2Km which means that p is 10s. So the saving certainly appears to be worthwhile.

## Slide 10: CSMA-CD Performance
CSMA-CD is a persistent strategy
When load is low,
  Negligible collisions
  Performs like persistent CSMA
When load is high,
Many collisions
  Collisions handled by “binary exponential back-off”
  Effectively a deferral
  Performs like non-persistent CSMA
Best of both worlds!
But …
  There is a cost (see next slide)
  CD is difficult in wireless networks
Notes: CSMA-CD is an effective protocol and is used on the most widespread LAN - Ethernet Since it takes 2p (worst case) to detect a collision all transmissions must last at least 2p.
CSMA-CD is a persistent strategy and, when load is low and there are few collisions, its performance is like that of p-CSMA. When the load increases, collision occur – and are detected. Collisions are handled by “binary exponential back-off”. Stations involved defer transmission by a random time with mean t. If collisions recur the strategy is repeated but with means 2t, 4t, 8t etc. This means that CSMA-CD behaves much like np-CSMA at high loads.
The down-side is the minimum frame-size requirement (see next slide) and the fact that collision detection is difficult in wireless systems – if is difficult to construct equipment that can transmit and receive the same frequency simultaneously.

## Slide 11: CSMA-CD
Protocol used on the original Ethernet
time
A
B
bit 1
p
bit 1
p
bit F
t
Must have t > 2p or collisions may be missed
For a given p there is a minimum frame-size
10Mbps Ethernet, min. frame is 64bytes
Problem: as bit rate increases more bits transmitted in 2p
  Reduce p or increase min. frame size – both undesirable
Modern Ethernets are often switched and avoid shared medium
Notes: The original commercial Ethernet ran at 10Mbps and had a maximum cable length of 2.5Km hence p = 25002x108sec = 12.5s. Thus t > 25s. At 10Mbps we can transmit 10 bits per s so the minimum frame size should be 250 bits - about 32 bytes, In fact we have to allow a bit for the electronics to react and then add on a little bit more just to be safe. Hence the 10Mbps Ethernet standard specifies a minimum frame size of 64 bytes.
This is unfortunate if we only want to send one byte but maybe not too bad. However the situation changes as the bit-rate increases. Fast Ethernet used 100Mbps and reduced the maximum cable length to 200m to compensate. Gigabit Ethernet (1000Mbps) increases the minimum frame size to 512 bytes.
In practice most modern so-called Ethernet networks make limited use of CSMA-CD and have multiple “segments” joined by “switches”. If there is just one station per segment then there is no contention – hence no need for CSMA-CD. Such networks are discussed later in the course.

## Slide 12: Code Division Multiple Access
Division of capacity through use of codes
Related to Direct Sequence Spread Spectrum
Good performance – efficient use of bandwidth
Used in wireless networks
Good noise immunity
Bits divided into “chips”
  64 or 128 chips per bit
Each station has a unique (carefully allocated) “chipping code”
Notes: In the examples here we will assume there are 8 bits per chip. It turns out that the demonstration is simpler if we represent a 1 chip as +1 and a zero chip as –1.
This technique is related to Direct Sequence Spread Spectrum. The “spreading sequence” used in DSSS performs the same role as the “chipping code” here.

## Slide 13: CDMA Example
Assume 8 chips per bit, 4 stations A-D – chipping codes:
  A 00011011 (-1 –1 –1 +1 +1 –1 +1 +1)
  B 00101110 (-1 –1 +1 –1 +1 +1 +1 -1)
  C 01011100 (-1 +1 –1 +1 +1 +1 –1 -1)
  D 01000010 (-1 +1 –1 –1 –1 –1 +1 -1)
CDMA chipping codes are “orthogonal” e.g.
  A.C = (-1.-1 + -1.+1 + -1.-1 + +1.+1 +
  +1.+1 + -1.+1 + +1.-1 + +1.-1)/8
  = (+1 + -1 + +1 + +1 + +1 + -1 + -1 + -1)/8 = 0
To transmit a ‘1’ send the destination’s chipping code.
To transmit a ‘0’ send its complement.
Notes: CDMA chipping codes are carefully chosen to be orthogonal. i.e. the normalised inner product of any pair is zero. This means that when we compare two CDMA chipping codes we find as many chip pairs the same as we find different.
To send a 1 to a station send its chipping code; so to send a 1 to A send:
(-1 –1 –1 +1 +1 –1 +1 +1)
To send a 0 to a station send the complement of its chipping code; so to send a 0 to A send:
(+1 +1 +1 -1 -1 +1 -1 -1)
Note that,

## Slide 14: CDMA Example [2]
Suppose a 1 is sent to A, 0 to C and 1 to D
Combined signal will be:
  A 1: -1 –1 –1 +1 +1 –1 +1 +1
  C 0: +1 -1 +1 -1 -1 -1 +1 +1
  D 1: -1 +1 –1 –1 –1 –1 +1 –1
  S : -1 –1 –1 –1 –1 –3 +3 +1
  S : -1 –1 –1 –1 –1 –3 +3 +1
  D : -1 +1 –1 –1 –1 –1 +1 –1
  (+1+-1++1++1++1++3++3+-1)/8 = 1
For D to retrieve its transmission it computes S.D
Note that
Notes: We make two simplifying assumptions; that the stations are in bit synchrony and that the signals are of equal power so they add in a simple arithmetic way. The slide shows three bits being added. A station can then extract its bits simply by forming the inner product with its chipping code.
This is an illustration of synchronous CDMA. It is used, for example, in some mobile phone networks for transmissions from the base station. The single source ensures both synchronisation and equal power.
In other situations our assumptions would not be true. We would also have to contend with noise. However, it turns out that, provided the chipping codes are long enough, it is still possible for a receiver to extract its bits with high probability. In effect we would find that the result of the calculation would not come to exactly 1 (or –1) but would be close enough for us to decide, at high probability whether a 0 or 1 was encoded. Effectively the “interfering” transmissions are eliminated as noise.

## Slide 15: Summary
We have looked at some techniques for sharing the medium
  There are many others!
These techniques avoid central control
Contention-based
  ALOHA, CSMA and its variants
Code based
  CDMA
Techniques can be used on wired networks
  Now mainly used on wireless networks