## Slide 1: Dealing with Errors
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Errors and error rates
Bit Error Rate (BER):
  e.g. 10-12 is one error in 1012 bits (on average)
Signalled error rate (SER):
  detected errors
Residual error rate (RER):
  errors that are not detected or corrected
Error correction:
  if either SER/RER is unacceptable
Error detection:
  if RER is unacceptable
Notes: We can only conclude that a service has been guilty of error if we know the QoS it was supposed to provide. If we are using a CL service which gives no guarantees about sequenced delivery then we should not complain if it delivers out of sequence. However, there are a couple of situations that may be considered errors no matter what service we are considering:
delivery of a message which has been corrupted in some way, i.e. the bits received are not the same as the bits sent.
non-delivery of a message that was submitted.
We will begin by concentrating on these two error types. No service can offer a zero error rate. However, it is possible for the error rate to be effectively zero (negligible). For example, if a 64 Kb/s line has a BER of 10-12 there will be one bit in error in every 6 months of continuous operation. In most circumstances this is not worth worrying about; other associated bits of equipment are breaking much more frequently than that.
Two error rates are important:
the signalled error rate concerns errors that are detected and reported by the underlying service.
the residual error rate concerns errors that are missed by the underlying service.

## Slide 3: Redundancy
Here is a srelling mistake
Not all combinations of letters make legal words:
  if they did how would we detect error?
Redundancy:
  information that is not essential
  helps in detecting errors
To detect/correct errors, we need redundancy:
  how much do we need?
  what is the cost?
Notes: It is obvious that there is a srelling mistake in this sentence. It is obvious because the set of all possible words that can be made from English letters can be partitioned into two sets; English words and non-English words. Srelling belongs to the latter set as do dfede, msndasad, and qjykfda. In fact, vastly more “illegal” words can be made than “legal” ones. Suppose we somehow re-organised English spelling so that all combinations of letters spelled legal words. We would not now be able to tell whether a word had been mangled by a transmission service; the result would always be another legal word. We may still be able to detect the error from the context. However, this is really equivalent to saying the set of all possible sentences that can be made from English words can be partitioned into two sets; English sentences and non-English sentences.
Another way of putting this is to say that our spelling system has redundancy. All those illegal combinations are wasted as far as the business of encoding information is concerned. We saw this earlier when we looked at entropy.
If we adopted a more efficient encoding so that all the redundancy was removed, it would make the construction of cross-words trivial. Any combination of letters could be entered and all would be valid words. However, solving the puzzle would be much harder since a much larger range of possible solutions would fit. On the other hand, if English were much more redundant, construction of cross-words would be almost impossible.
What is true for spelling is also true for the way data must be encoded for data transmission. If we are to detect errors then there must be some redundancy. This means that error control has a cost in terms of throughput; the capacity of a channel is effectively reduced (with respect to the amount of information transmitted) since some of the bits it carries are redundant. We need to understand how much redundancy is needed in order to be able to detect errors.

## Slide 4: Error detection
Messages: size m
Codewords: size c
  c = m + r
  r error control bits
Example – ASCII (8-bit):
  7-bits data, 1-bit even parity
Hamming distance
A 0 100 0001
B 0 100 0010
C 1 100 0011
Min. Hamming distance = 2
parity
bit
1-bit error: 0100 0101 
0000 0010 
1000 0011 
2-bit errors: 1100 0011 ?
0110 0011 ?
0100 0001 ?
To detect h-bit errors: Hamming distance > h
Notes: To make the problem manageable we will assume that information is to be transferred in fixed-size chunks of m bits (m for “message”). Thus there are 2m different possible messages that might be sent. Messages are encoded for transmission as c bits where c = m + r. The additional r bits constitute the required redundancy. Note that it is not necessarily the case that we can classify each bit as “information” or “redundant” any more than we can say which letters in an English word are redundant. We call each of the c-bit objects a codeword. There are 2c possible codewords but only 2m of these are legal codewords – the ones corresponding to the messages. Bit errors alter bits in codewords. When this happens we would like the result to be an illegal codeword. If the result is a legal codeword then the error will be missed. For example, suppose we construct our codewords on the basis of applying even parity to 7-bit ASCII. This gives the following codewords:
A 0 1 0 0 0 0 0 1
B 0 1 0 0 0 0 1 0
C 1 1 0 0 0 0 1 1
If we alter one bit in any of these codewords the result is an illegal codeword since the parity would be wrong. However, if we alter two bits then the result will be legal. We can change “A” to “B” in this way. With this encoding, all legal codewords are a least two “bit changes” apart. The number of bits in which two codewords differ is called the Hamming distance. In the 8-bit ASCII code above, there are no two legal codewords with a Hamming distance of 1. We can say that the minimum Hamming distance is 2.
To detect all h-bit errors, minimum Hamming distance > h
8-bit ASCII has 1 redundant bit in 8. This is 12.5% redundancy.

## Slide 5: Single-bit parity: residual error rate
Example:
  8-bit bytes (+ 1-bit parity)
  raw BER of channel = 10-4
  P(A bit is in error) = p = 10-4, P(Bit not in error) = 1-p
No parity
  P(No bits in error) = (1-p)8
  P(At least one bit in error) = 1 – (1-p)8 = 8x10-4
Add a parity bit (nine bits in all)
  P(Exactly two bits in error) = 9C2p2(1-p)7 = 3.610-7
Parity-bit gives 3 orders of magnitude improvement(!)
Notes: With a single parity bit, r, for our codewords of length c, the value of r is such that it turns the number of 1 bits in the whole codeword to be odd (even). The pre-assigned codewords are separated by a Hamming distance of 2 or more. To see how the addition of a parity bit can improve error performance, consider the following example. A common choice of c is eight. Suppose that the raw BER, p, of the channel is measured to be p = 10-4. Then:
P{single bit error} = p
P{no error in single bit} = (1-p)
P{no single bit error in 8 bits} = (1-p)8
P{undetected error in 8-bits} = 1 - (1-p)8 = 8.0010-4
So the residual error rate is 7.910-4. With the addition of the parity check, we can detect single bit errors but we will fail if there are two errors. We will also fail if there are 4, 6 or 8 errors but we will ignore these are the probabilities are tiny.
P{exactly 2 errors in 9 bits} = 9C2p2(1-p)7 (Binomial distribution)
= 3.610-7
As can be seen, the addition of a parity bit has reduced the undetected error rate by three orders of magnitude.
Single parity bits are common in asynchronous, character/byte-oriented transmission. Where synchronous transmission is used, other methods are used (we shall look at one of these in detail later).

## Slide 6: Error correction
Hamming distance:
  h-bit error: allow correction?
  enough distance between codewords
  what is “enough”?
To correct h-bit errors: Hamming distance  2h + 1
legal codeword
Hamming space
h
h
1
illegal codeword
Min H.D. = 5
Codewords 2-bit error 3-bit error
00000 00000 00000 10001 00000 10001
00000 11111
11111 00000
11111 11111
Notes: Encodings that allow correction in addition to detection require more redundancy and a greater Hamming distance. Suppose we want to be able to correct all errors of h bits or fewer. We must ensure that the set of all possible illegal codewords that we can generate from a legal codeword by changing h bits or fewer does not intersect the similar set generated from any other legal codeword. If we receive one of these illegal codewords, (i.e. one generated from a legal code-word by altering h bits or fewer) we will always be able to tell from which legal codeword it was generated. We can think of each legal codeword as being surrounded by a region of illegal codewords which can be generated from it by altering h bits or fewer. None of these regions must intersect. We can state that:
To correct all h-bit errors, minimum Hamming distance  2h + 1
For example, to correct all 1-bit errors requires a minimum Hamming distance of 3. So 8-bit ASCII has no error correcting properties. Suppose we have a system with just four codewords:
0000000000 0000011111 1111100000 1111111111
This has a minimum Hamming distance of 5, so it should be able to correct all 2-bit errors. The nearest legal codeword is the result of seeing which are the fewest number of bits we need to alter to get to a legal codeword.

## Slide 7: How much Redundancy
Suppose we want to correct all 1-bit errors
c = m + r
Each circle includes 1+c codewords
There are 2m circles
There are 2c codewords
(1+c)2m  2c => 1+m+r  2r
E.g. m = 7, r = 4
legal codeword
Hamming space
1
1
1
illegal codeword
Notes: How much redundancy would be required to correct all 1 bit errors? We have 2m messages and hence 2m clouds. Since codewords are c bits long we can generate c illegal codewords from each by changing 1 bit of a legal codeword. So each region accounts for c+1 codewords (c illegal plus one legal). So, the total number of codewords in the clouds is 2m(c+1). This must be less than or equal to the absolute total number of codewords (there may be some illegal codewords not in any regions) so:
2m(c+1)  2c  2m(m+r+1)  2m+r (since c = m+r)
 m+r+1  2r
m = 7 (for ASCII) and using some values for r, we find the inequality is satisfied at r = 4.
This does not tell us how to construct a suitable code of course. All we know is that it must have 11 bits and that the minimum Hamming distance must be 3 or more. Fortunately Mr Hamming invented a way of doing the job …

## Slide 8: Hamming code
11 10 9 8 7 6 5 4 3 2 1
m m m r m m m r m r r
Check bit
Msg bit 08 04 02 01
11 1 0 1 1
10 1 0 1 0
09 1 0 0 1
07 0 1 1 1
06 0 1 1 0
05 0 1 0 1
03 0 0 1 1
A = 1 0 0 0 0 0 1
11 10 9 8 7 6 5 4 3 2 1
1 0 0 0 0 0 1 Tx
11 10 9 8 7 6 5 4 3 2 1
1 0 0 1 0 1 0 0 1 0 0 Rx
8 4 2 1
0 1 1 0 = 610
check
1 0 0 1
1
0 0 0 0
0
1 0 0 0 1 0
0
0
1 0 0 0 1 0
Notes: Hamming not only derived a limit on how many check bits would be needed, he devised a code that operated at that limit – the Hamming Code. Let us look at a Hamming Code for 7-bit ASCII. This must have 4 check bits. The check bits are placed in the power-of-2 positions; 1, 2, 4 and 8. The check bits act as 4 independent parity bits for combinations of the message bits. To see which message bit is checked by which check bit write the number of the message bits as binary numbers. This indicates that check bit 8 will check message bits 11, 10 and 9; i.e. bit 8 is chosen to give even (odd) parity to bits 11, 10, 9, and 8.
The table also shows which check bits will be affected by an error in a given message bit. For example, if bit 9 is altered, check bits 8 and 1 will yield the wrong parity, 4 and 2 will be unaffected. Therefore, if we find the checks for 8 and 1 fail whilst those for 4 and 2 succeed it must be bit 9 that is in error and we can correct it. Note also that if it is one of the check bits that is altered the other checks will be unaffected. The error correcting algorithm is:
“Write down a 1 under the check bits that fail and a 0 under those that succeed. Interpreting the result as a binary number gives the number of the bit that is in error.”
For example, ASCII “A” (100 0001), even parity, would be encoded as:
11 10 9 8 7 6 5 4 3 2 1
1 0 0 1 0 0 0 0 1 0 0
If this is received as:
11 10 9 8 7 6 5 4 3 2 1
1 0 0 1 0 1 0 0 1 0 0
Then we write:
8 4 2 1
0 1 1 0
since the checks for bits 4 and 2 fail. This tells us that bit 6 should be corrected. This procedure can be implemented very cheaply in hardware.

## Slide 9: Error detection codes
Parity check - limited use:
  large frames?
  burst errors?
Polynomial codes:
  cyclic redundancy check (CRC)
  frame check sequence (FCS)
Based on binary arithmetic mod 2
So: 3071/123 = 24 r 119
or: 3071 – 119 = (24123)
So: 8x6+3x4+x2+1 / x2+1 = 8x4-5x2+6, r -5
or: 8x6+3x4+x2+1 – (-5)= (8x4-5x2+6)(x2+1)
8x4 - 5x2 + 6
x2 +1|8x6 + 3x4 + x2 + 1
8x6 + 8x4
-5x4 + x2
-5x4 + -5x2
6x2 + 1
6x2 + 6
-5
24
123|3071
246
611
492
119
Notes: Simple parity checks are of only limited value. Errors in communication systems tend to occur in bursts which means that several bits in close proximity are likely to be affected. Instead, a cyclic redundancy check (CRC) (otherwise known as a polynomial code) is used. There are two major attractions of this method:
1. It is backed by some solid mathematical theory so its behaviour under different error conditions is predictable.
2. It is cheap to implement in hardware.
The method relies on the mathematical theory of polynomials. The general form of a polynomial is:
  anxn + an-1xn-1 + ...+ a2x2 + a1x + a0
This is said to be of degree n as this is the power of its highest term. The number ar is called the coefficient of xr; any of the coefficients except an may be zero. Note that a polynomial of degree n has n+1 terms. To give a concrete example:
  8x6 + 3x4 + x2 + 1
Is a polynomial of degree 6. Note that if we insist that all the coefficients are between 0 and 9 and we set x = 10 then this can be interpreted as a decimal number. Likewise, if all the coefficients are 0 and 1 and we set x to 2 we get a binary number. It is this interpretation which allows polynomial theory to be applied to error detection in binary messages. If we divide one polynomial by another the we get a quotient polynomial and a remainder polynomial. If the remainder is zero (all coefficients zero) the we say that the division is exact. Polynomial division is analogous to long division of decimal numbers.
There is a general rule; if you subtract the remainder before doing the division the result will be an exact division (i.e. the remainder will be zero). You can generalise long-division to polynomials.

## Slide 10: Polynomial codes [1]
Use remainder (R) as checkbits
Sender “subtracts” remainder from message (M)
Receiver re-computes remainder:
  If non-zero  error
Must chose “good” generator polynomial (G)
Mod 2 arithmetic - simple in hardware
1100100
1101|1011010110  1100100 r 10
1101
1100
1101
1101
1101
10
R always fewer bits than G
Arithmetic Mod 2
Notes: Notice that: degree(quotient ) = degree(dividend) - degree(divisor)
and: degree(remainder) < degree(divisor)
The crucial step in the calculation of a CRC is division and inspection of a remainder. In a CRC check, matters are so arranged that we expect the remainder to be 0 – if it is not 0 we conclude that an error has occurred. This is fine, but we must ask what chance there is that an error could occur and still the remainder is 0? Polynomial theory tells us the answer to this question and helps us choose a divisor which will minimise the chance of getting a 0 remainder even when an error has occurred.
Note that any digital message exchanged between two computers can be regarded as a binary number and, hence, as a polynomial. Calculation of a CRC involves division of this message by some well-known generator polynomial. Ordinarily, division is quite expensive computationally. Fortunately, we can replace ordinary division by binary division mod 2 without invalidating the polynomial theoretic results. The division mod 2 is very simple (and is also simple to implement in hardware) – the question “does x go into y” should be interpreted as “is the length of x  that of y”. There are neither borrows or carries. The addition and subtraction tables mod 2 are identical, and are the same as the XOR function.
The principle steps in the CRC algorithm are:
Chose a generator polynomial (i.e. a binary number) (G). (This has to be agreed in advance by sender and receiver).
Divide the message (M) by G and note the remainder R.
Subtract R from M. This will give a polynomial/binary number which is exactly divisible by G. The receiver checks this by doing the division and checking that the remainder really is zero.

## Slide 11: Polynomial codes [2]
M 11011100 message, degree 7, 8 bits
G 1100 generator polynomial, degree 3, 4 bits, x3 + x2
M’ 11011100000 extended message, degree 10, 11 bits
M’ 11011100000
R 100 -
Mt 11011100100
Receiver: divide Mt by G:
10010111
1100|11011100100
1100
1110
1100
1001
1100
1010
1100
1100
1100
0
Sender: divide Mt by G:
10010111
1100|11011100000
1100
1110
1100
1000
1100
1000
1100
1000
1100
100
R 100 degree 2, 3 bits
Notes: For the transmitter:
1. Choose a Generator Polynomial (G) of degree r. Effectively, this means choose a (r+1) bit pattern. The choice of this is crucial – in practice a few standard patterns are commonly used. Both sender and receiver must know what generator is being used. Note that the remainder after dividing by the generator will have degree < r, i.e. it will have r bits or fewer. This turns out to be important later.
2. Extend the message by appending r 0 bits to it. This ensures that the extended message is of degree at least r.
3. Divide the extended message by the generator (mod 2) and note the remainder (R). Effectively it is this remainder which is the checksum.
4. Subtract the remainder from the extended message. The result will be a polynomial (bit pattern) which will be exactly divisible by the generator. Since the remainder will have r bits (or fewer), and we extended the message with r 0 bits, the subtraction only affects the additional zero bits; the original message is unaltered. Although we have expressed these steps in terms of arithmetic operations, the result is simply the original message with the checksum appended.
5. Transmit the extended message.
For the receiver:
1. Divide the received message by the generator (mod 2)
2. If the remainder is not zero then an error has occurred in the transmission, else remove the least significant r bits and retrieve the original message.

## Slide 12: Polynomial codes [2]
Mt transmitted message
ME received message including error
E error
A 1-bit error => E= xn
Suppose G ends in a 1
will always have a remainder.
All 1-bit errors will be detected.
For this to give a non-zero remainder
E/G must give a non-zero remainder
Notes: In practice, it appears that errors occur in bursts; a group of (say) 10 bits will mostly be affected then there will be, perhaps, several thousand bits before another error occurs. The power of the CRC check lies in its ability to detect these kinds of burst errors. Recall that the simple parity check performs poorly with error bursts since each successive bit in error tends to mask the effect of the previous bit. Mathematically, a burst of errors is equivalent to adding (mod 2) some random number to the transmitted message. Suppose the transmitted message is Mt and the error added is E, then the received message will be Me = Mt+ E. The check the receiver will perform is:
(Mt+ E) = Mt + E
G G G
If this happens to give a zero remainder then the CRC check will have failed to detect the error. Since we already know that Mt is divisible by G, we can concentrate on the second term, E/G. If E/G gives a zero remainder we are in trouble; if not, we are OK.
Consider an error burst which affects one bit, leaves the next two bits intact, then affects the fourth bit. This is equivalent to adding 1001 to the message. However, it is also equivalent to adding, 10010, 100100, 1001000 etc. depending on exactly where in the message the error burst occurred. It is clear from this example that E will normally have many trailing zeros. We can infer from this the first and most simple rule about how G should be chosen; it must not have trailing zeros (otherwise it may well divide E exactly). Our generator (1100) is clearly a bad choice. Assuming G ends in a 1 it corresponds to a polynomial of the form xi + ... + 1. If the error burst affects only one bit this means E will have the form xn.
Thus E = xn which cannot be zero. Hence all 1-bit errors will be detected.
G (xi + ... + 1)

## Slide 13: Polynomial codes [3]
1. Assume E(x) has odd number of
non-zero coeffs. This means E(1) = 1
2. Choose G to have (x + 1) as a factor
then E/G will give 0 remainder only if
E(x) = (x + 1)F(x)
This means that E(1) = 0
1 and 2 are contradictory!
Therefore we do not get a
Zero remainder and the
Error is detected
So, G(x) = (x + 1)(xk + … + 1)
will detect:
all single bit errors
all odd-number bit errors
Lots of other properties possible …
CRC-16 x16 + x15 + x2 + 1
CRC-CCITT x16 + x12 + x5 + 1
Both give 16-bit checksums which will detect:
all 1 and 2 bit errors
all error bursts of up to 16 bits in length
all bursts affecting an odd number of bits
99.997% of 17 bit error bursts
99.998% of 18 and longer bursts
Notes: Suppose also that we choose G so that it has a factor (x + 1). E/G will only give a zero remainder if we can cancel out this factor – i.e. if (x+1) is also a factor of E. It is easy to show that e cannot have (x+1) as a factor if it represents an error burst affecting an odd number of bits:
1. an error burst affecting an odd number of bits can be represented as a polynomial E(x) which has an odd number of non-zero coefficients. Given that we are using mod 2 arithmetic, it is clear that E(1) = 1 (remember that 1 + 1 = 0).
2. if E(x) has (x+1) as a factor we can write E(x) = (x+1)F(x) so E(1) = (1+1)F(1) = 0
It is clear that 1. and 2. are contradictory hence we can see that E(x) cannot have (x+1) as a factor so the error will be detected.
So, we now know that if G ends in 1 and has (x+1) as a factor it will detect all 1-bit errors and all errors affecting an odd number of bits.
By exploiting other features of the theory of polynomials we can put further constraints on G so as to increase the effectiveness of the CRC. Careful study of what is required has led to the choice of a few standard polynomials, for example:
CRC-16 x16 + x15 + x2 + 1
CRC-CCITT x16 + x12 + x5 + 1
Both give 16-bit checksums which will detect:
all 1 and 2 bit errors
all error bursts of up to 16 bits in length
all bursts affecting an odd number of bits
99.997% of 17 bit error bursts
99.998% of 18 and longer bursts

## Slide 14: Other error correction techniques
FEC:
  correct error(s) at receiver
  computationally expensive
  additional redundancy
  may be useful for real-time communication or for channels with high data rates and high delays
Convolutional codes:
  Viterbi
Reed-Solomon
Notes: When errors are detected at the receiver, the receiver can arrange for the sender to re-transmit the erroneous message using automatic repeat request (ARQ) protocols (we look at these later).
In some cases, the use of error control with ARQ protocols is not sufficient, for example due to real-time constraints, where there is a large end-to-end delay, or large bandwidth-delay product. In such cases, we must use other methods, such as forward error correction (FEC) – correction of errors at the receiver. The Hamming code we examined earlier is not suitable for large blocks of data and other mechanism such as convolutional codes must be used. (We do not examine these in detail in this course.)

## Slide 15: ARQ and flow control: protocols
Protocol messages – PDUs:
  Data + PCI
  PCI: header, checksum (CRC)
Automatic Repeat Request (ARQ):
  Error control – repeat damaged PDUs
Limited resources at end-systems – flow control
data
header
checksum
protocol control information
PDU
ARQ
Stop and Wait
Continuous Request
Go-back N
Selective Reject
Notes: This section discusses automatic repeat request (ARQ) protocols. The general form of the protocol data units (PDUs) sent by these protocols consists of a header followed by the data itself followed by a checksum. The header contains various pieces of protocol control information (PCI). This includes many items some of which (PDU type, sequence numbers etc.) are relevant to this discussion and others (addresses etc.) which are not. If present, the checksum usually comes at the end as it is calculated by the serial interface hardware, whilst the bits are put on the line and is then tacked on at the end. The checksum also counts as PCI; it will only be needed if the residual error rate of the underlying service is unacceptable.
The data part carries the payload, i.e. it is data that the service user wishes to be transferred. The length of the PCI as a fraction of the total length of the PDU constitutes part of the protocol overhead which reduces the effective bandwidth and so should be as small as possible. Not all PDUs contain data. Some are sent entirely for control purposes.
ARQ protocols specify rules to be followed by the two “ends” of the communication. Often these rules are implemented by programs. Instances of these programs are called protocol entities (PEs). We must remember that all this activity is being done on behalf of two “users”. No DATA PDUs need be sent unless a user requests it. Any data received by a PE must be passed up to the user. Note that a PE may not be able to deal with a user request straight away - it may already have a queue of data in its buffers awaiting transmission. Similarly, a user may not be able to accept incoming data immediately, it may be busy doing something else. In this case the PE will have to buffer data and, perhaps, use one of the flow control techniques, discussed later, in order to slow the transmitter down. The amount of data that PEs are prepared to buffer on behalf of their users depends in part on the protocol in use and in part purely on implementation issues like how much memory is available.

## Slide 16: Stop-and-Wait [1]
Tx sends PDU:
  contains data
Rx checks CRC in PDU:
  sends ACK
Tx uses timeout:
  re-transmit PDU
  RTT
Tx
Rx
time, t
ACK
DATA
bad CRC
DATA.req
DATA.ind
DATA
CRC ok 
timeout
DATA
DATA.ind
ACK

Notes: These are the simplest of ARQ protocols. They are also sometimes called idle request (idle-RQ) protocols. This reflects the fact that the transmitter remains idle until the receiver asks for more data. Although these protocols often work in duplex mode, discussion is simplified if we look at a simplex version. Two PDU types are relevant:
DATA PDUs: which carry data from transmitter (Tx) to receiver (Rx)
ACK PDUs: which carry acknowledgements from Rx to Tx
Procedure is simple:
1. Tx sends a DATA PDU and then waits for an ACK PDU
2. When Rx receives a DATA PDU it checks for errors: If the PDU is OK it sends an ACK and generates a DATA.ind.
3. When Tx receives an ACK it is happy and can send another DATA PDU.
Of course, if an error occurs, the ACK may never come. This can only be resolved by introducing a timeout. When Tx transmits a DATA PDU it starts a timer of a pre-determined length. If this expires before an ACK is received then the PDU is re-transmitted. The length of the timeout must be carefully chosen; if it is too long then error recovery will be unnecessarily delayed. If it is too short then it may generate unnecessary re-transmissions. The length of the transmission timeout is related to the round trip time (RTT) ‑the time it normally takes to send a PDU and get a reponse. Unfortunately this is not always constant.
Some variants of stop-and-wait have negative acknowledgements (NACK) as well as ACKs. However, since we cannot be certain that a NACK will be received successfully, we have to have a timeout mechanism in any case. Therefore, it is always possible to do without NACKs and we will ignore them.

## Slide 17: Stop-and-Wait [2]
At Tx:
  lost ACK or lost DATA?
At Rx:
  duplicate DATA?
How to detect duplicates?
  sequence numbers (SN) for DATA
  last packet or new packet?
  only 1 bit required
Tx
Rx
time, t
ACK
DATA-a
ACK
DATA-b
DATA-b(R)
ACK
duplicate data? new data?
timeout
?
?
a
b
Notes: The use of a transmission timeout introduces another problem. There is no way in which Tx can distinguish between the loss of a DATA PDU and the loss of an ACK PDU. In both cases the timeout will expire and the DATA PDU will be re-translated. Thus, it is possible that Rx will receive a duplicate copy of a DATA PDU.
In the diagram the second transmission of DATA-b is a re-transmission, indicated by “(R)” on the arrow marking the PDU in the time sequence diagram.
If Rx is to be able to detect duplicates it must be able to distinguish one DATA PDU from the next. The easiest way to do this is to include a sequence number (SN) in the PCI of the DATA PDUs. We want to allocate a fixed length field in the header for the sequence number and, in order to reduce the protocol overhead, this field should be as short as possible. When we reach the maximum SN we go back to zero and start to re‑use the SNs. We need to know how many different SNs (i.e. how many SN bits) are required in order that this can be done safely. For stop-and-wait, the ambiguity concerns just two PDUs. Rx needs to decide “is this a new PDU or is it a repeat of the last one”. We need just two different SNs to resolve this situation so we can allocate 1 bit in the header. When all is going well, the SNs will alternate between 1 and 0 in successive PDUs. Rx and Tx must both record their notions of what the next SN should be. This is part of the protocol state information which PEs must have. A protocol definition must say what state information is required, how it should be used, and what initial values should be assumed.

## Slide 18: Stop-and-Wait [3]
Tx
Rx
time, t
Suppose SN are only in DATA PDUs:
  short timeout causes problem
  SN in ACKs also
DATA-1
ACK
0
ACK
DATA-0
timeout
DATA-0(R)
ACK
1
next SN
next SN
1
DATA-0(R)
0
0
1
DATA-0
ACK
timeout
DATA-1
0
timeout
DATA-1(R)
ACK
0
ACK
this data is never
delivered to user
at Rx
1
1
ACK
DATA-1
0
0
ACK
DATA-0
Notes: Notice that the receiver sends an ACK even for a duplicate. This is necessary as the duplicate was probably generated as a result of a lost ACK and Tx will still be waiting for one. This is not always the case however. A duplicate can also be generated if the timeout at Tx is too short so that a re-transmission occurs before the ACK has had time to arrive. This can cause disaster as Rx will now generate a second ACK. Tx will have been happy with the first ACK and will have moved on to the next PDU. It will now imagine that the second ACK is acknowledging this next PDU and the protocol will fail. To defeat this problem it is necessary for ACKs also to carry sequence numbers. This enables Tx to determine unambiguously which PDU is being acknowledged.
Note that a sort timeout may, in fact, be caused by a delayed ACK. This is a particular problem when working across a network like the Internet which has highly variable delays.

## Slide 19: Stop-and-Wait [5]
Tx
Rx
D-1
Tx
Rx
D-1
Tx
Rx
D-1
Tx
Rx
A-1
Tx
Rx
A-1
Tx
Rx
A-1
Notes: Stop-and-wait tends to be inefficient when the propagation dalay is large compared with the transmit time.
We can see a representation of this inefficiency with the satellite channel with simple snapshots in time of a single DATA/ACK PDU exchange. Note how much of the channel capacity remains unused.

## Slide 20: Continuous-RQ [1]
Tx continues sending data before first ACK:
  pipelining
Capacity of “pipe”:
  bandwidth-delay product: data-rate  RTT
What if:
  path data-rate changes?
  RTT changes?
  Tx produces data faster than Rx can process it?
Notes: The solution to stop-and-wait inefficiency is to allow the transmitter to continue sending DATA PDUs whilst waiting for the first ACK PDU to arrive. This technique is called pipelining. One of the keys to efficient protocol performance is keeping the pipeline full. This is especially difficult to achieve in the case where the propagation delay varies, as it does in some computer networks.
Protocols which continue to transmit whilst waiting for an ACK are called continuous-request (continuous RQ) protocols. We cannot allow Tx to continue transmitting indefinitely. For one thing, all DATA PDUs which have been transmitted but not ACKed must be buffered by Tx in case re-transmissions are required. Buffers are often in short supply since they may be large (say 1000 bytes) and there may be many connections operating simultaneously.
The pipeline itself can be thought of having a capacity with respect to sender and receiver, which is sometimes called the bandwidth-delay product and is data-rate  RTT. For a satellite link at 64Kbps this is 64Kb/s  540ms  34.56Kb. With 1000bit PDUs, this means there could be up to 36 PDUs “in flight” at any one time. On the other hand, on a LAN we expect the transmission time to be much greater than the propagation delay so that there will be less than one PDU in flight on average.
However:
it is not always possible to know the end-to-end data rate on a particular path across a network with many hops (network layer and transport layer). However, at the link layer, this is usually not a problem.
the end-to-end data rate and RTT may change during the life-time of the data exchange. This effect is not so visible at the link layer (unless Rx is under heavy load), but may be very visible at the network layer and/or transport layer
the receiver may not be able to cope with data at the bandwidth-delay product rate
We will see later how the last of these items is dealt with using flow control.

## Slide 21: Continuous-RQ [2]
Tx
Rx
D-1
Tx
Rx
D-2
D-1
Tx
Rx
D-3
D-2
D-1
Tx
Rx
D-4
D-3
D-2
A-1
Tx
Rx
D-5
D-4
D-3
A-1
A-2
Tx
Rx
D-6
D-5
D-4
A-1
A-2
A-3
Notes: We can see how pipelining improves things by re-visiting our simple snapshots in time until the first ACK is received by the transmitter.

## Slide 22: Continuous-RQ [3]
Tx
Rx
time, t
Window size
3
DATA-2
1
DATA-3
0
DATA-1
2
1
2
3
4
5
6
7
1
DATA-4
0
DATA-5
1
0
DATA-6
1
0
DATA-7
2
1
ACK-1
1
ACK-2
2
ACK-3
ACK-4
3
4
ACK-5
ACK-6
ACK-7
1
2
3
5
6
7
Window size:
  Tx PDU “credits”
  can only send if window (credits) available
Rx may also have notion of window:
  must know which SNs to expect
Notes: The number of DATA PDUs which may be outstanding (i.e. transmitted but not ACKed) at any one time is called the window size. A DATA PDU which one is currently entitled to leave outstanding is said to be in the window. At any time, the current window is specified by giving the range of the sequence numbers of the DATA PDUs which are in the window. Once the window is full, i.e. all DATA PDUs in the window are outstanding, Tx must cease transmissions. It should be clear that the window size should be sufficient to keep the pipeline full.
The discussion above views the window from the transmitter’s point of view. The receiver also has a window which specifies the SNs of the DATA PDUs it is currently willing to receive. ACK PDUs ensure that the transmit and receive windows remain consistent - though the fact that there are PDUs in the pipeline ensure that they are not necessarily the same.
We can see with the contrived example above how windows may also help in flow control.

## Slide 23: Continuous-RQ [4]
Continuous RQ:
  works well for reliable underlying service
What if some PDUs:
  get lost/corrupted?
  arrive out of order ?
Re-transmission strategies:
  go-back-N
  selective reject
  trade-off: network traffic vs. buffer space + complexity
Notes: Rx would be happy to receive a steady stream of DATA PDUs with consecutive sequence numbers. However, if a PDU is damaged or lost, this will not be the case. Suppose some disaster afflicts the underlying service so that Rx successfully receives DATA PDUs with SNs 0, 1, followed by 3, 4, 5 etc.; 2 having had a bad CRC. Two strategies are possible:
1. ignore 3, 4 and 5 (and any subsequent DATA PDUs) and wait for Tx to go back to the last DATA PDU successfully received (2) and then continue from there. This is the go-back-n strategy. In this case, the receive window size is always 1.
2. buffer 3, 4 and 5 (and any subsequent DATA PDUs) and wait for Tx to fill in the gaps. This is the selective reject (or selective re-transmission) strategy. Note that, if an ordered-delivery style service (e.g. virtual circuit service) is being implemented, then 3, 4 and 5 cannot be passed up to the user until 2 has been received, otherwise sequenced delivery is not being achieved.
These two strategies make a trade-off between the network traffic generated as a result of re-transmissions against the need for added buffer space and complexity of the communication protocol.

## Slide 24: Go-back-N [1]
If PDU lost:
  wait for retransmission
  ignore all additional PDUs
Window size (w)
SN modulus (m)
m > w
Tx
Rx
time, t
DATA
ACK
timeouts
2
2
2
3
3
3
4
4
4
5
5
5
unnecessary
retransmissions
1
1
0
2
3
4
5
0
Notes: It should be clear that continuous request protocols must have sequence numbers in the ACKs so that Tx is clear which frame is being acknowledged.. Here PDU 2 is lost leading to the eventual re-transmission of 2, 3, 4 and 5. Note that sequence numbers must be carried in PDUs, which means a fixed number of bits must be allocated to them in the PCI. Thus sequence numbers will eventually wrap round.
There is a relationship between the sequence number modulus (m) and the maximum window size (w). Suppose a complete window is transmitted and all the ACKs are lost. The complete window will now be re-transmitted. At this point Rx does not know anything has gone wrong and is expecting the “next” DATA PDU with SN q (say). What it actually gets are w re-transmitted DATA PDUs and it must be able to recognise these as such. It can only do this if none of the re-transmitted PDUs has SN q. Therefore we need at least (w + 1) distinct SNs which means m > w. Note that, since the SN field in the header will be of fixed length, it is natural to choose the modulus to be a power of 2. In fact, in most practical cases the modulus m is chosen m = 2x-1, where x = 8, 16, 32, 64, i.e. the header field carrying m is byte-aligned or word-aligned.

## Slide 25: Selective re-transmission [1]
Rx ACKs each packet
If PDU lost/corrupted:
  ACK additional PDUs
  wait for re-transmission
Tx sees “hole” in ACKs
Rx waits for missing PDU before delivering data
Tx
Rx
time, t
DATA
ACK
timeouts
1
1
0
2
3
4
5
0



2,3,4,5
2

Notes: Selective re-transmission solves the go-back-N problems by ensuring that only frames genuinely in error are re-transmitted. It achieves this at the cost of greater complexity and greater buffering requirements. Since the receiver may have to hold PDUs whilst waiting for re-transmitted frames to arrive, the receiver as well as the transmitter must have buffers.
Pure selective re-transmission requires that a separate acknowledgement (ACK) or negative acknowledgement (NACK) be received for each packet sent. For an ACK-based scheme, a “hole” in the sequence of ACKs at the sender allows it to determine missing packets at the receiver – an implicit re-transmission scheme. In the NACK-based scheme, there is an explicit re-transmission mechanism.
Above, we show implicit retransmission.
There are all sorts of variants on the theme. For example, the Internet TCP protocol:
Numbers bytes rather than packets
Transmitter uses go-back-n strategy
Receiver buffers frames received out of order and waits for the missing one to fill the gap
An ACK for byte n implies that all bytes up to n have been received successfully
The relationship between the sequence number modulus (m) and the maximum window size (w) is different from that for go-back-N. Suppose, as before, that a complete window is transmitted and all the ACKs are lost. The complete window will now be re-transmitted. This time, Rx is expecting any of the “next” w DATA PDUs with SN q to q + (w - 1) inclusive. It actually gets w re-transmitted DATA PDUs and must be able to recognise these as such. It can only do this if none of the re-transmitted PDUs have SN in the range q to q + (w - 1) inclusive. Therefore we need at least 2w distinct SNs which means m > 2w - 1.

## Slide 26: Full duplex service
Duplex case:
  protocol operations in both directions, simultaneously
ACKs can be piggybacked on DATA:
  separate SN fields for data and ACK in header
Relies on two-way data flow:
  many “pure” ACKs still possible (e.g. WWW access)
Implementations:
  large data frames delay ACKs: timeouts
  delayed ACK (e.g. TCP)
Notes: Thus far, all our protocols have offered a simplex service. Converting these to full‑duplex is essentially a matter of operating a pair of independent instances of the protocol – one in each direction. There are two points to note however:
a) The set of events that can occur at any moment is much richer since it can now include the receipt of data spontaneously generated by the other PE.
b) Since data is now flowing in both directions, DATA PDUs from A to B may be used to carry ACKs of DATA PDUs flowing from B to A.
The technique in b) is termed piggybacking. If this is used then every DATA PDU header contains two sequence number fields; one for the sequence number of this PDU, the other for the sequence number of the DATA PDU being acknowledged. We cannot rely on there always being a DATA PDU conveniently waiting to carry an acknowledgement. So sometimes pure ACK PDUs will have to be sent. It should be clear though that piggybacking can greatly reduce the number of PDUs sent in the full duplex case. (piggybacking is used in TCP.) This is an important advantage as, in most implementations, there is a non-negligible processing cost in just sending a PDU, irrespective of its size. The disadvantage is that ACKs will be delayed if they have to be transported in long DATA PDUs as these take more time to transmit. A sequence of long frames can cause an accumulating delay in the receipt of acknowledgements which will eventually cause an unnecessary timeout.

## Slide 27: Flow control: sliding window [1]
Rx tells Tx how much data to send – window
Rx can:
  vary window size (increase or decrease)
  reduce window to 1: stop-and-wait
  other window sizes allow selective re-transmit
ACK from Rx contains:
  SN for data to be acknowledged (A)
  window size for Tx to use (W)
Tx can send (W - u) packets:
  u is the number of packets outstanding
Notes: The go-back-N and selective re-transmission algorithms presented above belong to the class of sliding window protocols. The name reflects the fact that sequence numbers which define the transmission window advance as PDUs are acknowledged. Each acknowledgement received allows the sender’s window to be advanced; thus enabling the transmission of further PDUs. Clearly, if acknowledgements cease, then Tx will fill its window and then stop. This can be used as the basis for a flow control mechanism. Furthermore, it is one which is fail-safe since the loss of an ACK PDU causes Tx to stop rather than to continue.
Rather than have the receiver simply stop sending ACKs we can gain more subtle control by allowing the receiver to vary the window available to the transmitter. Each ACK PDU contains a maximum window size (W) in addition to the acknowledgement sequence number (A). Tx must calculate its current window from W ‑u, where u is the current number of PDUs outstanding (PDUs transmitted but that have not yet been ACK’d).

## Slide 28: Flow control: sliding window [2]
A=0,W=3
A=1,W=3
A=2,W=2
A=3,W=1
A=4,W=0
A=4,W=0
A= 4,W=1
A= 5,W=1
Tx
Rx
time, t
DATA
ACK
0
1
2
3
4
5
0,1,2,3,4,5
window
sent not ACK’d
Rx controls TX rate with ACKs
Often used in Transport layer
0
1
2
1
2
2
2
3
3
3
4
4
4
5
5
5
Notes: Initially, Tx’s window is 3 and the first two ACK PDUs maintain it at this size. At this point, Tx knows that it has PDUs 1 and 2 outstanding (u = 2) and is allowed a maximum window of 3. Therefore, one PDU, number 3, can be sent. From now on, Rx begins to reduce the maximum window so that Tx’s current window cannot advance. Eventually Tx must stop. Rx can maintain this situation indefinitely – occasionally sending an ACK PDU with A = 4 and W = 0 in order to keep the connection alive (sometimes called a keep-alive). There is no problem with re-transmission timeouts as Tx has no PDUs outstanding. Later, Rx opens up the maximum window to 1 allowing PDU 5 to be sent. It then maintains the window at this size – effectively reducing the protocol to stop-and-wait. Notice that Rx did not so much reduce the window as let it fade away. This is responsible behaviour. An irresponsible receiver might reduce the window so fast that a PDU already transmitted would suddenly become “outside the window”. Sophisticated schemes like this one tend to be found in the transport layer where they operate above networks with variable delays. TCP uses this kind of strategy though the windows and acknowledgements are measured in bytes rather than in PDUs.