## Slide 1: Spectra and Modulation (Background Material)
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Baseband vs. Broadband
Baseband
Use full channel bandwidth
Signal transmitted directly in channel
Used in LANs:
  need media access control
Used in WANs:
  need multiplexing e.g. TDM
Broadband
Channel may be used by many signal sources
Frequency translation of original signal
Modulation:
  carrier frequency (wave)
Used mainly in WANs
(Wireless radio LANs)
“High data rate”:
  (over 2Mb/s)
Notes: In a baseband transmission system, the whole of the bandwidth available on the communication channel is for the use of a single signal. This kind of transmission is commonly used where high data rates are required, e.g in LAN environments. When used on a shared media LAN, there is usually some form of medium access control to allow multiple end-systems connected to the medium eventually to gain access to the medium for a transmission. When used in a WAN environment, some form of multiplexing, e.g. TDM, is usually used to allow access to multiple end-systems.
In a broadband transmission system, the available bandwidth is split into separate sub-channels, and some mechanism is used to allow different signals that would otherwise occupy the same bandwidth to be transmitted simultaneously by being frequency translated into the various sub-channels. The mechanism for frequency translation is normally called modulation and requires that the original signal is somehow combined with a carrier signal that is of the correct frequency for a particular sub-channel. Broadband transmission is used mainly in WANs, though some broadband techniques are also used in radio-based wireless LANs. The basic mechanisms of modulation (e.g. AM or FM) and frequency translation are, of course, familiar from radio and TV broadcasts.
In the context of datacomms, the word “broadband” has also come to mean a data system with a high data rate, typically 2Mb/s or greater.

## Slide 3: Baud rate and bit rate
Signal change:
  e.g. voltage level, light level
Bit rate:
  data rate
  capacity
  bit rate, bits/s
Signalling rate:
  transmission signal rate
  change in signal value
  one signal value my represent more than one bit
  baud rate, baud/s
time
0
1
bit rate = baud rate
00
11
01
10
time
bit rate  baud rate
Notes: Ones and zeros can be represented by the use of voltages, light intensities, audio/radio frequencies etc., as appropriate for a particular physical link technology. We do not necessarily need to use only two signal levels (for 0 and 1) but could use several signal levels. For example, with two signal levels we may choose:
However, we could choose to use four signal levels representing the bit patterns 00, 01, 10 and 11, respectively. In this case, each signal level would represent two bits rather than one bit. So we can see that the rate of the change of the signal – the signalling rate or baud rate – is not necessarily the same as the bit rate of the link. In this case a signalling rate of 9.6 Kbaud would give a bit rate of 19.2 Kbps.

## Slide 4: Signals and spectra (Revision) [1]
Time domain:
  variation of signal in time
Frequency domain – spectrum:
  discrete – zero bandwidth
-0.5
0.5
-1
0
1
-0.4
-0.2
0
0.2
0.4
0.6
0.8
1
time
sinusoidal wave
A
T = 1/f

0
0.2
0.4
0.6
0.8
1
1.2
0
0.2
0.4
0.6
0.8
1
1.2
1.4
frequency [Hz]
sinusoidal wave
Notes: Quick revision …
The simplest wave is a sinusoidal wave described mathematically by the expression:
s(t) = A cos (t + )
The quantities A, , and  are called the amplitude, frequency and phase of the wave, respectively.
Signals can usually be analysed by decomposing them into multiple sinusoidal waves. We can describe a signal in two ways. One way is to describe its evolution in time (time domain model) - the equation for s(t) is a mathematical representation of the time evolution of a wave. The second way is to describe its frequency content (frequency domain model). The wave defined by s(t), has a single frequency,  = 2f. In general signals contain many frequencies in different proportions.
The sinusoidal wave is a periodic signal, i.e. it has a cycle that repeats at a regular interval. The time taken for our signal to go through one complete cycle, i.e. the repeat interval, is called the period, and is usually denoted by the letter, T. The frequency (f) of the signal the number of cycles that the signal completes in one second, and has units Hertz (Hz). Most mathematical treatments tend to use units of “radians per second”. If  is in radians per second and f is in Hz then we have  = 2f.
PTO

## Slide 5: Signals and spectra (Revision) [2]
Fourier Theorem:
  sinusoidal components
0
0.2
0.4
0.6
0.8
1
1.2
0
2
4
6
8
10
12
time
square wave
0
2
4
6
8
10
frequency [Hz]
square wave
Notes: We can see that our simple wave has a single frequency and we see this clearly in the frequency domain graph. (Note that signal spectra are sometimes shown with pairs of positive and negative frequency components – this is a mathematical convenience in examining the signal.)
Note that this simple, repeating wave tells us nothing (other than if it is present or not present) – it gives us no information. In the frequency domain, we see that lines marking the frequency components have no width, i.e. there is nowhere to “put” information. To allow this signal to carry information we must somehow change its form so that there is an aperiodic change that can carry our information. This will also increase the bandwidth of our signal, as we shall see.
In digital communications, signals make sharp transitions rather than the smooth changes of the sinusoidal wave. It is instrucctive to consider a square wave. This is also periodic and its amplitude alternates between the values 0 and 1. Typically, an aperiodic version of such a signal – sometimes called a pulse train – is used in data communication systems, with the 0 and 1 bits being represented by the 0 and 1 (or low and high) amplitudes of the signal. Our periodic square wave can be described in time as:
s(t) = 1; 0  t < , 2  t < 3, …
= 0;   t < 2, 3  t < 4, …

## Slide 6: Signals and spectra (Revision) [3]
Notes: In fact, any periodic wave can be shown to be composed of sinusoidal components of varying amplitude and frequency. This is Fourier’s Theorem. For our square wave, we find that it can be represented by the expression:
i.e., it consists of an infinite number of sinusoidal waveforms added together. In the frequency domain, we see that this signal has infinite bandwidth. However, we can see that such a signal – a simple periodic pulse train – would give us no more information than the periodic sinusoidal waveform.
The period of the square wave is 2 secs so the frequency is 1/ 2 Hz. This is also the frequency of the first component in the Fourier series – sin(t). However, the next component – sin(3t) has a frequency 3 times as much and the next – sin(5t) 5 times as much.
We can examine the contribution each component makes to the final waveform. We note that as more components are added, they make the waveform appear more and more like a square wave. We can see that the higher frequency components add detail, whereas the lower frequency components are responsible for the basic shape and the amplitude of the wave – most of the power is in the first components.

## Slide 7: FSK [1]
Use two frequencies:
  fC0 for a 0
  fC1 for a 1
Equivalent to two ASK signals:
  twice the bandwidth?
  in practise, similar bandwidth to ASK
Better immunity to noise:
  need only to detect signal presence
More complex Tx and Rx than ASK
0
0
0
1
1
1
fC0
fC1
Notes: With frequency shift keying (FSK), two carriers are used, one to carry the 1 bits and one to carry the 0 bits. In its simplest form, this is effectively two ASK signals, and so it would seem that FSK needs about twice the bandwidth of ASK. However, if we treat the two separate carriers as each carrying half the transmitted bits (assuming of course we have roughly equal numbers of 1’s and 0s in our source bit stream), we can reduce our bandwidth requirement and effectively have two ASK signals operating at half the bandwidth each. This means that it is possible to produce an FSK signal that uses approximately the same bandwidth as an ASK signal for the same data rate.
Also, FSK is less prone to errors as the receiver does not need to know the signal level, just whether or not the signal is present or not.
The receiver and transmitter are more complex than an ASK receiver.

## Slide 8: FSK [2]
fC1
fC0
not to scale
fC1
fC0
Notes: s’(t) has 1s where s(t) has 0s and vice versa. It is essentially the same signal and will have the same spectrum. Hence we can assume
The modulated signal is just the sum of s(t) times one carrier plus s’(t) times the other. We know that the the Fourier Transform is linear – i.e. that
It is then easy to show that the resulting spectrum will be the superposition of two spectra centred at f0 and f1 respectively.
In the simplest FSK schemes, called wideband-FSK, the separation between the two carriers is such that the sidebands of each carrier do not overlap. Narrowband schemes, where the sidebands overlap, are also possible, but add extra complexity and other modulation schemes are likely to be used.

## Slide 9: PSK and BPSK [1]
Single carrier
Same bandwidth as ASK
Better noise immunity than ASK and FSK
Require reference carrier at receiver
Absolute phase values:
  +0 for 1
  + (180) for 0
0
0
0
1
1
1
Notes: We can also alter the phase of our carrier in order to represent 1s and 0s using phase shift keying (PSK). A simple PSK scheme is binary-PSK (BPSK), and we shall use this as an example.
In BPSK, we use a phase shift of , to represent a 0 and a phase shift of 0 to represent a 1. This is equivalent to an ASK scheme where a 1 is represented by the signal level +1 and a 0 is represented by a signal level of –1. Such a signal is called bipolar, whereas our original scheme with 0 represented by 0 is unipolar.
This scheme has better immunity to noise than ASK and FSK, but requires a reference carrier signal at the receiver in order to determine the absolute value of the phase shift (and hence the value of the transmitted bit, 1 or 0).

## Slide 10: PSK and BPSK [2]
not to scale
fC
fC
Spectra for bipolar and unipolar representations will be similar
  Side-bands either side of carrier frequency
BPSK has similar effect to ASK
Receiver multiplies by carrier as for ASK
0
1
0
1
-1
unipolar
bipolar
Notes: Since BSPK is equivalent to ASK of a bipolar signal, the analysis is similar to that of ASK.
The demodulation process for BPSK is much the same as for ASK, i.e. multiply the received signal with a replica of the carrier generated locally at the receiver, however we need an additional functional module in the receiver to detect the absolute value of the phase shift in the received signal.

## Slide 11: DPSK
Differential-PSK
Use relative (differential) phase changes:
  +/2 (90) for 0
  +3/2 (270) for 1
No need for reference carrier
Less complex circuitry than BPSK
Notes: The need for a reference carrier signal can be removed by using differential-PSK (DPSK). This relies on the use of a a phase change to indicate a 0 or 1 rather than an absolute phase value. For example, a +/2 (90) phase shift can be used to signal a 0, and +3/2 (270) phase shift can be used to signal a 1. In practise, this has the same bandwidth requirements as BPSK but actually requires less complex circuitry, as well as removing the need to a reference carrier signal.

## Slide 12: Phase diagrams
Multi-level techniques:
  one signal change represents more than one bit
Use a combination of ASK and PSK
Represented as phase diagrams:
  constellation
0
+90
+180
+270
1
0
BPSK
Notes: ASK, FSK and PSK are the basic techniques for modulation (although we will look at some more sophisticated techniques – spread spectrum – later). As we have seen them so far, these techniques use a signal change to represent a single bit and have, effectively, two signal levels to represent a 1 and a 0, respectively. However, a combination of ASK and PSK can be used to provide multi-level schemes, where a single signal change represents more than one bit. These levels of such schemes are often represented on phase diagrams or constellation diagrams that show how the combination of amplitude and phase shift results in representation of bits.

## Slide 13: QPSK
Use four phase shifts, e.g.:
  0 for 00
  +/2 (90) for 01
  + (180) for 10
  +3/2 (270) for 11
Each signal change represents 2-bits
Better immunity to noise than ASK, FSK and BPSK
8-PSK, 16-PSK possible:
  problems with noise
0
+90
+180
+270
QPSK
00
01
10
11
Notes: It is possible to use four phase values to let each signal change represent two bits of information – recall that the number of bits of information is log2(K) where K is the number of signal levels. Quadrature-PSK (QPSK) or 4-PSK uses four separate phases each to represent a two bit pattern – 0 for 00, +/2 (90) for 01, + (180) for 10 and +3/2 (270) for 11.
It is possible to have 8-PSK and 16-PSK, but as the number of phases increase, the system becomes more susceptible to disruption by noise and the circuitry required becomes increasingly complex and expensive. To obtain higher numbers of signal levels, ASK and PSK are combined in quadrature amplitude modulation (QAM).

## Slide 14: QAM
QAM:
  amplitude variation
  phase variation
K-QAM:
  K-level QAM, e.g.: 16-QAM 64-QAM
Constellation diagram
0
+90
+180
+270
16-QAM
Notes: A combination of phase values and amplitude values is used in a scheme called quadrature amplitude modulation (QAM). QAM is usually qualified by a number, K, to indicate the number of levels being used, e.g. 16-QAM, 64-QAM. A single signal level is a phase/amplitude combination and a constellation diagram is normally used to indicate these combinations and the bit values associated with them. QAM is used in environments where there is a fairly controlled noise regime, typically on cable based systems.