## Slide 1: The Internet Layer
Graham Knight G.Knight@cs.ucl.ac.uk

## Slide 2: The Internet Approach
Link, MAC, Physical – Technology dependent, unaltered
Convergence – encapsulation, address resolution
Common – datagrams, forwarding, fragmentation (maybe)
Transport – end-to-end
R
R
Internet
Common
Convergence
Link/MAC
Physical
Transport
Notes: As noted earlier, the Internet service is an abstract one which can be implemented on any network technology. In the slide the two lowest layers are technology dependent. All that is required of them is that they provide some means of carrying arbitrary data between their stations. In fact they may not be single physical networks – a collection of LANs connected by IEEE bridges could be viewed as a single network by IP.
The next layer, labelled “convergence” implements a mechanism for exploiting a specific network technology to carry IP datagrams. Depending on the nature of the technology this may be simple or quite complex – perhaps involving the setting up and taking down of connections. It will always involve address resolution, in which IP addresses are mapped to technology dependent addresses and encapsulation in which IP datagrams are inserted into technology dependent frames (not necessarily 1-1).
In this section we will look at the “common” layer which deals with ensuring that IP datagrams are correctly forwarded towards their final destination.

## Slide 3: A global network service
Able to “converge” all network technologies
Simple to implement
  => CL service not CO
Have its own (technology-independent) addresses
Must have good scaling properties
  Address aggregation
  Partition into management domains
  Dynamic routing
  Traffic filtering
Support different QoS requirements
IP Service!







Not quite yet!
Notes: The Internet IP service satisfies most of what we want:
  It is simple and is easy to carry in almost any network – i.e. the convergence protocols are easy to implement
  It has global Internet addresses which are independent of any particular technology
  It scales well – in particular the partitioning of IP addresses into network and host parts assists with routing, management and traffic filtering.
The main problem is that IP’s simple CL service hides potentially useful features in the underlying networks – in particular, QoS related features. Work is in progress (DIFSERV) to remedy this.

## Slide 4: Internet - Fundamentals
“The internet protocol implements two basic functions: addressing and fragmentation.
The internet modules use the addresses carried in the internet header to transmit internet datagrams toward their destinations. The selection of a path for transmission is called routing.”
(Operation on a single datagram = “forwarding”)
Notes: The text in the slide is from the Internet Protocol specification – RFC791 – which was written down in 1981. RFC791 gives a summary of the functions provided by IP which remains both concise and precise:
Note that the term “routing” should be taken to mean the processes involved in deciding the possible routes to a destination. The term “forwarding” should be applied to the process of choosing the “next hop” of a route for an individual datagram and dispatching the datagram on its way. (This terminology is not always respected).

## Slide 5: Internet – Fundamentals (2)
“The internet modules use fields in the internet header to fragment and reassemble internet datagrams when necessary for transmission through “small packet” networks.”
Fragmentation now thought best done at source
  IPv6 allows it only at source
  IPv4 allows it at source and in routers
Notes: Again, the text is from RFC791.
Later work revealed fragmentation in routers to be problematic and this has been removed from the latest version of IP. This is discussed later.
RFC = “Request for Comments” – a series of documents which started life as discussion documents. Some (by no means all) eventually became “Internet standards”. RFCs have always been freely available online. Several sites maintain a full set, for example: http://www.ietf.org/rfc.html. This open discussion of drafts is regarded by many as one of the key strengths in the development of the Internet.
Most of the Internet still uses IPv4 as described in RFC791. However, a new version – IPv6 – exists and is described in RFC1883

## Slide 6: The Internet
IP subnet
IP subnet
IP subnet
“IP subnets” (“networks”?) connected by “routers”
Routers may be connected by “point-to-point” links
Interfaces generally have IP addresses assigned.
IP subnet may not correspond to one physical network
“Interface” may not correspond to one physical interface
no IP address required
Notes: The Internet approach is described very fully in RFC1122. The world is modelled as a series of IP networks (usually called IP subnets today) interconnected by routers. These IP subnets are a logical concept and do not necessarily correspond one-to-one with real, physical networks such as LANs (though sometimes they do). Hosts are the end-points of communication, they are the computers on which applications such as web browsers or servers run. Hosts are connected to IP subnets. Hosts on the same IP subnet can communicate directly, without the need for routers. Sometimes, two routers are connected directly together via a point-to-point link.
The Internet service is a simple, connectionless one. Internet hosts may transmit PDUs called Internet Protocol (IP) datagrams.
An “interface” is a place where a computer attaches to a network. For example a wireless network adaptor provides an interface between a host and an IEEE 802.11 network. Hosts typically have just one physical interface (though they often have additional virtual interfaces to virtual networks). Routers generally have several interfaces. Most interfaces have a single IP address assigned to them. However, sometimes there may be zero or more than one IP address assigned.

## Slide 7: IP Subnets – The Rules
Hosts on same IP subnet share same network ID
Hosts with same network ID must be able to communicate directly
Hosts with different network IDs must communicate via a router
IP Address
Network Id
Host Id
Boundary varies
H
H
H
IP Subnet
H
H
H
H
IP Subnet
H
B
IP Subnets
H
H
H
H
R
Notes: IP subnets are logical concepts. An IP subnet may be 1-1 with a real network but may also encompass several real networks. Also, it is possible to partition one real network into several IP subnets.
IP subnets are defined by the addresses allocated to the interfaces attached to it. All interfaces in one IP subnet must share the same network ID.
Note:
The comments above apply equally if the phrase “IP subnet” is replaced by either “IP network” or IP supernet”. “IP network” and “IP subnet” are now used interchangeably
“Network Id” may sometimes be called “Subnet ID”, “Network Prefix”, “Subnet Prefix” or just “Prefix”.

## Slide 8: Simple Forwarding Algorithm
For hosts with just one interface:
If destination network id = local network id then“send direct”.
Else “Send to “default” router.”
IP subnet B
IP subnet A
Notes: This is the simplest case. Many LAN hosts are configured like this.

## Slide 9: IPv4 Addresses [1]
32 bits – e.g. 11000000101010000000000010000000
Written as 4 decimal bytes – e.g. 192.168.0.128
To interpret, we need length of network id
  Explicit 192.168.0.128/25
  Mask 255.255.255.128
Allocated in blocks with common network id
  11000000101010000000000010000000
  …
  11000000101010000000000011111111
  Gives an IP network with 128 host ids.
192.168.0.128/25
Notes: IPv4 address allocations are (ultimately) controlled by the Internet Assigned Numbers Authority (IANA) in the US. Other bodies, such as Réseaux IP Européens (RIPE), control allocation in particular geographical regions. ISPs and backbone network providers get their IP addresses from bodies such as RIPE. Other users get their addresses from their ISP.
IP addresses are allocated to ISPs who then allocate them to customers. Allocations cannot be arbitrary. Blocks must be allocated with a common network id otherwise IP routing will not work.

## Slide 10: IPv4 Addresses [2]
Can be further subdivided. E.g.
  If you own 192.168.0.128/25
  1100000010101000000000001.......
  Could allocate 2 more bits to network id
  192.168.0.128/27 (1000000)
  192.168.0.160/27 (1010000)
  192.168.0.192/27 (1100000)
  192.168.0.224/27 (1110000)
Or
  192.168.0.128/27 (1000000)
  192.168.0.160/27 (1010000)
  192.168.0.192/26 (1100000)
4 subnets
3 subnets
Notes: An ISP or a customer may further sub-divide a block. However, the “common network id” rules must be preserved.
Partitioning addresses in this way is useful to a large organisation who can then operate several “subnets” interconnected by routers. This allows (for example):
  Incompatible technologies to be connected via routers;
  “Firewall” routers to control access to sensitive parts of the network.

## Slide 11: IPv4 addresses - history
0
10
110
1110
1111
network id
host id
network id
network id
host id
host id
multicast (group) address
experimental use
Class A
Class B
Class C
Class D
Class E
No need for explicit network id length
e.g. marston.cs.ucl.ac.uk: 128.16.20.1 (class B)
0
8
16
24
(31)
Notes: Unicast IPv4 addresses were originally allocated from one of three IP address classes, class A, class B or class C. It was possible to identify the class, hence the length of the Network Id, by inspecting the first few bits of the address. One of the main problems with the class-based approach is the inefficiency that can result with class A and class B addresses when the host id space is not fully utilised within a single IP network. The addresses cannot be used by any other IP network that is connected to the Internet. Few networks now rely solely on classes. Instead they over-ride the class by means of a subnet mask or explicit length.
Unicast IPv4 addresses identify one interface connected to the Internet. Hence, a normal host machine (a workstation or a server) typically has only a single IPv4 address and a single network interface.
Multicast (which we look at later in the course) uses class D addresses to identify not a single interface, but a group of interfaces.
Class E is reserved for experimental use.
.

## Slide 12: Subnets, Supernets and CIDR
128.16.16.0/20
  10000000000100000001000000000000
  …
  10000000000100000001111111111111
  This is a “subnet” within a class B network (128.16.0.0)
200.16.16.0/20
  11001000000100000001000000000000
  …
  11001000000100000001111111111111
  This is a “supernet” formed from 16 class C networks
    200.16.16.0 through 200.16.31.0
212 host ids
212 host ids
Notes: The class-based scheme is still present in the background in that you cannot pretend that an address which starts with (say) 200 is anything other than a class C address. This is reflected in the terminology. A network formed by subdividing a single class x network is termed a “subnet”. A network formed by merging several class x networks is called a “supernet”. However, you will often hear all IP networks referred to as “IP subnets”.
The more flexible scheme used today is termed “Classless Internet Domain Routing” or CIDR. Today we assume that the network id length must be stated explicitly in which case routing cannot take place in the absence of this knowledge.

## Slide 13: IPv4 Special Addresses
255.255.255.255 - Limited broadcast.
  If the local network supports broadcast then broadcast the datagram. This is never passed on by routers.
x.x.255.255 – Net-directed broadcast
127.0.0.0 – Loopback (does not go out on net)
0.0.42.6 – Used as source ad. by host which does not know its network id.
0.0.0.0 – Used as source ad. by host which does not know its IP address
Notes: Some IPv4 addresses have special significance. They are used for administrative purposes or for specially controlled transmission, e.g. loopback and broadcast.

## Slide 14: Private IPv4 address space
Private IP networks:
  Intranets
Use IP, so need IP addresses:
  can use any address
  hosts must not be directly connected to the Internet
Special network ids (RFC1918):
  10/8
  172.16/12
  192.168/16
  Not forwarded by routers
Notes: There are many networks that do not need direct external access for each host, but would like to use the Internet Protocols and applications. They would like to run an IP network, but not one that is necessarily connected to the Internet at the IP level. Such networks are private IP networks, (an Intranet). When using IP, we need to have IP addresses for hosts. If the hosts are not directly connected to the Internet, then, in principle any IP address can be used. However, if hosts that had such randomly chosen IPv4 addresses were to connect directly to the Internet (by accident or design!), they could cause havoc with the normal operation of the Internet.
To minimise the risk of such occurrences, but still allow the use of private IP networks, RFC1918 specifies three address groups that can be used in numbering hosts on private networks. These are:
10.0.0.0 - 10.255.255.255 (10/8 network id)
172.16.0.0 - 172.31.255.255 (172.16/12 network id)
192.168.0.0 - 192.168.255.255 (192.168/16 network id)
Routers on the public Internet must not forward IP datagrams which use these either as source or destination.

## Slide 15: IP v4 Datagram Header
vers.
IHL
DIFFSERV
total length
identification
flags
fragment offset
TTL
protocol
header checksum
source IP address
destination IP address
options
options
padding
data
0
8
16
24
(31)
Notes: version: 4 for IPv4, 6 for IPv6
IHL: The length of the IP header in 32 bit words. This is normally 5 but will be longer if any of the options are in use.
DIFFSERV: QoS requirement (originally “type of service)
total length: total length in bytes (including the header).
identification and fragment offset: used to implement fragmentation and re-assembly.
flags: bits used to mark fragmentation status.
time to live (TTL): hop count before packet must be discarded.
protocol: a number to identify the protocol that this datagram is carrying – TCP, UDP etc.
header checksum: used to pick up transmission errors that might corrupt header fields.
source address and destination address: IPv4 address of sender of datagram and IPv4 address of destination of datagram, respectively.
options: rarely used (includes source route, record route and timestamp, etc.)

## Slide 16: More Complex Forwarding
“Routing Table” – a logical table in host or router
Columns
  Destination network (Network id and length)
    Choose the most explicit match
    “Longest match”
  Next hop IP address
    Sometimes referred to as “gateway”
  Interface IP address
    Needed if machine has more than one interface
  Metric
    A number used for tie-breaks
Notes: Although it is convenient to think of a routing “table” that does not mean that a routing table is necessarily stored as an array. It is vital that the time needed to look up a destination and find the next hop address should be as short as possible. Therefore data structures will be chosen which optimise this process.
You can view the routing table on many systems using the command
route print

## Slide 17: IP forwarding
Dest. Subnet | Interface | Next hop
128.16.64.0/20 | 128.16.64.1 | direct
128.16.23.22/32 | 128.16.64.1 | 128.16.64.28
128.16.16.0/20 | 128.16.64.1 | 128.16.64.28
128.16.0.0/20 | 128.16.0.1 | direct
128.16.23.0/24 | 128.16.64.1 | 128.16.64.29
0.0.0.0/0 | w.x.y.z | ??.??.??.??
128.16.0/20
128.16.64/20
128.16.20/24
128.16.23/24
128.16.16/20
C
A
Internet
128.16.0.1
128.16.64.1
w.x.y.z
B
128.16.64.28
128.16.64.29
128.16.23.22





Notes: The routing table is for router C.
Today, destination subnet specifications explicitly include the length of the network id (sometimes expressed as a subnet mask). Consider a datagram destined for 128.16.23.2. This matches four lines in the routing table as shown below:
10000000.00010000.00010111.00000010 target
10000000.00010000.01000000.00000000 line 1 n
10000000.00010000.00010111.00000010 line 2 y
10000000.00010000.00010000.00000000 line 3 y
10000000.00010000.00000000.00000000 line 4 n
10000000.00010000.00010111.00000000 line 5 y
Default line 6 y
The rule is to take the longest match (“default” counts as a zero-bit match) – so line 2 is chosen and the datagram is routed via router A. Any other host on the same network – 128.16.23.3 say - would match to line 5 and would be routed via router X.

## Slide 18: Address Aggregation
IP subnet 128.16.0.0/16 - potentially thousands of hosts
“Rest of the world” needs just one table entry
  All traffic routed via R1
Within 128.16.0.0/16
  One entry for 128.16.16.0/20
  One entry for “rest of the world”
128.16.0.0/16
128.16.16.0/20
128.16.20.0/24
R1
R2
R3
Rest of the world
Notes: The idea of networks and subnets within subnets greatly reduces the size of routing tables. One routing table entry can provide routing information for many thousands of hosts.
Routing may be hierarchical – i.e. traffic for a host in 128.16.20.0/24 would be routed via R1, R2 and R3. However hierarchical routing is not mandated and may be inefficient in some cases. It would be possible for R3 (say) to have a direct link to the rest of the world and for traffic to be routed directly to it.
Although this 3 level hierarchy is useful, the top level is an organisation (UCL-CS in this case) and there is no easy way to aggregate addresses above this level. One might like, for example, for UCL-CS to be a subnet of UCL which would be a subnet of “UK-Academic” etc. One motivation of IPv6 is to allow this sort of aggregation. In order to see what is required, we look, in the next few slides, at the high-level organisation of the Internet.

## Slide 19: The Global Internet
A collection of networks
No single administration
“Organic growth”
Broadly hierarchical structure
  Core networks (National Service Providers – NSP)
  Transit networks
  ISPs
  Private networks
Autonomous systems
Notes: The Internet has a very loose structure. Its topology is mainly a consequence of perceived commercial need being satisfied by a network service. However, the result is a broadly hierarchical structure with some operators concentrating on providing “core” networks, others concentrating on connecting private users, and still others providing transit between users and the core.
In terms of Internet routing, the highest level entities are “autonomous systems” –collections of networks, links and routers run by a single administration and implementing a single external routing policy. Autonomous systems handle routing internally in whatever way they choose. However, they exchange information with each other via standard routing protocols.

## Slide 20: NAPs, MAEs and Peers
Local ISP
NSP A
NSP B
NSP C
NAP
NAP
Private Peering
Regional ISP
Regional ISP
Local ISP
Users
Local ISP
Notes: The core networks (called “National Service Providers” in the US) compete with each other to carry Internet traffic. They have high bandwidth links between their routers – gigabits and upwards. NSPs connect with each other in two ways:
  Through independent “Network Access Points” (NAPs). These are commercial operations and provide high bandwidth switching between networks. They are generally confined to a small geographical area, e.g. a single building, and consist of high-speed networks such as gigabit Ethernet which host routers belonging to the NSPs. NAPs are sometimes called Metropolitan Area Exchanges (MAE).
  Though private “peering” arrangements. These are direct connections between NSPs.
Regional ISPs are next in the hierarchy. As the name suggests they cover a smaller geographical area than an NSP. In order to provide a service they must connect to an NSP. This may be either direct or through a NAP.
NSPs and regional ISPs need flexibility as well as capacity. They may use ATM or SDH in order to manage their internal capacity between routers.
Local ISPs connect end-users to the Internet. This may be via dial-up (for many private users) or leased line ( for corporate users). Local ISPs may be big (NTL etc.) or tiny (you or me with a few modems and a couple of Linux boxes).

## Slide 21: How the money flows
NAPs charge NSPs and ISPs for their interconnection service
NSPs charge ISPs
ISPs charge their customers
Private peering charges depend on traffic flows
Charges tend to be based on link bandwidth
Differentiated Services (DIFFSERV) make all this more complex …
  Different costs for different service levels
Notes: It is not easy to get details of who charges what to whom – it is all commercially sensitive. In principle anyone could construct a NSP or ISP and negotiate with existing operators to obtain interconnections. Existing operators may or may not welcome the newcomer – it is all a matter or commercial policy.
Peering arrangements are varied. Two operators may simply agree to carry each other’s traffic or there may be payments in one direction or the other. Possibly an operator may agree to carry only certain traffic – based on source or destination for example.
DIFFSERV will make all this more complex as it allows packets to be marked as to how they should be treated (low delay, low jitter etc.). Operators may need to establish service level agreements and accounting procedures to deal with this.

## Slide 22: Routing
Autonomous Systems do their own routing internally
  Invisible to other ASs
An “Exterior Gateway Protocol”
  Used to exchange “reachability” information between autonomous systems
AS advertise to their neighbours the ASs that they can reach
  Not obliged to advertise them all
Notes: Over the years there have been several Exterior Gateway Protocols including one which was actually called “Exterior Gateway Protocol”. Currently the favoured Exterior Gateway Protocol is the Border Gateway Protocol (BGP).
Routing within an AS may be quite dynamic and intended to optimise traffic flow in the face of frequent load and topology changes.
Routing between ASs is much less dynamic since topology changes at this level are comparatively rare and route choice often reflects long-term commercial agreements rather than short-term load changes.

## Slide 23: IPV6 OBJECTIVES
To solve the address space problem for the foreseeable future
To provide for new services that IPv4 cannot cope with such as:
    nomadic users
    networked entertainment
    device control
To add security at the IP level
To be able to move gradually and (reasonably) seamlessly from IPv4
Notes: <header>
Slide <number>
12
Apart from the address space problem, there are other major driving factors towards a change in IP. The portable PC is becoming increasingly used and, as IP addresses are for the network connection, not the device connected, a different IP address is needed for every point that a mobile user connects to the Internet.
Networked entertainment brings with it a number of tough requirements including high volumes of data for extended periods. This is often real-time, delay and delay-variation sensitive data, such as audio, voice and motion video; the sudden extra delay of a video frame may mean that it arrives too late for display.
Device control; control of heating, lighting, motors, remote telemetry (reading domestic meters, etc) is a very large market but needs simple, reliable solutions.
Along with reliability is security, there has been much publicity about security breaches and hackers on the Internet; IPv6 must address this problem comprehensively.
Of course, there are millions of installed IPv4 users round the world. It is unthinkable that on one great day, everybody must change their protocol suite on every one of these computers. Instead, there must be a gradual transition, lasting perhaps years, when the two protocols can co-exist.

## Slide 24: IPv6 Addresses
128 bits long - 2128  1038 (which is a lot!)
Unicast
  Provider based
  Similar scheme to IPv4 but deeper hierarchy
  Link local
  Based on MAC address - auto-configuration
  Etc.
Multicast - Identifies a group all of whom should receive transmissions
Anycast - Identifies a group one of whom should receive transmissions
Notes: <header>
Slide <number>
Perhaps the most compelling reason for introducing a new IP was the depletion of the IPv4 address space. Although techniques such as CIDR have extended the life of the IPv4 address space, it seems clear that the continuing exponential growth of the Internet, plus the drive to apply Internet communications at an ever finer granularity ("an IP address for every light-bulb"), will, eventually, exhaust the supply. IPv6 addresses are 128 bits long allowing 2128 addresses which is approximately 1038. Even though the partitioning of the address-space will ensure we are able to use only a fraction of these, it should keep us going for quite a while!
There are three types of address; unicast, multicast and anycast. The latter can be applied to a group of hosts any one of which can provide a service. The idea is that a datagram sent to an anycast address should be delivered to the "nearest" member of the group. Several allocation schemes are possible within the unicast addresses. A couple are described on the next slide.

## Slide 25: Aggregatable Global Unicast Address
Subnet Id
Interface Id
Global Routing Prefix
64 bits
64-n bits
n bits
Managed by “customer”
Identifies “customer”
Assume n = 48
32 bits
16 bits
Managed by ISP
Identifies ISP
(say) 14 bits
18 bits
Managed by RIR
Identifies RIR
Notes: This is the preferred format for unicast addresses.
The Interface ID is always 64 bits – typically this will be constructed algorithmically from an IEEE MAC address.
The GRP identifies the customer (UCL for example). The length of the GRP is not fixed. If, for example, it is 48 bits there can be 248 (about 1014) customers and there are then 16 bits for the subnet id. This allows the customer to allocate up to 216 subnets(!).
The GRP is itself structured though no particular structure is specified. It is expected that GRPs will be allocated by “Regional Internet Registries” RIR like RIPE in Europe. The slide shows an example where the RIR is identified by 14 bits and uses 18 bits to identify each of its ISPs (218 ISPs). This leaves an ISP 16 bits to identify each of its customers (216 customers).
Although it is not required that the routing hierarchy reflects the address allocation hierarchy it will probably do so to some extent. For example, the RIR might allocate a 24 bit identifier to a regional ISP and 32 bit identifiers to each of the local ISPs it serves – each sharing the same 24 bit prefix. The rest of the Internet can then route to the regional ISP using the 24 bit prefix. Routers within the regional ISP then use the next 8 bits to route to a local ISP. One problem with this approach is that a customer which changes its ISP should really change all its IP addresses to reflect the new routing. Fortunately IPv6 “autoconfiguration” makes this relatively painless. (See later).

## Slide 26: IPv6 – “Local” addresses
Link local
  Prefix (10) Padding (54) Interface Id (64)
  1111111010 Zeros Derived from MAC
  Use on a single link – will not be routed
Site local
  Prefix (10) Padding (54) Subnet Id (16) Interface Id (64)
  1111111011 Zeros Local choice Derived from MAC
  Use on a private network (like IPv4 private networks)
  Can be routed locally – not globally
Both schemes support “auto-configuration”
Notes: These formats are important in that they allow simple, isolated IPv6 configurations to work automatically. This is is useful for applications like automated control of domestic appliances.
A system can always work out its link local address and may then use this during “autoconfiguration” in which an IPv6 system “discovers” its IP address. (See later).

## Slide 27: IPv6 Header
Notes: <header>
Slide <number>
The basic IPv6 header is quite simple and is shown in the slide. The "Next Header" field indicates the type of header following this one. This will be either TCP or UDP, or one of the IPv6 "extension headers" which, if included, cover additional facilities such as fragmentation and security.
Flows
The IPv6 header includes a 20-bit "Flow Label". This may be set by a source to identify a flow for which resources can be reserved. It is intended to ease the work of the packet classifier function in a router.
Traffic Class
This replaces the IPv4 “Type of Service” field and may be used to carry the service class codes specified in DIFFSERV.
Fragmentation
This may only be done at source. The necessary fields (offset, identifier etc.) are carried in an extension header.
Security
Two extension headers have been defined; the "Authentication Header" provides packet integrity and authentication, the "Encapsulating Security Payload Header" provides privacy.

## Slide 28: Fragmentation and re-assembly (IPv4)
MTU: e.g. 1500bytes for Ethernet
IP SDU sent as multiple IP datagrams:
  Identifier, MF flag
  Split on 8-byte boundary
Fragmentation: at source or router (not v6!)
Re-assembly: at destination
Each fragment is treated as an individual datagram
Suppose: 2048 bytes of data, MTU: 1496 bytes
Notes: IPv4 datagrams can be up to 65,535 bytes long yet network technologies impose a maximum size on the data units they can carry which is, typically, very much less. For example, Ethernet frames can be no more than 1500 bytes, ATM cells are as little as 53 bytes. The Internet term for this maximum size is Maximum Transmission Unit (MTU). If we are to send arbitrary length IP datagrams over such networks then these must be fragmented and, subsequently, re-assembled.
Four fields in the IP header are used to implement fragmentation; Total Length, Identification, Flags and Fragment Offset. A datagram that has been fragmented must be reassembled before it is delivered. The Identification field, which is chosen by the sender, will be copied into all fragments. This enables the receiver to sort out all the fragments of a particular datagram from all the others it receives. The sender must be careful to ensure that no two datagrams en route to a particular destination use the same identifier. Suppose an IP datagram with 2048 bytes of data has to traverse a network with an MTU of 1496 bytes. Assuming the normal IP header of 20 bytes, the first fragment will contain a maximum of 1496-20 = 1476 bytes of data. The IPv4 rules say that we must fragment on an 8-byte boundary; 1476/8 = 184 r 4 so the first fragment will be 184 x 8 = 1472 bytes. The second fragment will be 2048 - 1472 bytes + 20 byte header = 596 bytes with offset 184.

## Slide 29: Problems with fragmentation
Wastage of resources:
  extra packets generated without knowledge of MTU
TCP header 20 bytes
IP header 20 bytes
2028 byte segment
MTU 1496 bytes
24 fragments, length 1492 bytes
24 fragments, length 596 bytes
1 datagram, length 1368 bytes
49 packets
File transfer: 50,000 bytes
TCP header 20 bytes
IP header 20 bytes
1456 byte segment (1496-40)
MTU 1496 bytes
34 datagrams, length 1496 bytes 1 datagram, length 536 bytes
35 packets
Loss of fragment:
  error recovery in higher layers
  whole SDU must be re-sent
Re-assembly:
  how long to wait for all fragments?
Notes: In IPv4, fragmentation can occur at the sending host or at any router along the path. In fact it is possible that fragments are themselves further fragmented by routers. However, re-assembly always takes place at the destination.Given that each fragment is routed independently, we cannot be certain that all fragments will pass through any particular router and the absence of just one fragment would make re-assembly impossible.
There are some serious problems with fragmentation and re-assembly.
Suppose we transfer 50,000 bytes using TCP and choose a segment size of 2028 bytes. With the TCP header this will give 2048 bytes of IP data. Suppose the smallest MTU on the path to the destination is 1496 bytes. We then have the situation of the example in the previous slide. All but the last segment will fragment for a total of 49 packets. If, instead, we pay attention to the minimum MTU and select a TCP segment size of 1496-40 = 1456 there will be no fragmentation and a total of 35 packets will be sent. The cost of a transmission is normally dominated by the per-packet overheads; making routing decisions, calculating checksums etc. Therefore, sending fewer packets is a highly desirable objective.
Note that, with 2028-byte segments, if a single packet is lost the whole segment is lost and the TCP retransmission will cause 2 packets to be re-transmitted. With 1456-byte segments a single packet lost causes a single packet retransmission.
PTO

## Slide 30: Fragmentation – IPv6
Path MTU discovery
H1 sends IP datagram length 4096 bytes to H2
R2 deletes, sends “Packet too big” message to H1
Message includes packet header + next MTU (2048)
Fragment datagram and send fragment length 2048 bytes
R3 deletes etc….
R1
H2
H1
MTU 1500
MTU 4096
MTU 4096
MTU 2048
R2
R3
Notes: The path from source to destination might involve a dozen routers or more. If a single fragment is lost early along the path then resources are wasted at all the subsequent routers in passing along fragments that must, ultimately, be discarded.
IPv6 bans fragmentation in routers for the reasons discussed above. IPv6 hosts are expected to choose datagram sizes to suit the path to the destination. Ideally this size should be the “path MTU” – the smallest MTU along the path. Hosts are recommended to follow the algorithm in the slide to discover this. The results (e.g. the current path MTU for H1’s network) can be cached but the H1 needs to be prepared to re-learn at any time since paths may vary.
Ideally H1 should make path MTU available to the transport (and higher?) layers so that, for example, TCP can choose a sensible segment size. Failing that H1 will fragment large datagrams.
The “Packet Too Big” message is one of several that can be sent using the “Internet Control Message Protocol” (ICMP)
Note that a similar but slightly cruder mechanism for path MTU discovery can be used in IPv4.
* Why not 2048?

## Slide 31: Getting Started
A host needs:
  An IP address
  The address (network id) of the local subnet
  The IP address of a router
  The IP address of a DNS server
Configure statically?
  Requires expertise
Configure automatically
  Requires protocols
Notes: Slide suggests the minimum information. There might be other information such as default TTL, MTU …

## Slide 32: IPv4 - DHCP
Dynamic Host Configuration Protocol
Host sends DHCPDISCOVER
  Source 0.0.0.0, Destination 255.255.255.255, Port 67
  Random no.
DHCP server responds with DHCPOFFER
  Source ?.?.?.?, Destination 255.255.255.255, Port 68
  Same random no.
  IP address, mask, router address, DNS address etc.
  Lease period
Notes: It is common to run a DHCP server on each subnet. Clients do not need to know the address of this server since communication is broadcast.
Addresses are allocated for a fixed period (lease) after which they may be re-allocated to other hosts. Clients can use the DHCP protocol to extend the lease.

## Slide 33: IPv6 Autoconfiguration
Replaces IPv4 ARP, redirect …
Host constructs “link local” address
Transmit packet to this address (should be no reply)
Multicast “Router Solicitation” message
  Use link local address as source
Router(s) reply includes
  Global network prefix and length
  Router’s Interface Id
Host constructs global address
“Link local” prefix
Interface Id
Global prefix
Interface Id
Notes: <header>
Slide <number>
Autoconfiguration is inherent to IPv6. This should free administrators from the need to worry about configuring IP addresses, masks and default routers in hosts. This is essential in the case of embedded devices using IP. It is also vital when large numbers of addresses must be modified as a result, for example, of moving to a new ISP.
The slide shows the so-called “stateless” autoconfiguration which does not involve the use of a server. (There is also a stateful version which is referred to as DHCPv6). A host begins by constructing a “link local” address. This is an algorithmic process consisting of pre-pending a standard prefix to the local “Interface Id”. The latter is derived through a simple transformation of the local MAC address. The host then tests the local uniqueness of this address by transmitting an ICMPv6 message to it. If a reply is received then the Interface Id must be changed.
Once the link local address is established it is used as the source address in an ICMPv6 “router solicitation” message. This message is multicast to the “all-routers” multicast address to which all IPv6 routers must listen. One or more router will reply with an ICMPv6 “router advertisement” message which will include; a) the global network prefix to use (and its length), b) the router’s interface ID
The host can now use the global network prefix to construct a global IPv6 address. It has also learnt the IPv6 address and interface ID (effectively a MAC address) for each local router.

## Slide 34: IPv4 Network Address Translation
192.168.1.1
192.168.1.2
192.168.1.3
Private IP addresses
Priv. IP
192.168.1.1
192.168.1.1
192.168.1.3
192.168.1.3
TCP port
256
42
42
123
TCP port
94
95
96
97
126.16.5.2
Use private addresses internally
Appear to use “real” addresses externally
Internet
126.16.5.2
Notes: <header>
Slide <number>
Sites with insufficient real IPv4 addresses may use “Network Address Translation” (NAT). There are various forms of this.
The slide shows a common approach which allows several hosts to share a single real IP address. The three hosts have private IP addresses. In order to allow multiple TCP connections simultaneously, the NAT gateway also looks at the source TCP port. This too is mapped in such a way that all concurrent connections have a different source port. The TCP source port will be the destination port in incoming IP datagrams. This is used to index the mapping table and restore the original addresses – which will now be destination address and port.
This is basically a hack. There are a number of problems, for example:
  The source port is transport-protocol specific. If a new transport protocol is introduced, the NAT gateway will have to be modified.
  Some applications, notably FTP, send IP addresses as data and these are subsequently used by the destination to set up a connection in the reverse direction. Clearly this will not work – unless we modify the gateway to know about FTP …
  DNS needs to be spoofed

## Slide 35: Virtual Private Networks
Behaves like a real, independent, physical network
  No access for “outsiders”
  Full access for “insiders”
Motivation
  Cheaper than real dedicated network
  Easier to modify than real dedicated network
  More secure than using public network
Several varieties:
  VLANs, virtual ATM networks, Internet VPNs
Notes: The term “VPN” is used in many contexts. Here we will be mainly interested in VPNs implemented over the Internet, The objective is to give the effect of a private intranet with dedicated routers and links whilst actually using the public Internet infrastructure.

## Slide 36: Internet VPNs
Implemented by “tunnelling”
  Encapsulation of one type of network traffic within another
In this case “IP in IP”
  VPN IP datagrams carried in public IP datagrams
A
D
I
T
P
Normal
A
D
T
P
I
Tunnelling
I
Notes: Normally the IP layer interfaces to a data link or MAC layer whose function it is to carry IP datagrams across the next hop. With tunnelling IP datagrams belonging to the VPN employ IP itself in place of a physical data link or MAC layer.

## Slide 37: Internet VPN - Example
Send packet from HA to HB
128.16.0.12
128.16.1.45
214.16.0.23
128.16.0.1
128.16.1.5
HA
HB
VPN 128.16.64.0/24
DA SA Prot 1. HB HA TCP
2. PS ?? GRE HB HA TCP
3. PS PC GRE HB HA TCP
128.16.0.0/24
Encap./ encryp.
VPN Client
VC
PC
Internet
DA SA Prot 4. HB HA TCP
5. HB HA TCP
128.16.1.0/24
VS
VPN Server
PS
Decryp./ decap.
Central site
Remote LAN
Client and server roles swapped for HB to HA
128.16.64.12
217.139.6.4
Notes: There are several ways of operating a VPN using the Internet as a carrier. The slide shows one example. Suppose HB is a server at the central site on subnet 128.16.1.0/24, HA is a workstation on a remote subnet 128.16.0.0/24.
Initially, VPN client authenticates itself with the VPN server and is allocated an IP address on the VPN (VC = 128.16.64.12)
Suppose HA sends a TCP packet to HB.
  Routing s/w in HA directs the packet to the VPN client.
  VPN client behaves as a router with three interfaces; one to the local subnet, one to the ISP and one virtual interface. Routing s/w directs the packet to the virtual interface which performs encryption and encapsulation. The destination address is now PS; the ISP address of the VPN server at the central site. The protocol is now GRE - the “Generic Routing Encapsulation” protocol. This provides a short header identifying the protocol of the encapsulated packet.
  The new packet is returned to the VPN client which sends it out through PC. Normal Internet routing delivers this packet to the VPN server.
  The VPN server recognises the GRE protocol, performs decryption and decapsulation and passes the extracted packet to the routing s/w.
  Normal routing now delivers the packet to HB.

## Slide 38: Internet VPN - Example 2
192.168.0.3
128.16.1.45
128.16.11.245
128.16.1.5
HA
HB
VPN 128.16.114.7/24
Encap./ encryp.
NAT Router
Internet
128.16.1.0/24
VS
VPN Server
PS
Decryp./ decap.
Central site
128.16.114.7
192.168.0.50
216.15.27.5
Notes: The slide shows a second VPN configuration such as might exist in a home equipped with an ADSL router. Here the VPN function is implemented on a host (e.g. a PC). The next slide shows the changes that would be made to the host’s routing table when the VPN is started. The effect is that packets for 128.16.0.0/16 are routed via a virtual interface where encryption and encapsulation takes place. The encapsulated packet is then sent via the Ethernet interface and ADSL router which also performs a NAT function mapping private IP addresses to the public one (216.15.27.5). Note that the VPN and NAT functions are completely independent.

## Slide 39: Internet VPN – Example 2
Dest. Mask Gateway Interface Metric
0.0.0.0 0.0.0.0 192.168.0.50 192.168.0.3 30
192.168.0.0 255.255.255.0 192.168.0.3 192.168.0.3 30
192.168.0.3 255.255.255.255 127.0.0.1 127.0.0.1 30
Dest. Mask Gateway Interface Metric
0.0.0.0 0.0.0.0 192.168.0.50 192.168.0.3 31
128.16.0.0 255.255.0.0 128.16.114.7 128.16.114.7 1
128.16.11.245 255.255.255.255 192.168.0.50 192.168.0.3 30
128.16.114.7 255.255.255.255 127.0.0.1 127.0.0.1 50
192.168.0.0 255.255.255.0 192.168.0.3 192.168.0.3 30
192.168.0.3 255.255.255.255 127.0.0.1 127.0.0.1 30
Notes: These two host routing tables are derived from the output of the “route print” command. Some detail, including loopback, broadcast and multicast routes has been deleted.
The upper table shows the normal routing: traffic for “self” is sent to the loopback interface (line 3); traffic for the local subnet is sent direct (line 2); traffic for everywhere else is sent via the gateway 192.168.0.50. (The latter also performs NAT but that is a quite separate issue and need not concern us here.)
The second table shows what happens after the host has joined a VPN. This is different from the previous slide in which the VPN was implemented on a router. Three new lines have been added:
Line 2 picks up all traffic for the 128.16.0.0/16 subnet and sends it via an interface with address 128.16.114.7. This is a virtual interface which performs encryption and encapsulates the packet in a new one with destination address 128.16.11.245. This is the address of the VPN server at the remote site.
Line 3 is a “host route”. It picks up only packets for the VPN server and sends them out through the gateway. Without this line encapsulated packets would be picked up by line 2 and encapsulated again …
Line 4 ensures that packets send to the virtual interface loop back correctly.
N.B. This is slightly different from the way Microsoft does it.

## Slide 40: Mobile IP [1]
An IP host moving within a network is not “mobile”
  Traffic can still be routed through the same router
Internet
R1
R2
1
2
3
An IP host moving to another network is mobile (“nomadic”)
  Routing has to change
Notes: <header>
Slide <number>
A mobile device “dialled-in” to an ISP via GSM retains the same IP address no matter where it roams within the GSM world. As far as the rest of the Internet is concerned, the device is always accessible via the ISP’s router just as it would be if it were connected via a “fixed” telephone line. In IP terms, the device is not mobile even though it may move half-way across the globe.
The problem for IP comes when a host moves from one IP network to another and thus becomes accessible via a different router - such hosts are termed “nomadic”. Nomadic hosts need not be connected via wireless networks. A common example is a lap-top plugged in to a LAN at a foreign site

## Slide 41: Mobile IP [2]
Internet
2) MH completes registration procedure with FA.
2)
foreign network
FA
home network
HA
remote network
Host A
3) MH updates HA with its new CoA (i.e. the FA).
3)
4) Host A now tries to contact MH. Packets for MH are
intercepted by HA.
4)
7) The packets from MH to Host A are sent directly from the FN.
7)
1) MH arrives at FN, and locates FA
1)
MH
5) HA tunnels the packets from Host A to the CoA for MH
5)
6)
6) FA de-encapsulates the IP packet and transmits to MH.
IP
IP
IP
Tunneling
Notes: The main problem is that the mobile host (MH) has an IP address belonging to its home network. Thus, any packets sent to MH will be delivered to the home network not the foreign network. Mobile IP solves this by forwarding packets to the foreign network.
When a MH arrives at the foreign network (FN), it must try and locate a foreign agent (FA). This can be done either by making a solicitation for a FA on the FN, or picking up agent advertisements on the FN.
MH also contacts its home agent (HA) to inform it of its new location. HA will now intercept any incoming packets for MH (it does this by spoofing ARP replies on behalf of MH). When HA intercepts a packet for MH it sends it to FA which relays it to MH.
Communication between HA and FA uses IP in IP encapsulation - i.e the packet for HA is carried as data in a packet for FA.

## Slide 42: IPv6 and mobility
No need for “foreign agent”
  IPv6 autoconfiguration allows MH to acquire a “care of” address
IPv6 routers incorporate “home agent” role.
Mobile host may send “binding” message to its correspondent(s)
  home address <-> care of address mapping
Correspondents use care of address
  home address in IPv6 extension header
  Avoids encapsulation overhead
  Avoids “triangular routing”
Notes: <header>
Slide <number>
IPv6 autoconfiguration makes it easy for a visiting mobile host to be allocated a local address. A home router can then be told to tunnel incoming packets to the newly allocated address.
New connections opened by the MH can use the newly allocated address as source. This leads to completely conventional routing.
MH can tell it’s “correspondents” of its care of address. They may then use that address to reach it.