## Slide 1: Internetworking and Integration
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: How do you communicate?
Post
Telephone (land line)
Telephone (mobile)
Email
Internal post
Local Address
Global Address
CO
CL
Notes: Five possible methods of person-to-person communication are shown. Suppose we want to inter-work between them? For example, to make a phone call that results in an email message being delivered. Almost anything is possible but some are much easier to implement than others. We must consider:
Service compatibility:
Telephone services are CO – we make a call and then use it to exchange a stream of short messages. The other services are CL – each message is a separate event separately addressed.
Address (number) compatibility:
Although email and the postal service are both CL, if you put a letter in the post addressed to g.knight@cs.ucl.ac.uk it will not arrive.
Note that addressing schemes must be organised so as to avoid duplicate addresses. This implies an “authority” to allocate addresses – probably through some sort of hierarchical devolution. Some schemes have global scope (e.g. international telephone numbers). Some have local scope (e.g. internal post – “G Knight, Computer Science” is not globally unique).
The two telephone services provide compatible services and share a global addressing scheme, so inter-working is easy. Email and the post provide compatible services but use different addressing schemes. Interworking requires a mapping service between the schemes – “address resolution.”

## Slide 3: How do computers communicate?
Ethernet (IEEE 802.3)
WiFi (IEEE 802.11)
ATM
Internet
LANE
Local Address
Global Address
CO
CL
Notes: Many “network” technologies are available for communication between computers. A few are shown in the slide (LANE is “LAN Emulation over ATM – see later). We can classify them as CO/CL and we can look at their addressing schemes. All the technologies in the slide use globally unique addresses but they do not all use the same scheme.
All the IEEE LANs (plus LANE) use 48-bit MAC addresses which are guaranteed to be globally unique. Each address consists of a manufacturer number (allocated by the IEEE) and a serial number (allocated by the manufacturer). All these technologies provide a similar CL service. Because of these compatibilities we would expect to be able to inter-work between them in a way similar to that realised in mobile/land-line telephone inter-working. I.e. we would hope that an Ethernet station could transmit a frame with an address belonging to a WiFi station and expect it to be delivered.
ATM is a very different from the IEEE LAN technologies; CO service and a different addressing scheme. This makes it much more difficult to inter-work. Imagine trying to design a system to interface a telephone conversation to a series of letters. One solution is to wrap up ATM so that it looks like a LAN to its users – this is the approach with LANE.
“Internet” is quite different from the others. By itself it can do nothing. It must exploit the other technologies to carry it’s datagrams between hosts. Like LANE it “wraps up” other technologies. Unlike LANE it does not try to emulate anything. It is a pure internetworking technology.

## Slide 4: Internetworking Approaches
Similar service, global addresses
Incompatible services.
Emulate
E
E
Incompatible services.
I
I
I
I
I
I
Internet layer
- easy to relay
B
B
- easy to relay
B
- easy to relay
R
R
Notes: The first diagram shows the IEEE approach; you can have lots of different technologies but all share a common, global addressing scheme (which guarantees no address conflicts) and provide a closely similar service. In fact the service – called the MAC service is a simple CL one. It is quite easy to design a device which can receive an item from one network and transmit it on the next. The IEEE terms such devices “bridges”. Nowadays the bridge function is most often incorporated in a box that can inter-connect several networks and is called a “switch”.
IEEE LANs have been so successful that non-IEEE technologies, such as ATM, can be provided with interface software which emulates an IEEE LAN. Once this has been done a standard IEEE bridge function can be used for inter-connection.
The Internet approach is much more general. An abstract internetwork service is defined which can then be implemented (usually by software) on any network technology. Devices can then be designed to relay between these abstract networks (often called IP subnets). These are called “routers” in Internet terminology. There does not have to be a 1-1 relation between real networks and IP subnets. The three networks in the top diagram could be incorporated as a single IP subnet with the internet service being implemented solely at the extreme ends.
Note that interfaces may now have two addresses; a real “physical” address plus an emulated or abstract one.

## Slide 5: Addresses and Routing
Must ensure data delivered to correct host on correct network.
Devices must map destination address -> next hop
  “Forwarding table”
  One entry for every host? Big??
  One entry for every “network”? Smaller
Latter requires “structured” addresses
  Address = Net Id + Host Id
  E.g. 128.16.5.2/16
Notes: The approaches in the previous slide solve the basic incompatibility problems. In each case we end up with an internet (small ‘i’) consisting of many, similar “networks” – even if some “networks” are emulated or abstract. There may be dozens, perhaps hundreds of such networks connected by “bridges” or “routers”. The two services we have considered – the IEEE MAC service and the Internet (big ‘i’) service - both send data units which normally contain two addresses; source and destination. How can the hosts and relay devices combine to use this address information to deliver the data to the correct place? The relay devices must have forwarding tables in which they look up destination addresses in order to determine the “next hop”? A large internet may possess tens of thousands of hosts. We would like to avoid having a separate table entry for each of these. Internet addresses (and telephone numbers and postal addresses) have a structure which makes the identity of the destination network explicit. This means that forwarding tables just need one entry per network – a much more manageable number (this is termed “address aggregation”). The down side of this is that addresses must be allocated accurately and that moving a host to a new network means changing it’s address.
IEEE MAC addresses do not have a useful structure, which is one reason to limit the size of a bridged network. However, it does make it simple to move devices between networks without changing addresses.

## Slide 6: Address Structure
Hierarchical addresses guarantee global uniqueness
www.ucl.com is globally unique
  it doesn’t tell you what its is, where it is, or how to get there.
  tells you who it belongs to
CS Dept., UCL, WC1E 6BT, UK is globally unique
  tells you country, sorting office, delivery round, department
128.16.5.2 is globally unique
  probably tells where it is (128.16 => UCL-CS)
  but suppose host is nomadic ….
Notes: A major reason for using hierarchical addresses is to assist with the management of global uniqueness. A “top level” authority delegates to a number of uniquely named “next level” authorities and this process then recurses. E.g. the Internet naming authority delegates to “country code” authorities such as “uk”. “uk” then delegates to authorities such as “ac” etc. As long as each authority issues names which are unique within its scope then global uniqueness is assured.
Such a scheme may assist with routing and this is the case with postal addresses. However, this need not be the case.
Hosts that move cause particular problems. IPv4 addresses used to tell you where (in the networking sense) a host could be found. Now that hosts may move and attach to different subnets this is no longer the case. (Consider also mobile phone numbers – especially when travelling abroad.)

## Slide 7: The IEEE Transparent Bridge
“MAC Bridge” role – relay MAC frames between LANs
“Transparent”
  Hosts/bridges do not need to know network topology
  Hosts do not need to know location of destination
  Bridges “learn” forwarding tables
Intended to work between any pair of IEEE LANs
B
B
IEEE 802.x
IEEE 802.y
IEEE 802.z
Notes: The MAC bridge “role” is very simple, it just copies a frame from one LAN onto another. Nowadays it is not common to find a box sold as a “bridge”. Instead the bridge role may be found incorporated into devices such as Ethernet switches, wireless ADSL routers etc.
The “transparent” version of the IEEE bridge was designed to work without human intervention; no re-configuration of hosts or addresses, no human input to forwarding tables etc.

## Slide 8: MAC bridge - problems
Interconnection between different LAN types?
  Maximum frame lengths may differ
  Data rates different
  Technology-specific features
Latency
  Store and forward delay
  Different bit-rates prevents “cut-through” between segments
Filtering
  Only relay frames when necessary
  Security – restrict access to LANs
Notes: LAN differences:
  maximum frame lengths are different e.g. Ethernet has a maximum frame size ~1500 bytes, token ring uses a maximum of ~4000 bytes. Generally there is no provision for fragmentation in the MAC layer so there is a tendency to go for lowest common frame size.
  the data rates are different, e.g. Ethernet is 10Mb/s or 100Mb/s, token ring is 4Mb/s or 16Mb/s.
  some LANs have special features which have no equivalents on other LANs, e.g. token ring has priorities and acknowledgements, Ethernet does not.
All this may cause difficulty for bridging.
Bridges also impose a store-and-forward delay. This may be minimised by using “cut-through” – i.e. begin to forward frame on next hop as soon as destination address has been recognised. Cut-through is impossible if LANs operate at different bit rates.

## Slide 9: Why not one big LAN?
Shared medium - traffic increases => contention
Solution – partition into separate LANs
Ultimately – “switched LAN”
  One host per segment
A
B
C
D
A
B
C
D
Br
D
C
A
B
Sw
AB, CD
AB, CD
AB, CD
AC, BD
Notes: As load increases on a shared-medium LAN, contention increases and performance drops.
Often, traffic is localised – however, two transmissions between physically distant pairs of hosts still cause a collision.
Solution: partition the LAN via bridges. Each partition is more lightly loaded than the original LAN.
Ultimately a LAN switch can be employed. This is a multiport bridge – usually with a non-blocking architecture. If there is just one host on each segment then contention is completely eliminated.
Sometimes the motivation is that two geographically separated LANs exist and it is desired to link these. A bridge, or a pair of “half-bridges” linked by a serial line, can achieve this.

## Slide 10: Transparent bridge
Backward learning:
  look for source address
  forwarding table entry in reverse direction
  destination unknown: flood
  frames refresh table entries
X 1
Y 3
X 1
Y 2
BA
BB
1
2
3
2
1
X
Q
P
R
S
Y
BA Forwarding Table
Address Interface
BB Forwarding Table
Address Interface
3. BB learns X reached via 1
2. BA floods the frame on LANs P and R
4. BB floods the frame on LAN S
1. XY, BA learns X reached via 1
7. BA learns Y is accessible through 3
5. YX, BB learns Y reached via 2
6. BB forwards the frame on LAN R
8. BA forwards the frame on LAN Q
Notes: The bridge achieves transparency by operating in promiscuous mode; i.e. it processes all frames whether or not they were addressed to it. (Note that all stations “see” all frames but, normally, they ignore those not addressed to themselves). The bridge can then build up a forwarding table by backward learning. If bridge BB receives a frame with source address X on interface 1 then it knows that interface 1 would be a good place to send any subsequent frames that have X as their destination address. This information is stored as a forwarding table entry. Of course, if it receives a frame with destination address X through interface 1 it can ignore it as the frame is already on the right LAN. If a frame is received for which no forwarding table entry exists it will be flooded on all interfaces except the one it arrived on. [N.B. “flood” is not the same as “broadcast”. A broadcast frame is addressed to all hosts. A flooded frame is addressed to a single host but is flooded because the location of that host is unknown.]
If routes are not refreshed frequently by the receipt of an incoming frame they are timed-out and re-learnt. This allows the bridge to adapt to topology changes and host re-locations.
A certain amount of intelligent filtering is both desirable and possible. Hence it is generally possible for a manager to instruct a bridge to restrict forwarding to a list of known MAC addresses. Note that this is more clumsy than with a router due to the flat MAC address space.

## Slide 11: Loop problem
Problem with flooding strategy
Frame from X arrives at BB via two route
BC
1
2
BA
BB
1
2
3
2
1
X
Q
P
R
S
Confusion!!
Spanning tree algorithm
  Blocks ports to eliminate loops
Notes: The flooding algorithm causes problems if the topology contains loops as a bridge will eventually receive a flooded frame on two of its interfaces with resultant confusion. For example, a frame from host X for an unknown destination will be flooded by both bridges BA and BC. Two copies will eventually appear on LAN R. Bridges BA and BB will see this as a frame for an unknown destination and will forward the frame and so on.
An algorithm which allows bridges to negotiate a spanning-tree has been devised to cope with this problem. The spanning-tree algorithm overlays a spanning-tree on the network and so prevents loops forming. It does this by effectively disabling some bridge interfaces. For example, we might disable interface 3 on bridge A. This fixes the problem but at the expense of introducing sub-optimal forwarding paths, and makes load-sharing impossible.

## Slide 12: Ethernet Switches
Multiport bridge
  Non-blocking architecture
  Simultaneous transmission between any pair of ports
Different speeds on different ports
Single host – full duplex operation – no collisions
Notes: Nowadays only very lightly loaded LANs rely on a single, shared Ethernet segment and CSMA-CD.
For heavier loads Ethernet switches are used – effectively these are multi-port MAC bridges. The network is thus partitioned into separate Ethernets one per port. Recall that a MAC bridge relays frames from one Ethernet to another. These Ethernets are separate; a transmission on one cannot collide with a transmission on another. Ultimately with one host per port there will be no collisions.
A high-performance switch will be able to deal with several concurrent relay operations so that station A on net 1 may transmit to station B on net 2 at the same time as station C on net 3 is transmitting to station D on net 4.
Switches can accommodate different speeds on different ports so 10 Mbps, 100Mbps and 1000Mbps versions may interwork.

## Slide 13: Switch Latency [1]
CRC
Store and forward operation
  Buffer the entire packet
  Check checksum - filter out errors
  Mixed speeds
High latency
Src Ad
Dst Ad
Data
Notes: <header>
Slide <number>
With store-and-forward operation the entire frame is received into memory (the CRC being checked by the network interface card), the forwarding table is refreshed with the source address, the destination address is looked-up in the forwarding table and the frame is queued for subsequent transmission on the appropriate port(s).
The switch latency is the time taken for this process (i.e. the additional time introduced by the presence of the switch). At a minimum it will be the time taken to receive the frame, process it and then start to transmit it. At 10 Mbit/sec the serialisation time for a 1500 byte frame is just over 1 millisecond and the latency must, therefore, be greater than this.

## Slide 14: Switch Latency [2]
Cut-through operation
  Only process the address
  Immediately begin transmission on next hop
  Low latency
Cannot check errors, no mixed speeds
CRC
Src Ad
Dst Ad
Data
Notes: <header>
Slide <number>
In cut-through mode the latency can be reduced by starting to forward the frame on the output port as soon as the source address has been received and processed. This is called cut-through switching and it reduces the latency to the time taken to receive the preamble and addresses - 20 bytes or 16 microseconds (at 10Mbps) plus, typically, 24 microseconds processing delay. It can be reduced further still by not processing the source address - this saves 6 bytes serialisation or 5 microseconds plus typically 20 microseconds processing delay.
However there are several circumstances where cut through switching will not work or is undesirable.
  If the destination port is busy the frame must go into an output queue and so will be store and forward
  Broadcasts will go out on all ports and there is a good chance that at least one of those will be busy - thus most switches automatically go into store and forward mode for broadcasts
  Multicast frames are usually processed in store and forward mode for the same reason, but some switches will attempt cut through mode first
  Frames to unknown destinations (which usually includes the first frame or frames) are flooded and hence processed in store and forward mode
  Source and destination ports must be operating at the same speed.

## Slide 15: VLANS - Virtual LANS
Associate LAN stations according to logical criteria (rather than physical)
  E.g. separate LAN for accounts department
Restrict scope of broadcast and multicast
Ethernet switches can do selective forwarding
  Some LAN stations physically connected but logically disconnected
Flexible configuration to achieve what is desired
Notes: <header>
Slide <number>
The most convenient configuration of switches, backbones etc. may not be the best logical configuration. For example, it might make sense to place all the accounts department’s computers on one LAN and restrict access to it from outside. However, the members of the accounts department may occupy several offices widely distributed throughout an office building making a physically separate LAN costly to install. A VLAN would allow the members of the accounts department to be physically connected to several separate LAN segments but logically connected to a single “virtual” LAN.
This might be done for security reasons. It also serves to restrict the scope of broadcast and multicast frames which would otherwise appear on all connected LAN segments.
Ethernet switches can be configured to implement VLANs by deliberately restricting their forwarding capabilities so that some LAN segments may not communicate with others. Typically this is done by labelling ports as belonging to a particular VLAN. Switches will only forward frames between ports with identical labels.

## Slide 16: Level 2 VLANS - Example
VLAN A  VLAN A 
VLAN A  VLAN B 
Servers are on both VLANs
Could install a router to allow IP-level connectivity
VLAN A
VLAN B
S
S
Router?
Y
X
Switch C
Switch A
Switch B
Backbone LAN with servers
Notes: <header>
Slide <number>
The network above has two VLANs.
LAN segments belonging to VLAN A are distributed between ports on three switches as are those of VLAN B. The switches will refuse to output VLAN A traffic on a VLAN B segment and vice versa. However, traffic belonging to either VLAN may pass through the backbone LAN and switch C so that all hosts may access the servers.
If desired, a router could be installed to provide IP connectivity between the two VLANs. Such a router would not pass LAN broadcast or multicast traffic. In addition, it is generally possible to configure routers to disallow traffic to/from certain hosts or carrying certain kinds of traffic. These features allow a good measure of management control of traffic passing between the two VLANs.
Paths via the router shown on the slide can be quite tortuous. For example when X sends to Y, the packet must pass through switches A, C and B a in order to reach the VLAN B half of the router. It then traces a similar route from the VLAN A half of the router on to host Y. Presumably the network designers were more concerned with a proper separation of the VLANs than with efficiency. If the latter consideration were more important, a different configuration would be needed.

## Slide 17: LAN Emulation over ATM
IEEE MAC service
  CL service
  MAC frames
  48-bit MAC addresses
  Broadcast and multicast
  Promiscuous mode
AAL5 – fragmentation and re-assembly
Set up VCCs as required
Need to map to ATM addresses
Use ATM point-multipoint?
E
E
B
ATM
IEEE 802.x
Notes: A full emulation of a LAN must cover all the features shown in the slide:
  The emulation must either use PVCs or must set up VCCs as required. Once these are set up they can carry CL frames between hosts. AAL5 can be used to fragment frames into cells.
  We will need a set of genuine 48-bit MAC addresses. These are the only addresses LAN MAC interfaces understand. However, ATM interfaces use a different style of addressing. We will need to keep address resolution tables to map between the two. We could keep such a table on a disc at each ATM host – but this would be costly both in hardware and management. A better solution is to have a server on the ATM network which can hold mappings.
  We could emulate broadcast by setting up point to multipoint connections from each ATM host to all the others. However, in a large system this would mean a huge number of connections. Something which scales well is needed.
  Promiscuous mode is essential for bridge operation. Bridges need to receive all frames for which the destination is currently unknown.

## Slide 18: Address Resolution in General
Different technologies use different addressing schemes
Network interfaces may have several addresses
  E.g IP address + MAC address
Address Resolution = Mapping between schemes
ARP – a protocol to handle the mapping
ARP request
  “I know an address x from scheme A. What is corresponding address in Scheme B?
ARP response
  x in scheme A = y in scheme B
Notes: Address resolution arises in several contexts. A common case is mapping IP addresses to MAC addresses. The protocol to do this makes use of the MAC broadcast service. In the case of LANE the problem is to map MAC addresses to ATM addresses. Since ATM does not have an efficient broadcast service an “address resolution server” is used instead.

## Slide 19: Address Resolution - LANE
Not all ATM stations will want to take part in ELAN
Cannot set up VCCs “everywhere”
Something must keep track of membership
Something must record MAC/ATM address mappings
Need a server – “LAN Emulation Server” (LES)
  Answers ARP (“LEARP”) requests
ATM network
B
Notes: LANE (LAN Emulation) is a specification produced by the ATM Forum. It describes a method of emulating Ethernet-type LAN facilities on an ATM network. The reason for using LANE is to the huge number of applications and services that expect a LAN-like, connectionless frame interface instead of the connection oriented cell-stream based interface offered by ATM. The LANE standard is complex and allows many optional ways of working. Only a brief sketch of basic operation is given here.
True IEEE LANs have a broadcast service – sending a frame to “all hosts” in an efficient way. ATM does not have this and, in any case, “all hosts” are probably not taking part in the emulation. Therefore LANE has a server (“LAN Emulation Server” – LES) which tracks which stations are taking part and records their ATM/MAC addresses. A second server (“Broadcast and Unknown Server” – BUS) handles broadcasts.
LANE includes mechanisms for stations to register with the LES and for the LES to learn address mappings. When a station wishes to transmit a MAC frame to another station it will normally set up a duplex VCC to carry the cells (and leave it in place until the traffic between them ceases). To do this it needs to resolve the MAC address to an ATM one. It sends an LEARP request to the LES in order to do this.

## Slide 20: LANE – Transmit Logic
Station maintains:
  a) AR cache, b) List of open VCC/MAC address pairs
Suppose we are sending a frame to dest. MAC addr. M
If (M is in VCC list) {send(VCI, data); return;}
If (M is in AR cache)
{map M->A via cache;}
else
{A = arpReq(M);};
VCI = openVCC(A);
send(VCI, data); return;}
return;
Notes: The slide shows a simplified version of the logic employed and is intended mainly to show how the data structures are employed.
A is the ATM address to which M resolves. We assume that a side-effect of openVCC() is to add the new VCC to the VCC list and that a side-effect of arpReq() is to add an entry to the ARP cache. arpReq() constructs an ARP request, sends it to the LES and receives the response.
send() constructs an AAL-5 frame from the data and sends it on the designated VCC,
Note that both openVCC() and arpReq() involve sending messages and receiving replies – therefore they take considerable time. Consequently the complete process for a new destination would take quite a while and LANE provides a short-cut mechanism (not-shown) to allow transmission via the BUS (see later) in order to allow transmission in parallel with address resolution.
Generally there will be a cost involved in keeping a VCC open. Consequently idle VCCs may be timed out. The corresponding ARP cache entry may be retained so that the VCC can be re-established quickly if necessary.

## Slide 21: LANE – Broadcast and Multicast
B
ATM network
B
BUS
Broadcast and Unknown Server (BUS)
Send frame to BUS (unicast)
BUS does point-to-multipoint
Can also be used whilst waiting for VCC set-up
Notes: The BUS has a point-to-multipoint connection with all stations in the ELAN. A station wishing to broadcast or multicast sends a frame to the BUS which then distributes it to other stations.
There is one LES and one BUS per ELAN. Note that the word “server” in these terms does not necessarily imply a dedicated machine. LES and BUS are logical roles, They may be implemented in the same machine and may, in fact, be implemented in the same box as an ATM switch.
I station wishing to transmit to another for which no VCC yet exists may transmit the frame via the BUS in order to avoid waiting for address resolution and VCC set-up to complete.

## Slide 22: LANE – How to sell it
Manufacturers want it to be easy to adopt ATM + LANE
LANE host support hidden behind NDIS interface
ATM Network
Host
LANE support
ATM h/w
NDIS interface
ATM switches provide LES and BUS roles
Notes: An ATM interface card equipped with LANE support can be provided with (say) an NDIS interface so that it looks exactly like an Ethernet card to host software. This achieves one of the main objectives of LANE – an easy upgrade path.
Manufacturers of ATM switches may include support for LANE by implementing the LES and BUS roles in the switch.

## Slide 23: LANE and the bridge role
Problem: how does A resolve B’s MAC address?
  How is MAC B <-> ATM x mapping learned?
How can L exploit normal bridge behaviour?
B -> A => Br floods
  L updates LES with B<->x mapping
A -> B. Initially LEARP fails => A sends via BUS
  L floods all “unknown” BUS traffic
  Probably B will reply
ATM
Br
IEEE
B
A
x
L
I
Notes: We want to end up with all the MAC addresses on the IEEE LAN mapped to the bridge ATM address x. We must assume bridge role is completely normal – no special allowance for LANE. It is up to the LANE module L to handle the address resolution problem.
Suppose A and B have not previously communicated.
Case 1: B transmits first.
Br will not have A in its forwarding table so it will flood.
L will not have B’s MAC in it’s cache. It updates its cache and informs LES of the B<-> x mapping.
Case 2: A transmits first.
LEARP will fail. A will send via the BUS. L has no mapping for B so floods as does Br and the frame will reach B.
Probably B will reply causing L to learn the mapping and inform the LES.

## Slide 24: The Internet Approach
Link, MAC, Physical – Technology dependent, unaltered
Convergence – encapsulation, address resolution
Common – datagrams, forwarding, fragmentation (maybe)
Transport – end-to-end
R
R
Convergence
Link/MAC
Physical
Internet
Common
Transport
I
I
I
I
I
I
R
R
XXX
YYY
ZZZ
Notes: As noted earlier, the Internet service is an abstract one which can be implemented on any network technology. In the slide the two lowest layers are technology dependent. All that is required of them is that they provide some means of carrying arbitrary data between stations. In fact they may not be single physical networks – a collection of LANs connected by IEEE bridges could be viewed as a single network by IP (see example later).
The next layer, labelled “convergence” implements a mechanism for exploiting a specific network technology to carry IP datagrams. Depending on the nature of the technology this may be simple or quite complex – perhaps involving the setting up and taking down of connections. It will always involve address resolution, in which IP addresses are mapped to technology dependent addresses and encapsulation in which IP datagrams are inserted into technology dependent frames (not necessarily 1-1).
Finally there is a “common” layer which deals with ensuring that IP datagrams are correctly forwarded towards their final destination. Transport protocols such as TCP then use the resulting Internet services to carry their PDUs end-to-end between hosts.
Further information on specific address resolution and encapsulation mechanisms is given later in the course.

## Slide 25: Complicated? – IP View
IP Datagrams
Link Layer Frames
HA Ethernet, HB LANE, Bridge B Ethernet+LANE
HB
ELAN
Br
HA
B
ATM
IP View
HA
HB
Notes: The slide combines a number of concepts from this section. A MAC bridge (B) connects an Ethernet and an emulated LAN which uses the LANE protocol. Host HA is on the Ethernet, HB is on the emulated LAN.
However, none of the underlying complexity is of concern to the “common” layer logic. HA and HB can communicate directly, therefore they can be on the same IP subnet and IP datagrams can be sent directly between them without the need for a router. Thus when HA sends to HB the common layer logic in HA will pass the datagram to the convergence layer giving HB as the next hop*.
The convergence layer will do whatever is necessary to ensure the datagram reaches HB.
* This, of course, is the IP forwarding function and is typically implemented by software within the operating system. Note that if HA has interfaces to several networks then we must also select the correct interface and its corresponding convergence software.

## Slide 26: Complicated? – MAC View
IP Datagrams
Link Layer Frames
HA Ethernet, HB LANE, Bridge B Ethernet+LANE
HB
ELAN
Br
HA
B
ATM
IP View
Br
B
MAC frames
MAC frames
MAC View
HA
HB
Notes: Continuing with the same example, the link layer provides the IEEE MAC service. This neither knows nor cares that its job is to carry IP datagrams. If HA is sending to HB, the MAC layer logic in HA will simply be asked to transmit a block of data to HB’s MAC address and will pass this request to the Ethernet NIC. The fact that there is a transparent bridge between HA and HB is of no concern to HA – this is precisely what is meant by “transparent”!
B must carry out the transparent bridge role (Br) – updating its forwarding table, flooding as necessary etc. In this example it will forward the frame from HA onto the ELAN i.e. it will pass the frame to the module which implements LANE.

## Slide 27: Complicated? – LANE View
IP Datagrams
Link Layer Frames
HA Ethernet, HB LANE, Bridge B Ethernet+LANE
HB
ELAN
Br
HA
B
ATM
IP View
Br
B
MAC frames
MAC frames
MAC View
HA
HB
Br
B
MAC frames
AAL5 frames
LANE View
ATM cells
L
L
Notes: The LANE module (L) in B must perform whatever LANE processing is necessary. For example, it must resolve the destination MAC address to an ATM address which may require communication with the LES. It may also need to request the setting up of an ATM VCC. It will then pass the MAC frame to the AAL5 module which will encapsulate it in ATM cells etc.

## Slide 28: Even more complicated?
HA Ethernet, HB CIPA, Bridge B Ethernet+LANE
ELAN
HA
B
Br
HB
ATM
IP View
HA
HB
R
Fo
R
Fo
IP Datagrams
IP Datagrams
Notes: In this example HB is not on the ELAN. Instead it implements CIPA* - a mechanism for sending IP datagrams directly over ATM. HA and HB cannot communicate directly as they do not share a common link layer. Therefore they must be placed on different IP subnets and must communicate via a router (R). When HA sends an IP datagram to HB its forwarding function will determine R as the next hop and will pass the datagram to the convergence layer asking for it to be sent to R**.
The communication path between HA and R is exactly the same as the path between HA and HB in the previous example. Hence the modules and processing involved will be just as before.
* The CIPA protocol is described in Notes 19.
** Of course, the IP destination address will still be HB’s

## Slide 29: Even more complicated?
HA Ethernet, HB CIPA, Bridge B Ethernet+LANE
ELAN
HA
B
Br
HB
ATM
IP View
HA
HB
R
Fo
R
Fo
IP Datagrams
IP Datagrams
CIPA View
HB
R
Fo
AAL5 Frames
ATM Cells
C
C
Notes: Finally, we look at the R-HB hop. When R receives an IP datagram from HA with IP destination address HB its forwarding function (Fo) will determines that it can be sent directly via the CIPA service. Thus it passes the datagram to the CIPA layer (which is responsible for any communication with the AAS, setting up ATM VCCs etc.*) and thence to the AAL5 and ATM layers.
The crucial thing in analysing examples such as these is modularity. When thinking, for example, about the IP layer you should be concerned solely with IP concepts such as IP addresses, and forwarding. You should not be concerned with, for example, MAC layer objects such as transparent bridges. In this way the complex processing involved in the final example (IP, MAC, transparent bridge, LANE, IP-MAC address resolution, MAC-ATM address resolution, CIPA, IP-ATM address resolution, AAL5 etc., etc.) can be separated out and considered in isolation where they become (relatively!) simple.
* The CIPA protocol is described in Notes 19.

## Slide 30: Summary
“Easy” to interconnect similar networks
  MAC bridge does this for IEEE LANs
    Backward learning, loop problem
Dissimilar networks must be wrapped up so they look similar
LANE – wrap up ATM to look like IEEE LAN
  MAC bridge can now be used
Internet – wrap up anything to look like an IP subnet
  Join up with routers
LAN switches
  Multiport bridge. Reduced contention, increased performance