## Slide 1: Internet Deployment
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: The Global Internet
A collection of networks
No single administration
“Organic growth”
Broadly hierarchical structure
  Core networks (National Service Providers – NSP)
  Transit networks
  ISPs
  Private networks
Autonomous systems
Notes: The Internet has a very loose structure. Its topology is mainly a consequence of perceived commercial need being satisfied by a network service. However, the result is a broadly hierarchical structure with some operators concentrating on providing “core” networks, others concentrating on connecting private users, and still others providing transit between users and the core.
In terms of Internet routing, the highest level entities are “autonomous systems” –collections of networks, links and routers run by a single administration and implementing a single external routing policy. Autonomous systems handle routing internally in whatever way they choose. However, they exchange information with each other via standard routing protocols.

## Slide 3: NAPs, MAEs and Peers
Local ISP
NSP A
NSP B
NSP C
NAP
NAP
Private Peering
Regional ISP
Regional ISP
Local ISP
Users
Local ISP
Notes: The core networks (called “National Service Providers” in the US) compete with each other to carry Internet traffic. They have high bandwidth links between their routers – gigabits and upwards. NSPs connect with each other in two ways:
  Through independent “Network Access Points” (NAPs). These are commercial operations and provide high bandwidth switching between networks. They are generally confined to a small geographical area, e.g. a single building, and consist of high-speed networks such as gigabit Ethernet which host routers belonging to the NSPs. NAPs are sometimes called Metropolitan Area Exchanges (MAE).
  Though private “peering” arrangements. These are direct connections between NSPs.
Regional ISPs are next in the hierarchy. As the name suggests they cover a smaller geographical area than an NSP. In order to provide a service they must connect to an NSP. This may be either direct or through a NAP.
NSPs and regional ISPs need flexibility as well as capacity. They may use ATM or SDH in order to manage their internal capacity between routers.
Local ISPs connect end-users to the Internet. This may be via dial-up (for many private users) or leased line ( for corporate users). Local ISPs may be big (NTL etc.) or tiny (you or me with a few modems and a couple of Linux boxes).

## Slide 4: How the money flows
NAPs charge NSPs and ISPs for their interconnection service
NSPs charge ISPs
ISPs charge their customers
Private peering charges depend on traffic flows
Charges tend to be based on link bandwidth
Differentiated Services (DIFFSERV) make all this more complex …
  Different costs for different service levels
Notes: It is not easy to get details of who charges what to whom – it is all commercially sensitive. In principle anyone could construct a NSP or ISP and negotiate with existing operators to obtain interconnections. Existing operators may or may not welcome the newcomer – it is all a matter or commercial policy.
Peering arrangements are varied. Two operators may simply agree to carry each other’s traffic or there may be payments in one direction or the other. Possibly an operator may agree to carry only certain traffic – based on source or destination for example.
DIFFSERV will make all this more complex as it allows packets to be marked as to how they should be treated (low delay, low jitter etc.). Operators may need to establish service level agreements and accounting procedures to deal with this.

## Slide 5: DNS [1]
Global, distributed name space
Nodes form a tree:
  Hierarchical delegation
Domain:
  single IP network, e.g.: cs.ucl.ac.uk
  multiple IP networks: ibm.com
DNS servers:
  servers for each domain
ac
co
uk
edu
com
gov
fr
us
cs
darhu
ucl
surrey
cambridge
darhu.cs.ucl.ac.uk
Notes: Why do we need names and addresses? In the context of data communications, the answer is that names are that a) relatively permanent and are used by humans and b) addresses are, potentially, changeable and are used directly by communications hardware and software. So, we need a service (much like a telephone directory) that will map between names and IP addresses and this is the Domain Name System (DNS). A heavily pruned portion of the DNS naming tree is shown. Each node (leaf or non-leaf) represents a domain which consists of itself and all the nodes in the sub-tree beneath it. A Fully Qualified Domain Name (FQDN) is a concatenation of the labels on the path from a node all the way back to the root, for example darhu.cs.ucl.ac.uk.
Authority to allocate names is delegated. The authority for a zone is responsible for ensuring that no two sibling nodes it administers have the same name. It is clear that, provided this is done, there will be global uniqueness of DNS names. The top-level domains include the world-wide generic domains (com, org, net, edu etc.) and country code domains (e.g., us for the United States, uk for the United Kingdom, etc.).
Though the DNS name-space and the IP address-space both involve hierarchies, these are completely independent. Because two hosts have similar domain names does not imply they have similar IP addresses and vice-versa.

## Slide 6: DNS [2]
Query to local server:
  iterative mode
  recursive
Authoritative answer:
  from domain server
Non-authoritative answer:
  from cache at local server
Resource Records:
  A
  PTR
  MX
local server
root server
(.com)
remote server
(ibm.com)
www.ibm.com
1
2
3
4
5
6
204.146.18.33
Notes: The solution to the name-mapping problem is to maintain a table mapping names to addresses and to make this available across the Internet. It makes no sense to postulate a single server for the whole Internet, therefore we need a distributed service with multiple servers. The DNS protocol allows hosts to query these mappings and so to map names onto addresses. Local DNS servers hold mappings for local machines and answer queries for these directly. Non local names are passed on to other DNS servers.
There are two different modes in which DNS look-ups can operate. Steps 2 and 3 show the iterative mode; the root nameserver does not answer the query but refers its questioner to a different nameserver. Steps 1, 4, 5 and 6 show recursive mode; the client sees only a request and response, the local nameserver has taken the responsibility of passing the query on. The local nameserver will cache the result of the query so that, next time around, we will see, at most, steps 1 and 6. Some implementations cache results in the client as well. In such cases, there would be no network activity at all for the second and subsequent look-ups. As with all caching strategies, there is a danger that the cached information will become out-of-date, so a timeout is used. In addition to this, nameserver responses always contain a flag to indicate whether they are authoritative - i.e. whether they come direct from a primary nameserver. It is possible for a client to insist in a query that an authoritative response be provided.

## Slide 7: Routing
Autonomous Systems do their own routing internally
  Invisible to other ASs
An “Exterior Gateway Protocol”
  Used to exchange “reachability” information between autonomous systems
AS advertise to their neighbours the ASs that they can reach
  Not obliged to advertise them all
Notes: Over the years there have been several Exterior Gateway Protocols including one which was actually called “Exterior Gateway Protocol”. Currently the favoured Exterior Gateway Protocol is the Border Gateway Protocol (BGP).
Routing within an AS may be quite dynamic and intended to optimise traffic flow in the face of frequent load and topology changes.
Routing between ASs is much less dynamic since topology changes at this level are comparatively rare and route choice often reflects long-term commercial agreements rather than short-term load changes.

## Slide 8: The Internet Approach
Link, MAC, Physical – Technology dependent, unaltered
Convergence – encapsulation, address resolution
Common – datagrams, forwarding, fragmentation (maybe)
Transport – end-to-end
Convergence
Link/MAC
Physical
Internet
Common
Transport
I
I
I
I
I
I
R
R
XXX
YYY
ZZZ
IP Subnet
R
R
IP Subnet
IP Subnet
Notes: As noted earlier, the Internet service is an abstract one which can be implemented on any network technology. We have looked at the “common” aspects of the implementation of the service, now we look at the “convergence” sub-layer that implements a mechanism for exploiting a specific network technology to carry IP datagrams. Depending on the nature of the technology this may be simple or quite complex – perhaps involving the setting up and taking down of connections. It will always involve address resolution, in which IP addresses are mapped to technology dependent addresses and encapsulation in which IP datagrams are inserted into technology dependent frames (not necessarily 1-1).

## Slide 9: IP and the IEEE MAC service
Similar services (CL), frame size big enough
Could be carrying many protocols: IP, ARP, …
  How do we know which?
Ether type field – not always present
  General method for “protocol discrimination”
MAC
CRC
L
IP
IP data
S
MAC Addresses etc.
LLC Header (3 bytes)
SNAP (5 bytes)
SNAP includes 2-byte “type”. 0800 for IPv4, 0806 for ARP, 86DD for IPv6
Notes: MAC frames can carry a variety of payloads; IPv4 is just one possibility. It is important that the receiving system can decide what protocol is carried quickly and unambiguously. “Well-known” numbers are assigned to protocols (0x0800 for IPv4 for example see http://www.iana.org/assignments/ethernet-numbers for a complete list). The original Ethernet frame has a field designed to carry these values. Unfortunately this field is not present in all IEEE MACs, not even in all versions of Ethernet. The mechanism in the slide is a more general (though wasteful) alternative.
The LLC header was designed to do protocol discrimination and is part of the IEEE architecture. Unfortunately it allocates only 8 bits to the job which does not allow for enough protocols. Therefore the field is set to 0xAA which means “see SNAP header”. The SNAP (SubNetwork Access Protocol) has a 16-byte type field which is where the type value is placed. So, the cost of generality is that 8 bytes are used to do the work of 2. Note that this reduces the MTU of an Ethernet from 1500 bytes to 1492 bytes.

## Slide 10: Address Resolution on a LAN
ARP results are cached
  Timeout if not “refreshed”
All hosts learn mapping for requestor
Want to send to 128.16.8.177 Need Ethernet address
128.16.8.177 08:00:20:0d:23:34
128.16.8.78 08:00:20:0d:1b:96
128.16.8.74 08:00:20:0d:2a:3b
128.16.8.135 08:00:20:0d:5a:4b
It’s me! My address is 08:00:20:0d:23:34
ARP req (b/cast) Who is 128.16.8.177?
ARP resp 08:00:20:0d:23:34
Notes: All IEEE LANs support a broadcast service. This is the basis for the LAN Address Resolution Protocol (ARP).
An IP host (or router) begins by knowing the IP address of the host to which it wants to send a datagram (128.16.8.177 in the slide). It broadcasts an ARP request messages which contains the following information (refer to the slide):
“I am IP address 128.16.8.135, Ethernet address 08:00:20:0d:5a:4b. What is the Ethernet address of 128.16.8.177?”
All hosts receive this message and hence learn the address mapping for the requestor – a useful side-effect of ARP. One host recognises its IP address and responds with the information:
“I am IP address 128.16.8.177, Ethernet address 08:00:20:0d:23:34”
The response is not broadcast.
The requestor can now construct an Ethernet frame with destination address 08:00:20:0d:23:34 the data part of which will be an IP datagram with destination address 128.16.8.177.
All mappings are cached so that ARP generally has to be used only for the first datagram sent. However, we cannot assume that mappings will be constant for evermore – a new Ethernet card might be installed for example. Thus mappings are timed out if not refreshed and are subsequently re-learned.

## Slide 11: Classical IP over ATM (CIPA)
H
H
H
AAS
ATM address  IP Address mapping
H
H
H
CLS
PVC  IP Address mapping
PVC mode
SVC mode
IEEE Payload
IP
IP data
L
S
AAL-5
Notes: The basic connectivity architecture for IP over ATM from the IETF is Classical IP and ARP over ATM (CIPA) (RFC2225).
Encapsulation places IP datagram + LLC + SNAP in an AAL5 frame.
PVC mode
  All traffic goes via the CL Server
  Two hops for every transmission
SVC mode
  ATM ARP Server (AAS) used for address resolution
  SVCs set up as needed
  One hop for every transmission
This is referred to as the “Classical” model as it conforms to Logical IP Sub-network (LIS) connectivity model. In the LIS model, all hosts on the same LIS are considered to be directly connected without any router hops. All communication between hosts that are on different LISs must be via a router, even if they are physically connected to the same network.

## Slide 12: Logical IP Subnets
Consider 2 IP subnets on same ATM net
IP rules say packets between them must go via router
Router
ATM
S
D
S does routing as normal
  Use ARP server to get ATM address of router
  Encapsulate and send
Router forwards
Decapsulate
Resolve, encapsulate and send
AAS
AAS
Notes: CIPA treats ATM as a link layer and does not exploit any special features of ATM. In cases where several IP subnets exist on the same ATM network this can lead to unnecessary work.

## Slide 13: Next-Hop Resolution Protocol
Let’s break the rules!
ATMARP server
  Knows mappings for local IP subnet only
NHRP Server (NHS)
  Knows mappings for several subnets
NHS
Router
ATM
S
D
S does routing as normal
  Send to router
  Use ARP server to get ATM address of router
S also asks NHS for D’s ATM address
  Set up VC to D
  Send packets direct to D
AAS
AAS
Notes: The NHRP can be used with all “Non-Broadcast Multiple Access” (in practice VC) networks. This means ATM but also Frame-relay, X.25 etc. The existence of an NHRP Server (NHS) is assumed. This behaves in a way similar to that of an ATM ARP server in CIPA. I.e, hosts register their IP to ATM address mappings and the NHS delivers these mappings on request. The difference is that an NHS may have mappings for several distinct LISs.
Hosts that wish to exploit NHRP need to have a modified routing behaviour. The recommended behaviour is that they begin in “classical” mode. Thus S will determine that D is on a foreign IP network and will perform a routing step which will indicate that packets must be sent via the router – this should work as normal.
At the same time S looks up D’s IP address at the NHS. Assuming D has registered the mapping S will learn D’s ATM address. It can then set up an ATM VCC direct to D and use this to send packets – thus avoiding the router.
(S and D may be hosts but they may also be routers).

## Slide 14: Point-to-point links
Digital circuits
  ISDN links
  Dial-up lines
  ADSL
  ???
Need framing mechanism
  HDLC
  ATM
  ???
Need protocol discrimination
Need authentication?
Notes: Point-to-point links typically provide a duplex, bit-stream. To carry data some kind of framing is required. Traditionally this has been done using HDLC flags. (ATM framing is an alternative).
In principle the links may carry more than one traffic type. Hence there is a need for protocol discrimination. Finally, if a switched service is in use (PSTN or ISDN for example) some sort of authentication and authorisation may be needed before data transfer can begin.
Various mechanisms have been used but the combination of HDLC together with the Point-to-Point Protocol (PPP) predominates today.

## Slide 15: Framing and PPP
Point-to-Point Protocol (PPP) [RFC 1661]
Framing – serial line use HDLC
“Protocol” identifies payload
  IPv4 = 33, IPv6 = 87, BPDU = 49 etc.
User authentication at connection set-up
Set parameters (compression etc.), allocate IP address
01111110
. . .
Flag
Address
Control
Protocol (33 = IPv4)
Data (n bytes)
CRC
HDLC header
. . .
11111111
00000011
00000000
????????
00100001
????????
????????
????????
01111110
Flag
PPP Frame
Notes: Point-to-Point Protocol (PPP) [RFC 1661] provides “a standard method for transporting multi-protocol datagrams over point-to-point links”.
Provides:
Framing – usually HDLC if this is easily available. This would be the choice for dial-up since PC serial ports do HDLC framing and bit stuffing in hardware. In principle the bits in the HDLC control byte can be used to implement an ARQ protocol but this is not normally used.
Protocol identification. PPP typically carries IPv4 but other things are possible
  – IPv6
  - Various PPP control protocols
  - MAC frames for remote bridging etc.
Link management; option negotiation, authentication etc.

## Slide 16: PPP and ATM
IP
IP data
ATM framing (not HDLC) often used on ADSL links
PPP used for
  Protocol discrimination
  Link negotiation and authentication
  IP address allocation
AAL5 used for fragmentation into ATM cells
Use of PPP fits with procedures designed for dial-up
AAL-5
Trailer
P
PPP Protocol
Notes: ISPs have been familiar with PPP from the early days of modems and dial-up Internet. Their authentication and accounting systems are geared to it even when, as in the case of ADSL, there is really no dialing done.
The slide shows the simplest version of this encapsulation (there are several others) called PPPoA VC-Mux. The “VC-Mux” implies that all frames sent on this VCC will be PPP frames, this must be agreed in advance by the two end-points. If any other ATM traffic is present it must use a different VCC. Note that there is no need to use either the HDLC flags nor its header – only the PPP protocol field is included.
[N.B. there is also a standard for PPP over Ethernet which is sometimes used over ADSL].

## Slide 17: Access to the Internet
Requirements
  Framing between ISP and customer
    PSTN? ISDN? ADSL? Cable? Leased line?
  Customer can choose ISP
    By subscription? On demand?
  How are ISPs identified
    IP address? telephone number? Something else?
  Authentication, authorisation
  Accounting: Who? How much?
  Billing:Tariff, Collection
Notes: Packet service
We need a physical layer to provide a digital service. We need link layer framing
Choice and identification of ISP
Competition rules require that the ISP should be independent of the company which provides the physical connectivity. Ideally we would want to allow the customer to have accounts with several ISPs and be able to switch between them on demand – possibly exchanging traffic with several ISPs simultaneously. The way this is achieved will dictate the means of identifying the ISP.
Security, Accounting, Billing
ISP needs to be able to identify the customer and ensure they are entitled to use the service. ISP then needs to account for usage. Technological, and marketing considerations affect the mechanism chosen.

## Slide 18: Asymmetric Digital Subscriber Loop
Uses local loop
  POTS + (typically) 2 Mbps downstream, 512 Kbps upstream
  Frequency-Division Multiplexing
N.B. relative bandwidths - Shannon
Notes: ADSL is an advanced way of exploiting the local loop. The local loop provides an electrical connection between the home and the local telephone exchange. It is a simple two-wire circuit typically using twisted pair cable. Although simple, this technology can have quite high capacity – the actual quantity depending on the quality of the wiring (which may be inversely proportional to its age), its length and the amount of external noise. Typical commercial offerings provide 576K bps to 8M bps towards the home (“downstream”) and somewhat less from the home (“upstream”) - the disparity accounts for the use of “asymmetric” in the name. The basis of the technology is Frequency Division Multiplexing (FDM) which is used to provide three logical analogue channels. The slide shows the spectra used for these channels. Three different frequency bands are allocated with gaps in between to prevent interference. The first band (labelled “POTS” for “Plain Old Telephone Service”) is used for ordinary voice traffic. This is needed so that the local loop can continue to provide a telephone service alongside the ADSL data services. The remaining bands are used for upstream and downstream data traffic. Notice that the downstream band has greater width – as one would expect from Shannon’s theorem due to its greater capacity.

## Slide 19: ADSL – organisation
Physical
Logical
Notes: ADSL provides three analogue channels. We need to provide two functions in the home: a splitter to separate the voice and the data channels and provide a separate physical socket for each; and a modem to enable digital data to be sent over the data channels. There is a similar situation at the telephone exchange where a splitter function diverts the POTS channel to the conventional telephone exchange whilst the data channels connect to a device called a “Digital Subscriber Line Access Multiplexor” (DSLAM). Of course the exchange will be dealing with many (several hundred) ADSL connections each of which must be split and connected to the POTS exchange and the DSLAM.
Deregulation means that there may be DSLAMs from several providers at the exchange site.

## Slide 20: ADSL +Internet – typical approach
Need high-speed link to ISP (PSTN infrastructure too slow)
Need switching between ISPs
Use ATM?
Notes: How should we make the connection from customer to ISP? We cannot use the PSTN infrastructure as it provides 64 Kbps circuits at best. An ATM network is one solution since it can have plenty of capacity and allows VCCs to be switched between ISPs as required. Unfortunately VCC switching is not widely deployed. Consequently the VCCs are “permanent virtual circuits” (PVC) that are set up when the customer subscribes to the service and are left in place. These PVCs terminate at a so-called “Layer 2 Tunneling Protocol Access Concentrator” (LAC). A single duplex PVC is established from each home system to the LAC. There is a single PVC from the LAC to each ISP – so traffic from several customers is multiplexed on a single PVC. PPP does not support multiplexing so, between the LAC and the RAS, PPP frames are carried in another protocol (the Layer 2 Tunneling Protocol – L2TP) which includes a “Session Id” field in its headers. Session Ids are used to distinguish traffic belonging to different users.
In the slide we show one LAC and one DSLAM; in practice one LAC would support several DSLAMs (roughly speaking we need one DSLAM at each local telephone exchange).

## Slide 21: ADSL + Internet – the LAC
Duplex PVCs from customers to LAC
Duplex PVCs from LAC to ISPs
LAC authenticates customers
  Customer names include ISP name
  E.g. knight1234@btinternet.com
LAC “extends” PPP connection to ISP
  PPP connections multiplexed in L2TP
LAC relays data between customer and ISP PVCs
Notes: When a customer’s equipment wishes to begin communicating (typically at boot time) it initiates a PPP connection to the LAC - there is no need for it to do anything to establish ATM connectivity, it simply uses the existing PVC. During PPP set-up, the home system authenticates itself to the LAC identifying itself with a name of the form <username>@<ISP domain name> – for example knight1234@btopenworld.com. A user may have several such names registered with the LAC, each one corresponding to a different ISP. Assuming the proffered name matches one of these, the LAC “extends” the PPP connection to the appropriate ISP “remote access server” (RAS) using the already established PVC (and L2TP). This allows limited flexibility to the user who, by choosing the appropriate name can select from amongst several ISPs with which they are registered.
[Note that the “home PCs” shown could just as easily be routers providing access to a home network.]

## Slide 22: ADSL + Internet - Summary
ATM PVCs provide “link” between customer and ISP
LAC allows PVCs to be “switched” between ISPs
PPP used for protocol identification authentication and IP address allocation
PPP
AAL5
ATM
ADSL
ATM
ADSL
ATM
PHY
ATM
PHY
ATM
PHY
PPP
AAL5
ATM
PHY
PC/Router + Modem
ATM switch in DSLAM
LAC
ISP RAS
IP
IP
AAL5
L2TP
L2TP
AAL5
Notes: The protocol stacks show the situation once everything is set up correctly. During set-up, the customer’s system negotiates with the LAC. At that point, the PPP and AAL5 layers terminate at the LAC. After negotiation they are “extended” as shown in the slide.

## Slide 23: ADSL Example 1
Notes: This information was taken from the status screen of an ADSL router.
For information (not examinable).
G.dmt – denotes the standard which specifies details of the modulation in use.
-38 dBm/Hz - Engineers often express power as a ratio with 1 milliwatt and then convert to decibels. In this case the power has first been divided by the bandwidth to give a measure of the average power across the frequency range.
SNR Margin – ADSL modems can vary their power and will raise it in the presence of noise. The SNR margin is target ratio the modem tries to maintain.
Line Attenuation – the ratio of the power of the transmitted signal to the power of the received signal. So 30dB = 10log10(x) => x = 1000. So only one thousandth of the signal survives.

## Slide 24: ADSL Example 2
Notes: The slide shows configuration information from an ADSL router.
Notes
1. The VPI/VCI numbers identify a PVC from customer to LAC and seem pretty standard in the UK. Of course, it does not matter that everyone uses the same numbers VPI/VCI have only local scope.
2. Service category is UBR, CBR is also selectable – though I doubt the service would support it.
3. Encapsulation identifies the standard used to send IP over ADSL and is one of several possibilities. PPPoA VC-MUX implies PPP frames are carried in AAL5 over ATM. The “VC-MUX” implies that, if protocols other than PPP are to be carried then a distinct VCC should be used.
4. MRU/MTU Maximum Receive/Transmit Unit – specifies the maximum size of IP frames that can be carried.
5. MSS I think this is a hack to modify the MSS in TCP SYN packets to a value suitable for the PPP MTU.
6. Authentication is in use and the CHAP protocol is employed.

## Slide 25: Quality of Service - Questions
How can we classify application QoS requirements?
Can we specify useful service classes?
What mechanisms exist to help such applications?
How can we communicate application requirements to the network?
How can we ensure customers pay for enhanced priority?
Notes: The basic Internet service has very simple characteristics.
  Guarantee of delivery: None (best effort service)
  End-to-end delay: Variable and un-bounded
  Throughput: Whatever is available
  Sequenced delivery: No
  Duplicate detection: No
Although this seems poor, it turns out to be fine for traditional data communications applications like file transfer, WWW access, etc. These applications do require guaranteed, sequenced, delivery without duplicates. Fortunately, these features can be provided by employing TCP as an end-to-end transport protocol.
Some newer applications have tighter timing constraints; “streaming” applications such as live video are examples. The basic Internet service is not well-suited to these applications. A network which can support many different kinds of applications is called an “integrated services network”.

## Slide 26: QoS - Analysis
“Flow” (“Microflow”) – a sequence of packets between applications. Identified by e.g.
  Src/dest IP address + src/dest port
  IPv6 flowid
Per flow QoS requirements (from INTSERV)
  “Guaranteed” – for real-time streams
    Specified max. delay and jitter, assured bandwidth
  “Controlled load” – for “adaptive” real-time streams
    Protected from congestion
  “Best effort”
    Normal Internet
Notes: INTSERV was a major IETF project aimed at adding QoS selection to the Internet. The concept of a “flow” was identified and the broad QoS requirements of flows were analysed. As a result, three QoS classes were specified:
The “best effort” class is simply the standard Internet service. It is considered suitable for so-called “elastic” applications – those with weak timing constraints – file transfer and email for example.
The other classes are for “inelastic” applications – those with stronger timing constraints – VoIP and video streaming for example. Some of these can tolerate very little delay and jitter and require constant bandwidth – effectively they require the guarantees offered by a dedicated circuit. The “Guaranteed” class serves these applications.
Other real-time applications are “adaptive” and can tolerate some jitter and bandwidth variation – usually through the use of intelligent buffereing strategies and variable-rate coding. They can work happily on a lightly loaded Internet but must be protected from the effects of congestion. The “Controlled Load” class serves these applications.

## Slide 27: QoS - Implementation
Resources allocated by router: link bandwidth, queuing priority
Guaranteed class
  B/w reserved close to sum of peak flow b/ws (little statistical multiplexing)
  Highest queue priority
Controlled load class
  B/w reserved < sum of peak flow b/ws (statistical multiplexing)
  Low probability of congestion
  Medium queue priority
Best effort class
  Whatever is left
  Starvation?
Notes: Providing the guaranteed service requires routers to make close to worst-case assumptions about competing flows and to reserve sufficient resources that a flow can never be hampered. This is costly as resources may be reserved which may never be used. One would expect to have to pay heavily for “guaranteed” QoS.
The router can marginally over-book the resources available to controlled load flows with the expectation that only rarely will all of them reach peak load simultaneously; i.e. we can do some statistical multiplexing. However, we cannot take this too far or congestion might occur breaking the “lightly loaded” contract.
Best effort traffic takes whatever resources remain. It can be transmitted whenever there is spare capacity on the outgoing link. In practice some minimal resource must be reserved to prevent “starvation” – the complete blocking of best effort traffic by the other traffic types.

## Slide 28: DIFFSERV
Explicit marking of packets
  Type of Service byte  DIFFSERV byte (6 bits used)
  DS byte indicates DIFFSERV QoS class
  Routers implement “per-hop behaviours” for each class
Service-level agreements (SLA)
  For example, customer pays ISP to have all packets from a certain subnet given high priority
  Token bucket (see later)
Packets can be marked by network provider
  No changes to host software
Notes: <header>
Slide <number>
DIFFSERV standards specify classes and corresponding “per-hop behaviours”. The latter indicate how routers should treat traffic interms of queuing strategy and priority, packet drop priority etc.

## Slide 29: DIFFSERV - Example
Ingress Router
  Classify datagrams
  Mark them (DIFFSERV field)
  “Police” them
  (Possibly) “shape” the traffic
Ingress router
Core router
Core router
  Examine DIFFSERV field
  Apply “behaviour”
    Choose a queue
    Force to head of queue etc.
DIFFSERV
domain
Notes: The slide shows a DIFFSERV domain. The “ingress router” (IR) does most of the work as datagrams enter.
Assuming packets entering the domain have not already been assigned to DIFFSERV classes the IR does it on the basis of some combination of fields in the IP and Transport headers. It then sets the class in the IP DIFFSERV field. There will probably be a SLA in force for each class, typically specified by a token bucket. The IR will check conformance with the SLA (“policing”) and may force conformance (“shaping”).
Routers in the DIFFSERV core examine the DIFFSERV field and apply an appropriate “behaviour”. This may mean assigning the datagram to a particular queue or pushing itto the head of a queue for example.

## Slide 30: Burstiness
Consider a buffered switch or router
  Mean packet size 1000 bytes,  = 1000,  = 1500
M/M/1 – mean no. in sys. 2, mean time in sys. 2ms
100ms
900ms
1000 packets
100
667
1000
850
Packets
ms
Notes: The slide shows the dramatic effect that burstiness of a flow can have on delay and buffering requirements. In both cases the load is the same – a mean rate of 1000 1000 byte packets per second.
  With M/M/1 assumptions the buffering requirement is modest with a correspondingly modest delay.
  With a very bursty traffic pattern we see that the output process will be overwhelmed and that a lot of traffic must be buffered. The buffering requirements and delays are 2 orders of magnitude greater than with the comparatively “smooth” M/M/1 traffic profile.
The second flow is much more costly to handle. The switch or router must either allocate much more buffering to the flow or it must reserve much more capacity on the output side – i.e. it must increase . Because of this we would expect a customer that insists on generating the second type of flow to have to pay more. Alternatively, it is in the customer’s interest to spread the bursts over a longer period so as to smooth the traffic and save some money. This is known as traffic shaping.

## Slide 31: Traffic shaping
Source (e.g. video CODEC) produces bits at a variable rate
Shaper “smooths” the traffic
  Buffering => some traffic delayed a bit
  Playout buffer restores timings
Smoothed traffic should encounter fewer queuing delays and less packet loss
Source
Shaper
Byte/s
Byte/s
time
time
Notes: The slide shows the principle involved. Essentially we have a trade-off; the shaper will delay traffic during a high-bit-rate period but it does it in a controlled way. Ideally we will be able to predict the maximum delay. This will enable us to implement a “playout buffer” at the receiver which will allow the original timings to be restored.
If the network knows the “shape” of the traffic then it should be able to allocate resources which ensure there is enough buffering and link capacity. Without the shaper the traffic would be subject to unpredictable queuing delays (and possible congestion loss) making it much more difficult to restore the original timings.
One complication, glossed over in the diagram, is that the source data is packetised – so the rate curves are not really smooth.

## Slide 32: Leaky Bucket Shaper
Source
Packets buffered
Packets transmitted to give constant byte rate
Implementation
Source
Shaper
Bytes/s
Bytes/s
time
time
Bytes arrive at a varying rate
Bucket holds up to b bytes
Bytes leave at a constant rate r bytes/sec
Model
Notes: The so-called “leaky bucket” is one approach. Conceptually, bytes arrive in a bucket at a varying rate and “drip out”at regular intervals as long as the bucket is not empty. (This does not exactly correspond to the physics of a leaky bucket!). If a packet arrives when the bucket is full it must be discarded. The parameters of the leaky bucket must be carefully chosen with respect to the source so that this is a rare event. In the worst case, the system imposes a delay equal to the time it takes the bucket to drain – approximately b/r sec.
The implementation only approximates the model because it has to deal in packets rather than bytes. Thus, if a packet of l bytes is to be transmitted we must wait l/r sec before beginning the transmission of another packet. This does not necessarily mean that the packet transmission time is l/r sec. If the capacity of the output link is C bytes/sec we must have C  r – i.e so we may use only a portion of the capacity. Hence the packet transmission time will be l/C. Despite the packetisation, the delay bound – b/r - remains approximately true.
This is simple to implement and to model, and it produces a very smooth output profile. However, it might be that the network is actually capable of handling a higher rate for a short period until a burst has been cleared. The leaky bucket model does not exploit this possibility.

## Slide 33: Token Bucket Shaper
Packets arrive at irregular intervals
Source
Packets buffered
Packets transmitted provided tokens are available
Implementation
Tokens arrive at r bytes/s
Bucket holds up to b bytes
Departing packets consume tokens
Model
Source
Shaper
Bytes/s
Bytes/s
time
time
Notes: A token bucket specification has two parameters; the token replenishment rate r, and the bucket size b. Logical tokens drip into the bucket at a constant rate r bytes/s. A packet of length s bytes logically consumes s bytes of tokens when it leaves. If there are not s bytes in the bucket, then the packet cannot be transmitted. When a token bucket is used as a shaper, such a packet would be buffered.
There are two key differences compared with the leaky bucket:
  If the capacity of the output link is C bytes/sec, the leaky bucket shaper will space out the packets to achieve a short-term and long-term output rate of r bytes/sec. However, with the token bucket, provided there are enough tokens available, a burst of packets will be transmitted at C bytes/sec (C  r). Thus, although the long-term rate remains r bytes/sec, the short term rate can rise to C bytes/sec – so the smoothing is less severe.
  If there is a pause in packet arrivals then the bucket fills - but only until it contains b bytes of tokens. Nevertheless, this means that the source acquires credit during an idle period which can be used when the next burst comes along.

## Slide 34: Token Bucket Shaper (2)
We may wish to allocate only a fixed portion of the output link capacity – e.g. 10Mbps on a 1Gbps link
Simple! Follow the token bucket with a leaky one!
Token bucket (b, r)
Leaky bucket (b, R)
Link capacity C
C  R  r
Burst emerging from TB now transmitted at an average rate of R bytes/sec
Notes: We may want to ensure that a particular traffic class does not exceed a certain proportion of the output capacity. This can be achieved by following the token bucket by a leaky one.

## Slide 35: Token Bucket Shaper Example
Time 0 1 2 3 4 5 6 7 8 9 10(sec)
Arr. | 0 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 0 | (Mb)
Dep. | 0 | 3 | 2 | 1 | 0 | 0 | 0 | 0 | 3 | 1 | (Mb)
Bucket 2 3 1 0 0 1 2 3 3 1 1 (Mb)
Buffer 0 0 3 1 0 0 0 0 0 1 0 (Mb)
p = 6MBps, r = 1MBps, R = 3MBps, b = 3MB
(Assume new tokens are added at the start of each interval)
Input Output
Rate (MBps)
Time (sec)
Notes: In the slide p is the peak rate at which the source generates bursts of data. The table shows data volumes in MB at one second intervals. It is worth following this example carefully!
(We assume that the output is determined by the number of tokens available at the start of each interval and that this includes the new tokens that will arrive during the interval. E.g. there will be a total of 3+1 = 4 tokens available at the start of the interval (1,2).
For example, in the interval (1,2) 6MB arrive at the peak rate (p) there are 3MB of tokens at the start (b) and 1MB arrive (r). Potentially we can transmit 4Mb therefore. However we are limited by the output rate (R) of 3MB/s so we can only transmit 3MB. This leaves one token and 3MB in the buffer.
In the interval (2,3), although there are 3MB buffered and R = 3MBps, we can only transmit 2MB because we are constrained by the token availability (1 at the start and 1 which will arrive).
The graph illustrates the smoothing of the output compared with the input.
Note that this is “shaping” not “policing” – packets are buffered not discarded.

## Slide 36: Token Bucket Shaper Example (2)
Long-term: input rate  output rate  r
Short term:
  output rate > r (1,2) or output rate < r (5,6)
  input rate > r (1,2) or input rate < r (2,3)
2
4
6
8
10
2
4
1
3
5
6
7
8
9
10
Input Output Tokens received Bucket
Time (sec)
Volume (MB)
Notes: The slide gives a different view of the previous example, this time concentrating on volumes rather than rates.
We can see that the input and output rates (i.e. the slopes of the lines) vary above and below the (constant) token rate. The output rate may be constrained by:
  The absence of data to transmit (5,6)
  The lack of sufficient tokens (2,4)
  The output capacity (R) (1,2)

## Slide 37: Token Bucket Policing
Switch/router checks source for conformance with TB
No input buffer. If not enough tokens:
  Discard or
  Forward but mark as “vulnerable”
May still have an output buffer (i.e. LB)
  Constrain output rate to R bytes/sec
Yes – buffer packets for output at R bytes/sec
Source
TB (b,r)
Enough tokens in bucket?
No – mark or discard
Notes: The second use for a token bucket is in a router or switch that needs to “police” traffic. This is likely to be necessary as the network will have offered QoS guarantees on the basis that traffic conforms to a specification which includes the parameters of a token bucket. We would expect that the source will have shaped its traffic to conform to the same parameters (and so eliminate the extremes of “burstiness”). However, if the source cheats then the network needs to detect the cheating and act.
When used for policing there is no input buffer. If a packet arrives and there are not enough tokens then either the packet will be discarded or it will be marked as “vulnerable” and forwarded. Vulnerable packets will be prime candidates for discard should congestion occur downstream. Their service class will likely be changed to “best effort”. [In practice there would need to be some flexibility since timings are never 100% accurate.]
The slide shows a leaky bucket filter after the TB. This is not strictly necessary and packets could be transmitted at the link rate.

## Slide 38: Token Bucket - Arithmetic
In t sec rt tokens arrive. Thus, if bucket is full at the start we can use b + rt tokens in time t.
  Basic conformance constraint: for any interval of length t we must transmit < b + rt bytes
How long can we transmit at the max. rate R?
  In tmax we transmit Rtmax bytes, so Rtmax < b + rtmax
  tmax < b/(R-r)
From earlier e.g. r = 1MBps, R = 3MBps, b = 3MB
  tmax < b/(R-r) = 3/(3-1) = 1.5 sec
  We can send up to 3 x 1.5 = 4.5MB in the burst
Notes: Basic conformance constraint:
  “For any interval of length t we must transmit < b + rt bytes”
Note this is for any interval no matter how big or how small.
If t is big we can ignore b and the constraint is approximately:
  “For any interval of length t we must transmit < rt bytes”
i.e. the long term average rate is simply r.
The slide shows how the constraint imposes a limit on how long the peak output rate R may be sustained.
[Note, as usual, that these relations are approximate as we have taken no account of packetisation.]

## Slide 39: Token Bucket Arithmetic (2)
Suppose t sec burst arrives at peak input rate p byte/sec
Must be enough tokens available so pt < b +rt
  Thus t < b/(p-r). So burst size B < pb/(p-r) bytes.
If p > R > r we will have an output queue
Time T to transmit B bytes at R bytes/sec T =
So delay imposed is approx. bounded by b/R
In the example, maximum delay  3/3 = 1 sec.
Notes: The calculation in the slide shows that the delay to a flow conforming to a token bucket (r,b) with an output rate R is approximately bounded by b/R. This remains true whether R represents a reserved share of line capacity or its full capacity. [Note, as before, that we have not allowed for packetisation.]
Thus we can obtain various combinations of mean throughput, peak throughput and delay bound simply by juggling the two token bucket parameters and the reserved bandwidth. For example, to reduce the delay we can reserve more capacity (make R bigger) for which, presumably, we will pay. Alternatively we can reduce b which means we must apply more smoothing to our traffic.

## Slide 40: Dynamic Routing
Context – within an autonomous system
Metric – some measure of the “cost” of a route
  Hop count
  Delay
  Sum of link costs
  Proportion of bandwidth in use
  Queue lengths
Two basic approaches
  Distance vector – report global view to neighbours
  Report local view to whole network
Issues
  Speed of convergence
  Consistency
Notes: “Dynamic Routing” means a mechanism whereby routers (or switches) exchange information enabling new forwarding tables to be calculated.
The Internet pioneered the use of dynamic routing and there are standards specifying how it should be done. It is up to the management of an AS to decide which, if any, scheme should be used.
Many networks are managed via static routing. The managers prefer the control and stabilitythis offers over the resilience of dynamic routing.

## Slide 41: Distance vector algorithms [1]
Distance:
  hop count, queue length, …
Each node:
  evaluates distance to all other nodes
  distributes information to adjacent nodes
  finds shortest (lowest distance) route to to all other nodes
Distances are always estimates
  Different nodes may make different estimates
Notes: The distance vector in the name is a table, computed by each node in the network, which indicates the “distances” between the node and all other nodes in the network. (In practice this table will probably also include the preferred “next-hop” to each destination. Thus it doubles as a forwarding table). These vectors are transmitted to all adjacent nodes at frequent intervals. “Distance” (the routing metric) can mean a variety of things; hop count, delay, number of packets queued up along the route etc. Once a node has received distance vectors from all its neighbours it can begin to compute a new routing table. In order to do this, the node must also have an estimate of its distance from each of its neighbours. The computation is according to the “distributed Bellman-Ford algorithm” illustrated on the next slide.
The most famous example of this class of algorithm was that used in the original ARPANET. This used the lengths of the queues on the different links as the measure of “distance” and sent out distance vectors every 128 ms.
An example of a distance vector protocol is the Routing Information Protocol (RIP) (RFC2453) used in IP networks.

## Slide 42: Bellman-Ford
1
A
C
B
F
E
D
2
2
1
1
1
3
3
5
5
Notes: In the network shown, the numbers on the links are the metrics observed by the nodes. (In practice all nodes would probably not see quite the same picture but, for simplicity, we will assume that they do). We will consider routing table calculations for node A.
A begins with the metrics it can observe on its local links. Periodically it receives distance vectors from its neighbours. These show each neighbours estimates of the distance to all other nodes. The calculation for routes to node E is shown. Essentially A makes new estimates by adding its local observations to the estimates of its neighbours and chooses the smallest. It can be seen that the route via D is best with a distance of 2. This calculation is repeated for all nodes leading to the new forwarding table. This also provides the information needed to construct the distance vector that must be sent to the neighbours at the next routing update.

## Slide 43: Distance vector problems
A
B
C
D
1
1
1
“Counting to infinity” – bad news travels slowly
Routing tables inconsistent during changes
  Routing loops possible
Solutions possible to ameliorate problems (RIP etc.)
Notes: A number of problems are inherent to distance-vector algorithms
  When the network is large the distance vectors are large and may not fit into one packet. If two or more packets must be sent then there is the danger that one will be lost leading to inconsistency.
  News of changes spreads by one hop at each routing update. Thus there will be times when only a portion of network nodes is aware of the change. There will be an inconsistent view of the “best” route to a destination and this can lead to routing loops
  News of link failure spreads rather slowly. (“Bad news travels slowly”)
This last point is illustrated by considering what happens when the link between A and B fails. Initially, the link between A and B is fine and the forwarding table entries for B, C and D will show delays to A of 1, 2 and 3 respectively. Suppose the link to A from B is now cut. At the next routing update, B will announce the 1 unit delay to A from its current table. B will hear nothing from A but will hear that C has a route to A with delay 2. Assuming that B has by now twigged that its delay along the B-A link is effectively infinite it will be happy to use the path that C apparently has. Since C is one unit away, B now thinks it can get to A with delay 3 via C – etc.
The algorithm can be modified to ameliorate these problems as in the Internet “Routing Information Protocol” (RIP) which is used within small ASs.

## Slide 44: Link-state algorithms
Each node:
  Assesses metric on local links
  Distributes information to all nodes
    Multicast or flooding
  Receives information from all nodes
  Finds lowest cost path to all other nodes
Dijkstra’s Algorithm:
  shortest-path (SP) tree to all other nodes
All nodes shares same information, perform same calculation
  Hence no routing loops
Notes: In distance vector algorithms, nodes send information to their neighbours about their distances from all other nodes. In link-state algorithms, nodes send information to all other nodes about their distances from their neighbours.
The distribution of routing updates is done by flooding. Every node forwards routing updates on all links except those on which the updates arrived. Hop counters or sequence numbers are used to ensure that the process eventually terminates. Although flooding sounds an expensive process when compared with the distance vector method, in practice, this is not the case. Routing updates in distance vector algorithms must be done frequently in order that information about changes can reach all nodes in the network reasonably quickly. Routing updates in link-state algorithms reach all nodes in the network very quickly and so need be much less frequent – say about once every few minutes. A further advantage of the link-state algorithm is that the size of routing update packets is independent of network size – so the algorithm scales well.
Once the routing updates have been received each node possesses complete knowledge of the state of the network and can begin to calculate its forwarding table. If every node has the same information and performs the same calculation then forwarding tables will be consistent.

## Slide 45: Dijkstra’s Algorithm [1]
A
B
C
D
E
5
2
1
1
3
4
A
D
2
A
B
C
D
1
5
3
1
3
More candidates
A
B
C
D
1
5
3
2
Add C to SP tree
A
D
2
B
C
1
A
5
D
3
1
4
Prune and add D to SP tree
A
B
C
D
1
5
3
1
Add candidates
Notes: A semi-formal description of Dijkstra’s Algorithm is as follows:
At the start of each iteration there will be:
  A set of nodes already added to the SP tree. One of these nodes will be the “most recently added node”. The tree represents the shortest paths discovered so far.
  A set of candidate nodes. These might represent shortest paths but we may discover a shorter path as the algorithm proceeds.
  The remaining nodes that the algorithm has not yet encountered.
Each iteration involves two steps:
1) Update the set of candidate nodes. To do this:
  Add all the neighbours of the “most recently added node” to the candidate set and calculate their path lengths
  Prune the candidates. I.e., if any node appears more than once, retain only the one with the shortest path
2) Update the SP tree.
PTO

## Slide 46: Dijkstra’s Algorithm [2]
A
B
C
D
E
5
2
1
1
3
4
E
A
D
2
B
C
1
1
4
5
More candidates
E
A
D
2
B
C
1
1
4
6
Add A
E
A
D
2
B
C
1
1
4
7
No more candidates
E
A
D
2
B
C
1
1
4
8
Add E
Notes: At this point, the candidate nodes represent shortest paths encountered so far. However, one candidate – the one with the shortest path cost amongst all candidates – is special. It will certainly be impossible to reach this node via one of the others at lower cost. Therefore:
Select the candidate node with the shortest path and add it to the SP tree
Iterations continue until all nodes have been added.
In the example, the resulting shortest path tree is used to update the routing table for node B.
The Internet “Open Shortest Path First” routing protocol (OSPF) is a link state algorithm which is suitable for large, complex ASs.