## Slide 1: Network Models, Concepts and Terminology
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Modelling Data Networks
View “communications service” as a “black box”
Service is defined by its interface
  Similar idea to Java objects
  “Service users” make requests (like calling methods)
  Service may generate “indications” (like interrupts)
  “Service provider” implements the black box (like implementing methods)
TCP
IP
Ethernet
ATM
HTTP
Virtual circuit
Serial Line
UDP
Request
Indication
Communications Service
User A
User B
Interface
Notes: Networks are complicated with many different technologies and protocols. Sometimes these are alternatives, sometimes they are complementary. It is useful to have an abstract way of thinking about networks. This should help us to understand how various components can be fitted together. The best-known model is the ISO 7-layer model for “Open Systems Interconnection” (OSI). In the 1980s, OSI was seen as as a set of standards that would grow to replace everything else (Internet included!). It has completely failed in this for a variety of reasons; technical, political and chronological. However, the abstract model remains rather like the smile on the Cheshire cat.
The starting point is a black-box model of a “communicatuions service”. The idea here is the same as that in object-oriented programming. In order to use an object we need to know what its methods are and what they do. I.e. we need to know its interface to the outside world. Exactly the same is true of a communications service. A service user can make a “request” to a service - for example we can ask it to deliver a piece of data to another user. If the service carries out the request successfully. the receiving user will receive an “indication”. (Note that communication services do not always succeed in carrying out requests).
To take a familiar example, when we pots a letter we are making a request to the postal service. When a letter drops onto our doormat, that is an indication from the postal service.

## Slide 3: Confirmed and Unconfirmed
1. Request
2. Indication
Unconfirmed Service
User A
User B
Interface
Confirmed Service
User A
User B
Interface
1. Request
2. Indication
4. Confirm
3. Response
Notes: The ordinary postal service is an example of an “unconfirmed service”; once a letter is delivered, the postal service takes no more interest in it.
Sometimes we would like the postal service to extend its responsibility and to tell us that the letter was definitely delivered into the hands of the recipient. This is an example of a “confirmed service”. The recipient has to tell the service that they have received the indication. This is called a “response”. Eventually the service tells the sending user that all has been completed successfully. This is a “confirm”.
Notice that two users can turn an unconfirmed service into a confirmed one by agreeing between them that the recipient will always send an ordinary letter in reply. The difference, however, is that the responsibility for following this procedure rests entirely with the users. With a confirmed service, the service itself takes the responsibility.

## Slide 4: Connectionless and Connection Oriented
1. DATA Request
Connectionless Service
User A
User B
Interface
2. DATA Indication
2.
“Connect” Service
User A
User B
Interface
1.
4.
3.
2.
“Data” Service
User A
User B
Interface
1.
2.
“Disconnect” Service
User A
User B
Interface
1.
4.
3.
Time
Connection Oriented
Usually, “Data” service is used repeatedly
Notes: The postal service is an example of a “connectionless” (CL) service; each letter posted is an entirely separate event with no special relationship with any other letters sent in the past or to be sent in the future. The IP datagram service which transports all data in the Internet is also a connectionless service.
The telephone service is an example of a “connection oriented” (CO) service. Before such a service can be used to carry voice or data, a “connection” must be set up. The existence of this connection is known both to the users and to the provider of the service. It will be understood that all data sent on the connection should be delivered to the same place. During the data phase there will normally be many data requests. Eventually there will be no more data to send. At that point, one or other user will make a “disconnect” request and the connection will be terminated. CO services are always characterised by these three phases: connection set-up, data transfer and disconnect.

## Slide 5: OSI Jargon
Some services are partitioned into service elements – for example:
  Connection establishment
  Data transfer
  Disconnection
Each service element has a set of service primitives
  Request
  Indication
  Response
  Confirm
Notes: A “service” is somewhat analogous to an “object” in an object-oriented programming language. Service elements correspond to the methods of the object. Request and Response primitives correspond to method calls. Indication and Confirm correspond to interrupts.
Generally, each service primitive has some associated primitives. For example, a “Connection establishment” request would need a parameter specifying the address of the remote party; think of dialling a telephone number.
There may also be some rules of procedure. For example, you cannot use the “data transfer” service element without first successfully using the “connection establishment” service.
A description of all primitives of all service elements complete with parameters and rules of procedure is a complete description of the service. OSI service specifications have precisely this form.
Note that “service element” is often (and confusingly) abbreviated to “service”.

## Slide 6: Unicast, Multicast, Broadcast
Unicast
  One transmitter, one receiver
Multicast
  One transmitter many receivers
  Many transmitters, many receivers
Broadcast
  All stations receive
Limited broadcast
  Range limited to a sub-net
  IP broadcast
Notes: Most traditional data communications is “unicast”.
“Multicast” services send data to a clearly defined set of receivers. Such services are becoming very important for applications such as video distribution and conferencing. Efficient multicast should only send one copy of the data along each link (and use as few links as possible).
“Broadcast” is useful when all nodes have to be accessed – perhaps to ask if any is prepared to provide a particular service. Broadcast can be costly as all nodes have to process broadcast data. “Limited broadcast” confines a broadcast to the locality of the transsmitter.

## Slide 7: Services and Protocols
Service – what it does
Protocol – how it does it
PEs are usually on different systems
Protocol Entities exchange messages (PDUs) in order to implement the service.
The rules they follow are the “protocol”
In order to communicate PEs use an underlying service
Notes: Some mechanism is needed in order to provide a communication service. In practice this mechanism will be a set of rules for sending messages between the two “ends” of the communication. Such rules are called “protocols”; they specify such things as header formats, when acknowledgements should be sent and so on. The processes at each end which implement these rules are called “protocol entities” (PE). The messages sent between Pes are called “Protocol Data Units” (PDU).
Although PEs logically exchange messages directly with each other, in practice they must make use of some other service to carry their PDUs. For example, we have seen that TCP and UDP make use of IP to carry their PDUs.
This leads to the idea of “layers” of communication services. Each layer provides a service. It employs a protocol in so doing and this protocol uses the service provided by an underlying layer to carry its PDUs.

## Slide 8: An example from the Internet
Request for web page
TCP header added
IP header added
Ether header added
Notes: We start with a “request for a web page”. This is a message (in fact a message in ASCII text) generated by a browser like Netscape and directed to a WWW server. The browser software passes this to the TCP layer. The TCP layer is usually software incorporated into the operating system– so “passing a message to TCP” implies a system call.
The TCP layer adds its header including sequence numbers and ports. This completes a TCP “protocol data unit” which can then be passed to the IP software also in the operating system.
IP also adds it header, including IP addresses and so on. The completed IP datagram (an IP PDU) is passed to the Ethernet card. The means of doing this are somewhat system dependent but standard interfaces – e.g. NDIS – do exist.
The Ethernet card can now construct a frame and transmit it.
Assuming the frame arrives successfully it will travel up through the leaves with each layer processing and deleting its header. Finally the original web request is delivered to the WWW server software.

## Slide 9: The End-to-End Argument
WWW access – needs reliable, sequenced delivery
  Use TCP
Voice over IP – needs low delay and jitter
  Use UDP
TCP and UDP are in the “end-systems” (hosts)
We can choose which to use without altering the network
Suppose IP did ARQ error correction …
IP – connectionless, unconfirmed
Good design choice!!
Notes: We have seen that different applications require different kinds of communication services; the WWW requires reliable, sequenced delivery and is tolerant of delay and jitter. VoIP is very sensitive to delay and jitter but can tolerate some data loss. Fortunately, two services, those offered by TCP and UDP, are available to meet these requirements.
The reason we have the flexibility to choose between the TCP and UDP services is that these services are implemented entirely in the end systems. We don’t have to negotiate with the Internet in order to chose between them -it doesn’t care what we do.
Suppose we re-invented the Internet with a view to “improving” the service it gave. For example, we might give it the responsibility of delivering data in sequence and of recovering any packets that were lost. This would be fine for the WWW but hopeless for VoIP.
The “end-to-end argument” says that services should be simple so as to leave as much flexibility as possible to the end-points of a communication (what we have been calling the “users”). The justification is that only the users really know what they need from the communications between them. Any attempt by a service provider to second-guess the users will, surely lead to trouble.
The simple connectionless, unconfirmed service offered by IP is very much in line with the end-to-end argument and is a major contributor to the succss of the Internet.

## Slide 10: The full OSI model
A application N network logical (peer-to-peer) communication
P presentation L (data) link actual end-to-end message path
S session Ph physical
T transport
network
A
P
S
T
N
L
Ph
A
P
S
T
N
L
Ph
N
L
Ph
N
L
Ph
N
L
Ph
N
L
Ph
Notes: The slide shows the full 7 layer OSI model. The functions of the 7 layer are shown in the next slide.
The end-systems or hosts have the full seven layers. In between them there may be several routers (called intermediate systems in OSI jargon). These have only the lower three layers. The Network layer corresponds to IP in the Internet. The Transport Layer corresponds to either TCP or UDP.

## Slide 11: OSI Reference Model
7 application
6 presentation
5 session
4 transport
3 network
2 data link
1 physical
application-specific protocols
data representation and encoding
dialog and synchronisation
message transfer
(and maybe error control, flow control, connection management)
network routing and addressing
(and maybe connection management)
data link control
(framing, data transparency and maybe error control)
mechanical, electrical and optical interface
application- oriented
end-to-end
hop-by-hop
Notes: The OSI referencemodel has 7 layers, numbered 1 to 7 from the bottom up. These layers are:
the application layer (layer 7): application-specific protocols
the presentation layer (layer 6): representation and encoding of data
the session layer (layer 5): end-to-end dialog and application-level synchronisation
the transport layer (layer 4): end-to-end message transfer
the network layer (layer 3): network addressing and routing between end-systems
the data link (or just link) layer (layer 2): link-level control and framing
the physical layer (layer 1): physical connectivity
In the Internet, layers 5-7 are merged; thus the HTTP standard for WWW includes information on how to represent information, how to stop and start communication and so on.
The lower two layers only make sense on point-to-point links. On a LAN we need an extra layer for the MAC protocol.

## Slide 12: The “Network” Abstraction
H
G
H
H
H
Address
Address
Address
Address
Address
Abstract "Network”"
Interfaces have “addresses”
Connectionless operation
  Host or g/w may send a “message” to any other
Connection Oriented operation
  Host or g/w may set up a connection to any other
Abstract network may comprise several “real” networks
Notes: We can view all networks as consisting of a connectivity technology (represented in the slide by the “cloud”) and a collection of hosts or gateways.
  Hosts are computers on which applications run – for example PCs on LANs and WWW servers.
  Gateways are computers which relay data to and from other networks – for example, Internet routers
From the point of view of the “network”, hosts and routers are indistinguishable.
The interfaces between hosts/gateways and the network have addresses. Generally hosts have just one network connection so that the interface address can be thought of as the address of the host. These addresses are technology dependent – i.e. they are understood by the technology of this particular network but would be meaningless to other kinds of network technology. Thus LANs have IEEE 802 MAC addresses, ATM networks have E.164 addresses and so on.
  Networks may offer a “Connection Oriented” service, in which case any host/gateway may set up a connection to any other. In order to do this it uses the address of the remote host or gateway’s interface. This connection may then be used to carry data messages. ATM and Frame-relay networks provide a connection-oriented service.
  Networks may offer a “Connectionless” service, in which case any host/gateway may send a data “message” to any other. In order to do this it uses the address of the remote host or gateway’s interface. The Ethernet LAN provides a connectionless service.
Networks may be built from other networks. The black-box approach is often useful here – i.e. our starting point should be the service the network provides and not how it provides it.

## Slide 13: Access protocols
Between a host and a network
  Used to request a service
  Used to notify incoming messages
  Also known as “signalling”
Mesh-type WANs
  Signalling is between host and local switch
  Connection oriented
    Ask for connection
    Notify connection request
    Negotiate QoS
    Admission control
  Signalling also takes place between switches
LANs
  Access protocol = MAC algorithm
S
S
S
S
H
G
H
H
H
H
S
S
S
Access protocol
H
H
H
Notes: There will be rules for the interaction between host and network – an access protocol.
This is most obvious in CO mesh-type WANs where there is a more-or-less complex negotiation between host and network during connection set-up. The initiating host specifies what it wants – destination address, QoS required and so on – to its local switch. The local switch then negotiates with other switches to determine if the request can be met. The remote host will be contacted to determine if it is willing to accept the connection. All of this host/network communication uses the access protocol and is referred to as “signalling”. Specifically this is “user-network” signalling to distinguish it from “network-network” signalling which takes place between internal switches.
In LANs we can regard the MAC algorithm as an access protocol though, generally there is no explicit network entity taking part in the protocol. Instead, the protocol takes place between hosts.

## Slide 14: In-band signalling
Remote ‘phone signalled - rings
S
S
S
S
S
Caller dials number
Capacity for one voice call reserved and used to carry signals
Maybe no-one answers!
Notes: With in-band signalling the signalling and data share one channel. This means that when signalling is taking place no data can be transferred. The analogue telephone network use in-band signalling. During call set-up a voice channel had to be reserved across the network in order to carry the signalling. In many cases the call set-up failed because the remote subscriber was engaged or not available to answer. This meant that valuable capacity had been reserved but no revenue had been generated. Telephone companies do not like such situations.
A second disadvantage is that, should signalling be required in the course of a connection, data flow must be interrupted to make way for it. The “local loop” between telephone customers and their local exchange still uses in-band signalling – usually by means of tones sent over the voice channel. Signalling during a call – for example notification that there is another call waiting – necessarily obtrudes in the voice call. With ISDN, which has a separate signalling channel, a visual notification of “call waiting” could be given without disrupting the ongoing call.

## Slide 15: Out-of-band signalling
S
S
S
S
S
Signalling network
Data (voice) network
Remote ‘phone signalled - rings
Caller dials number
Signals carried in “common” signalling channel – shared with other calls
Maybe no-one answers!
Notes: Out-of-band signalling provides a separate, dedicated signalling network. Modern telephone systems use this scheme. In effect there is a separate signalling network over which signalling messages are sent. There is no need to reserve voice-capacity channels until it is certain that call set-up will succeed. This reduces the cost associated with failed calls.
In practice the signalling network is multiplexed onto the physical network. Of course the capacity allocated to signalling is wasted when no signalling is taking place. However, since the signalling network carries the signalling for multiple data or voice channels, it can be kept adequately busy. In the ISDN, for example, the “Primary Rate “ interface provides one signalling channel for 30 data channels.

## Slide 16: The OSI lower layers
IS
IS
IS
H
IS
H
H
H
Links
Scope of the Network Layer
Scope of the Transport and higher Layers
Scope of Access Protocol
Scope of the Data Link and Physical Layers
Notes: The OSI lower layers were conceived with a CO mesh-type network in mind – consequently they were never as general as their designers claimed.
  The data link and physical layers were concerned with a single, physical link – a piece of wire or fibre. In particular this was the physical link which connected the user’s host to the local network switch.
  The network layer was concerned with setting up connections across the network. OSI network layer protocols essentially defined an access protocol that a host could use to request a network connection.
  The transport layer just involved the hosts and allowed hosts to enhance the QoS provided by the network to that required by an application.

## Slide 17: The IEEE LAN model
Different MAC algorithms
  CSMA-CD, token passing, etc.
All support the same service
  CL, 48-bit addresses
No MAC layer in OSI model
LLC layer offers OSI DL-service interface
Notes: The OSI lower layer model does not really work for LANs. The IEEE designed a different model for LAN lower layers. This is introduces the MAC layer which encapsulates algorithms like CSMA-CD, Token Passing and so on.
The MAC service is CL. In order to bridge the gap to the CO data link service in the OSI model, the Logical Link Layer was introduced. The idea was to make LANs and WANs look the same at the Data Link level. This should have made it easy to port network layer software between these two environments. In practice this never really happened since LANs developed along the Internet route which was quite happy with a CL Data Link service.

## Slide 18: LLC flavours
LLC1 – connectionless
  Does almost nothing!
  Does allow protocol discrimination
  Field in LLC header indicates IP, IPX, etc.
Data
LLC
IP
X
MAC
CRC
MAC frame carrying LLC and IP
LLC2 – connection oriented
  LAN hosts must set up connections
  Extended LLC header includes sequence numbers etc.
Almost never used
Notes: LLC2 was the CO version referred to above.
LLC1 is a CL Data Link service which adds little to the basic MAC service. Its main contribution is “protocol discrimination”. This is accomplished via a field in the LLC1 header which indicates the “next” protocol. This there is one number which indicates “IP” another which indicates “IPX” and so on. This makes life easy for the software which receives a packet to determine what kind of packet it is and, therefore, what processing would be appropriate.

## Slide 19: Service and Internal Organisation
Like “service”-”protocol” split
  Service – what the network offers to users
  Broadly – CO or CL?
Internal Organisation
  How the network “works”
  Broadly – VC or datagram
“Natural” mappings
  CO goes with VC
  CL goes with datagrams
BUT …
Notes: We should keep in mind the distinction between what a network does (the service) and how it does it (the mechanism).
Often there is a close correspondence between the two. Networks which use VCs internally (e.g. frame relay) fit naturally with a service which has distinct “set-up”, “use” and “disconnect” phases – a CO service. Networks which use datagrams internally (e.g. LANs) fit naturally with a CL service. However, there are exceptions …

## Slide 20: Natural Combinations
Notes: The slide shows some “natural” combinations between mechanisms and services. Note that circuit-switching networks naturally provide a CO service.

## Slide 21: An Unnatural Combination
A
B
H1
Logical network providing CO service
H2
Logical connection
T
S
Datagram operations
Notes: In the slide we suppose that the network is providing a CO service to its customers. Thus H1 and H2 employ an access protocol which includes requests to set up and tear down connections. VCIs are then allocated to each connection. However, the network itself uses datagrams rather than VCs internally. Switches S and T must keep track of the connections that are open and must record the destination address of each. When H1 sends a packet to H2, S looks up H2’s address and constructs a datagram which is sent across the net to T.
CO networks often guarantee sequenced delivery. The datagram core of the net in the slide cannot guarantee this. This means that S and T must deploy a re-sequencing protocol – for example TCP – between them. H1 and H2 do not see this protocol. They see only a CO service with sequenced delivery.
The Timenet X.25 network in the USA operated in this way.

## Slide 22: Another unnatural combination
A
B
H1
Logical network providing CL service
H2
T
S
Virtual Circuit operations
Notes: In this case we start with a network which uses VCs internally but we want to offer a CL service. When switch S receives CL message request from H1 for H2 it notes that T looks after H2 and so sets up a VC to T. This VC can be used to carry data from H1 to H2. Of course there is no need to set up a new VC for each message, the same one can be re-used. Typically, if the flow of messages stops then S and T will disconnect the VC.
This architecture is surprisingly common. Examples include:
  All mappings of IP onto CO network technologies – in particular IP over frame relay and ATM
  The “LAN over ATM Emulation” scheme (LANE) which makes an ATM network look like an IEEE LAN
  Dial-up IP connectivity where the need to send IP datagrams triggers the set-up of a PSTN or ISDN call. In the case of the PSTN, set-up may require human intervention. In the case of ISDN set-up is usually automatic.

## Slide 23: Admission control and policing
Multimedia applications need to reserve resources
  Guarantee minimum throughput
  Guarantee maximum delay
  Guarantee maximum jitter
Resources reserved by signalling
  CO networks – reservations at call set-up
    “Admission control”
  CL networks – reservations apply to “flows”
Network and user must adhere to “contract”
  Limitation on traffic volume and burstiness
  “Policing” – excess traffic may be dropped
Notes: Multimedia applications require more-or-less strict QoS guarantees. They are often “delay sensitive” and need guarantees about the minimum throughput and maximum delay and jitter they can expect. Networks may be able to offer such guarantees provided they know in advance what volumes of traffic they can expect. In fact it turns out that networks need to know not only the average traffic rate but also the “burstiness”.
There has to be a negotiation between the user (in practice the user’s computer) and the network in which the user’s traffic characteristics and the network’s guarantees are agreed. In CO networks this is usually done when a connection is set up. If the requirements cannot be met then the connection will be refused – this is “admission control”. In CL networks resource reservations apply to “flows”. These are sequences of “related packets” – for example all packets travelling between a particular source address/port and destination address/port.
Once a reservation has been made the network will “police” the user – i.e. it will ensure that the average traffic rate and burstiness do not exceed what was agreed. If the contract is broken then the network may start to discard some of thee user’s packets.
There is more on this topic elsewhere in the course.