## Slide 1: The Internet Layer
Graham Knight G.Knight@cs.ucl.ac.uk

## Slide 2: The Internet Approach
Link, MAC, Physical – Technology dependent, unaltered
Convergence – encapsulation, address resolution
Common – datagrams, forwarding, fragmentation (maybe)
Transport – end-to-end
Convergence
Link/MAC
Physical
Internet
Common
Transport
I
I
I
I
I
I
R
R
XXX
YYY
ZZZ
IP Subnet
R
R
IP Subnet
IP Subnet
Notes: In this section we concentrate on the IP layer – the “common” layer shown on the slide. In section 12 we will look at the transport layer which operates end-to-end above the common layer. In section 13 we will look at the convergence layer.
Note that we concentrate on IP v4 which is still the most widely deployed version. IP v6, which actually has several advantages, is not yet widely deployed.

## Slide 3: IP - a Global Network Service
Should be able to “converge” all network technologies
be simple to implement
  => CL service not CO
Have its own (technology-independent) addresses
Have good scaling properties
  Address aggregation
  Partition into management domains
  Dynamic routing
  Traffic filtering
Support different QoS requirements
IP Service!







Not quite yet!
Notes: The Internet IP service satisfies most of what we want:
  It is simple and is easy to carry in almost any network – i.e. the convergence protocols are easy to implement
  It has global Internet addresses which are independent of any particular technology
  It scales well – in particular the partitioning of IP addresses into network and host parts assists with routing, management and traffic filtering.
The main problem is that IP’s simple CL service hides potentially useful features in the underlying networks – in particular, QoS related features. Work is in progress (DIFSERV) to remedy this.

## Slide 4: Internet - Fundamentals
“The internet protocol implements two basic functions: addressing and fragmentation.
The internet modules use the addresses carried in the internet header to transmit internet datagrams toward their destinations. The selection of a path for transmission is called routing.”
(Operation on a single datagram = “forwarding”)
Notes: The text in the slide is from the Internet Protocol specification – RFC791 – which was written down in 1981. RFC791 gives a summary of the functions provided by IP which remains both concise and precise:
Note that the term “routing” should be taken to mean the processes involved in deciding the possible routes to a destination. The term “forwarding” should be applied to the process of choosing the “next hop” of a route for an individual datagram and dispatching the datagram on its way. (This terminology is not always respected).

## Slide 5: Internet – Fundamentals (2)
“The internet modules use fields in the internet header to fragment and reassemble internet datagrams when necessary for transmission through “small packet” networks.”
Fragmentation now thought best done at source
  IPv6 allows it only at source
  IPv4 allows it at source and in routers
Notes: Again, the text is from RFC791.
Later work revealed fragmentation in routers to be problematic and this has been removed from the latest version of IP. This is discussed later.
RFC = “Request for Comments” – a series of documents which started life as discussion documents. Some (by no means all) eventually became “Internet standards”. RFCs have always been freely available online. Several sites maintain a full set, for example: http://www.ietf.org/rfc.html. This open discussion of drafts is regarded by many as one of the key strengths in the development of the Internet.
Most of the Internet still uses IPv4 as described in RFC791. However, a new version – IPv6 – exists and is described in RFC1883

## Slide 6: The Internet
IP subnet
IP subnet
IP subnet
“IP subnets” (“networks”?) connected by “routers”
Routers may be connected by “point-to-point” links
Interfaces generally have IP addresses assigned.
IP subnet may not correspond to one physical network
“Interface” may not correspond to one physical interface
no IP address required
Notes: The Internet approach is described very fully in RFC1122. The world is modelled as a series of IP networks (usually called IP subnets today) interconnected by routers. These IP subnets are a logical concept and do not necessarily correspond one-to-one with real, physical networks such as LANs (though sometimes they do). Hosts are the end-points of communication, they are the computers on which applications such as web browsers or servers run. Hosts are connected to IP subnets. Hosts on the same IP subnet must communicate directly, without the need for routers. Sometimes, two routers are connected directly together via a point-to-point link.
The Internet service is a simple, connectionless one. Internet hosts may transmit PDUs called Internet Protocol (IP) datagrams.
An interface is a place where a computer attaches to a network. For example a wireless network adaptor provides an interface between a host and an IEEE 802.11 network. Hosts typically use just one physical interface. Routers generally have several interfaces. Most interfaces have a single IP address assigned to them. However, sometimes there may be zero or more than one IP address assigned.

## Slide 7: IP Subnets – The Rules
Hosts on same IP subnet share same network ID
Hosts with same network ID must be able to communicate directly
Hosts with different network IDs must communicate via a router
IP Address (32 bits)
Network Id (n bits)
Host Id (32-n bits)
Boundary varies
H
H
H
IP Subnet
H
H
H
H
IP Subnet
H
B
IP Subnets
H
H
H
H
R
Notes: IP subnets are logical concepts. An IP subnet may be 1-1 with a real network but may also encompass several real networks. Also, it is possible to partition one real network into several IP subnets.
IP subnets are defined by the addresses allocated to the interfaces attached to it. All interfaces in one IP subnet must share the same network ID.
Note:
The comments above apply equally if the phrase “IP subnet” is replaced by either “IP network” or IP supernet”. “IP network” and “IP subnet” are now used interchangeably
“Network Id” may sometimes be called “Subnet ID”, “Network Prefix”, “Subnet Prefix” or just “Prefix”.

## Slide 8: Simple Forwarding Algorithm
For hosts with just one interface which only knows about a single router (the “default”):
If destination network id = local network id then“send direct”.
Else “Send to “default” router.”
IP subnet B
IP subnet A
Notes: This is the simplest case. Many LAN hosts are configured like this.

## Slide 9: IPv4 Addresses [1]
32 bits – e.g. 11000000101010000000000010000000
Written as 4 decimal bytes – e.g. 192.168.0.128
To interpret, we need length of network id
  Explicit 192.168.0.128/25
  Mask 255.255.255.128
Allocated in blocks with common network id
  11000000101010000000000010000000
  …
  11000000101010000000000011111111
  Gives an IP network with 128 host ids.
192.168.0.128/25
Must include ALL host ids
Notes: IPv4 address allocations are (ultimately) controlled by the Internet Assigned Numbers Authority (IANA) in the US. Other bodies, such as Réseaux IP Européens (RIPE), control allocation in particular geographical regions. ISPs and backbone network providers get their IP addresses from bodies such as RIPE. Other users get their addresses from their ISP.
IP addresses are allocated to ISPs who then allocate them to customers. Allocations cannot be arbitrary. Blocks must be allocated with a common network id otherwise IP routing will not work.

## Slide 10: IPv4 Addresses [2]
Can be further subdivided. E.g.
  If you own 192.168.0.128/25
  1100000010101000000000001.......
  Could allocate 2 more bits to network id
  192.168.0.128/27 (1000000)
  192.168.0.160/27 (1010000)
  192.168.0.192/27 (1100000)
  192.168.0.224/27 (1110000)
Or
  192.168.0.128/27 (1000000)
  192.168.0.160/27 (1010000)
  192.168.0.192/26 (1100000)
4 subnets
3 subnets
Notes: An ISP or a customer may further sub-divide a block. However, the “common network id” rules must be preserved.
Partitioning addresses in this way is useful to a large organisation who can then operate several “subnets” interconnected by routers. This allows (for example):
  Incompatible technologies to be connected via routers;
  “Firewall” routers to control access to sensitive parts of the network.

## Slide 11: IPv4 addresses - history
0
10
110
1110
1111
network id
host id
network id
network id
host id
host id
multicast (group) address
experimental use
Class A
Class B
Class C
Class D
Class E
No need for explicit network id length
e.g. marston.cs.ucl.ac.uk: 128.16.20.1 (class B)
0
8
16
24
(31)
Notes: Unicast IPv4 addresses were originally allocated from one of three IP address classes, class A, class B or class C. It was possible to identify the class, hence the length of the Network Id, by inspecting the first few bits of the address. One of the main problems with the class-based approach is the inefficiency that can result with class A and class B addresses when the host id space is not fully utilised within a single IP network. The addresses cannot be used by any other IP network that is connected to the Internet. Few networks now rely solely on classes. Instead they over-ride the class by means of a subnet mask or explicit length.
Unicast IPv4 addresses identify one interface connected to the Internet. Hence, a normal host machine (a workstation or a server) typically has only a single IPv4 address and a single network interface.
Multicast uses class D addresses to identify not a single interface, but a group of interfaces.
Class E is reserved for experimental use.
.

## Slide 12: Subnets, Supernets and CIDR
128.16.16.0/20
  10000000000100000001000000000000
  …
  10000000000100000001111111111111
  This is a “subnet” within a class B network (128.16.0.0)
200.16.16.0/20
  11001000000100000001000000000000
  …
  11001000000100000001111111111111
  This is a “supernet” formed from 16 class C networks
    200.16.16.0 through 200.16.31.0
212 host ids
212 host ids
Notes: The class-based scheme is still present in the background and is reflected in the terminology. A network formed by subdividing a single class x network is termed a “subnet”. A network formed by merging several class x networks is called a “supernet”. However, you will often hear all IP networks referred to as “IP subnets”.
The more flexible scheme used today is termed “Classless Internet Domain Routing” or CIDR. Today we assume that the network id length must be stated explicitly in which case routing cannot take place in the absence of this knowledge.

## Slide 13: IPv4 Special Addresses
255.255.255.255 - Limited broadcast.
  If the local network supports broadcast then broadcast the datagram. This is never passed on by routers.
x.x.255.255 – Net-directed broadcast
127.0.0.0 – Loopback (does not go out on net)
0.0.42.6 – Used as source ad. by host which does not know its network id.
0.0.0.0 – Used as source ad. by host which does not know its IP address
Notes: Some IPv4 addresses have special significance. They are used for administrative purposes or for specially controlled transmission, e.g. loopback and broadcast.

## Slide 14: Private IPv4 Address Space
For use by computers not directly connected to the Internet
  Isolated “Intranets”
  Private networks that share a single public IP address via a “NAT” gateway.
    Most home networks do this
Special network ids (RFC1918):
  10/8
  172.16/12
  192.168/16
Not permitted on public Internet
Not forwarded by routers
Notes: These were intended for use in isolated networks not connected to the public IP network. However the shortage of IPv4 addresses has led to their widespread use on private networks in homes or small offices. Here the ISP allocates a single public IP address to the network whilst the individual hosts use private addresses. A mechanism called Network Address Translation (NAT) maps between the private and public addresses as datagrams pass on and off site. (See later)

## Slide 15: IP v4 Datagram Header
vers.
IHL
DIFFSERV
total length
identification
flags
fragment offset
TTL
protocol
header checksum
source IP address
destination IP address
options
options
padding
data
0
8
16
24
(31)
Notes: version: 4 for IPv4, 6 for IPv6
IHL: The length of the IP header in 32 bit words. This is normally 5 but will be longer if any of the options are in use.
DIFFSERV: QoS specification (originally “type of service)
total length: total length in bytes (including the header).
identification and fragment offset: used to implement fragmentation and re-assembly.
flags: bits used to mark fragmentation status.
time to live (TTL): hop count before packet must be discarded.
protocol: a number to identify the protocol that this datagram is carrying – TCP, UDP etc.
header checksum: used to pick up transmission errors that might corrupt header fields.
source address and destination address: IPv4 address of sender of datagram and IPv4 address of destination of datagram, respectively.
options: rarely used (includes source route, record route and timestamp, etc.)

## Slide 16: More Complex Forwarding
“Routing Table” – a logical table in host or router
Columns
  Destination network (Network id and length)
  Next hop IP address
    Sometimes referred to as “gateway”
  Interface IP address
    Needed if machine has more than one interface
  Metric
    A number used for tie-breaks
Destination addresses are tested against each line in the table
  The longest match is chosen
Notes: Although it is convenient to think of a routing “table” that does not mean that a routing table is necessarily stored as an array. It is vital that the time needed to look up a destination and find the next hop address should be as short as possible. Therefore data structures will be chosen which optimise this process.
You can view the routing table on many systems using the command
route print

## Slide 17: A Sample Routing Table
Destination Netmask Gateway Interface Metric
0.0.0.0 0.0.0.0 192.168.0.50 192.168.0.3 20
127.0.0.0 255.0.0.0 127.0.0.1 127.0.0.1 1
192.168.0.0 255.255.255.0 192.168.0.3 192.168.0.3 20
192.168.0.3 255.255.255.255 127.0.0.1 127.0.0.1 20
192.168.0.255 255.255.255.255 192.168.0.3 192.168.0.3 20
224.0.0.0 240.0.0.0 192.168.0.3 192.168.0.3 20
255.255.255.255 255.255.255.255 192.168.0.3 192.168.0.3 1
“Gateway” means “Next-hop address”
Default route
The (single) physical interface
The loop-back interface
Broadcast addresses
Gateway = Interface  “this” subnet
Local subnet route
Notes: This is a (slightly edited) version of what MS-Windows produces when you type route print.
The fact that there are just two addresses in the Interface column means this computer has just two interfaces one of which is the loop-back interface. “Real” traffic will pass through the interface with the (private) IP address 192.168.0.3.
The Gateway column shows the IP address of the “next hop”. This is not the same as the destination address and, in general, will not be found in the IP header.
The local subnet has address 192.168.0.0/24. All hosts on this subnet (e.g. 192.168.0.2) match the third row of the table. Gateway and interface in this row show the same address. This is MS’s means if indicating that this is the local subnet and that the datagram should not be sent via a router.
If the broadcast, multicast and loop-back routes are ignored then just rows one (the default route) and three remain. In fact this table reduces to the simple logic given in slide 8.

## Slide 18: Longest Match
Destination Netmask Gateway Interface Metric
0.0.0.0 0.0.0.0 192.168.0.50 192.168.0.3 21
192.168.0.0 255.255.255.0 192.168.0.3 192.168.0.3 20
128.16.0.0 255.255.0.0 128.16.114.10 128.16.114.10 1
128.16.16.0 255.255.240.0 192.168.0.50 192.168.0.3 1
128.16.11.245 255.255.255.255 192.168.0.50 192.168.0.3 20
Consider destination 128.16.20.5 10000000000100000001010000000101
10000000000100000001010000000101
110000001010100000000000
Row 2 (24 bit)
10000000000100000001010000000101
1000000000010000
Row 3 (16 bit)
10000000000100000001010000000101
10000000000100000001
Row 4 (20 bit)
10000000000100000001010000000101
10000000000100000000101111110101
Row 5 (32 bit)





Notes: The slide shows a slightly more complex table with the broadcast etc. removed. This time there are two interfaces and two routers.
It is usually helpful to work in binary.
The mask in each row tells us how many bits to consider when trying for a match. Thus row 4 requires a 20-bit match (24010 = 111100002) and this is obtained.
Row 3 also matches but only for 16 bits.
Row 1 matches – it always does and counts as a zero-bit match.
Thus row 4 is the longest match and it will be chosen.

## Slide 19: Address Aggregation
IP subnet 128.16.0.0/16 - potentially thousands of hosts
“Rest of the world” needs just one table entry
  All traffic routed via R1
Within 128.16.0.0/16
  One entry for 128.16.16.0/20
  One entry for “rest of the world”
128.16.0.0/16
128.16.16.0/20
128.16.20.0/24
R1
R2
R3
Rest of the world
Notes: The idea of networks and subnets within subnets greatly reduces the size of routing tables. One routing table entry can provide routing information for many thousands of hosts.
Routing may be hierarchical – i.e. traffic for a host in 128.16.20.0/24 would be routed via R1, R2 and R3. However hierarchical routing is not mandated and may be inefficient in some cases. It would be possible for R3 (say) to have a direct link to the rest of the world and for traffic to be routed directly to it.
Although this 3 level hierarchy is useful, the top level is an organisation (UCL-CS in this case) and there is no easy way to aggregate addresses above this level. One might like, for example, for UCL-CS to be a subnet of UCL which would be a subnet of “UK-Academic” etc. One motivation of IPv6 is to allow this sort of aggregation. In order to see what is required, we look, in the next few slides, at the high-level organisation of the Internet.

## Slide 20: Fragmentation and re-assembly (IPv4)
MTU: e.g. 1500bytes for Ethernet
IP SDU sent as multiple IP datagrams:
  Identifier, MF flag
  Split on 8-byte boundary
Fragmentation: at source or router (not v6!)
Re-assembly: at destination
Each fragment is treated as an individual datagram
Suppose: 2048 bytes of data, MTU: 1496 bytes
Notes: IPv4 datagrams can be up to 65,535 bytes long yet network technologies impose a maximum size on the data units they can carry which is, typically, very much less. For example, Ethernet frames can be no more than 1500 bytes, ATM cells are as little as 53 bytes. The Internet term for this maximum size is Maximum Transmission Unit (MTU). If we are to send arbitrary length IP datagrams over such networks then these must be fragmented and, subsequently, re-assembled.
Four fields in the IP header are used to implement fragmentation; Total Length, Identification, Flags and Fragment Offset. A datagram that has been fragmented must be reassembled before it is delivered. The Identification field, which is chosen by the sender, will be copied into all fragments. This enables the receiver to sort out all the fragments of a particular datagram from all the others it receives. The sender must be careful to ensure that no two datagrams en route to a particular destination use the same identifier. Suppose an IP datagram with 2048 bytes of data has to traverse a network with an MTU of 1496 bytes. Assuming the normal IP header of 20 bytes, the first fragment will contain a maximum of 1496-20 = 1476 bytes of data. The IPv4 rules say that we must fragment on an 8-byte boundary; 1476/8 = 184 r 4 so the first fragment will be 184 x 8 = 1472 bytes. The second fragment will be 2048 - 1472 bytes + 20 byte header = 596 bytes with offset 184.

## Slide 21: Problems with fragmentation
Wastage of resources:
  extra packets generated without knowledge of MTU
TCP header 20 bytes
IP header 20 bytes
2028 byte segment
MTU 1496 bytes
24 fragments, length 1492 bytes
24 fragments, length 596 bytes
1 datagram, length 1368 bytes
49 packets
File transfer: 50,000 bytes
TCP header 20 bytes
IP header 20 bytes
1456 byte segment (1496-40)
MTU 1496 bytes
34 datagrams, length 1496 bytes 1 datagram, length 536 bytes
35 packets
Loss of fragment:
  error recovery in higher layers
  whole SDU must be re-sent
Re-assembly:
  how long to wait for all fragments?
Notes: In IPv4, fragmentation can occur at the sending host or at any router along the path. In fact it is possible that fragments are themselves further fragmented by routers. However, re-assembly always takes place at the destination.Given that each fragment is routed independently, we cannot be certain that all fragments will pass through any particular router and the absence of just one fragment would make re-assembly impossible.
There are some serious problems with fragmentation and re-assembly.
Suppose we transfer 50,000 bytes using TCP and choose a segment size of 2028 bytes. With the TCP header this will give 2048 bytes of IP data. Suppose the smallest MTU on the path to the destination is 1496 bytes. We then have the situation of the example in the previous slide. All but the last segment will fragment for a total of 49 packets. If, instead, we pay attention to the minimum MTU and select a TCP segment size of 1496-40 = 1456 there will be no fragmentation and a total of 35 packets will be sent. The cost of a transmission is normally dominated by the per-packet overheads; making routing decisions, calculating checksums etc. Therefore, sending fewer packets is a highly desirable objective.
Note that, with 2028-byte segments, if a single packet is lost the whole segment is lost and the TCP retransmission will cause 2 packets to be re-transmitted. With 1456-byte segments a single packet lost causes a single packet retransmission.
PTO

## Slide 22: Getting Started
A host needs:
  An IP address
  The address (network id) of the local subnet
  The IP address of a router
  The IP address of a DNS server
Configure statically?
  Requires expertise
Configure automatically
  Requires protocols
Notes: Slide suggests the minimum information. There might be other information such as default TTL, MTU …

## Slide 23: IPv4 - DHCP
Dynamic Host Configuration Protocol
Host sends DHCPDISCOVER
  Source 0.0.0.0, Destination 255.255.255.255, Port 67
  Random no.
DHCP server responds with DHCPOFFER
  Source ?.?.?.?, Destination 255.255.255.255, Port 68
  Same random no.
  IP address, mask, router address, DNS address etc.
  Lease period
Notes: It is common to run a DHCP server on each subnet. Clients do not need to know the address of this server since communication is broadcast.
Addresses are allocated for a fixed period (lease) after which they may be re-allocated to other hosts. Clients can use the DHCP protocol to extend the lease.

## Slide 24: ICMP – a little management
Internet Control Message Protocol
Messages for reporting problems
Messages to probe the network
All sent as datagrams
Not all routers and hosts support all messages
Notes: ICMP is the Internet Control Message Protocol. Strictly speaking, ICMP is a separate protocol from IP. However, it shares IP's header format and its messages are routed in just the same way as IP datagrams. It is at the same level as IP in the protocol hierarchy and can be thought of as a sideways extension of IP. The IPv4 version of ICMP is RFC 792. The IPv6 version is actually part of IPv6 itself.
ICMP messages are used mainly to convey information about errors or conditions that require attention. There are many message types, most of which have sub-types indicated by a code field. As an aid to diagnosis, all ICMP error messages include the first 8 bytes of the IP datagram which triggered the error.

## Slide 25: ICMP - echo request
All hosts and routers are supposed to respond to echo requests
Used to implement the “ping” program
Notes: All IP interfaces are supposed to implement the ICMP “echo request” and “echo response” services. These are used by the ping program to probe the network.

## Slide 26: ICMP - time exceeded
Tracing route to haig.cs.ucl.ac.uk [128.16.6.8]
1 1 ms <1 ms <1 ms router [192.168.0.50]
2 38 ms 37 ms 37 ms 78.146.240.1
3 36 ms 35 ms 36 ms 78.151.231.199
4 38 ms 38 ms 37 ms xe-11-0-0-… [78.151.225.37]
5 46 ms 38 ms 43 ms xe-11-2-0-r… [62.24.240.13]
6 38 ms 37 ms 38 ms host-78-144-0…[78.144.0.206]
7 37 ms 37 ms 38 ms host-78-144-0…[78.144.0.204]
8 40 ms 40 ms 38 ms linx-gw1.ja.net [195.66.224.15]
9 39 ms 38 ms 39 ms ae1.lond-sbr4.ja.net [146.97.35.181]
10 38 ms 40 ms 39 ms ….lond-sbr1.ja…[146.97.33.153]
11 38 ms 40 ms 38 ms LMN-LMN1.site.ja.net [146.97.42.62]
12 38 ms 38 ms 43 ms ucl.lmn.net.uk [194.83.102.82]
13 39 ms 39 ms 39 ms 128.40.125.13
14 * * * Request timed out.
15 38 ms 41 ms 39 ms cisco-cs.ucl.ac.uk [128.40.255.30]
16 41 ms 40 ms 40 ms haig.cs.ucl.ac.uk [128.16.6.8]
TTL
4
3
2
1
0
“Time exceeded”
Notes: Most often, the ICMP “time exceeded” message is sent back to a host because a datagram's TTL field has reached zero and it has been discarded by a router. This is exploited by an interesting program called "traceroute" which is available on many systems. Effectively, TTL is a hop counter. Traceroute begins by launching a datagram towards its destination with TTL set to 1. The first router on the path decrements the counter, finds it is now zero and discards the datagram. At the same time it sends an ICMP "time exceeded" message back to the source. Traceroute receives this and prints the source IP address from the ICMP datagram - which will be that of the first router. Traceroute now repeats the procedure with TTL equal to 2 and so discovers the IP address of the second router. By this means traceroute discovers the addresses of all the routers on the path to the destination.
Note, however, that the route may change between one transmission and the next. Thus traceroute does not give quite the snapshot of an IP route that the print-out suggests. In particular, a the RTD for a distant router may sometimes be longer than that for a nearby router. This is probably due to network congestion reducing between the early and late probes.

## Slide 27: IPv4 Network Address Translation
192.168.1.1
192.168.1.2
192.168.1.3
Private IP addresses
Priv. IP
192.168.1.1
192.168.1.1
192.168.1.3
192.168.1.3
TCP port
256
42
42
123
TCP port
94
95
96
97
126.16.5.2
Use private addresses internally
Appear to use “real” addresses externally
Internet
126.16.5.2
Notes: <header>
Slide <number>
Sites with insufficient real IPv4 addresses may use “Network Address Translation” (NAT). There are various forms of this.
The slide shows a common approach which allows several hosts to share a single real IP address. The three hosts have private IP addresses. In order to allow multiple TCP connections simultaneously, the NAT gateway also looks at the source TCP port. This too is mapped in such a way that all concurrent connections have a different source port. The TCP source port will be the destination port in incoming IP datagrams. This is used to index the mapping table and restore the original addresses – which will now be destination address and port.
This is basically a hack. There are a number of problems, for example:
  The source port is transport-protocol specific. If a new transport protocol is introduced, the NAT gateway will have to be modified.
  Some applications, notably FTP, send IP addresses as data and these are subsequently used by the destination to set up a connection in the reverse direction. Clearly this will not work – unless we modify the gateway to know about FTP …
  DNS needs to be spoofed