## Slide 1: Example Technologies
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Introduction
In this section we look at two example technologies
ATM
  A wide-area technology
  Switched virtual circuits
  Connection-oriented service
  Used mainly in large corporate networks
  Used in conjunction with ADSL for broadband Internet
IEEE 802.11 “WiFi”
  A local-area technology
  Shared medium
  Connectionless service
  Used in the home, office, pub etc.

## Slide 3: ATM Networks
Asynchronous Transfer Mode” (ATM)
  Switched technology for mesh-type networks
  Cell-switching, 53-byte cells
    48 bytes data, 5 bytes header
  CO service, neither error nor flow control
  “Integrated Services”
S
H
H
H
H
H
H
H
H
S
S
S
S
H
H
H
H
H
Notes: The technology is built around ATM switches which switch ATM packets – termed “cells”. ATM cells are fixed size – 53 bytes each. A small, local ATM network might have just one switch, large networks consist of a mesh of many switches.

## Slide 4: Design rationale
Integrated services => must control delay and jitter
Small cells minimise store and forward delay
  Small cells => no room for global addresses
    Must be virtual circuit based
Fixed size cells simplify switch design
Low delay/jitter => no error or flow control
Fast switching => no error or flow control
Notes: The rationale for cell-switching was as follows:
  Packet-switching has the ability to vary the capacity allocated to multiplexed streams as demand varies - just what was required.
  Packet-switching suffers from store-and-forward delays at switches. Delay is a problem for interactive traffic such as voice telephone. Store-and-forward delay is minimised if the packets are small.
  If the packets are small, there has to be more of them which means the packet-switches must handle packets at a much faster rate. It was felt that switch design could be made more efficient if all the packets were the same size.
  Small, fixed-size cells support "fine-grain" multiplexing. With variable sized packets, it could happen that a small, high-priority packet would have to wait a long time whilst a huge packet belonging to another application was transmitted. With cell-switching, the huge packet would be fragmented into cells. This allows the high-priority cell to be interleaved within the cells of the huge packet and so avoid the lengthy delay.
  Really small packets do not have space for full global addresses so a datagram-based approach is not possible. A VC-based approach has the bonus of making it easy to preserve sequence.
  PTO

## Slide 5: On the other hand …
Higher bit-rates reduce store and forward delays
  Packets could be bigger
Small cells mean higher switching rates
  Does this make switch design easier?
Fragmentation overhead
  9.5% “cell tax”
VCs – connection set-up overhead
Variable sized packets can be switched efficiently?
Notes:   Error-control and flow-control were not needed within the ATM network (if needed they would be provided by the end systems). The inherent error rate of optical fibre is good and ARQ mechanisms would increase jitter.
ATM has not been the success its designers hoped and many people from within the LAN and Internet communities have criticised the design rationale.
VCs take time to set up which is bad news for short, transaction-like, dialogues.
Most application-level messages have to be split into multiple cells and reassembled at the destination. This is an additional overhead in time and space and can lead to waste - if one cell goes missing, it is likely the whole lot will need to be retransmitted.
Small cells need higher switching rates - does this really make switch design easier?
The rationale for small cell-size is undermined by increases in transmission speeds. If the line-speed goes from 650Mbps to 650Gbps then cells take only 1000th as long to transmit. To put it another way, a cell with a 48Kbyte payload can then be transmitted in the time currently needed for a 48-byte one. This suggests that locking into a tiny cell-size was short-sighted.

## Slide 6: ATM Cell header
Notes: Generic Flow-Control - does not yet have an agreed purpose.
Virtual Path Identifier and Virtual Channel Identifier are virtual circuit identifiers. i.e they are used to identify individual virtual circuits as they pass through switches. Recall that virtual-circuit identifiers must be unique within the scope of a link. Optionally the GFC field may be used to extend the VPI to 12 bits allowing 4096 virtual path connections (VPC) which may be sufficient enabling the VCI to be ignored by switches. The VCI would then just have local (host) significance. (See next slide).
Payload Type - distinguishes between a cell carrying user data and one used for management purposes.
Cell-Loss Priority- can be set by the network to indicate that this packet is a candidate for deletion if congestion is experienced. This bit could be set if the user exceeds the traffic contract.

## Slide 7: VPI Switching
User data (e.g. a file transfer) is carried in a virtual channel connection
  Identified by VPI + VCI
Consider several VCCs between same pair of hosts
  All VCCs can follow same route
  All can share the same VPIs
VPI switching: switches process VPI, ignore VCI
  2 VPCs (2-57 and 3-79)
  VPIs change as they pass through switches
VCIs unchanged by switches
  Serve as VCC identifiers at the end systems
A
VPI 2 VCI 20
VPI 3 VCI 22
VPI 57 VCI 20
VPI 79 VCI 22
VPI 79 VCI 25
VPI 3 VCI 25
Notes: ATM is unusual in having two levels of virtual circuits; Virtual Path Connections (VPC) and Virtual Channel Connections (VCC). The slide shows a typical way of using VPIs and VCIs known as “VPI switching” – only the VPIs are used within the virtual-circuit mechanism. Often VPCs will be set up long-term. VCCs always remain within the same VPC so that no routing decisions are necessary when setting up a VCC so that VCC set up is quick.
Other modes are possible. For example a VCC may hop to a different VPC as it passes through a switch.
Note that although the original intention was that VCCs should be set up dynamically, in practice they are often set up administratively and left in place long-term – so-called permanent virtual circuits.

## Slide 8: ATM QoS
QoS may be specified when VPC or VCC is set-up
Admission control
  Network can accept or reject request
Policing
  Network may discard cells which exceed the contract
Service classes defined
  CBR, UBR, nr-VBR, rt-VBR etc.
Generally, strong timing constrains => high priority in switches => higher cost
Notes: Five service categories have been defined for ATM traffic. They have different needs in terms of Quality of Service.
CBR is used for applications with tight time constraints. The traffic is not at all bursty and the network allocates a fixed amount of bandwidth to these connections. (E.g. traditional 64Kbps telephony traffic)
rt-VBR. This is also for time constrained applications such as voice and video but the bit-rate may not be constant. (E.g MPEG video)
nrt-VBR is also for bursty traffic - usually traditional data traffic such as WWW.
UBR is for non-real time, bursty applications such as traditional computer comunications like file transfer and email. There are no traffic service guarantees and is a ‘best effort’ service. However, it is expected to be cheap on public networks.
ABR is a flow controlled service with no upper bound on cell delay variation. It is not intended for time critical applications.
PTO

## Slide 9: A possible API
class VCCService
public VCCService(int vpi, int service, param p);
public void connect(); // Initiate // connection
public void listen(); // Listen for // connection
public void send(byte[] data);// Send cell
public void recv(byte[] data);// Receive
// cell
public void close(); // Close connection
public int getVCI(); // Get the VCI value
Notes: We are assuming in the API in the slide that VPCs already exist. The constructor parameters allow us to specify the VPI (which identifies a VPC), the service category and any other relevant parameters.
connect() and listen() act to set up a VCC within the specified VPC.
We assume also that the interface is at the cell level – so send() and recv() always deal in 48 bytes of data.
There would be several get/set methods. The one shown enables the user to retrieve the VCI allocated to the VCC at this end-point.

## Slide 10: ATM Adaptation Layers
Specify how to carry different traffic types in ATM cells
AAL1 - constant bit rate traffic
  Place bits in cells
  Ensure timing relationships are maintained
AAL5 - packet traffic (e.g. IP)
  Fragment and reassemble packets
  Ensure packets are delimited
Other AALs exist ...
Notes: In order that ATM networks can carry data generated outside the ATM world, a number of "ATM adaptation layers" (AAL) have been designed. These specify how to take data of different types, place it in ATM cells, transfer the cells and unpack the data at the destination. Several AALs have been defined including:
  AAL1 which says how to put a bit-stream into ATM cells. This could be used, for example, to carry a 64Kbps voice channel across ATM.
  AAL2 which provides bandwidth-efficient transmission of low-rate, short and variable packets in delay sensitive applications. In contrast with AAL5 (below) packets boundaries need not coincide with cell boundaries which allows more efficient packing.
  AAL5 which says how to fragment typical “computer data” packets into ATM cells. This is used to carry IP datagrams across ATM. It works most efficiently when packets are much bigger than cells. Many broadband Internet systems use AAL5+ATM to carry IP traffic.
Note that AALs are not tied rigidly to the QoS classes in slide 10. However, in practice, they will be related; for example a 64 Kbps voice channel will use AAL1 and will specify the CBR service category when setting up a VCC.

## Slide 11: AAL-5
Trailer
  Length in bytes
  CRC
ATM header – payload type
  0 in all except last
Payload Data
Fragment
Pad
Trailer
0
0
0
1
ATM Headers
48 bytes
Notes: AAL-5 is efficient in that it adds few extra cells (0 in the illustration). The packet payload, together with an 8 byte trailer, is fragmented into 48-byte ATM payloads. Padding bytes are added as necessary. The final cell of a frame is marked by a 1 bit in the ATM header.
This means it is not possible to interleave other cells with those of an AAL-5 frame within a VCC.
In a typical use, the payload would be an IP datagram complete with IP header. Of course, the latter is of no special meaning within the ATM system.

## Slide 12: A possible API
class AAL5Service
// Initiate AAL5 service on existing VCC
public AAL5Service(int vpi, int vci, param p);
// Initiate AAL5 service to address a
public AAL5Service(address a, param p);
// Send PDU (may block)
public void send(byte[] data, int len);
// Receive a PDU (may block)
public int receive(byte[] data);
Notes: The first constructor assumes a VCC already exists. This would be the case for ATM over ADSL where VPI 0, VCI 38 is often used.
The second constructor nominates an ATM address (not an IP address!) identifying an end-point on an ATM network. In this case it would be up to the AAL5 service implementation to set up a VCC to the destination (assuming none already existed).
The parameter p could specify, amongst other things, a maximum PDU size.
Send and receive deal in arbitrary-length data up to the maximum. It is up to the service implementation to do the fragmentation and padding.

## Slide 13: ATM Summary
ATM – a virtual-circuit based multiplexing technology
Small, fixed-length cells chosen for QoS support
  Was this a good idea?
VPCs (long lived) carrying multiple VCCs (short-lived)
Service categories CBR, rt-VBR etc.
  Priority operation in switches
ATM adaptation layers

## Slide 14: IEEE 802.11x
Originally … IEEE 802.11
  2.4-2.5 gigahertz (GHz) ISM
  1Mbps, 2Mbps, radio and IR, not widely used
Then … IEEE 802.11b
  2.4-2.5 gigahertz (GHz) ISM
  Max. 11 Mbps, widely used
Then … IEEE 802.11a
  frequencies in the 5 GHz range
  Max. 54 Mbps, not common in Europe
Then … IEEE 802.11g
  2.4-2.5 gigahertz (GHz) ISM
  Max. 54 Mbps, widely used
Notes: Most versions use the 2.4-2.5 gigahertz (GHz) S-Band Industrial, Scientific, and Medical (ISM) frequency band shared with Bluetooth, microwave ovens etc.
Note that ranges vary and that the maximum bit rates are only available if range and noise are low. All versions will use a lower bit rate to combat noise.

## Slide 15: IEEE 802.11b/g
2.4-2.485 GHz => 85MHz b/w
FDM to separate networks
14 overlapping channels 5 MHz separation
  Interference between adjacent channels
  Should use widely separated channels
DSSS to provide noise immunity (802.11b)
Non-persistent CSMA as a MAC algorithm
Stop and Wait ARQ for error recovery. (N.B. no CD)
RTS/CTS for hidden and exposed terminal problems
Notes: We concentrate on IEEE 802.11 b and g. These share the same frequency range and partition it in the same way so as to allow co-located networks separated by FDM.
Several WiFi networks can exist in the same place. In such cases each should use a different channel and these should not be adjacent.
The CSMA algorithm controls access to the medium between the stations of a single network. Because there is no collision detection and ARQ mechanism ensures retransmissions when collisions do occur.
See later for explanation of RTS/CTS

## Slide 16: Architecture
Ad hoc
Infrastructure
Access Point
“Basic Service Set”
“Distribution System”
“Extended Service Set”
Notes: The simplest network (not considered further) is an ad hoc one set up between a set of wireless stations (hosts).
An infrastructure network consists of a wireless access point (AP) which coordinates activity between a set of stations. The operator of the AP decides which channel to use. Typical choice would be channel 1, 6 or 11 which are well enough separated to make inter-channel interference acceptable.
A simple network consisting of a single AP plus a collection of wireless stations is termed a Basic Service Set (BSS).
A collection of BSSs may be connected via a distribution system (which may be a wired or wireless network). These then constitute an Extended Service Set (ESS). Logically an ESS is a single network. Physically it consists of separate, independent LANs.
A stand-alone BSS or an ESS is given a name by the operator – termed a Service System Id (SSID)

## Slide 17: Frame format
Frame Contr.
Dur. or Id
Address 1
Address 2
Address 3
Seq. Control
Address 4
Data
CRC
2
2
6
6
6
2
6
4
0-2312
Version
Type
Subtype
To DS
From DS
More Frag.
Retry
Power
More
2
2
4
1
1
1
1
1
1
1
1
W
O
Fragmentation
MAC Protocol
Power Management
Notes: Protocol Version - indicates the version of IEEE 802.11 standard.
Type - Frame type: Management, Control, Data
Management Subtype - Authentication, Deauthentication, Association req/resp, Reassociation req/resp, Disassociation, Beacon, Probe req/resp etc.
Control Subtype - RTS, CTS, ACK, PS-Poll etc.
To DS - 1 => frame sent to Distribution System (DS) (i.e the AP)
From DS - 1 => frame received from the Distribution System (DS)
More Frag. - set to 1 when there are more fragments of this frame
Retry - retransmission of a previously transmitted fragment.
Power – switch Power Management on/off
More - more frames buffered to this station.
W - frame body is encrypted according to the WEP algorithm.
O - Order frame is being sent using the Strictly-Ordered service class.
Duration – used in the MAC algorithm
ID – Association ID (used in Power-Save poll messages).
Address fields (1-4) – used in MAC algorithm
Sequence Control - consists of fragment number and sequence number
Data - is information that is transmitted or received.
CRC - contains a 32-bit Cyclic Redundancy Check (CRC).

## Slide 18: Getting Started
AP may send beacon frames at intervals, station scans all channels
Station sends probe frames, AP may respond
S
AP
?
OK or Reject
Open Authentication
S
AP
?
OK or Reject
Challenge
Response
Shared Key Authentication
Association request (SSID + station information)
Association response (Association ID)
Notes: AP may keep quiet (no beacons) and need not respond to probes from unknown MAC addresses which provides some protection against intruders. However, it is fairly easy for a station to monitor for network activity.
With Open Authentication the two parties simply learn each other’s MAC addresses. With Shared Key Authentication the station demonstrates its knowledge of a (previously agreed) shared key. It does this by using the key to encrypt a number (the challenge) sent by the AP and returning the encrypted version. Unfortunately the key used is the same one that is used in WEP (Wired Equivalent Privacy) encryption which may subsequently be used to provide confidentiality of data transfer. The challenge/response exchange provides an attacker with vital information – a plain-text/encrypted-text pair – that can assist discovery of the key. For this reason it is actually safer to use Open Authentication.
Finally, the station sends an Association Request which includes the SSID of the network it want to join together with information about itself – supported data rates for example. The AP may then accept the association allocating a numeric ID to it.

## Slide 19: IEEE 802.11 - Typical Operation
AP, Router and ADSL modem may be in one box
  Router does NAT + Firewall + DHCP server
Manager chooses SSID and channel number
S/w on station host initiates scans and probes
  User selects network and association is attempted
Host uses DHCP to get Internet parameters
Internet
Router
AP
BSS
Notes: The slide shows a typical home system in which IEEE 802.11 is used in conjunction with ADSL to provide broadband internet to a small wireless LAN.
Note that the association steps described in the previous slide only affect the MAC layer. If it succeeds software in the host will begin establishing IP-level connectivity. It will probably do this by broadcasting a DHCP (Dynamic Host Configuration Protocol) request. The DHCP server will respond with an IP address, router address etc.
Note that a box sold as a “wireless broadband router” implements several distinct functions:
ADSL modem to implement a high-bit-rate stream
Framing mechanism
IP router
NAT
IEEE 802.11 AP
… plus, possibly several others …

## Slide 20: Basic MAC [1]
CSMA/CA (non-persistent)
Stop and Wait ARQ – assists error recovery
Tx senses for period DIFS
  If still free, begins DATA
Other stations defer transmission for random time
Rx senses for period SIFS
  If still free, begins ACK
SIFS < DIFS => ACK has priority over DATA
ACK
DATA
sense
DIFS
Tx
Rx
time
SIFS
sense
A
Notes: [Note that there are lots of options and subtleties in the IEEE standard. Only a simplified version is covered here.]
The MAC algorithm is built on CSMA/CA (CA = “Collision Avoidance). It is a non-persistent CSMA – stations finding the medium busy defer transmissions for a random time so avoiding systematic collisions. Unlike CSMA/CD, which is used on the Ethernet, this MAC algorithm does not detect collisions and arrange retransmissions. Therefore a stop and wait ARQ protocol has been added. If no ACK is received the frame will be retransmitted (note use of “Retry” field in frame format). In IEEE 802.11 terminology this is the “Distributed Coordination Function (DCF).
DIFS (DCF Inter-Frame Space) and SIFS (Short Inter-Frame Space) are chosen so that if there is contention with another station trying to transmit DATA (e.g. at A an the slide) the ACK will win.

## Slide 21: Basic MAC [2]
Hidden terminal problem; hosts “hear” AP but not each other
  CSMA/CA will fail
  “Virtual Carrier Sense”
RTS requests reservation for time t
CTS grants reservation for time t
All stations hear CTS and defer for time t
ACK
DATA
sense
SIFS
Tx
AP
time
sense
SIFS
A
RTS
CTS
SIFS
sense
DIFS
sense
CTS
Other
defer
Notes: For an infrastructure network (i.e one with an AP) the protocol includes an optional “Virtual Carrier Sense” (VCS) mechanism based on two frames:
RTS: Request to send, CTS: Clear to send
RTS includes an estimate of the time needed to send DATA and ACK (See “Duration” field in the frame format). CTS grants exclusive access to the channel for this time. All other stations, including the hidden one, hear the CTS and defer.
The VCS also has an impact on the “exposed terminal” problem where a station may “hear” the transmission of nearby a station on an adjacent network and defer unnecessarily. With VCS it will hear the RTS but not the CTS from the AP which is (presumably) further away. At this point it can conclude that its network is free and will transmit. Although time is lost waiting for the CTS this will generally be a shorter time than would be needed for a data frame.

## Slide 22: Other things
Need to support (at least) Ethernet frame size
  .. but noise => small frames
  hence fragmentation and re-assembly
Low power mode
  Station announces low power mode
  AP buffers frames
  Beacons include list of stations that should wake
  Stations must wake at beacon intervals
Encryption
  Wired Equivalent Privacy
Notes: All but the last fragment of a frame have the “More Fragments” bit set. The station gives a 12-bit frame ID to each frame (frames are numbered consecutively) + a 4-bit fragment number. These are combined in the Sequence Control field. Each fragment has a complete MAC header and is transmitted according to the MAC protocol rules described earlier.
Wireless devices are often battery powered so saving power is desirable. “Listening” uses power (about 700mW). To avoid this a station may set low power mode (“Power” bit in frame format) and cease listening (reducing power consumption to about 60mW). The AP must now buffer any frames that are transmitted to this station. The station must then wake up and listen at the time AP sends beacon frames – careful synchronisation is needed. Beacon frames include a list of stations for which data is buffered. Stations notified in this way send “PS-Poll” frames requesting that the buffered frames be sent. The AP uses the “More” bit to indicate if still more frames are buffered.
The Wired Equivalent Privacy (WEP) system is a shared key system designed to provide the sort of defence against eavesdropping that would be expected in a wired LAN. All stations in a BSS or ESS share the same key. Without knowledge of the key a station is effectively excluded so the use of WEP in effect provides access control as well as privacy.

## Slide 23: Address Usage
“Distribution System” (DS) – network used to inter-connect APs
Address 1 – Wireless receiver
  Not necessarily final destination
  All wireless stations filter on this
Address 2 – Wireless transmitter
  Not necessarily the originating source
Address 3 – final destination or originating source
Address 4 – Used in “wireless links”
Notes: Wired or wireless networks may be used to interconnect APs in an ESS. A network which performs this role is called a “Distribution System”.
When a frame passes (say) from a wireless LAN to an Ethernet-based DS there are three MAC addresses involved; the wireless transmitter, the AP’s wireless interface, and the destination LAN host. The IEEE architecture handles this by having 4 address fields in the header.
Note that addresses 1 and 2 always refer to wireless interfaces on the wireless network the frame is currently traversing.

## Slide 24: Address Examples
WHa
WHb
APx
APy
B
Y
A
-
1
0
1
2
3
4
F
T
X
A
B
-
0
1
1
2
3
4
F
T
A
B
S
D
2
WHa
WHb
APx
APy
B
Y
A
-
1
0
1
2
3
4
F
T
X
A
B
-
0
1
1
2
3
4
F
T
3
Y
X
B
A
1
1
1
2
3
4
F
T
WHa
WHb
APx
B
X
A
-
1
0
1
2
3
4
F
T
X
A
B
-
0
1
1
2
3
4
F
T
1
Notes: T = the “To DS” bit
F = the “From DS” bit
Example 1 shows a frame being relayed between hosts on the the same wireless LAN by an AP.
Example 2 shows a frame passing between wireless hosts via an Ethernet. Ethernet operation is normal with the Ethernet hardware associated with the APs behaving as transparent bridges – it is up to the APs to do the correct address mappings.
Example 3 replaces the Ethernet by a wireless link. On this link Addresses 1 and 2 identify the relevant wireless transmitter and receiver whilst 3 and 4 identify the original source and final destination.

## Slide 25: A Possible API
All IEEE 802 MACs provide the same service
  => Nothing specifically “wireless” in the API
CL service
class MACService
// Initialise the adaptor
public MACService(param p);
// Send len bytes of data
public void send(address a, byte[] data, int len);
// Receive a max of maxlen bytes (may block)
public int receive(address a, byte[] data, int maxlen);
Notes: Warning. This is a toy example – not really comprehensive.
A key aim of the IEEE LAN design is that all LANs provide essentially the same service. Therefore, we would expect the APIs for different LANs to differ only in some detailed initialisation parameters.
The constructor would be called once at the beginning. The parameters passed might specify filter criteria to select or reject incoming frames. There might also be some technology-specific information such as a WEP key, SSID etc. The initialisation activities performed by the service implementation will be technology-dependent. For example, a wireless adaptor may be caused to associate with an AP.
The addresses used here will be IEEE MAC addresses. For compatibility with other IEEE MACs these will be the originator (receive) and final destination addresses (send) (A and B in slide 33). It is up to the firmware in the wireless Network Interface Card (NIC) to fill in all the addresses and other fields in the frames.
We would not expect complex buffering strategies here; send and receive will be 1-1 with MAC frame transmission.
The data and address parameters in receive() are references to empty structures to be filled in when data is received. Thus the receiver can discover the source address.
There would also be several get/set methods which could be used to discover/set operational parameters.

## Slide 26: WiFi Summary
Ad hoc, infrastructure
BSS and ESS
FDM for network separation
DSSS for noise suppression (802.11b)
CSMA/CA for channel allocation between stations
Stop and Wait for error recovery
RTS/CTS virtual carrier sense enhancement
MAC address usage allows ESS operation
Association, authentication and privacy mechanisms