## Slide 1: Routing
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Section content
Choosing routes in mesh-type networks:
  principles
  dynamic routing
  routing in large networks
  Performance
Routing in the Internet
  RIP
  OSPF

## Slide 3: Networks and Internets
H
H
H
H
H
H
Notes: Some network technologies, for example ATM and Frame Relay, consist of “switches” joined by “links”. Hosts are connected to the switches on the boundary. These networks must solve the routing problem in order to be able to operate. Many use VCs internally so that routes are chosen only when a VC is set-up.
The Internet (and intranets) interconnect existing networks through the use of routers. The routers communicate with each other either by using the networks they interconnect or through dedicated links. The Internet uses datagrams so that routing decisions must be made each time a datagram is transmitted. Note that some of the interconnected networks may themselves be mesh-type networks so that the routing problem occurs at different levels.
The considerations that apply to network and internetwork routing are broadly similar and are discussed in the next slides.

## Slide 4: Routing and Forwarding
Routing functions
  Calculating best routes
  Disseminating routing information
  Disseminating routes
Routing objectives
  Correctness
  Simplicity
  Robustness
  Stability
  Fairness
  Optimality
Forwarding functions
  Deciding where to send individual packets
Notes: In this section we are concerned with routing; calculating the “best” routes; disseminating routing information or complete routes to the routing nodes. This is distinct from forwarding which is the decision made when an individual packet is switched through a node. In many cases the result of routing is the calculation of forwarding tables for each node. These tables show the “best” routes (or at least the next hop of that route) to all destinations and are consulted each time a packet is forwarded.
The problem is not only to ensure that the packets arrive at the right place but to ensure that they do so in a timely way and without using the resources of the network in an inefficient way. Many of the more interesting routing issues arise in datagram networks. Tanenbaum lists six objectives for the routing function:
1. “correctness”: no mis-directions; 2. “simplicity”: complicated things tend to go wrong; 3. “robustness”: the algorithm should not collapse if a node goes down or a link is severed; 4. “stability”: should not be to sensitive to load changes; 5. “fairness”: no bias towards particular paths; 6. “optimality”: maximise throughput? minimise delay?
Unfortunately these goals are in conflict. A network may be viewed as a giant queuing system. The way to maximise the utilisation of such a system is to ensure that the queues are never empty. However, such a strategy is sure to increase delays.

## Slide 5: Calculating routes: where and when?
Where?
  Distributed:
    Each node calculates next hops to all destinations
  Centralised:
    NCC: decides all routes
  Source:
    Originating host decides routes
When?
  Continual
    New calculation for each packet
  Periodic
    Every few secs
  Load change
    When congestion occurs
  Topology change
    Initiated by management
Notes: There are three possible models for locating the routing decision:
1) Distributed: each node makes decisions about the next hop ‑ i.e. on which link should the packet be forwarded. This is robust but can lead to consistency problems.
2) Centralised: a Network Control Centre (NCC) plots routes between pairs of hosts or exterior nodes and informs the relevant nodes. The NCC constitutes a single point of failure and so must be very robust.
3) Source: the originating host or exterior node chooses the route and this choice is recorded in the packet.
Generally, one can say that the more frequently routes are changed the more optimal they are likely to be. However, there will be increased costs involved in moving routing information around, updating tables, etc. Also, strategies that change routes frequently are more prone to problems resulting from inconsistent routing information. This may cause a packet to loop around the network without ever reaching its destination.

## Slide 6: Routing Information
Fixed topology
  What is supposed to be connected to what?
Dynamic topology
  What is actually connected to what?
Historic information
Metrics – “distance” to destination
  hop count
  link costs (in £££), link throughputs
  link delays, link jitters
  link error rates
  etc.
Notes: Such information is rarely current and is often no more than an estimate. One feature of the management of computer networks is that management information is carried by the network itself and propagates at the same speed as normal traffic. (Contrast this with something like an automatic train control system on an underground railway where information travels much faster than the trains). This makes it possible that different parts of the network have different information.
  The sort of information that is used includes:
  The fixed topology: what is supposed to be connected to what?
  The dynamic topology: what is the actual connectivity given that links/nodes may be down?
  Predicted network traffic patterns: we may know, from past experience, that certain routes should be chosen at certain times of the day
  A “metric” often referred to as the “distance” to a destination: several metrics are used; the number of hops and the delay to a destination are popular ones as is the length of a queue on a link. QoS-related factors such as link throughput, delay, jitter or error rates are increasingly important. Note that not all metrics are additive – for example end-to-end throughput is constrained by the minimum link throughput along the route.

## Slide 7: Routing Policies and Constraints
Administrative
  Commercial agreements to carry traffic from certain sources
  Priority routes for some traffic
Security
  Avoid “untrusted” networks
QoS
  Route certain traffic types via “suitable” links
Real cost (financial)
  Only use high-cost links when all else fails
Notes: All sorts of policies may be applied. Certain types of traffic may be excluded from some routes perhaps because it is low priority. Sometimes there are legal factors; private networks are not allowed to carry third-party traffic, US companies may not like their traffic being routed through Iraq etc. some factors that may be part of a routing policy include:
administrative-related information (e.g. for managing resources)
security-related issues for sensitive traffic
QoS factors for certain real-time applications
cost of sending data
Of course, some of these factors will be in conflict with others, e.g. QoS and real financial cost

## Slide 8: Distance vector algorithms [1]
Distance:
  hop count, queue length, …
Each node:
  evaluates distance to all other nodes
  distributes information to adjacent nodes
  finds shortest (lowest distance) route to to all other nodes
Distances are always estimates
  Different nodes may make different estimates
Notes: The distance vector in the name is a table, computed by each node in the network, which indicates the “distances” between the node and all other nodes in the network. (In practice this table will probably also include the preferred “next-hop” to each destination. Thus it doubles as a forwarding table). These vectors are transmitted to all adjacent nodes at frequent intervals. “Distance” (the routing metric) can mean a variety of things; hop count, delay, number of packets queued up along the route etc. Once a node has received distance vectors from all its neighbours it can begin to compute a new routing table. In order to do this, the node must also have an estimate of its distance from each of its neighbours. The computation is according to the “distributed Bellman-Ford algorithm” illustrated on the next slide.
The most famous example of this class of algorithm was that used in the original ARPANET. This used the lengths of the queues on the different links as the measure of “distance” and sent out distance vectors every 128 ms.
An example of a distance vector protocol is the Routing Information Protocol (RIP) (RFC2453) used in IP networks.

## Slide 9: Bellman-Ford
1
A
C
B
F
E
D
2
2
1
1
1
3
3
5
5
Notes: In the network shown, the numbers on the links are the metrics observed by the nodes. (In practice all nodes would not see quite the same picture but, for simplicity, we will assume that they do). We will consider routing table calculations for node A.
A begins with the metrics it can observe on its local links. Periodically it receives distance vectors from its neighbours. These show each neighbours estimates of the distance to all other nodes. The calculation for routes to node E is shown. Essentially A makes new estimates by adding its local observations to the estimates of its neighbours and chooses the smallest. It can be seen that the route via D is best with a distance of 2. This calculation is repeated for all nodes leading to the new forwarding table. This also provides the information needed to construct the distance vector that must be sent to the neighbours at the next routing update.

## Slide 10: Distance vector problems
A
B
C
D
1
1
1
“Counting to infinity”
Notes: A number of problems are inherent to distance-vector algorithms
  When the network is large the distance vectors are large and may not fit into one packet. If two or more packets must be sent then there is the danger that one will be lost leading to inconsistency.
  News of changes spreads by one hop at each routing update. Thus there will be times when only a portion of network nodes is aware of the change. There will be an inconsistent view of the “best” route to a destination and this can lead to routing loops
  News of link failure spreads rather slowly. (“Bad news travels slowly”)
This last point is illustrated by considering what happens when the link between A and B fails. Initially, the link between A and B is fine and the forwarding table entries for B, C and D will show delays to A of 1, 2 and 3 respectively. Suppose the link to A from B is now cut. At the next routing update, B will announce the 1 unit delay to A from its current table. B will hear nothing from A but will hear that C has a route to A with delay 2. Assuming that B has by now twigged that its delay along the B-A link is effectively infinite it will be happy to use the path that C apparently has. Since C is one unit away, B now thinks it can get to A with delay 3 via C. At the next routing update it will tell C it has a route to A with delay 3; unfortunately it will not mention that this route is actually via C itself. It can be seen that many updates must elapse before B, C and D conclude that A is inaccessible. This is problem known as counting to infinity.

## Slide 11: Counting to Infinity – “Solutions”
Include next-hop in update
  B would see it was on C’s advertised route to A
Split horizon
  Never send information about a route to a node from which the route was learnt
  C would not tell B about a route to A of length 2
Split horizon with poisoned reverse
  Advertise a distance of infinity to a node from which a route was learnt
  C would tell B its cost to A was “infinity”
  C still tells D its cost to A is 2
“Solutions” only work for a 2-node count to infinity
A
B
C
D
1
1
1
Notes: Counting to infinity can be tackled in a number of ways. The first is simply to include the next hop as part of the routing update. The second is called split horizon and has two modes. In the simplest mode, a router never advertises a route back along a link through which it learnt of a route, e.g. C’s routing updates to B would not include information about it’s distance to A. In the second mode, the router uses poisoned reverse – it advertises a distance of infinity back along the link through which it learnt of the route to a destination, e.g. C would tell B that it’s distance to A is infinity (but, of course, still tell D it’s distance to A is 2).

## Slide 12: DV Examples - RIP and RIPv2
RIP (RFC1058):
  hop-count for metric
  max. metric 16 (infinity)
Routing updates:
  {destination, cost}
  every 30s
  also triggered by local metric changes
Entries timed-out after 180s if not refreshed
Split horizon with poisoned reverse
RIPv2 (RFC2453)
Routing updates contain:
  additional routing information (route domain and route tag)
  IP address mask for classless addresses
  next-hop IP address
Simple authentication
Notes: RIP is quite an old, relatively simle DV algorithm. It is till used today for individual IP networks – autonomous systems (ASs) – within but not across the Internet as a whole. RIP exhibited some some deficiencies such as counting to infinity, and lack of support for classless IP addresses which have been remedied in RIPv2. RIPv2 also has a simple authentication mechanism used in routing updates to deter security attacks to subvert routing in IP networks.

## Slide 13: Why authentication?
C
210.50.5.2
210.50.5.0
210.50.6.0
210.50.7.0
210.50.7.8
N1
N2
N3
S
R1
R2
X
Suppose X wants to pretend to be C in order to subvert S
  Easy for X to put C’s address as source
  However, replies will still be routed to C
X pretends to be a router and advertises a low-cost route to R2…
Notes: Consider the simple network in the slide which shows a client C and a server S which we suppose are engaged in some sensitive transactions. X, meanwhile, is trying to subvert the situation by posing as C. It is surprisingly easy for X to assume C's IP address - it often involves nothing more than updating a local table. So, if S was hoping to validate C by checking the source IP address then it is undermined. However, any replies S sends to C will not reach X since they will be routed (correctly) to N1. However, if X, additionally, poses as a router, it may advertise a route to N1 with a metric lower than that offered by R1. This will convince R2 to change its routing tables and send all N1 traffic to X. The subversion will then be complete.
RIPv2 authentication is weak – involves sending passwords across the network.
Recent Internet work allows proper, strong authentication of origin – not widely implemented.

## Slide 14: Link-state algorithms
Each node:
  Assesses metric on local links
  Distributes information to all nodes
    Multicast or flooding
  Receives information from all nodes
  Finds lowest cost path to all other nodes
Dijkstra’s Algorithm:
  shortest-path (SP) tree to all other nodes
All nodes shares same information, perform same calculation
Notes: In distance vector algorithms, nodes send information about their distances from all other nodes to their neighbours. In link-state algorithms, nodes send information about their distances from their neighbours to all other nodes.
The distribution of routing updates is done by flooding. Every node forwards routing updates on all links except those on which the updates arrived. Hop counters or sequence numbers are used to ensure that the process eventually terminates. Although flooding sounds an expensive process when compared with the distance vector method, in practice, this is not the case. Routing updates in distance vector algorithms must be done frequently in order that information about changes can reach all nodes in the network reasonably quickly. Routing updates in link-state algorithms reach all nodes in the network very quickly and so need be much less frequent – say about once every few minutes. A further advantages of the link-state algorithm is that the size of routing update packets is independent of network size – so the algorithm scales well. Also, the flooding method makes it very likely that all nodes will receive the update. This makes it much less likely that routing tables will become inconsistent.
Once the routing updates have been received each node possesses complete knowledge of the state of the network and can begin to calculate its forwarding table. Dijkstra’s Algorithm is a common choice for this.

## Slide 15: Dijkstra’s Algorithm [1]
A
B
C
D
E
5
2
1
1
3
4
A
D
2
A
B
C
D
1
5
3
1
3
More candidates
A
B
C
D
1
5
3
2
Add C to SP tree
A
D
2
B
C
1
A
5
D
3
1
4
Prune and add D to SP tree
A
B
C
D
1
5
3
1
Add candidates
Notes: A semi-formal description of Dijkstra’s Algorithm is as follows:
At the start of each iteration there will be:
  A set of nodes already added to the SP tree. One of these nodes will be the “most recently added node”. The tree represents the shortest paths discovered so far.
  A set of candidate nodes. These might represent shortest paths but we may discover a shorter path as the algorithm proceeds.
  The remaining nodes that the algorithm has not yet encountered.
Each iteration involves two steps:
1) Update the set of candidate nodes. To do this:
  Add all the neighbours of the “most recently added node” to the candidate set and calculate their path lengths
  Prune the candidates. I.e., if any node appears more than once, retain only the one with the shortest path
2) Update the SP tree.
PTO

## Slide 16: Dijkstra’s Algorithm [2]
A
B
C
D
E
5
2
1
1
3
4
E
A
D
2
B
C
1
1
4
5
More candidates
E
A
D
2
B
C
1
1
4
6
Add A
E
A
D
2
B
C
1
1
4
7
No more candidates
E
A
D
2
B
C
1
1
4
8
Add E
Notes: At this point, the candidate nodes represent shortest paths encountered so far. However, one candidate – the one with the shortest path cost amongst all candidates – is special. It will certainly be impossible to reach this node via one of the others at lower cost. Therefore:
Iterations continue until all nodes have been added.
In the example, the resulting shortest path tree is used to update the routing table for node B.
  Select the candidate node with the shortest path and add it to the SP tree

## Slide 17: LS example - OSPFv2
More stable than RIPv2:
  quicker convergence
Load balance:
  multiple equal cost routes to same destination
Updates via multicast:
  not broadcast/flooding, so lighter network load
Authentication – prevents:
  denial-of-service
  man-in-the-middle
Open Shortest Path First (RFC2328)
More computationally expensive than RIPv2:
  router must evaluate whole network tree
Harder to implement than RIPv2(?)
Can use QoS factors for routing
Notes: The Internet community uses a link state routing protocol called Open Shortest Path First (OSPF). This now the generally favoured routing protocol for use within a single IP network – a single autonomous system (AS). However the simplicity and wide availability of RIPv2 means that there are still many networks using RIPv2, especially where multicast is used (we look at multicast later in the course).
OSPF also has the ability to perform (limited) QoS-based routing using the ToS field in the IPv4 header. Where there is more than one equal cost route for a particular destination, OSPF can perform load balancing by distributing traffic amongst these routes. OSPF can use multicast instead of broadcast/flooding to distribute router updates, thereby reducing the traffic load on the network. A simple authentication mechanism (as in RIPv2) is available, but more secure, cryptographic techniques are possible.
Also, OSPF uses strong authentication techniques which prevent denial-of-service and man-in-the-middle attacks to IP packets.

## Slide 18: OSPF – Type of Service Routing
Five routing protocols in parallel - one for each Type of Service
  Minimise monetary cost
  Maximise reliability
  Maximise throughput
  Minimise delay
  “Don’t’care”
Routing updates report metrics for each class classes
Routers maintain separate routing tables for each
Notes: In effect, OSFP operates five routing protocols in parallel - one for each Type of Service (ToS) offered by IP (minimise monetary cost, maximise reliability, maximise throughput, minimise delay or “don’t’care”). Routing updates report different metrics for each of these ToS classes and routers can maintain separate routing tables for each.
Although the IP ToS byte is not honoured by many routers – indeed it is in the process of being redefined as the DIFSERV byte – the fact that OSPF can deal with QoS-related routing is likely to be very important to the future of the Internet.