## Slide 1: Asynchronous Transfer Mode
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Technology drift
1980s Ethernet LAN
  Shared medium
  Data only
  Co-ax cable
  10 Mbps
Ethernet today
  Switched Ethernet (mesh)
  Integrated services
  Fibre, twisted pair
  1 Gbps
1980s B-ISDN WAN
  Virtual Circuits (mesh)
  Integrated Services
  Optical fibre
  120 Mbps (or more)
ATM today
  Multiplexing (e.g. broadband Internet
  LAN emulation
Notes: The slide compares the development of two technologies. Ethernet was originally conceived as a lightweight technology to provide connectivity within a single building. ATM was the technology selected by the telecoms industry to provide wide-area connectivity for “integrated services” (IS). It was seen as the technology that would replace the existing telephone system infrastructure with something that would support data and streaming applications as well as telephony. As was typical for WANs at the time, ATM is a virtual circuit technology. Some ATM equipment manufacturers thought they saw a market for ATM in the local area. In principle it could handle the typical LAN data applications as well as carrying voice, video etc. In order to promote this use they introduced “LAN Emulation” (LANE) which aimed to make ATM look like Ethernet from the point of view of existing operating systems. This was intended to make take-up of LANE/ATM as cheap as possible.
Meanwhile the promoters of Ethernet developed their technology. It went from 10 Mbps to 100 Mbps then 1 Gbps. Because of the nature of the CSMA-CD MAC algorithm, each increase necessitated either a reduction in range or an increase in minimum frame size. Partly in consequence of this today’s “Ethernets” often consist of single hosts per segment connected via “Ethernet switches” – in other words they have become mesh-type networks rather than shared media networks. Standards have now been added which allow prioritised operation in switches so that IS traffic can be supported.

## Slide 3: ATM Networks
Asynchronous Transfer Mode” (ATM)
  Switched technology for mesh-type networks
  Cell-switching, 53-byte cells
    48 bytes data, 5 bytes header
  CO service, neither error nor flow control
  “Integrated Services”
S
H
H
H
H
H
H
H
H
S
S
S
S
H
H
H
H
H
Notes: Although ATM has been much less successful than its designers hoped, it is still used – for example the infrastructure which carries broadband Internet traffic from the local telephone exchange to the ISP often uses ATM.
We look at it here as an example of a virtual circuit based technology in contrast the the shared medium technologies we have seen in wired and wireless LANs.
The technology is built around ATM switches which switch ATM packets – termed “cells”. A small, local ATM network might have just one switch, large networks consist of a mesh of many switches.

## Slide 4: Design rationale
Integrated services => must control delay and jitter
Small cells minimise store and forward delay
  Small cells => no room for global addresses
    Must be virtual circuit based
Fixed size cells simplify switch design
Low delay/jitter => no error or flow control
Fast switching => no error or flow control
Notes: The rationale for cell-switching was as follows:
  Packet-switching has the ability to vary the capacity allocated to multiplexed streams as demand varies - just what was required.
  Packet-switching suffers from store-and-forward delays at switches. Delay is a problem for interactive traffic such as voice telephone. Store-and-forward delay is minimised if the packets are small.
  If the packets are small, there has to be more of them which means the packet-switches must handle packets at a much faster rate. It was felt that switch design could be made more efficient if all the packets were the same size.
  Small, fixed-size cells support "fine-grain" multiplexing. With variable sized packets, it could happen that a small, high-priority packet would have to wait a long time whilst a huge packet belonging to another application was transmitted. With cell-switching, the huge packet would be fragmented into cells. This allows the high-priority cell to be interleaved within the cells of the huge packet and so avoid the lengthy delay.
  Really small packets do not have space for full global addresses so a datagram-based approach is not possible. A VC-based approach has the bonus of making it easy to preserve sequence.
  PTO

## Slide 5: On the other hand …
Higher bit-rates reduce store and forward delays
  Packets could be bigger
Small cells mean higher switching rates
  Does this make switch design easier?
Fragmentation overhead
  9.5% “cell tax”
VCs – connection set-up overhead
Variable sized packets can be switched efficiently?
Notes:   Error-control and flow-control were not needed within the ATM network (if needed they would be provided by the end systems). The inherent error rate of optical fibre is good and ARQ mechanisms would increase jitter.
ATM has not been the success its designers hoped and many people from within the LAN and Internet communities have criticised the design rationale.
VCs take time to set up which is bad news for short, transaction-like, dialogues.
Most application-level messages have to be split into multiple cells and reassembled at the destination. This is an additional overhead in time and space and can lead to waste - if one cell goes missing, it is likely the whole lot will need to be retransmitted.
Small cells need higher switching rates - does this really make switch design easier?
The rationale for small cell-size is undermined by increases in transmission speeds. If the line-speed goes from 650Mbps to 650Gbps then cells take only 1000th as long to transmit. To put it another way, a cell with a 48Kbyte payload can then be transmitted in the time currently needed for a 48-byte one. This suggests that locking into a tiny cell-size was short-sighted.

## Slide 6: Wide-Area Provision
Physical links – cables, fibres, microwave, etc.
  Digital (“bit-pipes”)
  Along railway lines, power cables etc.
  Providers BT, Cable and Wireless etc.
Portions of capacity sold to users. E.g.
  Newspapers for editorial/printing
  BBC for radio and television distribution
  “Value-added” providers
Value-added providers build on the bit-pipes
  Switches, routers, IP networks, ATM networks, etc.
Notes: There is a division of labour in wide-area provision (some of it enforced by legislation). At the bottom are companies who own physical, wide-area links with very large capacities. They sell this capacity on to users and also to other “value-added” providers; circuit-switching and TDM techniques are used in order to sell slices of capacity tailored to the needs of individual users. The capacity is leased – a company pays for a fixed capacity between two points for a fixed period, for example one year. A fixed charge is made which is independent of the usage the customer makes of the capacity. Leased services are offered at a set of standard rates according to the Plesiochronous Digital Hierarchy (PDH) (up to ~600Mbps) and Synchronous Digital Hierarchy (up to ~160Gbps) (see support material).
Companies may lease capacity in order to link their offices and plants both for telephony and data networking. In the latter case some higher level data communications system (e.g. Internet, ATM) will be implemented over the leased lines in order to provide switching and multiplexing.
Alternatively companies might buy data network services from “value-added” providers who implement such services over capacity leased from the physical network providers.

## Slide 7: Network Provision Solution 1
Provide digital circuits (say):
  2.048 Mbps = 32x64Kbps for telephony
  155.52 Mbps for Internet
  8.448 Mbps for video conferencing
Fixed allocations:
  Waste when not used
  Cannot move between application areas
A
B
C
Notes: We suppose a company (“Fluffco”) needs to provide telephony, Internet and conferencing links between three offices. The slide shows a rather “traditional” solution in which point-to-point links are leased from a provider. [The slide shows “logical” circuits. In practice a single logical circuit may jump between several physical cables or fibres as it passes across the country]. Fluffco would pay a fixed sum each month for each circuit.
Advantages:
  Fluffco knows exactly what it will get, for example a maximum of 30 simultaneous telephone calls between sites;
  “Standard” equipment can be connected directly to the circuits.
Disadvantages:
  Fluffco pays whether or not it sends any traffic;
  Fluffco cannot easily reallocate capacity between traffic types – it would have to re-negotiate with the provider.

## Slide 8: Network Provision Solution 2
“Value-added” provider has ATM switches connected by high-capacity links.
Fluffco has ATM switches on its sites and connects to provider switches via fibre.
Fluffco leases ATM “Virtual Paths” A-B, B-C, C-A
Fluffco sets up ATM “Virtual Channels” on demand.
A
B
C
Notes: In this case a “value-added” provider sits between Fluffco and the owner of the physical links. The value-added provider leases links and uses these to interconnect ATM switches. Managing its resources via ATM holds out the prospect of better utilisation of the links since these will be shared between Fluffco and other customers through ATM statistical multiplexing. On the previous slide Fluffco would expect to waste most of the 155.52Mbps allocated to Internet since this would only be needed for a few peak periods each day. With statistical multiplexing capacity unused by Fluffco becomes available to other customers.
Fluffco would need its own ATM switches in order to connect to the network. In this example Fluffco is leasing ATM “Virtual Path Connections” (VPC) between its sites. These are ATM virtual circuits which, once set up, are left in place long-term – so-called “permanent virtual circuits” (PVC). In the full ATM model Fluffco will set up ATM “Virtual Channel Connections” (VCC) on demand – for example, when a video conference begins, a new VCC will be started. VCCs used in this way can be viewed as sub-channels within a VPC. Since all the routing decisions and table set-up was completed when the VPC was established, setting up a VCC should be quite quick.

## Slide 9: VPI Switching
Typically: VPC long-term, VCC “as needed”
VPC and VCC most both be identified at switches – VPI and VCI
VPI switching: switches process VPI, ignore VCI
  2 VPCs (2-57 and 3-79)
  VPIs change as they pass through switches
VCIs unchanged by switches
  Serve as VCC identifiers at the end systems
A
VPI 2 VCI 20
VPI 3 VCI 22
VPI 57 VCI 20
VPI 79 VCI 22
VPI 79 VCI 25
VPI 3 VCI 25
Notes: ATM is unusual in having two levels of virtual circuits; Virtual Path Connections (VPC) and Virtual Channel Connections (VCC). The slide shows a typical way of using VPIs and VCIs known as “VPI switching” – only the VPIs are used within the virtual-circuit mechanism. Often (as in the Fluffco example on the previous slide) VPCs will be set up long-term. VCCs always remain within the same VPC so that no routing decisions are necessary when setting up a VCC so that VCC set up is quick.
Other modes are possible. For example a VCC may hop to a different VPC as it passes through a switch.

## Slide 10: ATM Cell header
Notes: ATM must use a pair of virtual circuit identifiers – one for VPCs and one for VCCs. At the user-network interface, 8 bits are allocated to the VPI and 16 to the VCI. The header format is shown in the slide.
Here the "generic flow-control" field does not yet have an agreed purpose. The "payload type" field can be used to distinguish between a cell carrying user data and one used for management purposes. If user data is indicated, then one bit of the payload type may be used to indicate "congestion experienced".
CLP is "cell-loss priority" and can be set by the network to indicate that this packet is a candidate for deletion if congestion is experienced. This bit could be set if the user exceeds the traffic contract.
Although 8 bits for the VPI is probably enough at the user-network interface (allowing 256 VPCs), it may not be enough inside the network where a large switch may want to multiplex thousands of VPCs down a single link. Consequently, inside the network, the generic flow control field is eliminated and four extra bits are allocated to the VPI.

## Slide 11: ATM QoS
QoS may be specified when VPC or VCC is set-up
Admission control
  Network can accept or reject request
Policing
  Network may discard cells which exceed the contract
Service classes defined
  CBR, UBR, nr-VBR, rt-VBR etc.
Generally, strong timing constrains => high priority in switches => higher cost
Notes: Five service categories have been defined for ATM traffic. They have different needs in terms of Quality of Service.
CBR is used for applications with tight time constraints. The traffic is not at all bursty and the network allocates a fixed amount of bandwidth to these connections. (E.g. traditional 64Kbps telephony traffic)
rt-VBR. This is also for time constrained applications such as voice and video but the bit-rate may not be constant. (E.g MPEG video)
nrt-VBR is also for bursty traffic - usually traditional data traffic such as WWW.
UBR is for non-real time, bursty applications such as traditional computer comunications like file transfer and email. There are no traffic service guarantees and is a ‘best effort’ service. However, it is expected to be cheap on public networks.
ABR is a flow controlled service with no upper bound on cell delay variation. It is not intended for time critical applications.
The QoS parameters that are used for ATM are:
  Maximum and Mean Cell Transfer Delay - how long the cell takes to get from source to destination.This is an absolute delay and may not matter for many types of traffic. Other types, e.g. where telecontrol of equipment is taking place, this delay matters a lot.
PTO

## Slide 12: Network Provision Solution 3
Solution 2 ATM provides:
  statistical multiplexing and QoS control
But …
  ATM has efficiency problems (see slide 5)
  ATM-specific h/w, s/w is expensive
Use ATM or SDH for links then use IP
  Routers at A, B, C
  VoIP, INTSERV etc.
A
B
C
Notes:   Cell Delay Variation. This is how much the delay varies from cell to cell. Where there is a real-time display of information, e.g. video, a constant delay can be tolerated but if an individual cell arrives late then it may not be in time for display and the picture quality will suffer.
  Cell Loss ratio. This is how many cells have been dropped by the network. Dropping cells is the standard way for ATM switches to deal with congestion.
Solution 2 fits the vision of the ATM designers; integrated services co-existing on a common infrastructure with ATM providing statistical multiplexing. However, it is difficult for this solution to compete with one based on Internet protocols. To some extent this is due to inherent defects in the ATM architecture (see slide 5). Just as important is the weight of the installed base and cost-effective availability of Internet hardware and software.
Fluffco is likely to have extensive IP use at its three sites and we already know there is a requirement to carry Internet traffic between the sites. Fluffco may well decide to build on this Internet connectivity for the other two applications; telephony and video conferencing. These are both time-sensitive applications for which a “best-efforts” network like the Internet is not inherently well suited. However, provided the inter-site links are not
PTO

## Slide 13: A possible API
class VCCService
public VCCService(int vpi, int service, param p);
public void connect(); // Initiate // connection
public void listen(); // Listen for // connection
public void send(byte[] data);// Send cell
public void recv(byte[] data);// Receive
// cell
public void close(); // Close connection
public int getVCI(); // Get the VCI value
Notes: congested and perhaps with the assistance of Internet QoS extensions such as INTSERV, these can work adequately. If this approach is adopted then ATM is reduced simply to a multiplexing technology permitting the network provider to share capacity in a flexible way between its various customers. However, given the aforementioned inefficiencies we might be better off eliminating ATM and just providing a single high-capacity SDH link between each pair of sites.
We are assuming in the API in the slide that VPCs already exist. The constructor parameters allow us to specify the VPI (which identifies a VPC), the service category and any other relevant parameters.
connect() and listen() act to set up a VCC within the specified VPC.
We assume also that the interface is at the cell level – so send() and recv() always deal in 48 bytes of data.
There would be several get/set methods. The one shown enables the user to retrieve the VCI allocated to the VCC at this end-point.

## Slide 14: ATM Adaptation Layers
Specify how to carry different traffic types in ATM cells
AAL1 - constant bit rate traffic
  Place bits in cells
  Ensure timing relationships are maintained
AAL5 - packet traffic (e.g. IP)
  Fragment and reassemble packets
  Ensure packets are delimited
Other AALs exist ...
Notes: In order that ATM networks can carry data generated outside the ATM world, a number of "ATM adaptation layers" (AAL) have been designed. These specify how to take data of different types, place it in ATM cells, transfer the cells and unpack the data at the destination. Several AALs have been defined including:
  AAL1 which says how to put a bit-stream into ATM cells. This could be used, for example, to carry a 64Kbps voice channel across ATM.
  AAL2 which provides bandwidth-efficient transmission of low-rate, short and variable packets in delay sensitive applications. In contrast with AAL5 (below) packets boundaries need not coincide with cell boundaries which allows more efficient packing.
  AAL5 which says how to fragment typical “computer data” packets into ATM cells. This is used to carry IP datagrams across ATM. It works most efficiently when packets are much bigger than cells. Many broadband Internet systems use AAL5+ATM to carry IP traffic.
Note that AALs are not tied rigidly to the QoS classes in slide 10. However, in practice, they will be related; for example a 64 Kbps voice channel will use AAL1 and will specify the CBR service category when setting up a VCC.

## Slide 15: AAL-5
Trailer
  Length in bytes
  CRC
ATM header – payload type
  0 in all except last
Payload Data
Fragment
Pad
Trailer
0
0
0
1
ATM Headers
48 bytes
Notes: AAL-5 is efficient in that it adds few extra cells (0 in the illustration). The packet payload, together with an 8 byte trailer, is fragmented into 48-byte ATM payloads. Padding bytes are added as necessary. The final cell of a frame is marked by a 1 bit in the ATM header.
This means it is not possible to interleave other cells with those of an AAL-5 frame within a VCC.
In a typical use, the payload would be an IP datagram complete with IP header. Of course, the latter is of no special meaning within the ATM system.

## Slide 16: A possible API
class AAL5Service
// Initiate AAL5 service on existing VCC
public AAL5Service(int vpi, int vci, param p);
// Initiate AAL5 service to address a
public AAL5Service(address a, param p);
// Send PDU (may block)
public void send(byte[] data, int len);
// Receive a PDU (may block)
public int receive(byte[] data);
Notes: The first constructor assumes a VCC already exists. This would be the case for ATM over ADSL where VPI 0, VCI 38 is often used.
The second constructor nominates an ATM address (not an IP address!) identifying an end-point on an ATM network. In this case it would be up to the AAL5 service implementation to set up a VCC to the destination (assuming none already existed).
The parameter p could specify, amongst other things, a maximum PDU size.
Send and receive deal in arbitrary-length data up to the maximum. It is up to the service implementation to do the fragmentation and padding.

## Slide 17: Summary
ATM – a virtual-circuit based multiplexing technology
Small, fixed-length cells chosen for QoS support
  Was this a good idea?
VPCs (long lived) carrying multiple VCCs (short-lived)
Service categories CBR, rt-VBR etc.
  Priority operation in switches
ATM adaptation layers