## Slide 1: Internet Convergence Technology
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: The Internet Approach
Link, MAC, Physical – Technology dependent, unaltered
Convergence – encapsulation, address resolution
Common – datagrams, forwarding, fragmentation (maybe)
Transport – end-to-end
R
R
Convergence
Link/MAC
Physical
Internet
Common
Transport
I
I
I
I
I
I
R
R
XXX
YYY
ZZZ
Notes: As noted earlier, the Internet service is an abstract one which can be implemented on any network technology. We have looked at the “common” aspects of the implementation of the service, now we look at the “convergence” sub-layer that implements a mechanism for exploiting a specific network technology to carry IP datagrams. Depending on the nature of the technology this may be simple or quite complex – perhaps involving the setting up and taking down of connections. It will always involve address resolution, in which IP addresses are mapped to technology dependent addresses and encapsulation in which IP datagrams are inserted into technology dependent frames (not necessarily 1-1).

## Slide 3: IP and the IEEE MAC service
Similar services (CL), frame size big enough
Could be carrying many protocols: IP, ARP, …
  How do we know which?
Ether type field – not always present
  General method for “protocol discrimination”
MAC
CRC
L
IP
IP data
S
MAC Addresses etc.
LLC Header (3 bytes)
SNAP (5 bytes)
SNAP includes 2-byte “type”. 0800 for IPv4, 0806 for ARP, 86DD for IPv6
Notes: MAC frames can carry a variety of payloads; IPv4 is just one possibility. It is important that the receiving system can decide what protocol is carried quickly and unambiguously. “Well-known” numbers are assigned to protocols (0x0800 for IPv4 for example see http://www.iana.org/assignments/ethernet-numbers for a complete list). The original Ethernet frame has a field designed to carry these values. Unfortunately this field is not present in all IEEE MACs, not even in all versions of Ethernet. The mechanism in the slide is a more general (though wasteful) alternative.
The LLC header was designed to do protocol discrimination and is part of the IEEE architecture. Unfortunately it allocates only 8 bits to the job which does not allow for enough protocols. Therefore the field is set to 0xAA which means “see SNAP header”. The SNAP (SubNetwork Access Protocol) has a 16-byte type field which is where the type value is placed. So, the cost of generality is that 8 bytes are used to do the work of 2. Note that this reduces the MTU of an Ethernet from 1500 bytes to 1492 bytes.

## Slide 4: Address Resolution on a LAN
ARP results are cached
  Timeout if not “refreshed”
All hosts learn mapping for requestor
Want to send to 128.16.8.177 Need Ethernet address
128.16.8.177 08:00:20:0d:23:34
128.16.8.78 08:00:20:0d:1b:96
128.16.8.74 08:00:20:0d:2a:3b
128.16.8.135 08:00:20:0d:5a:4b
It’s me! My address is 08:00:20:0d:23:34
ARP req (b/cast) Who is 128.16.8.177?
ARP resp 08:00:20:0d:23:34
Notes: All IEEE LANs support a broadcast service. This is the basis for the LAN Address Resolution Protocol (ARP).
An IP host (or router) begins by knowing the IP address of the host to which it wants to send a datagram (128.16.8.177 in the slide). It broadcasts an ARP request messages which contains the following information (refer to the slide):
“I am IP address 128.16.8.135, Ethernet address 08:00:20:0d:5a:4b. What is the Ethernet address of 128.16.8.177?”
All hosts receive this message and hence learn the address mapping for the requestor – a useful side-effect of ARP. One host recognises its IP address and responds with the information:
“I am IP address 128.16.8.177, Ethernet address 08:00:20:0d:23:34”
The response is not broadcast.
The requestor can now construct an Ethernet frame with destination address 08:00:20:0d:23:34 the data part of which will be an IP datagram with destination address 128.16.8.177.
All mappings are cached so that ARP generally has to be used only for the first datagram sent. However, we cannot assume that mappings will be constant for evermore – a new Ethernet card might be installed for example. Thus mappings are timed out if not refreshed and are subsequently re-learned.

## Slide 5: Classical IP over ATM (CIPA)
H
H
H
AAS
ATM address  IP Address mapping
H
H
H
CLS
PVC  IP Address mapping
PVC mode
SVC mode
IEEE Payload
IP
IP data
L
S
AAL-5
Notes: The basic connectivity architecture for IP over ATM from the IETF is Classical IP and ARP over ATM (CIPA) (RFC2225).
Encapsulation places IP datagram + LLC + SNAP in an AAL5 frame.
PVC mode
  All traffic goes via the CL Server
  Two hops for every transmission
SVC mode
  ATM ARP Server (AAS) used for address resolution
  SVCs set up as needed
  One hop for every transmission
This is referred to as the “Classical” model as it conforms to Logical IP Sub-network (LIS) connectivity model. In the LIS model, all hosts on the same LIS are considered to be directly connected without any router hops. All communication between hosts that are on different LISs must be via a router, even if they are physically connected to the same network.

## Slide 6: Logical IP Subnets
Consider 2 IP subnets on same ATM net
IP rules say packets between them must go via router
Router
ATM
S
D
S does routing as normal
  Use ARP server to get ATM address of router
  Encapsulate and send
Router forwards
Decapsulate
Resolve, encapsulate and send
AAS
AAS
Notes: CIPA treats ATM as a link layer and does not exploit any special features of ATM. In cases where several IP subnets exist on the same ATM network this can lead to unnecessary work.

## Slide 7: Next-Hop Resolution Protocol
Let’s break the rules!
ATMARP server
  Knows mappings for local IP subnet only
NHRP Server (NHS)
  Knows mappings for several subnets
NHS
Router
ATM
S
D
S does routing as normal
  Send to router
  Use ARP server to get ATM address of router
S also asks NHS for D’s ATM address
  Set up VC to D
  Send packets direct to D
AAS
AAS
Notes: The NHRP can be used with all “Non-Broadcast Multiple Access” (in practice VC) networks. This means ATM but also Frame-relay, X.25 etc. The existence of an NHRP Server (NHS) is assumed. This behaves in a way similar to that of an ATM ARP server in CIPA. I.e, hosts register their IP to ATM address mappings and the NHS delivers these mappings on request. The difference is that an NHS may have mappings for several distinct LISs.
Hosts that wish to exploit NHRP need to have a modified routing behaviour. The recommended behaviour is that they begin in “classical” mode. Thus S will determine that D is on a foreign IP network and will perform a routing step which will indicate that packets must be sent via the router – this should work as normal.
At the same time S looks up D’s IP address at the NHS. Assuming D has registered the mapping S will learn D’s ATM address. It can then set up an ATM VCC direct to D and use this to send packets – thus avoiding the router.
(S and D may be hosts but they may also be routers).

## Slide 8: Point-to-point links
Digital circuits
  ISDN links
  Dial-up lines
  ADSL
  ???
Need framing mechanism
  HDLC
  ATM
  ???
Need protocol discrimination
Need authentication?
Notes: Point-to-point links typically provide a duplex, bit-stream. To carry data some kind of framing is required. Traditionally this has been done using HDLC flags. (ATM framing is an alternative).
In principle the links may carry more than one traffic type. Hence there is a need for protocol discrimination. Finally, if a switched service is in use (PSTN or ISDN for example) some sort of authentication and authorisation may be needed before data transfer can begin.
Various mechanisms have been used but the combination of HDLC together with the Point-to-Point Protocol (PPP) predominates today.

## Slide 9: Framing and PPP
Point-to-Point Protocol (PPP) [RFC 1661]
Framing – serial line use HDLC
“Protocol” identifies payload
  IPv4 = 33, IPv6 = 87, BPDU = 49 etc.
01111110
. . .
Flag
Address
Control
Protocol (33 = IPv4)
Data (n bytes)
CRC
HDLC header
. . .
11111111
00000011
00000000
????????
00100001
????????
????????
????????
01111110
Flag
PPP Frame
Notes: Point-to-Point Protocol (PPP) [RFC 1661] provides “a standard method for transporting multi-protocol datagrams over point-to-point links”.
Provides:
Framing – usually HDLC if this is easily available. This would be the choice for dial-up since PC serial ports do HDLC framing and bit stuffing in hardware. In principle the bits in the HDLC control byte can be used to implement an ARQ protocol but this is not normally used.
Protocol identification. PPP typically carries IPv4 but other things are possible
  – IPv6
  - Various PPP control protocols
  - MAC frames for remote bridging etc.
Link management; option negotiation, authentication etc. (see next slide).

## Slide 10: PPP link control
Link Control Protocol (0xC021)
  Used at the start
  Negotiate max. frame sizes, authentication method etc.
Challenge Handshake Authentication Protocol
Client
ISP
Random 19003910…
1
Challenge 19003910…
2
Algorithm
Secret 45230…
Secret 45230…
Result 40036621…
3
Response 40036621…
4
Success/Failure
6
Algorithm
5
Check
Notes: Before it will transmit any real data frames PPP launches the "Link Control Protocol" (LCP). This is a short exchange of packets which establishes that both parties are willing to go ahead and which options are to be used. Options include: the max. size frame to be used; what, if any, authentication should be used and whether data compression should be employed.
It is common to apply authentication at this stage as it gives each party confidence that it is dealing with a known peer who is entitled to establish a link. Several authentication mechanisms may be used, the Challenge Handshake Authentication Protocol (CHAP) [RFC 1994] being a common choice. The protocol relies on the fact that client and ISP share a pre-arranged secret. This acts something like a password which uniquely identifies the client. However, one advantage of CHAP is that this password is never transmitted across what may be an insecure link. The ISP begins (1) by generating a random number which is sends to the client (2). The client feeds this random number together with the shared secret to an agreed "hash" algorithm (3). The output of this algorithm is another number which the client sends to the ISP (4). The hash algorithm is carefully designed so that an intruder who captures both the challenge and response messages is unable to derive the shared secret. The ISP performs the same calculation as the client. If the results match (5) the ISP can be confident that the client is who it claims to be and sends a success message (6). Of course, this assumes that both client and ISP have kept the shared secret secret.

## Slide 11: PPP – Network Control
One “Network Control Protocol” (NCP) per protocol
  One for IPv4, one for IPv6 etc.
PPP Internet Protocol Control Protocol (IPCP = 0x8021) allows negotiation of:
  IP header compression
  IP address (to be used by client)
Once LCP and IPCP negotiation is complete, data transfer can begin
Notes: Having negotiated and authenticated the link there is still one more initialisation stage to go through before data transfer can begin. This is called "network control", the name reflecting the fact that it performs initialisation on behalf of a particular network protocol. This means there are many network control protocols; one for IP version 4, one for bridging, one for IP version 6 and so on. We mention here just one aspect of the PPP Internet Protocol Control Protocol (IPCP) which is used when PPP carries IP traffic. This is the "IP-Address" option which allows a client to request an IP address from an ISP. Given that IP addresses are in short supply. ISPs tend to keep a pool which they hand out to clients as and when they dial in. IPCP provides the mechanism to provide this useful service. (N.B. this duplicates DHCP functionality).
Once we have completed the network control protocol negotiation for our traffic type we are (finally) ready to begin. Traffic now will consist of frames like that in slide 14 with protocol and data field chosen appropriately.

## Slide 12: PPP and ATM
IP
IP data
ATM framing (not HDLC) often used on ADSL links
PPP used for
  Protocol discrimination
  Link negotiation and authentication
  IP address allocation
AAL5 used for fragmentation into ATM cells
Use of PPP fits with procedures designed for dial-up
AAL-5
Trailer
P
PPP Protocol
Notes: ISPs have been familiar with PPP from the early days of modems and dial-up Internet. Their authentication and accounting systems are geared to it even when, as in the case of ADSL, there is really no dialing done.
The slide shows the simplest version of this encapsulation (there are several others) called PPPoA VC-Mux. The “VC-Mux” implies that all frames sent on this VCC will be PPP frames, this must be agreed in advance by the two end-points. If any other ATM traffic is present it must use a different VCC. Note that there is no need to use either the HDLC flags nor its header – only the PPP protocol field is included.
[N.B. there is also a standard for PPP over Ethernet which is sometimes used over ADSL].

## Slide 13: Access to the Internet
Requirements
  Framing between ISP and customer
    PSTN? ISDN? ADSL? Cable? Leased line?
  Customer can choose ISP
    By subscription? On demand?
  How are ISPs identified
    IP address? telephone number? Something else?
  Authentication, authorisation
  Accounting: Who? How much?
  Billing:Tariff, Collection
Notes: Packet service
We need a physical layer to provide a digital service. We need link layer framing
Choice and identification of ISP
Competition rules require that the ISP should be independent of the company which provides the physical connectivity. Ideally we would want to allow the customer to have accounts with several ISPs and be able to switch between them on demand – possibly exchanging traffic with several ISPs simultaneously. The way this is achieved will dictate the means of identifying the ISP.
Security, Accounting, Billing
ISP needs to be able to identify the customer and ensure they are entitled to use the service. ISP then needs to account for usage. Technological, and marketing considerations affect the mechanism chosen.

## Slide 14: Dial-up
Telephone exchange
Session: {customer, circuit, ISP}
Authentication on circuit set-up
Accounting/billing – often based on circuit duration
PSTN/ISDN Infrastructure
ISP A
ISP B
ISP C
Customer
Customer
Customer
Customer
Customer
Customer
Customer
Customer
Customer
Local loops (Dedicated)
Circuits (Switched)
Notes: Typically the customer uses a modem and PSTN. The circuit (telephone call) to ISP is set up at the start of Internet activity and terminated when activity ceases. ISDN usage is generally similar though set up and termination may be more dynamic reflecting the rapid circuit switching. Clearly the customer can have only one circuit (two for ISDN) at a time so access to multiple ISPs is serial rather than concurrent. In principle this model allows the customer to dial-in from anywhere, though security considerations may disallow this.
Circuit set up provides an opportunity for authenticating the user. The authentication is then valid for the rest of the session. Accounting is often based on session duration. This is simple to implement and is familiar model for customers. Calls are typically charged at a local rate. This is simple for the provider to implement since ordinary telephone calls are themselves subject to a duration-based tariff. As an alternative a “flat-rate” tariff may be offered under which customers pay a fixed sum each month. These sums are paid to the ISP which must then pay the PSTN/ISDN provider for the circuit time used by their customers.
Given the high volume of calls to major ISPs, the PSTN/ISDN provider may install permanent circuits from their telephone exchange direct to the ISP – thus removing the load from the normal infrastructure.

## Slide 15: Asymmetric Digital Subscriber Loop
Uses local loop
  POTS + (typically) 576 Kbps downstream, 288 Kbps upstream
  Frequency-Division Multiplexing
N.B. relative bandwidths - Shannon
Notes: ADSL is an advanced way of exploiting the local loop. The local loop provides an electrical connection between the home and the local telephone exchange. It is a simple two-wire circuit typically using twisted pair cable. Although simple, this technology can have quite high capacity – the actual quantity depending on the quality of the wiring (which may be inversely proportional to its age), its length and the amount of external noise. Typical commercial offerings provide 576K bps to 8M bps towards the home (“downstream”) and somewhat less from the home (“upstream”) - the disparity accounts for the use of “asymmetric” in the name. The basis of the technology is Frequency Division Multiplexing (FDM) which is used to provide three logical analogue channels. The slide shows the spectra used for these channels. Three different frequency bands are allocated with gaps in between to prevent interference. The first band (labelled “POTS” for “Plain Old Telephone Service”) is used for ordinary voice traffic. This is needed so that the local loop can continue to provide a telephone service alongside the ADSL data services. The remaining bands are used for upstream and downstream data traffic. Notice that the downstream band has greater width – as one would expect from Shannon’s theorem due to its greater capacity.

## Slide 16: ADSL – organisation
Physical
Logical
Notes: ADSL provides three analogue channels. We need to provide two functions in the home: a splitter to separate the voice and the data channels and provide a separate physical socket for each; and a modem to enable digital data to be sent over the data channels. There is a similar situation at the telephone exchange where a splitter function diverts the POTS channel to the conventional telephone exchange whilst the data channels connect to a device called a “Digital Subscriber Line Access Multiplexor” (DSLAM). Of course the exchange will be dealing with many (several hundred) ADSL connections each of which must be split and connected to the POTS exchange and the DSLAM.
Deregulation means that there may be DSLAMs from several providers at the exchange site.

## Slide 17: ADSL +Internet – typical approach
Need high-speed link to ISP (PSTN infrastructure too slow)
Need switching between ISPs
Use ATM?
Notes: How should we make the connection from customer to ISP? We cannot use the PSTN infrastructure as it provides 64 Kbps circuits at best. An ATM network is one solution since it can have plenty of capacity and allows VCCs to be switched between ISPs as required. Unfortunately VCC switching is not widely deployed. Consequently the VCCs are “permanent virtual circuits” (PVC) that are set up when the customer subscribes to the service and are left in place. These PVCs terminate at a so-called “Layer 2 Tunneling Protocol Access Concentrator” (LAC). A single duplex PVC is established from each home system to the LAC. There is a single PVC from the LAC to each ISP – so traffic from several customers is multiplexed on a single PVC. PPP does not support multiplexing so, between the LAC and the RAS, PPP frames are carried in another protocol (the Layer 2 Tunneling Protocol – L2TP) which includes a “Session Id” field in its headers. Session Ids are used to distinguish traffic belonging to different users.
In the slide we show one LAC and one DSLAM; in practice one LAC would support several DSLAMs (roughly speaking we need one DSLAM at each local telephone exchange).

## Slide 18: ADSL + Internet – the LAC
Duplex PVCs from customers to LAC
Duplex PVCs from LAC to ISPs
LAC authenticates customers
  Customer names include ISP name
  E.g. knight1234@btinternet.com
LAC “extends” PPP connection to ISP
  PPP connections multiplexed in L2TP
LAC relays data between customer and ISP PVCs
Notes: When a customer’s equipment wishes to begin communicating (typically at boot time) it initiates a PPP connection to the LAC - there is no need for it to do anything to establish ATM connectivity, it simply uses the existing PVC. During PPP set-up, the home system authenticates itself to the LAC identifying itself with a name of the form <username>@<ISP domain name> – for example knight1234@btopenworld.com. A user may have several such names registered with the LAC, each one corresponding to a different ISP. Assuming the proffered name matches one of these, the LAC “extends” the PPP connection to the appropriate ISP “remote access server” (RAS) using the already established PVC (and L2TP). This allows limited flexibility to the user who, by choosing the appropriate name can select from amongst several ISPs with which they are registered.
[Note that the “home PCs” shown could just as easily be routers providing access to a home network.]

## Slide 19: ADSL + Internet - Summary
ATM PVCs provide “link” between customer and ISP
LAC allows PVCs to be “switched” between ISPs
PPP used for protocol identification authentication and IP address allocation
PPP
AAL5
ATM
ADSL
ATM
ADSL
ATM
PHY
ATM
PHY
ATM
PHY
PPP
AAL5
ATM
PHY
PC/Router + Modem
ATM switch in DSLAM
LAC
ISP RAS
IP
IP
AAL5
L2TP
L2TP
AAL5
Notes: The protocol stacks show the situation once everything is set up correctly. During set-up, the customer’s system negotiates with the LAC. At that point, the PPP and AAL5 layers terminate at the LAC. After negotiation they are “extended” as shown in the slide.

## Slide 20: ADSL Example 1
Notes: This information was taken from the status screen of an ADSL router.
For information (not examinable).
G.dmt – denotes the standard which specifies details of the modulation in use.
-38 dBm/Hz - Engineers often express power as a ratio with 1 milliwatt and then convert to decibels. In this case the power has first been divided by the bandwidth to give a measure of the average power across the frequency range.
SNR Margin – ADSL modems can vary their power and will raise it in the presence of noise. The SNR margin is target ratio the modem tries to maintain.
Line Attenuation – the ratio of the power of the transmitted signal to the power of the received signal. So 30dB = 10log10(x) => x = 1000. So only one thousandth of the signal survives.

## Slide 21: ADSL Example 2
Notes: The slide shows configuration information from an ADSL router.
Notes
1. The VPI/VCI numbers identify a PVC from customer to LAC and seem pretty standard in the UK. Of course, it does not matter that everyone uses the same numbers VPI/VCI have only local scope.
2. Service category is UBR, CBR is also selectable – though I doubt the service would support it.
3. Encapsulation identifies the standard used to send IP over ADSL and is one of several possibilities. PPPoA VC-MUX implies PPP frames are carried in AAL5 over ATM. The “VC-MUX” implies that, if protocols other than PPP are to be carried then a distinct VCC should be used.
4. MRU/MTU Maximum Receive/Transmit Unit – specifies the maximum size of IP frames that can be carried.
5. MSS I think this is a hack to modify the MSS in TCP SYN packets to a value suitable for the PPP MTU.
6. Authentication is in use and the CHAP protocol is employed.