## Slide 1: Channel Capacity
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Signals and signal representation
Analogue and digital: introduction
Signal representation
Signal spectra
Signal bandwidth
Channel capacity: noise and bandwidth

## Slide 3: Questions
What is the difference between analogue and digital representations?
  why use digital?
How do we describe and characterise signals?
Characteristics of a communication channel:
  constraints: noise and bandwidth
  why can we get 1Gb/s on Ethernet, but not on ADSL?
Notes: We are concerned with the transmission and reception of some kind of signal across a communication channel. Communication channel is an abstract concept. It could mean a piece of wire or fibre, a network or the air in a room in which people are talking. We do not involve ourselves too deeply with the particular details of any particular medium (e.g. copper wire or optical fibre) but look at some general issues concerning any (all) communication channel(s).

## Slide 4: Analogue and Digital Representations [1]
Analogue
Signal level is analogue of information value
E.g. microphone – electrical wave mirrors sound wave.
Typically continuous, smoothly varying
  voice/speech, video
Easy to capture:
  mature (old!) technology
Digital
Information represented by an encoding
Discrete signal levels:
  E.g. written text, numbers, morse code
  Sampled speech
Anything can be converted to a digital representation
New(er) technology
time
time
Notes: We are trying to transmit information. Information must be represented as some physical quantity. Analogue representations use a physical quantity which varies in a way which mirrors changes in the information. For example, if the information is a stream of spoken words, it comprises a continuously varying air pressure. A microphone converts this to a continuously varying electrical voltage – the voltage is (ideally) proportional to the sound pressure. The electrical signal is the “analogue” of the sound. Analogue signals are typically “smoothly varying” and may take any values within some restricted range.
Digital representations use some form of encoding. The resulting signals consist of discrete symbols. Each symbol must be represented by a discrete value of some physical quantity. Familiar symbols are the letters of the English alphabet and the Arabic numerals represented by shapes drawn on paper. Here is an example of an encoding with 28 symbols.
Computers today use binary representations of symbols; consequently, it is common to encode symbols as a series of bits. Familiar coding schemes are ASCII for the English alphabet and binary numbers for Arabic numerals; both of these are binary codes. However, non-binary codes are used in some digital communication systems.

## Slide 5: Analogue and Digital Representations[2]
Analogue:
  continuous, infinite range
Transmission:
  subject to noise in media
  interference, e.g. radio
Digital – discrete “symbols”
E.g. Binary numbers:
  1010102  42
  Only have to transmit and receive ones and zeros:
  e.g. use two approximate voltage levels
time
Notes: One of the benefits of digital transmission becomes clear if we consider noise (see later) and how information is transmitted. In both analogue and digital transmission, a physical quantity must be transmitted. In the case of analogue transmission, this requires the original signal be somehow converted into the transmitted signal while maintaining the relative signal strengths (signal amplitude or “volume”) from the source. As the signal is transmitted across the transmission medium (e.g. copper, or radio channel) it is subject to noise, including interference from other signals (man-made and natural). This makes it harder to detect the original signal at the receiver. The problem is that, with a source that produces an infinitely variable signal, how do we spot the perturbations due to noise rather than the natural changes in the signal? Clever electronics and some knowledge about the noise signal can help to filter this noise, but not totally remove it.
With digital systems the noise still affects the transmitted signal but we are transmitting discrete symbols. For example, for binary data we could use two voltage levels. Even though we add noise to the signal, we can always decide whether the received voltage is close to the 1 or 0 level. Of course, if there is a lot of noise we will often be wrong. However, if we intercept the signal before “too much” noise has accumulated we can recover (and regenerate) the original signal with arbitrary accuracy.

## Slide 6: Digital Representation - Summary
High fidelity:
  better error control (detection and correction)
Source independence:
  “anything” (audio, video, etc.) can be digitised
Time independence:
  transmission rate  recording/capture rate
Encoding:
  security
  compression
Notes: The use of digital signals has great advantages over analogue systems. These are:
high fidelity: in principle, the discrete nature of digital signals makes it easy to recover the signal even when corrupted by noise. Very high quality transmission is possible.
time independence: a digital signal is a stream of symbols and so may be transmitted at a rate that is different from its recording rate.
source independence: the digital signals may represent information from a variety of sources ; voice, video, data etc.
signals may be encoded: the same information may be transmitted using a wide range of numbers or bit patterns (symbols), allowing the original information to be encoded in some way, e.g. encrypted or compressed.
The main disadvantage are the overheads involved in encoding into a digital form and subsequent decoding. This can be quite complex and can cause delay.

## Slide 7: Communications Channels
Communications Channel – abstract, generic concept
Transmitter (Tx), Receiver (Rx)
Signal – something that represents information
Noise – anything that interferes
  Electrical interference, cosmic rays etc.
  Attenuation – signal gets weaker with distance
  Distortion – frequency dependent attenuation
Bandwidth – difference between highest and lowest frequencies carried by a channel (Cycles/sec or Hertz (Hz))
Capacity - maximum rate at which information can pass (Bits/sec or symbols/sec (baud))
communication
channel
Rx
Tx
noise (+distortion)
Notes: Physically a communications channel could be copper wire, optical fibre a radio channel through the atmosphere or the air in a lecture theatre. The transmitter contains mechanisms (typically electronics) to ensure information is in a suitable form for transmission. The receiver and other parts of the communication system have to cope with noise.
Noise comes from many sources: other signals in nearby wires (cross-talk) or from the atmosphere (radio signals); radio signals from space, signals induced by strong magnetic fields (e.g. electric motors) and a whole host of other sources. Optical transmission is immune from such electro-magnetic (EM) interference. However, all media are subject to thermal noise, which (in most practical) situations, is impossible to remove. Also, the medium itself may distort and/or attenuate the signal. This is due to the physical nature of the medium and can also be hard to counteract.
The bandwidth of a channel is an important quantity as it is one of the main determinants of its capacity. In fact, the term “bandwidth” is often used (loosely and inaccurately) to mean “capacity”. We rarely know channel bandwidth precisely. For example our ability to hear diminishes as the frequency of sound increases but there is no hard cut-off.
Capacity may be measured in bits/sec or symbols/sec (= baud). If the symbols are binary then these two measures are the same. However, if the symbols can take (say) 8 levels then each symbol corresponds to 3 bits (23 = 8) and the bit-rate will be 3 times the baud-rate.

## Slide 8: Channels and Signals
Signals may be analysed -> signal bandwidth
Channel must be suitable for signal it carries
  In particular channel bandwidth > signal bandwidth
Suppose signal has frequency range from 400 Hz to 3400Hz
  signal b/w 3kHz
Suppose channel has effective frequency range from 1kHz to 9kHz
  channel b/w 8kHz
  channel bandwidth > signal bandwidth
But we need to modify signal so it fits the channel
  Modulation – e.g. radio
Notes: Signals (such as the human voice) can be analysed and their bandwidth can be approximated. If the signal bandwidth is less than the channel bandwidth the something will be lost, which is generally undesirable (but see below). So a high bandwidth signal requires a high bandwidth channel which generally costs more.
Even if a channel has sufficient bandwidth it may not carry the “right” frequencies. In general though we can modify the signal so it fits the frequency range carried by the channel. For example audio signals must be modulated so they fit the frequency range of a radio channel.
Note that sometimes we may accept the loss of some frequencies from a signal provided what remains is useful. For example, the telephone system has traditionally filtered the human voice leaving only the frequencies between 400Hz and 3400Hz. This is much less than the full range of the voice but is enough for intelligible speech.

## Slide 9: Signals and spectra [1]
Time domain:
  variation of signal in time
Frequency domain – spectrum:
  discrete – zero bandwidth
-0.5
0.5
-1
0
1
-0.4
-0.2
0
0.2
0.4
0.6
0.8
1
time
sinusoidal wave
A
T = 1/f

0
0.2
0.4
0.6
0.8
1
1.2
0
0.2
0.4
0.6
0.8
1
1.2
1.4
frequency [Hz]
sinusoidal wave
Notes: Quick revision …
Most signals carried by communication channels are modulated forms of sinusoidal waves. A sinusoidal wave is described mathematically by the expression:
s(t) = A cos (t + )
The quantities A, , and  are called the amplitude, frequency and phase of the wave, respectively. We can describe this signal in two ways. One way is to describe its evolution in time (time domain model) and the equation for s(t) is a mathematical representation of this evolution. The second way is to describe its frequency content (frequency domain model). The cosine wave, s(t), has a single frequency,  = 2f.
The time taken for the wave to go through one complete cycle is called the period and is usually denoted by the letter T. The frequency of the signal, ( f = 1/T) is the number of cycles the signal completes per second and has units Hertz (Hz). Most mathematical treatments use units of radians per second ().
A sinusoidal wave alone tells us nothing (other than if it is present or not present) – it carries no information. Signals which carry information are aperiodic though, as we will see, such signals can be analysed in terms of sinusoidal waves.

## Slide 10: Signals and spectra [2]
Fourier Theorem:
  sinusoidal components
0
0.2
0.4
0.6
0.8
1
1.2
0
2
4
6
8
10
12
time
square wave
0
frequency [Hz]
square wave
1
2
3
2
5
2
7
2
9
2
Notes: Fourier’s Theorem states that any periodic signal can be represented as a sum of sinusoidal components of varying amplitude and frequency. For example, a square wave can be represented by the expression:
The period of the square wave is 2 secs so the frequency is 1/ 2 Hz. This is also the frequency of the first component in the Fourier series – sin(t). However, the next component – sin(3t) has a frequency 3 times as much and the next – sin(5t) 5 times as much.
The diagram on the right shows the spectrum of the square wave. For a periodic function this will be discrete.
[Note. For a proper analysis of aperiodic waves you need Fourier Transforms which are beyond the scope of this course.]

## Slide 11: Signals and spectra [3]
Notes: We can examine the contribution each component makes to the final waveform. We note that as more components are added they make the waveform appear more and more like a square wave. We can see that the higher frequency components add detail whereas the lower frequency components are responsible for the basic shape and the amplitude of the signal – most of the signal power is in the first components. This is an important result, and applies to many “real” signals which are aperiodic, such as voice and video, not just periodic square waves and pulse trains.

## Slide 12: Channel Bandwidth and Digital Signals
High-frequency components are lost
  Symbols (hence information) still recoverable
0
0.2
0.4
0.6
0.8
1
1.2
0
2
4
6
8
10
12
time
square wave
Notes: The analysis of a square wave yields an infinite series hence, theoretically, an infinite bandwidth. This is generally true of digital signals.
Real channels, of course, have a finite bandwidth. Fortunately, as the slide shows, losing the high frequency components of a digital signal still leaves much of it intact. Hence the symbols and consequently the information they carry may still be recovered.

## Slide 13: Analogue to digital conversion (ADC)
signal
sampling signal (freqency s)
0
1
2
3
4
5
6
7
8
quantisation
levels
Problem 1 – are we sampling often enough?
  Nyquist sampling theorem:
  s  2F
Problem 2 - precision
  Must round measurements
  quantisation error (noise)
  b bits/sample => Q = 2b quantisation levels
  b = log2(Q)
Audio, video – need to convert analogue signal to digital
Measure height of wave at regular intervals
Notes: In order to send analogue signals over a digital communication system, or process them on a digital computer, we need to convert analogue signals to digital ones and back again. This is referred to as coding and decoding and the hardware or software that dose it is called a CODEC.
The slide shows how coding is equivalent to measuring the height of the waveform at regular intervals. It also shows that rapid changes in the original signal will be lost if the sampling frequency is too low. Harry Nyquist proved that all will be well provided the waveform is sampled at a rate s equal to at least twice the maximum frequency i.e.
s  2F
Sampling at rates greater than 2F does not give any advantage.
Each sample yields a height which must be represented as bits. If we allocate b bits per sample than have just 2b quantisation levels and must round to the nearest of these. This rounding introduces a quantisation error. The more bits we use the smaller the quantisation error will be.
Example, Pulse Code Modulation (PCM), as used in telephony, uses just this method, with 8000 samples per second (s = 8KHz) and 8-bit quantisation (256 levels), hence the data rate of such a PCM stream is 64kb/s.

## Slide 14: Channel Capacity - Nyquist
Nyquist says:
  Sample rate must be at least s = 2F to retrieve all the information in the signal
  Sampling faster than 2F does not yield extra information
We can regard the samples as a set of symbols of a digital data stream
  How much information can this stream carry?
  There cannot be more than 2F symbols per sec (baud)
  (Otherwise we would be extracting more information than Nyquist says we can)
Suppose we have Q quantisation levels
  log2Q bits/sample
  bit rate is slog2Q = 2Flog2Q bps
If we know a signal has a max. frequency F then
  Its maximum information rate is 2Flog2Q bps
Also, if a channel carries a maximum capacity of F then
  Its capacity C = 2Flog2Q bps
Notes: The slide shows an important argument which takes us from the sampling theorem to a result which relates the capacity of a channel to the maximum frequency it transports.
We can see that this capacity also relates to the number of quantisation levels which, as we will see, is limited by the noise that is fed into the channel.

## Slide 15: Channel Capacity with Noise - Shannon
How many quantisation levels can there be?
  i.e. how many bits per symbol?
Number of distinct symbols is limited by noise
E.g. suppose 8 symbols at 1v intervals
  If noise adds 0.25v we will interpret voltage correctly
  if noise adds 0.75v we won’t
Shannon: no. of distinct symbols =
  S, N are signal and noise power
No. of bits/symbol =
Thus Channel capacity C =
Notes: If we could distinguish an infinity of distinct symbols (voltages, colours of light etc.) then channel capacity would be infinite. In practice the number is limited by noise; interference which tends to transform one symbol into another.
Claude Shannon showed that, with reasonable assumptions, a limit could be placed on the maximum number of distinct symbols given a particular signal to noise ratio. He also introduced the concept of the bit as a unit of information. This enabled him to calculate a maximum information carrying capacity of a channel (in bits/sec) as shown in the slide.

## Slide 16: Channel Capacity – Shannon - Finally
Suppose a channel passes a max. frequency F and a min. frequency f
  The lower limit means a capacity of flog2(1+S/N) is unavailable
  Remaining capacity C = (F-f)log2(1+S/N)
C = Blog2(1+S/N), where B is the “bandwidth”
  This is the Shannon-Hartley Theorem
Notes: The slide shows the normal statement of the Shannon-Hartley theorem. It is a fundamental theorem of communications. Note that we have not proved it with any sort of rigour. Instead we have illustrated how it is related to Nyquist’s theorem. Nyquist’s theorem (as stated) applies when bandwidth is limited above but not below. However, Shannon’s theorem is true when bandwidth is restricted above and below.
This is an important and fundamental result up along there with e = mc2 etc!

## Slide 17: Signal and noise – SNR
Noise always present in a communication system
Meaningful assessment of noise needed
Signal to noise ratio – SNR:
  ratio of signal power (S) to noise power (N)
  usually quoted in dB (deciBels)
  SNRdB = 10log10(S/N)
Typical SNR is 1000  30dB:
  3dB  factor of two increase/decrease
Notes: Noise is ever present and, as we have seen, affects the capacity of the communication channel. A meaningful assessment of the effect that noise has on a communication channel is not to look at the absolute amount of noise in isolation, but to assess the relative strength of the noise to the strength of the transmitted signal. Engineers measure signal strength in terms of signal power which can be measured using the appropriate equipment. So the measure used for assessing the performance of a channel with respect to noise is the signal to noise ratio SNR.
Note that SNRdB = 10log10(S/N) dB (deciBels), where S is the power of the transmitted signal in Watts (determined by system design) and N the noise, also in Watts.
For example, suppose we double S/N and re-compute SNRdB. This will give:
SNRdB = 10log10(2xS/N) = 10(log10(2) + log10(S/N))
= 10(0.301 + log10(S/N))  3 +10log10(S/N)
So doubling S/N is roughly equivalent to a 3dB increase in SNRdB.

## Slide 18: Channel capacity example
For example local loop (copper wire from home to telephone exchange.
  B = 1.5MHz, SNR = 20dB (typical)
  20 = 10log10(S/N)  S/N = 102 = 100
Shannon:
Channel capacity increased by:
  greater (more) bandwidth
  greater (better) SNR
Notes: The channel capacity C of a communication channel is a measure of its maximum theoretical information carrying capacity and is measured in bits/s (bps). Note that this theorem states what is possible and not how it might be achieved!
The example is for a copper local loop – the wire that runs between the home and the local telephone exchange. The actual numbers will be affected by the quality and length of the wire. The calculation is, of course, relevant to ADSL.

## Slide 19: A Noisy Example
Wireless channel: plenty of bandwidth but lots of noise
Shannon
Suppose we want C=1Mbps but SNR is –10 dB
VERY noisy!
Notes: The slide shows that, in principle, we can defeat the noise if we throw enough bandwidth at the problem – but we need lots! (Note that the SNR here is 10-1 – i.e. there is 10 times as much noise as there is signal.)
We need a way to spread our signal over a huge range of frequencies. In a later note we look at a spread-spectrum technique which is designed to do this.

## Slide 20: Properties of different media
Copper:
  twisted pair, co-ax, parallel
Radio, microwaves:
  lower frequencies, higher frequencies, satellite
Light:
  free space and optical fibre
Why do we use many different media?
What are their relative advantages and disadvantages?
Notes: There are many different media used for interconnecting communications equipment; wired connections made of various copper cabling to optical fibre based systems, as well as systems that use radio or light through the atmosphere. We look briefly at these various different forms of media.

## Slide 21: Copper cabling – twisted pair
Cheap – widely available
Versatile
Easy to connect
Subject to interference
Signal “leakage”
Relatively high attenuation
Widely used:
  smart Tx/Rx electronics at termination
  speeds upto 1Gbps
telephone
wire
Ethernet
cable
(CAT5 UTP)
with plug
(RJ45)
Notes: A transmission line is a pair of conducting wires held apart by an insulator or dielectric. They come in a variety of constructions. The simplest and least expensive form is two-wire cable or copper-pair. Unshielded twisted-pair (UTP) cable consists of (often sets of) two wires sheathed in an insulator and twisted together. Shielded twisted pair (STP) cable contains (often sets of) two wires sheathed in a insulator as for UTP, but now surrounded by a conducting foil shield that provides some protection from external signals.
Twisted-pair is by far the most common form of datacomms in the LAN. CAT5 UTP (Category 5 unshielded twisted pair) with and RJ45 plug is the wiring/connection used in most LAN installations. This will support up to 1Gbps.
Twisted-pair is also the telephone wire that comes into your home. It has reasonable propagation characteristics, but is subject to interference and cross-talk. Recent developments in line termination equipment has enabled high data rates (several Mb/s) over distances of several hundred metres, i.e. using digital subscriber line (DSL) technology.
Twisted pair becomes impractical for use at high electrical bandwidths – above ~200MHz. At such high bandwidths, it is only usable for short cable lengths.

## Slide 22: Radio, Microwaves etc.
Easy to set-up network:
  no wiring
High data rates possible
Mature technology:
Local and nationwide
Global – satellites
Interference
Security
Spectrum regulation
Safety
Notes: Propagation of waves in free-space is different from that in cable. With respect to signal propagation, cables are one-dimensional systems, and the signal is attenuated relatively little as travels along the cable. With radio, in three-dimensions, waves radiate spherically. For each doubling of the distance between the source and receiver, a 6dB loss is experienced. For all frequencies up to millimetre-wave frequencies, this free-space loss is the most important source of loss. Free-space systems usually require much more power than cable or fibre systems.
However, radio systems generally are relatively easy to set-up and there is much mature technology to support radio transmission and reception.
Radio spectrum is subject to international regulatory control, so it is not possible to use just any part of the spectrum at will – you have to obtain a licence. The regulations govern not only which parts of the spectrum are used but also give rules about the power output of transmitters in order to minimise interference with other parties who may be using the same frequencies in another geographical area. There are some frequency bands set aside for industrial, scientific and medical (ISM) use, however and these are used for wireless LANs at low power.
Also, by their very nature, one must be concerned about security as the radio broadcast is receivable by anyone within range of the transmitter and having suitable equipment.

## Slide 23: Light and Infra-red – free space
High data rates possible
No interference from radio/electrical signals
No regulations
Safety:
  laser sources need care
Line-of-sight:
  clear path
  may need to use diffusers/reflectors
Mainly infra-red
Uses:
  (remote control handsets)
  connections between laptops and peripherals
  small mobile systems, e.g. PDAs
  floor-floor communication (e.g. within lift-shafts)
Notes: As with any light-based system, the transmission path is immune to electromagnetic interference. However, use of light in free space is restricted to clear line of sight paths (or approximately line of sight paths). In some scenarios, e.g. connectivity between peripheral devices and a computer, personal digital assistants (PDAs), and remote control hand-sets, the signal can be propagated by reflections from walls and ceilings within a room.
Unlike radio communication, there are no regulations that govern the use of light for free-space transmission systems. High power lasers are often a good source of light for transmission but care must be taken that they do not damage human sight.

## Slide 24: Optical fibre [1]
Cladding
stepped
index
Core
Multiple paths take different times
Pulses “spread” restricting distance and bit-rate
graded
index
Multiple paths take similar times
Less “spread” -> greater distance and bit-rate
mono
mode
Single path
Greatest distance and bit-rates
Notes: The use of optical (light) waves as a carrier wave provides an enormous potential bandwidth. Optical carriers are in the region of 1013Hz to 1016Hz, i.e. three to six orders of magnitude higher than microwave frequencies. Optical fibre is a waveguide. The fibre consists of a core of glass of one refractive index, and a cladding of a slightly lower refractive index. The fibre is then surrounded by a protective sheath. Fibre optic cable is available in three basic forms:
Stepped-index fibre. The core has a uniform refractive index throughout. This generally has a core diameter of 100m to 500m. Light reflects from the boundary between cladding and core. Multiple paths (or “modes”) are possible and light following different paths takes different times leading pulse gradually to spread. Distance and/or bit-rate must be restricted to prevent pulses interfering with their neighbours.
Graded-index fibre. The core has a refractive index that gradually decreases as the distance from the centre of the fibre increases. This generally has a core diameter of 50m. This is also a multi-mode fibre. However, the paths are of similar lengths so that spreading is reduced.
Mono-mode fibre. As the name suggests this fibre is that allows only a single ray path. The radius of the core of this type of fibre is much less than that of the other two, however it does have a uniform refractive index.
From step-index to graded-index to mono-mode fibres, we find that costs increase in return for longer transmission distances and higher capacities.

## Slide 25: Optical fibre [2]
Very high data rates (Gbps and Tbps)
No RF interference
Secure
Low signal loss
Small cable dimensions
Relatively expensive
Hard to connect cabling
Multi-mode + LED:
  most common
  LAN, a few Km
  need repeaters for long runs
Mono-mode + laser diode:
  higher data rates
  longer cable lengths possible
  more expensive
  harder to connect
Costs ~25% more than quality copper:
  connections still more expensive
Notes: In addition to the potential bandwidth, optical fibre communication offers a number of benefits:
  size, weight, flexibility: optical fibres have very small diameters. A very large number of fibres can be carried in a cable the thickness of a coaxial cable.
  electrical isolation: optical fibres are almost completely immune from external fields. They do not suffer from cross-talk, radio interference, etc.
  security: it is difficult to tap into an optical line. It is extremely difficult to tap into an optical line unnoticed.
  low transmission loss: Modern optical fibre now has better loss characteristics than coaxial cable. Fibres have been fabricated with losses as low as 0.2dB/Km and less.
The primary disadvantage of optical fibre are the technical difficulties associated with reliable and cheap connections and the development of an optical circuit technology that can match the potential data-rates of the cables.

## Slide 26: Summary
Analogue vs. digital
Waves and signals
Bandwidth
Noise
Sampling – Nyquist-Shannon:
  maximum rate of change of signal
Channel capacity – Hartley-Shannon:
  capacity and bandwidth are directly related
  other factors affect channel data rate
Physical media
  Copper wire, radio, microwaves, light and fibre