## Slide 1: Real Networks
Graham Knight
Room 112, Ext. 7366
G.Knight@cs.ucl.ac.uk

## Slide 2: Example Networks – X.25
First version 1976
Specifies “interface” between host and network
  An access protocol
Level 1 - Physical level - X.21 (like RS232c)
Level 2 -Data Link Level - LAPB
  HDLC framing, ARQ protocol for error and flow control
Level 3 - Network Level - X.25 PLP
  Multiplexes VCs onto data link
  Separate flow control on each VC - ARQ protocol again!
Notes: The ITU-T (formerly CCITT) began work on a recommendation for access to public packet-switched networks in 1974. The result, X.25 appeared in1976. The recommendation focuses solely on access - i.e. the interface between the customer's equipment and the switch to which this is attached. Although X.25 terms this an "interface", in terms of the OSI model this is a protocol - specifically an "access protocol". The designers partitioned their problem into three "levels":
  Level 1 The physical level which concerned physical and electrical aspects.
  Level 2 The data link level which enhances the basic physical connection by providing error recovery and flow control. Note that the scope of the error and flow control is confined to the customer-network link.
  Level 3 The network level which enables the customer to request the network to set up "virtual calls" to other customers and send and receive data. Note that a "virtual call" is not quite the same thing as a "virtual circuit" - X.25 applies no constraints on whether the network has a VC or a datagram organisation internally. Customers may multiplex virtual calls to several destinations concurrently. Each of these virtual calls can be individually flow-controlled and is "reliable" - which means that the network takes the responsibility ensuring that every packet is delivered correctly and in sequence. (Like all such guarantees, this one is probabilistic rather than absolute).

## Slide 3: X.25 Components
Notes: The scope of the three levels and the relationships between the various components is shown in the slide. X.25 uses the term "Data Terminal Equipment" (DTE) for the customer's equipment (i.e. the host) and "Data Circuit Terminating Equipment" (DCE) for the provider’s (the local switch). The picture reflects the world of 1976 where the connection between the customer's premises and the network would have been via an analogue leased line equipped with a pair of modems. Although one modem would be on the customer's premises, it was logically part of the DCE. In 1976 it would probably have remained the property of the network provider and be rented by the customer. The Physical level interface, therefore, was a computer-to-modem interface and closely resembled the RS232c interface which is provided by the serial port of a modern PC. As transmission technology developed, alternative physical level interfaces were added.
The data link level had to provide framing, error and flow control. Here, the ITU borrowed from an existing protocol developed by IBM and called "Synchronous Data Link Control" (SDLC). There are now a large number of variants of this protocol of which "High-level Data Link Control" (HDLC) is the best known. The X.25 version is called "Link Access Procedure B" (LAPB). These are robust, ARQ protocols - as they needed to be to provide acceptable reliability over error-prone analogue lines.

## Slide 4: X.25 Level 3 PDUs
Notes: The network level can be viewed by the DTE as a set "logical channels" each of which is identified by a small integer - a "logical channel number" (LCN). Each logical channel can be the first hop of a virtual call to a remote DTE - one virtual call is shown in the previous slide. One parameter of an X.25 interface is the maximum number of logical channels that may be used concurrently. Generally, the more you want, the more you pay.
In order to set up a virtual call, the DTE chooses an unused logical channel and sends a CALL REQUEST packet to the DCE including the appropriate LCN. If the call sets up successfully, the DTE may now send and receive data on it. The slide shows the packets used in the Level 3 protocol, which is known as "X.25 Packet Level Protocol" (X.25 PLP). This is another robust, ARQ protocol with sequence and acknowledgement numbers to provide flow and error control. Flow control uses sliding windows supplemented by as stop/go scheme (The RECEIVE NOT READY/RECEIVE READY packets). Note that these controls apply to individual virtual calls - so that one virtual call may be flow-controlled whilst the others continue unconstrained. The CALL and CLEAR packets can be regarded as user to network signalling. Since these are carried within the logical channel that is used for data, this is an example of in-band signalling.

## Slide 5: Example Network – N-ISDN
Modern Public telecommunications system consists of digital trunks interconnecting digital switches
Digital paths may be set up at 64Kbps, 2.048Mbps etc.
Infrastructure can support various (digital) data services as well as voice
An “Integrated Digital Network”
But ... different services have different interfaces
Integrated Services Digital Networks offer multiple services through a single interface (in theory)
Notes: From the 1970s onwards telecommunications networks began to use digital communication internally. This was suitable for carrying not only voice but also data. Thus, for example, a public X.25 network would share the same physical infrastructure as the voice network. This multipurpose infrastructure is called an “integrated Digital Network” (IDN).
The IDN integrates services internally but presents itself to customers as a set of discrete services; voice telephony, digital leased lines, packet-switched network and so on. Customers need physically different network termination equipment to access these different services each with its separate physical connection to the local exchange. The “Narrowband - Integrated Services Digital Network” (N-ISDN) concept addresses this difficulty. The idea is that all the different service types offered by an IDN should be accessible through a single, digital interface. In order to be economically viable, N-ISDN had to make as much use as possible of what already existed. Two important conclusions were drawn from this:
  N-ISDN should be based on the existing multiplexing structure of the IDN - i.e. of 64 Kbps bit-streams and multiples thereof;
  N-ISDN should be accessible over the existing copper local loops.

## Slide 6: N-ISDN Service
Circuit-switched 64Kbps digital
Basic Rate interface
  Two 64Kbps “B-Channels” through copper local loop
Primary Rate interface
  30 64Kbps “B-Channels” through 2Mbps co-ax cable
Common channel signalling
  Out of band
  One signalling channel (“D-Channel”) per interface
    BR - 16Kbps, PR 64Kbps
Circuit-switched service is in the Physical Layer of the OSI model
Notes: The question then arose as to how many 64 Kbps channels could be provided over the existing copper loop technology? In fact, these loops varied greatly in quality; some would were old, covered long distances and would never really be suitable, others were new, comparatively short and could carry digital data quite efficiently. Eventually it was decided that two 64 Kbps channels could be supported on sufficient local loops to make it worthwhile. The fact that it was two channels rather than one was vital from the marketing point of view. N-ISDN had to offer some added-value. It would have been difficult to sell a single-channel service which would allow users to make one voice-call at a time - which they could already do. Further, users would have to invest in expensive digital telephones in order to use the service. Remember that all this was planned in the late 1970s long before anyone anticipated a market for high-quality data services in the home. Two channels at least offered the possibility of two concurrent voice calls through the existing local loop.
The interface provided to customers over the local loop is called the "Basic Rate Interface". This supplies 2 x 64Kbps "B-channels" plus 1 x 16Kbps "D-channel" for signalling - 144Kbps full duplex in total. In practice, slightly more is needed to cover framing overheads. A common system alternates bursts at 80Kbaud in each direction. Each signal has 4 possible amplitudes and so carries two bits. This gives 160Kbps. Common channel, out-of-band, signalling is used so that the signalling channel is always available even when both B-channels are in use. This allows things like "call waiting" to be signalled to users without disrupting existing conversations. The signalling protocol is packet based and supports a rich range of “supplementary services” such as call diversion, camp on busy, conference calls etc. In fact, this rich range of signalling was seen as another example of the added value of N-ISDN.
N-ISDN also offers a "Primary Rate Interface". In Europe this offers 30 64Kbps B-channels and one 64 Kbps D-Channel - which does the signalling for the other 30. This is often referred to as 30B+D, the US equivalent is 23B+D. The Primary Rate Interface was intended mainly for connecting digital “Private Branch Exchanges” (PBX) to the N-ISDN.

## Slide 7: Typical BR-ISDN usage
Notes: The slide shows the sort of configuration that is possible. This shows a PC with an N-ISDN card which is equipped with a CODEC. The card can set up B-channel calls on behalf of the PC. It can also interpret the DTMF signalling from the analogue phone, convert this to N-ISDN signalling and so make ordinary voice calls. Clearly, with two B-channels available, we can have concurrent voice and data calls. "NT" is the "network termination" which is physically represented by the box the provider fixes on the wall. The one shown is offering the so-called "S-interface" which actually allows up to eight ISDN devices to be attached - though, naturally, only two may be in use concurrently.
N-ISDN is a new interface to the existing IDN, it is not a new network in its own right. A 64 Kbps circuit set up via N-ISDN signalling is no different from a circuit set up via DTMF signalling down a conventional analogue local loop. A 64 Kbps PCM voice stream generated by the CODEC in the slide is no different from one generated by the CODECs at local exchanges. All this means that the telephone in the slide can call any analogue phone - not just those connected via ISDN. On the other hand, only N-ISDN equipment sees the raw 64 Kbps bit-stream. If this is to be used to carry data then we must have ISDN equipment at both ends.

## Slide 8: ISDN and the Internet
Internet access
  Network layer – IP
  Data-Link layer – HDLC framing + PPP
  Physical layer – ISDN B-Channel
Call set up on demand
Notes: Most ISPs now offer N‑ISDN connections to customers as an alternative to conventional dial-up via MODEMs. Notice that, in terms of the OSI model, a bit-stream service is a Physical Layer service. In order to connect to the Internet, we need to provide Data Link and Network Layer functions. The Network Layer is simple - we use IP. In the Data Link layer we just require framing - N‑ISDN B-Channels are comparatively error-free so we do not need Data Link error control. The normal choice is the Internet "Point-to-Point Protocol" (PPP) which provides, framing, some security, and protocol identification. The latter allows a link to be shared between IP and other Network Layer protocols.

## Slide 9: Example network – Frame Relay
Evolution from X.25
  Higher speed
  Lower and less variable delay
Initially proposed by CCITT
No error control, no flow control
  All that is left of Level 3 is LCNs!
  Move multiplexing to Level 2, drop Level 3
CO Layer 2 service with multiplexing
Logical channels - called Data Link Connections - established to remote DTEs
Notes: X.25 PLP and HDLC are heavyweight protocols and, each time a packet is forwarded, sequence numbers must be checked, acknowledgements generated and so on. Worse, this must be done for level 2 and for level 3. This imposes a very large processing load on the packet-switches, especially with modern networks which need to support much greater packet rates. Furthermore, delay-sensitive applications cannot tolerate the highly variable end-to-end delays produced by ARQ error recovery and would prefer not to have it. In any case, it can be argued that heavyweight error control is unnecessary on modern fibre-optic, digital technologies in which errors are inherently rare. Frame relay emerged from an examination by the ITU of what a modern X.25 should look like. The conclusions were:
  Remove all error control and flow control. These become the responsibility of the hosts;
  Retain the ability to multiplex traffic to several destinations concurrently;
  Retain sequenced delivery and elimination of duplicates;
  Retain the CO service;
  Use out-of-band signalling to set up connections.
With all the error-control, flow-control and signalling functionality removed from the layers 2 and 3 protocols, all that remained was, framing, checksums (layer 2 responsibilities), logical channel identification (a layer 3 responsibility) and sequenced delivery (layer 2 and layer 3). Sequenced delivery is simple to achieve if the internal structure of the network is VC-based. As long as each switch maintains sequence, the whole VC will maintain it, no protocol support is needed. The designers moved logical channel identification down to layer 2 and deleted the layer 3 protocol entirely. Since we are now exclusively in layer 2, the lumps we deal with are called frames rather than packets - hence "frame relay".

## Slide 10: LAN interconnect
Notes: In a typical implementation, a frame relay network consists of "frame-relay nodes" interconnected by fibre-optic links. A VC-based organisation is used internally. In frame-relay parlance, the VCs are "data link connections" (DLC) and the VCIs are "data link connection identifiers" (DLCI). Each data link connection is allocated a unique DLCI. The X.25 link layer protocol, LAPB, was modified with an extended header to carry these DLCI values and so provide the layer 2 multiplexing. The resulting protocol is referred to as LAPF.
The choices made in specifying the functionality of frame relay were good ones; so much so that frame relay acquired a life of its own independent of N-ISDN. Several providers, especially in North America have launched stand-alone frame-relay networks. These networks typically offer only PVCs to their customers so the N-ISDN signalling is not used. The most common application is LAN interconnection. A customer with LANs on several sites will ask for frame-relay DLCs to be set up between them. The operator will then tell the customer which DLCIs to use for which DLC. As is always the case for VC identifiers, A DLC will generally have a different DLCI at each end. Frames for transfer between LANs are simply launched along the appropriate DLC (see slide). This works well since there is a good match between the LAN and frame-relay services (neither has error-control nor flow-control, both employ variable sizes frames of similar lengths). Manufacturers of LAN interconnection equipment (bridges and routers and so on) usually offer frame relay interfaces on their kit. Frame relay access is available at various bit-rates up to several megabits per second.
Of course, the customer could achieve a similar effect by hiring digital leased lines rather than frame relay DLCs. However, the frame relay solution is likely to be cheaper since the provider is able to statistically multiplex traffic from several DLCs over the digital lines it uses to interconnect its frame relay nodes. It is thus likely achieve much better utilisation of these lines than a single customer would by leasing digital lines directly.