## Slide 1: Internetworking and the Internet
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: The Internet – an example
Backbone Network
ISP
Backbone Network
Transit Network
Servers: WWW, Email, DNS
Router
ISP
WWW Server
Access Network
PC
Local Loop
Mux.
Tel. Exchange
Notes: The Internet is a collection of physical networks connected together by routers and point-to-point links.
Physical Networks – LANs, MANs, WANs – anything! (One of the strengths of the Internet)
Router – a packet-switch designed to handle Internet Protocol (IP) datagrams
Point-to-to point links – cable, optical fibre, microwave etc.
The slide shows a home user connected via ADSL.The “local loop” telephone wire is used to connect to a multiplexor (which will serve many users) at the telephone exchange. A high-capacity access network then connects to a router at the Internet Service Provider (ISP) site. This site will have servers connected by, for example, Gigabit Ethernet together with routers providing access to the rest of the Internet. Servers will probably include:
Mail server – receives and stores email on behalf of users who may not be connected at the time of delivery
WWW server – perhaps including pages concerning the ISP’s service
Domain Name Server – see later
The word “server” is used to mean a program implementing a service (e.g. the Apache WWW server) as well as the host on which the service runs. It is possible to run several server programs on one server host.

## Slide 3: The Internet – an example
Access Network
PC
Local Loop
Mux.
Tel. Exchange
DNS
ISP
WWW Server Name: www.foo.com Address:129.16.3.1
?
?
!
!
?
!
?
?
?
?
?
?
?
?
?
?
?
?
www.foo.com?
129.16.3.1!
!
!
!
!
!
!
!
!
!
!
!
http://www.foo.com/foo.html
Notes: In the slide the ISP has a router giving access to the rest of the Internet via a point-to-point link to a transit network which might serve a region or country. The transit network will probably be owned by a different company. There will have to be a commercial agreement under which the transit network agrees to carry the ISP’s traffic. Not all ISP’s are equal. Some have rather congested links to the rest of the Internet and provide a poor service to customers.
The heart of the Internet are the backbone networks mainly in the USA. These are very high capacity networks which carry traffic between transit networks. Once more these are owned by separate (rival?) organisations so commercial agreements will be needed.
Every interface between a host or router and the Internet has an IP address – e.g. 129.16.3.1. These addresses appear in the headers of IP datagrams and are used by routers to determine to where a datagram should be sent next. Each router makes an independent decision as to where to send the datagram next. Normally a client starts with a domain name like www.foo.com. This must be mapped to an address. The Internet has a Domain Name Service (DNS) to perform this task automatically. Communication usually begins with a message to the ISP’s DNS server asking for a mapping. If this is successful, the client now has an address which can be put in the header of an IP datagram which can be launched towards its destination.

## Slide 4: DNS [1]
Global, distributed name space
Nodes form a tree:
  Hierarchical delegation
Domain:
  single IP network, e.g.: cs.ucl.ac.uk
  multiple IP networks: ibm.com
DNS servers:
  servers for each domain
ac
co
uk
edu
com
gov
fr
us
cs
darhu
ucl
surrey
cambridge
darhu.cs.ucl.ac.uk
Notes: Why do we need names and addresses? In the context of data communications, the answer is that names are that a) relatively permanent and are used by humans and b) addresses are, potentially, changeable and are used directly by communications hardware and software. So, we need a service (much like a telephone directory) that will map between names and IP addresses and this is the Domain Name System (DNS). A heavily pruned portion of the DNS naming tree is shown. Each node (leaf or non-leaf) represents a domain which consists of itself and all the nodes in the sub-tree beneath it. A Fully Qualified Domain Name (FQDN) is a concatenation of the labels on the path from a node all the way back to the root, for example darhu.cs.ucl.ac.uk.
Authority to allocate names is delegated. The authority for a zone is responsible for ensuring that no two sibling nodes it administers have the same name. It is clear that, provided this is done, there will be global uniqueness of DNS names. The top-level domains include the world-wide generic domains (com, org, net, edu etc.) and country code domains (e.g., us for the United States, uk for the United Kingdom, etc.).
Though the DNS name-space and the IP address-space both involve hierarchies, these are completely independent. Because two hosts have similar domain names does not imply they have similar IP addresses and vice-versa.

## Slide 5: DNS [2]
Query to local server:
  iterative mode
  recursive
Authoritative answer:
  from domain server
Non-authoritative answer:
  from cache at local server
Resource Records:
  A
  PTR
  MX
local server
root server
(.com)
remote server
(ibm.com)
www.ibm.com
1
2
3
4
5
6
204.146.18.33
Notes: The solution to the name-mapping problem is to maintain a table mapping names to addresses and to make this available across the Internet. It makes no sense to postulate a single server for the whole Internet, therefore we need a distributed service with multiple servers. The DNS protocol allows hosts to query these mappings and so to map names onto addresses. Local DNS servers hold mappings for local machines and answer queries for these directly. Non local names are passed on to other DNS servers.
There are two different modes in which DNS look-ups can operate. Steps 2 and 3 show the iterative mode; the root nameserver does not answer the query but refers its questioner to a different nameserver. Steps 1, 4, 5 and 6 show recursive mode; the client sees only a request and response, the local nameserver has taken the responsibility of passing the query on. The local nameserver will cache the result of the query so that, next time around, we will see, at most, steps 1 and 6. Some implementations cache results in the client as well. In such cases, there would be no network activity at all for the second and subsequent look-ups. As with all caching strategies, there is a danger that the cached information will become out-of-date, so a timeout is used. In addition to this, nameserver responses always contain a flag to indicate whether they are authoritative - i.e. whether they come direct from a primary nameserver. It is possible for a client to insist in a query that an authoritative response be provided.

## Slide 6: IP Networks – The Rules
Hosts on same “IP Network” share same network prefix
Hosts with same network prefix must be able to communicate directly
Hosts with different network prefixes must communicate via a router
IP Address
Network Prefix
Host Id
Boundary varies
Notes: IP networks are logical concepts. An IP network may be 1-1 with a real network but may also encompass several real networks. Also, it is possible to partition one real network into several IP networks.
IP networks are defined by the addresses allocated to the interfaces attached to it. All interfaces in one IP network must share the same network prefix.
(The comments above apply equally if the phrase “IP network” is replaced by either “IP subnet” or IP supernet”. “IP network” and “IP subnet” are now used interchangeably)

## Slide 7: Simple Forwarding Algorithm
For hosts with just one interface:
If destination network id = local network id then
Send Direct
Else
Send to “default” router.
IP network B
IP network A
Notes: This is the simplest case. Many LAN hosts are configured like this.

## Slide 8: How do we “send” a datagram
Each network technology has its own:
  Frame format – e.g. IEEE 802.11 frames
  Addressing scheme – e.g. ATM address
We must:
  Put datagram in frame – “encapsulation”
  Resolve “next hop” IP address to “physical address”
  N.B. “next hop” not “final destination”
  We may need to open a connection
Now we can send the frame
Notes: IP has its own addressing scheme and packet format. So does every networking technology and their schemes are different from IP’s. It is vital to keep this in mind!
A useful analogy is to think of each networking technology as providing it’s own style of envelopes and it’s own addresses (often referred to as “physical addresses”). In order to send an IP datagram we have to place it in an appropriate envelope (“encapsulation”) and write the correct type of address upon it. The process of discovering the physical address which corresponds to a particular IP address is called “address resolution”.
For each networking technology a standard has been defined which specifies how the encapsulation and address resolution should be done.

## Slide 9: IPv4 Addresses [1]
32 bits – e.g. 11000000101010000000000010000000
Written as 4 decimal bytes – e.g. 192.168.0.128
To interpret, we need length of network prefix
  Explicit 192.168.0.128/25
  Mask 255.255.255.128
Allocated in blocks with common network prefix
  11000000101010000000000010000000
  …
  11000000101010000000000011111111
  Gives an IP network with 128 host ids.
192.168.0.128/25
Notes: IPv4 address allocations are (ultimately) controlled by the Internet Assigned Numbers Authority (IANA) in the US. Other bodies, such as Réseaux IP Européens (RIPE), control allocation in particular geographical regions. ISPs and backbone network providers get their IP addresses from bodies such as RIPE. Other users get their addresses from their ISP.
IP addresses are allocated to ISPs who then allocate them to customers. Allocations cannot be arbitrary. Blocks must be allocated with a common network prefix otherwise IP routing will not work.

## Slide 10: IPv4 Addresses [2]
Can be further subdivided. E.g.
  If you own 192.168.0.128/25
  1100000010101000000000001.......
  Could allocate 2 more bits to network prefix
  192.168.0.128/27 (1000000)
  192.168.0.160/27 (1010000)
  192.168.0.192/27 (1100000)
  192.168.0.224/27 (1110000)
Or
  192.168.0.128/27 (1000000)
  192.168.0.160/27 (1010000)
  192.168.0.192/26 (1100000)
Notes: An ISP or a customer may further sub-divide a block. However, the “common network prefix” rules must be preserved.
Partitioning addresses in this way is useful to a large organisation who can then operate several “subnets” interconnected by routers. This allows (for example):
Incompatible technologies to be connected via routers;
“Firewall” routers to control access to sensitive parts of the network.

## Slide 11: IPv4 addresses - history
0
1 0
1 1 0
1 1 1 0
1 1 1 1
network id
host id
network id
network id
host id
host id
multicast (group) address
experimental use
Class A
Class B
Class C
Class D
Class E
No need for explicit network prefix length
e.g. marston.cs.ucl.ac.uk: 128.16.20.1 (class B)
0
8
16
24
(31)
Notes: Unicast IPv4 addresses were originally allocated from one of three IP address classes, class A, class B or class C. One of the main problems with the class-based approach is the inefficiency that can result with class A and class B addresses when the host id space is not fully utilised within a single IP network. The addresses cannot be used by any other IP network that is connected to the Internet.
Unicast IPv4 addresses identify one interface connected to the Internet. Hence, a normal host machine (a workstation or a server) typically has only a single IPv4 address and a single network interface.
Multicast (which we look at later in the course) uses class D addresses to identify not a single host interface, but a group of hosts.
Class E is reserved for experimental use.
.

## Slide 12: Dynamic IP addresses
“Server” hosts need permanent IP addresses, “Client” hosts do not
Allocate addresses to clients when they connect to network
  Easy configuration
  Optimal use of addresses
Pool of addresses:
  user allocated IP address from pool
  returned to pool at end of session
  next session may be using different address
DHCP, PPP, IPv6 etc….
Notes: A computer that provides a service (e.g. the CS department web server) usually needs a permanent IP address which can be advertised. (Think of the problem of phoning someone whose telephone number changes from day to day).
However, most computers do not offer services. Programs that run on them act as “clients” – they initiate all connections by sending requests to “servers”. These machines do not need permanent IP addresses. (The server can easily discover the client’s current IP address as this is contained in every datagram the client sends).
Systems exist which allocate IP addresses to clients dynamically each time they connect to the network. Such automation is useful since:
It relieves users of the responsibility of correctly configuring their computer with an IP address;
It deals easily with computers which move between IP networks (e.g. lap-tops)
It avoids wasted allocations to computers which are not currently operating.
Various protocols exist for managing that allocation including:
“Dynamic Host Configuration Protocol” (used on LANs)
“Point-to-point Protocol” (used for dial-up connections)
IPv6 has dynamic allocation built in

## Slide 13: Private IPv4 address space
Private IP networks:
  Intranets
Use IP, so need IP addresses:
  can use any address
  hosts must not be directly connected to the Internet
Special addresses (RFC1918):
  10/8 prefix
  172.16/12 prefix
  192.168/16 prefix
  not forwarded by routers
Notes: There are many networks that do not need direct external access for each host, but would like to use the Internet Protocols and applications. They would like to run an IP network, but not one that is necessarily connected to the Internet at the IP level. Such networks are private IP networks, such as an Intranet. When using IP, we need to have IP addresses for hosts. If the hosts are not directly connected to the Internet, then, in principle any IP address can be used. However, if such hosts that had such randomly chosen IPv4 addresses were to connect directly to the Internet (by accident or design!), they could cause havoc with the normal operation of the Internet.
To minimise the risk of such occurrences, but still allow the use of private IP networks, RFC1918 specifies three address groups that can be used in numbering hosts. These are:
10.0.0.0 - 10.255.255.255 (10/8 prefix)
172.16.0.0 - 172.31.255.255 (172.16/12 prefix)
192.168.0.0 - 192.168.255.255 (192.168/16 prefix)
Routers are configured not to forward these addresses onto interfaces connected to the Internet.

## Slide 14: IP v4 Datagram Header
version
IHL
type of service
total length
identification
flags
fragment offset
time to live (TTL)
protocol
header checksum
source IP address
destination IP address
options
options
padding
data
0
8
16
24
(31)
All IPv4 datagrams begin with a header as shown below
Notes: version: 4 for IPv4, 6 for IPv6
IHL: The length of the IP header in 32 bit words. This is normally 5 but will be longer if any of the options are in use.
type of service (ToS): handling requirements in the network – we shall return to these later in the course.
total length: total length in bytes (including the header).
identification and fragment offset: used to implement fragmentation and re-assembly.
flags: bits used to mark fragmentation status.
time to live (TTL): hop count before packet must be discarded.
protocol: a number to identify the protocol that this datagram is carrying – TCP, UDP etc.
header checksum: used to pick up transmission errors that might corrupt header fields.
source address and destination address: IPv4 address of sender of datagram and IPv4 address of destination of datagram, respectively.
options: rarely used (includes source route, record route and timestamp, etc.)

## Slide 15: IP Forwarding
Notes: In general, there are many possible routes from a source to a destination. We have to chose the “best” route – perhaps one which minimises the number of hops, though there are many other possibilities.
In virtually all cases, IP forwarding is done on a “hop-by-hop” basis. At no stage does any component attempt to work out the whole route from source to destination. Instead, each host and router works out just the next hop of the route and sends the datagram there. This is rather like setting out by car from London knowing only that the final destination is Glasgow. At every junction along the way we find a helpful local inhabitant, announce that we are going to Glasgow, and are told the way to go to the next junction.
This hop-by-hop approach tends to be robust. If a component breaks, the router nearest to the break will discover it and will begin routing packets differently. “Routing protocols” exist which enable routers periodically to exchange information about the state of the Internet and so vary their forwarding decisions. However, there are some disadvantages. If routing information is inconsistent we can have routing loops around which datagrams circulate for ever (in practice, they are automatically discarded after a while). Since each datagram is routed separately it is quite possible for one to overtake another and so be delivered out of order.

## Slide 16: IP Forwarding - detail
220.20.4.1
220.20.4.50
220.20.4.0/24
220.20.5.30
220.20.5.20
220.20.5.0/24
128.16.8.78
128.16.4.9
128.16.0.0/16
H4
R2
Notes: The slide shows the first two hops from H4 to H6.
The routing table for H4 is minimal; it just distinguishes between “local” (i.e. hosts on “my” IP network) and everything else. “Everything else” is sent to the default router – R2.
Relevant parts of R2’s routing table are shown – there would probably be many more entries. The destination address (128.16.8.78) matches the third entry and results in the datagram being forwarded to R1.

## Slide 17: IP Forwarding – detail
R1
220.20.4.1
220.20.4.50
220.20.4.0/24
220.20.5.30
220.20.5.20
220.20.5.0/24
128.16.8.78
128.16.4.9
128.16.8.78/16
Notes: The slide shows the last hop from H4 to H6.
Relevant parts of R1’s routing table are shown – there would probably be many more entries. The destination address (128.16.8.78) matches the third entry which indicates a local transmission.

## Slide 18: Encapsulation
L
LLC Header (3 bytes)
Start with an IP datagram
IP
IP data
IP Addresses etc.
Add SNAP and LLC headers
  Clumsy way of providing “protocol discrimination”
Place in Frame
S
SNAP Header (5 bytes)
For most technologies encapsulation begins in the same way:
Notes: Although most traffic today is IP v4 there are certainly other possibilities (IP v6 for example). The receiving equipment needs a quick way of determining what is being carried so it can pass the contents to the appropriate processing hardware or software. Each protocol has been allocated a unique number and this is carried in some extra bytes which precede the IP datagram. Principally for historical reasons 8 bytes are added to achieve this termed the SNAP and LLC headers. The details are unimportant.

## Slide 19: Encapsulation - Examples
MAC
CRC
Ethernet Addresses etc.
Ethernet – start with basic frame – max. 1500 bytes
ATM – all frames 48 bytes – too small
  Must use multiple frames
L
IP
IP data
S
  IP + SNAP + LLC carried as data (1492 bytes of IP)
L
IP
IP data
S
L
IP
S
ATM header.
Padding
Notes: IEEE frames (e.g. Ethernet) start with a MAC Header (which includes the source and destination MAC addresses) and conclude with a CRC. IP encapsulation is simple – the datagram simply becomes the MAC payload.
ATM is more complex since its frames are small and of constant length. We could “fragment” large IP datagrams into several smaller ones which would fit; but this would be inefficient since each fragment would need its own IP header. Instead a special mechanism is used – called “ATM Adaptation Layer 5” (AAL-5) which uses information in the ATM headers to indicate that successive ATM frames should be associated as a group.

## Slide 20: Address Resolution on a LAN
ARP results are cached
  Timeout if not “refreshed”
All hosts learn mapping for requestor
Want to send to 128.16.8.177 Need Ethernet address
128.16.8.177 08:00:20:0d:23:34
128.16.8.78 08:00:20:0d:1b:96
128.16.8.74 08:00:20:0d:2a:3b
128.16.8.135 08:00:20:0d:5a:4b
It’s me! My address is 08:00:20:0d:23:34
ARP req (b/cast) Who is 128.16.8.177?
ARP resp 08:00:20:0d:23:34
Notes: All LANs support a broadcast service. This is the basis for the LAN Address Resolution Protocol (ARP).
An IP host (or router) begins by knowing the IP address of the host to which it wants to send a datagram (128.16.8.177 in the slide). It broadcasts an ARP request messages which contains the following information (refer to the slide):
“I am IP address 128.16.8.135, Ethernet address 08:00:20:0d:5a:4b. What is the Ethernet address of 128.16.8.177?”
All hosts receive this message and hence learn the address mapping for the requestor – a useful side-effect of ARP. One host recognises its IP address and responds with the information:
“I am IP address 128.16.8.177, Ethernet address 08:00:20:0d:23:34”
The response is not broadcast.
The requestor can now construct an Ethernet frame with destination address 08:00:20:0d:23:34 the data part of which will be an IP datagram with destination address 128.16.8.177.
All mappings are cached so that ARP generally has to be used only for the first datagram sent. However, we cannot assume that mappings will be constant for evermore – a new Ethernet card might be installed for example. Thus mappings are timed out if not refreshed and are subsequently re-learned.

## Slide 21: Address Resolution via a Server
H
H
H
If network does not support broadcast efficiently (e.g. ATM) …
  Use an Address Resolution Server
Server holds mappings – e.g. IP address -> ATM address
Hosts send ARP requests to server
Hosts register mappings at start-up
AR Server
Notes: Not all network technologies support broadcast. In such cases a server machine is needed to store AR mappings. Before sending an IP datagram hosts must consult the server to obtain the physical addresses which corresponds to the IP address. Results are cached for future use.
Generally there is some mechanism whereby the server learns mappings. For example, hosts may provide their own IP->physical address mappings at start-up or when they send a request.

## Slide 22: Summary so far
IP
Mapping
Tech.
Host
Host
Router
Router
IP – connectionless service, global addresses, no guarantees about delivery, may deliver out of order, normally no qos guarantees
Routers
Mappings to network technologies - LANs, WANs etc.
Suppose we want reliable sequenced delivery?
  TCP
Suppose we don’t?
  UDP
Transport
Application
Notes: The IP protocol does not attempt very much – no error control, flow control etc. It just aims to deliver packets with a reasonable success rate.
Because it is simple, it is easy to implement on different network technologies. Mappings are defined for LANs, WANs, serial lines etc. We can think of these technologies as “underlying” IP. IP is a user of these technologies.
IP is used by applications. Many of these, like the WWW for example, require reliable, sequenced delivery. Rather than have each application implement its own ARQ procedures a common protocol, TCP, is used to provide this. TCP is an example off a “Transport Protocol”. TCP uses IP to convey its “Protocol Data Units” (PDU). The applications use TCP to convey their PDUs.
Some applications do not require reliable, sequenced delivery. These may use an alternative Transport Protocol – UDP.
Notice that Transport Protocols reside in the end-systems. The network (routers etc.) pays them no attention apart from carrying their PDUs from place to place.

## Slide 23: Transmission Control Protocol - TCP
“End-to-end” - routers are not aware of TCP
Reliable, sequenced delivery
  ARQ operation
  Connection oriented
Flow control
  Variable window
TCP
TCP data
IP
IP data
TCP
TCP data
IP Addresses etc.
TCP s.ns, ports etc.
Notes: TCP was first specified in the late 1970s. It is quite a complex protocol using ARQ for error control and a window-based mechanism for flow control. The receiver can vary the window in order to control the rate at which the transmitter may send packets.
TCP PDUs consist of a header + data. The header contains the sequence and acknowledgement numbers, the window values and the source and destination port numbers (see next slide). TCP PDUs become the data part of IP datagrams when they are transmitted.
TCP is “connection oriented”. The originator starts by sending a special PDU (called a SYN for “synchronise”) proposing a new connection. The receiver can accept or reject the connection. Once the connection is set up, data can be sent. Finally, one end will send a FIN PDU (“final”) proposing that the connection be terminated.

## Slide 24: TCP (and UDP) Ports
IP addresses identify hosts
Ports identify processes
  Like telephone extension numbers
  When packet arrives OS looks at ports and chooses process
Port 80 Proc.
Port 21 Proc.
Port 80 Proc.
Port 3309 Proc.
OS s/w
Port 53 Proc.
Port 2003 Proc.
Port 8777 Proc.
Port 21 Proc.
OS s/w
128.16.5.2
184.14.67.2
Notes: IP addresses identify hosts (more precisely they identify the host interface to the network). We need also to identify a particular service or process present on the host. This is achieved with the help of TCP/UDP ports. There is a close analogy with telephone extensions; the telephone number identifies the building, the extension number identifies an individual within the building.
However, the analogy is not quite exact. There can be two processes receiving datagrams on the same port (e.g. port 80 in the slide). This can happen when a particular service is provided by multiple processes. When a datagram arrives, s/w in the OS will look at the source and destination ports as well as the source and destination IP addresses in order to determine to which process it should deliver the datagram’s contents.

## Slide 25: Port Usage
“Well-known” ports – used by servers
  HTTP (WWW server) 80
  FTP (FTP server) 21
  Domain Name Server 53
  SMTP (Email) 25
  Network Time Protocol 513
“Ephemeral” ports – chosen by client
  Locally unique
Source and destination ports swapped in response datagrams
Notes: Public services usually use “well-known” ports (see slide). When a browser sets up a connection to a WWW server it must send a TCP SYN PDU with the destination port set to 80. The operating system on the server will have a table which tells it that port 80 belongs to the WWW server process. It will ensure the the WWW server process is informed about the new connection and takes responsibility for it.
The source port in the SYN PDU will have been chosen by the client host to be different from any other local ports it is currently using. Responses from the server will swap the source and destination ports from the request.

## Slide 26: User Datagram Protocol - UDP
IP
IP data
UDP
UDP data
UDP
UDP data
IP Addresses etc.
UDP ports
Not all applications want (or tolerate) ARQ delays. E.g. VoIP
  Each packet contains (say) 50ms of speech
  Retransmission might take 1 sec
Better to lose packet than retransmit
  => use UDP not TCP
Same service as IP but adds ports
End-to-end (routers do not know about UDP)
Notes: TCP does not suit all applications. For example Voice over IP (VoIP) suffers when jitter is high. Unfortunately, ARQ procedures, such as those in TCP, increase jitter since they introduce occasional very large delays when re-transmitting. A voice application would prefer these lost packets to be lost for ever rather than have to deal with the increased jitter. Losing one packet (ie. about 50ms of speech) will not be especially disruptive to a listener.
Therefore we want an alternative to TCP which does not use ARQ procedures. In the Internet, this is the “User Datagram Protocol” (UDP). UDP adds nothing to the basic IP service; thus UDP datagrams may be lost, delivered out of sequence etc. However UDP does have a small header which includes ports which are used in the manner previously described for TCP.