## Slide 1: Quality of Service Issues
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Quality of Service - Questions
How can we classify application QoS requirements?
Can we specify useful service classes?
What mechanisms exist to help such applications?
How can we communicate application requirements to the network?
How can we ensure customers pay for enhanced priority?
Notes: The basic Internet service has very simple characteristics.
  Guarantee of delivery: None (best effort service)
  End-to-end delay: Variable and un-bounded
  Throughput: Whatever is available
  Sequenced delivery: No
  Duplicate detection: No
Although this seems poor, it turns out to be fine for traditional data communications applications like file transfer, WWW access, etc. These applications do require guaranteed, sequenced, delivery without duplicates. Fortunately, these features can be provided by employing TCP as an end-to-end transport protocol.
Some newer applications have tighter timing constraints; “streaming” applications such as live video are examples. The basic Internet service is not well-suited to these applications. A network which can support many different kinds of applications is called an “integrated services network”.

## Slide 3: QoS - Analysis
“Flow” (“Microflow”) – a sequence of packets between applications. Identified by e.g.
  Src/dest IP address + src/dest port
  IPv6 flowid
Per flow QoS requirements (from INTSERV)
  “Guaranteed” – for real-time streams
    Specified max. delay and jitter, assured bandwidth
  “Controlled load” – for “adaptive” real-time streams
    Protected from congestion
  “Best effort”
    Normal Internet
Notes: INTSERV was a major IETF project aimed at adding QoS selection to the Internet. The concept of a “flow” was identified and the broad QoS requirements of flows were analysed. As a result, three QoS classes were specified:
The “best effort” class is simply the standard Internet service. It is considered suitable for so-called “elastic” applications – those with weak timing constraints – file transfer and email for example.
The other classes are for “inelastic” applications – those with stronger timing constraints – VoIP and video streaming for example. Some of these can tolerate very little delay and jitter and require constant bandwidth – effectively they require the guarantees offered by a dedicated circuit. The “Guaranteed” class serves these applications.
Other real-time applications are “adaptive” and can tolerate some jitter and bandwidth variation – usually through the use of intelligent buffereing strategies and variable-rate coding. They can work happily on a lightly loaded Internet but must be protected from the effects of congestion. The “Controlled Load” class serves these applications.

## Slide 4: QoS - Implementation
Resources allocated by router: link bandwidth, queuing priority
Guaranteed class
  B/w reserved close to sum of peak flow b/ws (little statistical multiplexing)
  Highest queue priority
Controlled load class
  B/w reserved < sum of peak flow b/ws (statistical multiplexing)
  Low probability of congestion
  Medium queue priority
Best effort class
  Whatever is left
  Starvation?
Notes: Providing the guaranteed service requires routers to make close to worst-case assumptions about competing flows and to reserve sufficient resources that a flow can never be hampered. This is costly as resources may be reserved which may never be used. One would expect to have to pay heavily for “guaranteed” QoS.
The router can marginally over-book the resources available to controlled load flows with the expectation that only rarely will all of them reach peak load simultaneously; i.e. we can do some statistical multiplexing. However, we cannot take this too far or congestion might occur breaking the “lightly loaded” contract.
Best effort traffic takes whatever resources remain. It can be transmitted whenever there is spare capacity on the outgoing link. In practice some minimal resource must be reserved to prevent “starvation” – the complete blocking of best effort traffic by the other traffic types.

## Slide 5: Reserving, Shaping and Policing
What resources does a flow require?
  Specified by a “token bucket” (see later)
Must reserve resources along the path
At boundary of QoS network
  Traffic may be “shaped” to conform to the reservation
  Traffic may be “policed”
    Non-conforming traffic may be deleted or relegated to best effort service
Notes: We must decide what resources to dedicate to each class. Therefore we need to know precisely what the flows require. A flow’s requirements can be specified as the parameters of a “token bucket” (see later) which effectively specifies the average and peak bandwidth and delay constraints.
Traffic may be smoothed by the network client so it conforms to the reservation made – i.e. bursts will be delayed and spread over time.
Traffic may be policed by the network provider to ensure that it does not exceed the resources reserved for it.

## Slide 6: Granularity
Fine grain (INTSERV)
  Resources reserved per flow when flow begins
    (Need a signalling protocol – RSVP)
  For each packet:
    Identify its flow
    Look up QoS table to determine treatment
  Very costly in core routers
Coarse grain (DIFFSERV)
  Resources reserved per QoS class
  QoS class explicit in packet header
Notes: The INTSERV model specified a signalling protocol – the Resource Reservation Protocol (RSVP) - which applications could use to reserve resources for a flow. As a consequence each router along the path would build up a table mapping flows to QoS reservations. The problem with this approach is that core routers would need to maintain state information on a huge number of flows. Further, each time a packet was forwarded, its flow must be identified and looked up in the state table. All this was considered to costly to employ in the core Internet.
The alternative, adopted in the later DIFFSERV approach, was that routers should not know about individual flows. Rather, they should deal with aggregates of flows which all required similar treatment. Effectively, therefore, resources are reserved for QoS classes rather than for individual flows. Since there is only a small number of classes there is room in the IP header to include an explicit indication of QoS class which greatly reduces the per-packet processing load in a router.
The DIFFSERV approach has largely prevailed and is now widely deployed in the Internet.

## Slide 7: DIFFSERV
Explicit marking of packets
  Type of Service byte  DIFFSERV byte (6 bits used)
  DS byte indicates DIFFSERV QoS class
  Routers implement “per-hop behaviours” for each class
Service-level agreements
  For example, customer pays ISP to have all packets from a certain subnet given high priority
Packets can be marked by network rovider
  No changes to host software
Notes: <header>
Slide <number>
DIFFSERV standards specify classes and corresponding “per-hop behaviours”. The latter indicate how routers should treat traffic interms of queuing strategy and priority, packet drop priority etc.

## Slide 8: DIFFSERV - Example
C - MF classifier
M – Marker
T – Traffic Meter
S - Shaper
C
M
S
T
Ingress router
B
P
P
P
Core router
B – BA classifier
P = Per hop behaviour
DIFFSERV
domain
Notes: The slide shows a DIFFSERV domain. Assuming packets entering the domain have not already been assigned to DIFFSERV classes they are first examined by the “Multi-field classifier”. This looks at a combination of fields in the IP and Transport headers and assigns a DIFFSERV class according to a previously established rule. For example, all packets using the Real-Time Protocol (RTP) might be assigned to the “Expedited Forwarding” class.
The Marker’s job is to put an appropriate value in the DIFFSERV byte in the IP header. It does this in accordance with the output of the MF classifier but also takes input from the Traffic Meter which is checking whether the flow is conforming to the agreed profile. Non-conforming traffic may be re-classified or marked with a high drop precedence.
Finally, the Shaper may delay or drop the packet to force conformance with the profile.
Packets arriving at a core router are processed by the Behaviour Aggregate Classifier which, essentially, looks at the DIFFSERV byte and queues it for processing by the Per Hop Behaviour module for the class.

## Slide 9: DIFFSERV PHBs
PHBs specify
  How packets should be prioritised
  How queues should be managed
  How link capacity should be allocated
Expedited Forwarding PHP (Codepoint 101110xx)
  Like INTSERV “Guaranteed”
Assured Forwarding PHP
  Similar to INTSERV “Controlled Load”
  4 prioritised sub-classes
  3 drop-precedence levels
Notes: The AF classes allow providers to offer 4 QoS behaviours of varying priority. Within these the drop precedence may be set to “high” or “medium” in cases where traffic in a flow is not conforming to the agreed profile. This ensures that it is packets belonging to the non-conforming flow that are dropped in the face of congestion rather than those belonging to conforming flows.

## Slide 10: Burstiness
Consider a buffered switch or router
  Mean packet size 1000 bytes,  = 1000,  = 1500
M/M/1 – mean no. in sys. 2, mean time in sys. 2ms
100ms
900ms
1000 packets
100
667
1000
850
Packets
ms
Notes: The slide shows the dramatic effect that burstiness of a flow can have on delay and buffering requirements. In both cases the load is the same – a mean rate of 1000 1000 byte packets per second.
  With M/M/1 assumptions the buffering requirement is modest with a correspondingly modest delay.
  With a very bursty traffic pattern we see that the output process will be overwhelmed and that a lot of traffic must be buffered. The buffering requirements and delays are 2 orders of magnitude greater than with the comparatively “smooth” M/M/1 traffic profile.
The second flow is much more costly to handle. The switch or router must either allocate much more buffering to the flow or it must reserve much more capacity on the output side – i.e. it must increase . Because of this we would expect a customer that insists on generating the second type of flow to have to pay more. Alternatively, it is in the customer’s interest to spread the bursts over a longer period so as to smooth the traffic and save some money. This is known as traffic shaping.

## Slide 11: Traffic shaping
Source (e.g. video CODEC) produces bits at a variable rate
Shaper “smooths” the traffic
  Buffering => some traffic delayed a bit
  Playout buffer restores timings
Smoothed traffic should encounter fewer queuing delays and less packet loss
Source
Shaper
Byte/s
Byte/s
time
time
Notes: The slide shows the principle involved. Essentially we have a trade-off; the shaper will delay traffic during a high-bit-rate period but it does it in a controlled way. Ideally we will be able to predict the maximum delay. This will enable us to implement a “playout buffer” at the receiver which will allow the original timings to be restored.
If the network knows the “shape” of the traffic then it should be able to allocate resources which ensure there is enough buffering and link capacity. Without the shaper the traffic would be subject to unpredictable queuing delays (and possible congestion loss) making it much more difficult to restore the original timings.
One complication, glossed over in the diagram, is that the source data is packetised – so the rate curves are not really smooth.

## Slide 12: Leaky Bucket Shaper
Source
Packets buffered
Packets transmitted to give constant byte rate
Implementation
Source
Shaper
Bytes/s
Bytes/s
time
time
Bytes arrive at a varying rate
Bucket holds up to b bytes
Bytes leave at a constant rate r bytes/sec
Model
Notes: The so-called “leaky bucket” is one approach. Conceptually, bytes arrive in a bucket at a varying rate and “drip out”at regular intervals as long as the bucket is not empty. (This does not exactly correspond to the physics of a leaky bucket!). If a packet arrives when the bucket is full it must be discarded. The parameters of the leaky bucket must be carefully chosen with respect to the source so that this is a rare event. In the worst case, the system imposes a delay equal to the time it takes the bucket to drain – approximately b/r sec.
The implementation only approximates the model because it has to deal in packets rather than bytes. Thus, if a packet of l bytes is to be transmitted we must wait l/r sec before beginning the transmission of another packet. This does not necessarily mean that the packet transmission time is l/r sec. If the capacity of the output link is C bytes/sec we must have C  r – i.e so we may use only a portion of the capacity. Hence the packet transmission time will be l/C. Despite the packetisation, the delay bound – b/r - remains approximately true.
This is simple to implement and to model, and it produces a very smooth output profile. However, it might be that the network is actually capable of handling a higher rate for a short period until a burst has been cleared. The leaky bucket model does not exploit this possibility.

## Slide 13: Token Bucket Shaper
Packets arrive at irregular intervals
Source
Packets buffered
Packets transmitted provided tokens are available
Implementation
Tokens arrive at r bytes/s
Bucket holds up to b bytes
Departing packets consume tokens
Model
Source
Shaper
Bytes/s
Bytes/s
time
time
Notes: A token bucket specification has two parameters; the token replenishment rate r, and the bucket size b. Logical tokens drip into the bucket at a constant rate r bytes/s. A packet of length s bytes logically consumes s bytes of tokens when it leaves. If there are not s bytes in the bucket, then the packet cannot be transmitted. When a token bucket is used as a shaper, such a packet would be buffered.
There are two key differences compared with the leaky bucket:
  If the capacity of the output link is C bytes/sec, the leaky bucket shaper will space out the packets to achieve a short-term and long-term output rate of r bytes/sec. However, with the token bucket, provided there are enough tokens available, a burst of packets will be transmitted at C bytes/sec (C  r). Thus, although the long-term rate remains r bytes/sec, the short term rate can rise to C bytes/sec – so the smoothing is less severe.
  If there is a pause in packet arrivals then the bucket fills - but only until it contains b bytes of tokens. Nevertheless, this means that the source acquires credit during an idle period which can be used when the next burst comes along.

## Slide 14: Token Bucket Shaper (2)
We may wish to allocate only a fixed portion of the output link capacity – e.g. 10Mbps on a 1Gbps link
Simple! Follow the token bucket with a leaky one!
Token bucket (b, r)
Leaky bucket (b, R)
Link capacity C
C  R  r
Burst emerging from TB now transmitted at an average rate of R bytes/sec
Notes: We may want to ensure that a particular traffic class does not exceed a certain proportion of the output capacity. This can be achieved by following the token bucket by a leaky one.

## Slide 15: Token Bucket Shaper Example
Time 0 1 2 3 4 5 6 7 8 9 10(sec)
Arr. | 0 | 6 | 0 | 0 | 0 | 0 | 0 | 0 | 4 | 0 | (Mb)
Dep. | 0 | 3 | 2 | 1 | 0 | 0 | 0 | 0 | 3 | 1 | (Mb)
Bucket 2 3 1 0 0 1 2 3 3 1 1 (Mb)
Buffer 0 0 3 1 0 0 0 0 0 1 0 (Mb)
p = 6MBps, r = 1MBps, R = 3MBps, b = 3MB
Input Output
Rate (MBps)
Time (sec)
Notes: In the slide p is the peak rate at which the source generates bursts of data. The table shows data volumes in MB at one second intervals. It is worth following this example carefully!
For example, in the interval (1,2) 6MB arrive at the peak rate (p) there are 3MB of tokens at the start (b) and 1MB arrive (r) so we can transmit 3MB at the output rate of RMBps. This leaves one token and 3MB in the buffer.
In the interval (2,3), although there are 3MB buffered and R = 3MBps, we can only transmit 2MB because we are constrained by the token availability (1 at the start and 1 which will arrive).
The graph illustrates the smoothing of the output compared with the input.

## Slide 16: Token Bucket Shaper Example (2)
Long-term: input rate  output rate  r
Short term:
  output rate > r (1,2) or output rate < r (5,6)
  input rate > r (1,2) or input rate < r (2,3)
2
4
6
8
10
2
4
1
3
5
6
7
8
9
10
Input Output Tokens received Bucket
Time (sec)
Volume (MB)
Notes: The slide gives a different view of the previous example, this time concentrating on volumes rather than rates.
We can see that the input and output rates (i.e. the slopes of the lines) vary above and below the (constant) token rate. The output rate may be constrained by:
  The absence of data to transmit (5,6)
  The lack of sufficient tokens (2,4)
  The output capacity (R) (1,2)

## Slide 17: Token Bucket Policing
Switch/router may check source for conformance with TB
No input buffer. If not enough tokens:
  Discard or
  Forward but mark as “vulnerable”
May still have an output buffer (i.e. LB)
  Constrain output rate to R bytes/sec
Yes – buffer packets for output at R bytes/sec
Source
TB (b,r)
Enough tokens in bucket?
No – mark or discard
Notes: The second use for a token bucket is in a router or switch that needs to “police” traffic. This is likely to be necessary as the network will have offered QoS guarantees on the basis that traffic conforms to a specification which includes the parameters of a token bucket. We would expect that the source will have shaped its traffic to conform to the same parameters (and so eliminate the extremes of “burstiness”). However, if the source cheats then the network needs to detect the cheating and act.
When used for policing there is no input buffer. If a packet arrives and there are not enough tokens then either the packet will be discarded or it will be marked as “vulnerable” and forwarded. Vulnerable packets will be prime candidates for discard should congestion occur downstream. Their service class will likely be changed to “best effort”. [In practice there would need to be some flexibility since timings are never 100% accurate.]
The slide shows a leaky bucket filter after the TB. This is not strictly necessary and packets could be transmitted at the link rate.

## Slide 18: Token Bucket - Arithmetic
In t sec rt tokens arrive. Thus, if bucket is full at the start we can use b + rt tokens in time t.
  Basic conformance constraint: for any interval of length t we must transmit < b + rt bytes
How long can we transmit at the max. rate R?
  In tmax we transmit Rtmax bytes, so Rtmax < b + rtmax
  tmax < b/(R-r)
From earlier e.g. r = 1MBps, R = 3MBps, b = 3MB
  tmax < b/(R-r) = 3/(3-1) = 1.5 sec
  We can send up to 3 x 1.5 = 4.5MB in the burst
Notes: Basic conformance constraint:
  “For any interval of length t we must transmit < b + rt bytes”
Note this is for any interval no matter how big or how small.
If t is big we can ignore b and the constraint is approximately:
  “For any interval of length t we must transmit < rt bytes”
i.e. the long term average rate is simply r.
The slide shows how the constraint imposes a limit on how long the peak output rate R may be sustained.
[Note, as usual, that these relations are approximate as we have taken no account of packetisation.]

## Slide 19: Token Bucket Arithmetic (2)
Suppose t sec burst arrives at peak input rate p byte/sec
Must be enough tokens available so pt < b +rt
  Thus t < b/(p-r). So burst size B < pb/(p-r) bytes.
If p > R > r we will have an output queue
Time T to transmit B bytes at R bytes/sec T =
So delay imposed is approx. bounded by b/R
In the example, maximum delay  3/3 = 1 sec.
Notes: The calculation in the slide shows that the delay to a flow conforming to a token bucket (r,b) with an output rate R is approximately bounded by b/R. This remains true whether R represents a reserved share of line capacity or its full capacity. [Note, as before, that we have not allowed for packetisation.]
Thus we can obtain various combinations of mean throughput, peak throughput and delay bound simply by juggling the two token bucket parameters and the reserved bandwidth. For example, to reduce the delay we can reserve more capacity (make R bigger) for which, presumably, we will pay. Alternatively we can reduce b which means we must apply more smoothing to our traffic.

## Slide 20: Making DIFFSERV work
Provider must give QoS guarantees
For each packet core routers must:
  Determine QoS class
  Apply correct queuing strategy
  Choose route which can support QoS requirement
Heavy per-packet processing
Difficult to accommodate change:
  Changed traffic patterns
  Changes to physical capacity and configuration
Notes: Having to implement differing QoS requirements increases per-packet processing. It also makes for more complex routing with some traffic types requiring special routing treatment – perhaps being sent down the least congested routes.
ISPs must offer guarantees to customers who have paid for a given QoS level. They must respond as traffic changes by re-routing traffic, by installing faster, better routers or by adding new high-speed links for example.
Dynamic routing protocols alone cannot provide the required guarantees. Human intervention is normally necessary with manual configuration of QoS routing tables. This constitutes a major management problem.

## Slide 21: Traffic Management - Example
New link
Congested link
Re-routing
EF Traffic
BE Traffic
Suppose EF traffic is routed X->C->Y but the C-Y link becomes congested.
New link installed X-Y
All EF traffic must be re-routed Complex routing table management
Is there an easier way?
X
Y
C
Notes: The slide shows an DIFFSERV domain which is treating transit traffic in two classes. Traffic in a class is an aggregation of traffic from many microflows with differing sources and destinations but with similar QoS requirements. The provider routes all the “Expedited Forwarding” (EF) traffic through the same route on which it can ensure suitable priority.
The scenario in the slide shows a link becoming congested. In this context we are not concerned with the sort of short-term congestion with which TCP is designed to deal. Instead we are interested in the observation of traffic loads over a period which indicates that congestion will soon threaten QoS guarantees.
The solution is to enable new capacity which will eliminate the congested link from the path taken by the EF traffic. Routing tables must now be adjusted in a way which affects all the microflows belonging to the EF class.
Label switching – as described next – provides a simple way of achieving this sort of re-configuration.

## Slide 22: Label switching [1]
New link
EF Traffic
BE Traffic
Streams of “related” packets. E.g. same entrance and exit routers, same QoS class
Same classification and forwarding decisions made repeatedly
Make decision once, then “label”
  Extra header
  Label is somewhat like a VCI
7
5
12
8
4
6
2
6
5
Re-routing
9
X
Y
C
4
Notes: The original idea was based on the observation that, often, a stream of related packets passes along the same route. The forwarding and classification decisions for every packet of such a stream will be the same. The label switching idea is to make the forwarding and classification decisions once and then to mark subsequent packets with a “label” which can be looked-up in a simple table.
Labels are integers which have many of the characteristics of VCIs used in VC networks. Each switch maintains a table mapping incoming labels onto a triple {outgoing label, link id., PHB}. Look-ups in this table can be implemented very efficiently which should decrease the forwarding time. Further, re-routing a labeled stream is a simple manner of adjusting the tables in the affected routers.
It is not expected that label switching should be adopted everywhere in the Internet. The idea is to implement it amongst a set of cooperating routers where traffic is particularly heavy.
Labeled streams are not exactly like VC’s. There is no explicit request from outside the network to set them up, the decision to label a stream is made inside the network - this may be done via a signalling protocol or administratively. Further, the mapping at a switch is not 1-1. Sometimes streams will merge, as in the slide.

## Slide 23: Label Switching [2]
Label switches forward solely on the basis of label field
  Extra field in (e.g.) IEEE 802 formats
  Can use VCI/VPI in ATM
Benefits
  Forwarding efficiency
  Traffic engineering
  VPNs
CRC
IEEE Payload
MAC
L
S
Lab
IP
IP data
Notes: The original idea was to speed up forwarding by eliminating the complexity of the IP forwarding decision, especially in the case of QoS-based routing. In fact, modern router designs can handle IP forwarding extremely efficiently without label switching. Label switching is now justified by:
  Traffic engineering
    Allows an operator to set the path that a traffic stream will take through the network and the priority to be assigned to it. Gives a more rigid control than that provided by IP routing which may change as load changes.
  VPNs
    Traffic between a customer’s sites can be given a unique label. There should be no possibility of this traffic being routed elsewhere or of other traffic reaching the customer’s sites.
  The slide shows how a label can be placed within an Ethernet frame (probably Gigabit Ethernet in this context). If the underlying network were ATM it could be adapted so as to use the VPI/VCI to carry a label. In this case label switching would eliminate the decapsulation/encapsulation steps.