## Slide 1: ARQ Operations
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Introduction [1]
checksum
Automatic Repeat reQuest protocols
  “Transmitter” (Tx) sends data PDUs to “Receiver” (Rx)
  Rx sends acknowledgement (ack) PDUs to Tx
  All data PDUs must be acked
  PDUs that are not acked within a timeout period must be retransmitted
Protocol – a set of rules
Protocol Data Unit (PDU) – an item sent between Protocol Entities (PE)
data
header
protocol control information (PCI
PDU
Notes: The slide introduces some of the basic terminology. Different protocols adopt their own terminology. For example, PDUs may be called packets, frames, cells, messages etc.
Note that there are many different protocols which employ ARQ techniques. They are used, for example, between computers communicating across the Internet (e.g. TCP) and between mobile devices and base stations. They operate in highly varied environments in terms of data transmission rate, error rate, propagation delay etc. Consequently they vary a good deal at the detailed level. These notes attempt to establish general principles rather than considering the details of particular protocols.

## Slide 3: Introduction [2]
“Outstanding packets” are those transmitted but not yet acked
  Limited by “transmit window size”
Flow control – Tx must stop when window is full
Error control – lost data PDUs are retransmitted
Many different versions mainly in Data Link and Transport layers
Notes: ARQ protocols implement:
Flow control: Receiver can force transmitter to reduce or increase the rate of PDU flow.
Error control: Receiver can force retransmission of missing or damaged PDUs.
Window size is often measured in PDUs. However, TCP measures its window in bytes.

## Slide 4: ARQ Usage
Host-to-host (e.g. TCP)
  Provide “reliable” sequenced delivery over “unreliable” network
  Provide flow control
  Not all applications need these!
“Data Link” layer (e.g. point-to-point links, wireless links)
  Enhance inherent error rate
  Hop-by-hop flow control
  Not all links need these!
Notes: The slide shows the two main areas of ARQ use.
Host-to-host ARQ protocols like TCP (sometimes called Transport Layer protocols) aim to provide a service suitable for applications that require a reasonably reliable stream of data to be delivered. Ideally a fair amount of data will be shifted during the life of a connection in order to justify the connection set-up costs.
Data link layer protocols operate just above the physical layer. The physical layer moves bits, the data link layer groups bits into frames and sends frames across the link. Where the physical layer has a high bit-error rate an ARQ link protocol may be used to fix errors and avoid these propagating up to the Transport layer. In the past, wired links were error-prone and ARQ usage was common. Modern wired links, including fibre links, are much better and ARQ usage is now less common. However, some modern wireless technologies operate in challenging, noisy environments and ARQ protocols may be used.

## Slide 5: ARQ and End-to-End
End-to-end argument: provide functions in the end systems not in the intervening components
Reasoning: end systems know what they want, nothing else does
Should we employ ARQ between A and B?
E2E says “no” - end systems may prefer data loss to jitter
But, if errors are recovered end-to-end then BC and CD links are affected.
A
B
C
D
Notes: There is no clear rule about where ARQ should be employed. The Internet has tended to favour flow control and error recovery close to the “end systems” via TCP (in accordance with the end-to-end argument). Link-layer error recovery via retransmission increases jitter (i.e. delay variance) and this will be the wrong trade-off for some applications.
However, if a particular link is very error prone then end-to-end error recovery becomes very inefficient since the load of retransmissions is borne by all links, not just the offending one.

## Slide 6: Time-sequence Diagrams
Useful to show the sequence of events in time
ab, data PDU transmission time
bc, Propagation time
cd, Processing time at Rx
de, ack PDU transmission time
ef, Propagation time
fg Processing time at Tx
We sometimes assume
  constant transmission times
  constant propagation times
  Negligible processing times
Tx
Rx
Time
DATA
ACK
a
b
c
d
e
f
DATA
g
Notes: Note that the relative values of transmission, propagation and processing times can vary hugely. Sometimes it may be valid to treat some values as negligible. E.g. if communicating between Earth and Mars then propagation time dominates everything.
These diagrams are a very useful aid to understanding event sequences but they must be drawn reasonable accurately and neatly!
You must be precise in the use of terms and distinguish correctly between:
Transmission time: depends on PDU size and bit-rate
Propagation time: depends on distance, propagation speed (normally a high fraction of the speed of light) plus any delays in intermediate systems (routers etc.)
Processing time: depends on processor speed, protocol complexity, operating system scheduling delays etc.

## Slide 7: Sequence Numbers [1]
Generally, PDUs include sequence numbers in their headers so we can tell which PDU is being acked
The second data PDU is a retransmission caused by the lost ack
  “Duplicate” must be detected
Rx PE must not deliver the second PDU to its user
  Data must not be delivered twice!
Rx must ack the retransmission
Tx
Rx
Time
DATA 3
ACK 3
rdy 3
DATA 3
Notes: “rdy 3” means that the data in that PDU is ready to be passed to the user (an “indication”). It would not necessarily be passed straight away or in one lump. It is possible, for example that the Rx PE will buffer several PDUs and pass them to the user in one indication.

## Slide 8: Sequence Numbers [2]
Tx must match acks to data
What does receipt of ACK 4 mean?
  Just DATA 4 received OK?
  DATA 4, 3, 2, … received OK?
Protocols vary!
Note that Tx has (at least) 2 data PDUs outstanding here
  Tx window is at least 2
Tx
Rx
Time
DATA 3
rdy 3
DATA 4
ACK 4
rdy 4
Notes: There are many different ARQ protocols which differ in many details. How should “Ack n” be interpreted?
Data PDU n received (“selective acknowledgement”)?
Data PDUs n, n-1, n-2 … received (“cumulative acknowledgement”)?
Send Data PDU n next?
Anything else?
All of these are used in different ARQ protocols.

## Slide 9: Transmit Window [1]
Suppose Tx window is 3 PDUs
At (a) PDUs 3, 4, 5 are “in the window”
At (b) PDUs 3, 4, 5 are “outstanding”
Receipt of ACK 3 means Txwindow is {4, 5, 6} – DATA 6 can be sent
At (c) the window is full. Tx must stop and wait for another ACK.
Tx
Rx
Time
DATA 3
rdy 3
DATA 4
rdy 4
DATA 5
DATA 6
ACK 3
rdy 5
rdy 6
ACK 2
(a)
(b)
(c)
Notes: Note that, at the start (after Ack 2) the Tx window comprised DATA PDUs 3, 4 and 5. After receipt of ACK 3 the window “slides” forward to comprise 4, 5 and 6. For this reason such protocols are termed “sliding window” protocols.

## Slide 10: Transmit Window [2]
Suppose Tx window is 2 PDUs
At (b) Tx window is full – Tx must stop
Time between (b) and (c) is wasted – poor performance
Tx window must be big enough!
(See later slide)
Tx
Rx
Time
DATA 3
rdy 3
DATA 4
rdy 4
DATA 5
ACK 3
rdy 5
ACK 2
(a)
(b)
(c)
Notes: The slide shows the importance of setting the Tx window size correctly. Why not make the Tx window enormous?
a) Enormous windows imply enormous sequence numbers which waste space in the PDU headers.
b) Tx must keep copies of outstanding PDUs in case these need to be retransmitted so there are storage implications.
c) Some protocols retransmit the entire window when an error occurs so large windows can cause unnecessary transmissions.
Tx window must be big enough but not too big. [Note also that some protocols deliberately manipulate the window size in order to provide flow control.]

## Slide 11: Receive Window of 1
DATA 4
Rx window = 1 (Tx window = 3)
=> Rx processes data PDUs in strict sequence
(a) 5 is received 4 is expected
  5 is ignored!
(b) Tx window is {4, 5, 6} so 6 can be sent
  6 will be ignored at Rx
No ACK arrives, 4 retransmitted
(c) 4 passed to user and ACKed
Tx
Rx
Time
DATA 3
rdy 3
ind
ACK 2
DATA 4
DATA 5
ACK 3
(a)
rdy 4
(c)
DATA 5
(b)
DATA 6
DATA 6
ACK 4
rdy 5
rdy 6
Notes: Note that although Rx window is 1 here we are using a Tx window of 3.
This is a simple strategy for the receiver but not necessarily efficient - note that DATA 5 and 6 are successfully received twice. “Ignored” means what it says - no record of these PDUs is kept at Rx.
Because Tx window is 3 PDUs Tx stops after transmitting DATA 6 for the first time.
Note that data is delivered to the user in the correct order and that acks are cumulative.
Because Rx will discard all out-of-sequence PDUs Tx must retransmit all of these.

## Slide 12: Rx Window = Tx window
DATA 6
DATA 5
DATA 4
Rx window = Tx window
=> Rx processes data PDUs in any order
(a) 5 is received but 4 expected
  DATA 5 is buffered!
(b) Tx window is {4, 5, 6} so 6 can be sent
  6 will be buffered at Rx
No ACK arrives, 4 retransmitted
(c) 4, 5 and 6 passed to the user, 6 ACKed
Tx
Rx
Time
DATA 3
ind
ACK 2
DATA 4
DATA 5
ACK 3
(a)
rdy 4, 5, 6
(c)
DATA 6
(b)
rdy 3
ACK 6
Notes: This strategy is more complicated for the receiver and requires it to buffer PDUs whilst waiting for gaps to be filled. It can be more efficient though - especially in situations where PDUs may suffer arbitrarily delays and be delivered out of sequence. This is possible on the Internet and, consequently, TCP receivers normally use this strategy.
Note, once more we assume a Tx window of 3 PDUs.
Note that in the example above we are assuming that ACKs are cumulative – so that ACK 6 implies receipt of DATA 6, 5 and 4. This is not the only possibility – see next slide.
[Comparing with the previous slide there is no reduction in the number of re-transmitted PDUs. However, this is not always the case and this strategy often results in a reduction in retransmissions.]

## Slide 13: Selective Acknowledgement
DATA 4
Rx window = Tx window
Rx uses “selective acknowledgement” (SACK)
(a) 5 received 4 expected
  5 is buffered and acked!
(b) Tx window is {4, 5, 6} 6 can be sent
  6 buffered and acked
(c) 5 is acked, 4 is missing so resend 4
(d) 4, 5 and 6 are passed to the user and 4 is ACKed
Tx
Rx
Time
DATA 3
ind
ACK 2
DATA 4
DATA 5
ACK 3
(a)
ACK 4
DATA 6
ACK 5
(b)
rdy 3
rdy 4, 5, 6
ACK 6
(d)
(c)
Notes: With selective acknowledgement each DATA PDU is acknowledged individually – i.e acks are not cumulative. This can mean more ACK PDUs are sent but can reduce the number of retransmissions. Compare with the previous slide and note that the earlier ACKs of DATA PDUs 5 and 6 mean these do not have to be transmitted.
The strategies “Rx window = 1”, “Rx window = Tx window + cumulative Acks”, “Rx window = Tx window + selective Acks” represent increasing efficiency at the cost of increasing complexity. Which is “best” will depend on such things as propagation delay, transmission rate and error rate.

## Slide 14: Tx Strategy – “Go Back N”
DATA 6
DATA 5
DATA 4
Diagram is from slide 12
Rx uses cumulative acks
After (b), Tx:
  knows DATA 3 received OK
  knows nothing about 4, 5, 6
At (c) Data 4 “times out”
All of 4, 5, 6 must be retransmitted
This is the Go Back N strategy
Tx
Rx
Time
DATA 3
ind
ACK 2
DATA 4
DATA 5
ACK 3
(a)
rdy 4, 5, 6
(c)
DATA 6
(b)
rdy 3
ACK 6
Notes: If Rx uses cumulative acks then:
If Tx does not receive an ack for a PDU n it knows n must be retransmitted
Also, Tx will not learn the fate of PDUs n+1, n+2 since these cannot be acked until n is received.
Therefore Tx must go back to PDU n and retransmit it plus all subsequent PDUs.
Note that this argument applies whether Rx window = 1 or Rx window = Tx window.

## Slide 15: Tx Strategy, Selective Retransmission
DATA 4
Diagram is from slide 13
Rx uses SACK
At (b) Tx knows 3, 5, 6 received OK, 4 might be lost
Only 4 need be retransmitted
This is the “Selective retransmission” strategy
Tx is idle until (c)
  Should use bigger window (6)
  7, 8, 9 could be transmitted
Tx
Rx
Time
DATA 3
ind
ACK 2
DATA 4
DATA 5
ACK 3
(a)
ACK 4
DATA 6
ACK 5
(b)
rdy 3
rdy 4, 5, 6
ACK 6
(c)
Notes: If Rx is using SACK, Tx has more precise information about which PDUs have been received and which (may) have been lost. (Note that Tx never knows whether it is the data PDU that is lost or its ack).
Tx can use “selective retransmission” and avoid unnecessary retransmissions (compare slides 11 and 13).
Tx can use the time saved by moving on to the next data PDUs 7, 8, 9 etc. But it can only do this if its Tx window is bigger. In this example the window needs to be 6 data PDUs.

## Slide 16: Summary So Far [1]
Tx and Rx strategies are linked
If Rx demands data PDUs in strict sequence
  This means Rx window = 1
  If data n is missing then all subsequent data PDUs will be ignored
  Tx must retransmit all outstanding PDUs => Go Back N strategy
  Acks are implicitly cumulative

## Slide 17: Summary So Far [2]
If Rx can accept data PDUs in any sequence
  Rx window = Tx window
  If data n missing then all subsequent data PDUs are buffered
  2.1 If acks are cumulative
    Ack n => n, n-1, n-2 .. received OK
    Ack n missing means whole window may have been lost => Go Back N
  2.2 If Rx uses Selective Ack
    Ack n => just n received OK
    Ack n missing means data n is missing => Sel. Retran.
Notes: Note the point at 2.1. If the last ack Tx receives is for n-1 then data n may have gone missing and must be retransmitted. The fate of n +1, n +2 … n +w (which may already have been sent) is not clear to Tx. Tx could just retransmit n and hope that n +2, n +2 etc. were received, in which case it will eventually receive an ACK for n +w. However, if any of n +1, n +2 … n +w was lost then time will have been wasted. Go Back N avoids this waste of time at the expense of (probably) unnecessary retransmissions.

## Slide 18: Sequence Numbers Re-visited
Sequence numbers are carried in PDU headers
  “Overhead” not “payload”
SNs should be as short as possible
SNs should be fixed length (ease of processing)
SNs will “wrap round”
  E.g. 2-bit SNs
  0, 1, 2, 3, 0, 1, 2, 3 etc.
  SN “modulus” is 4
How few bits can we get away with?
Notes: SNs are carried in the PDU header. It is always desirable that the header size should be minimised since, from the point of view of the user, header bits are not useful data bits. Consequently we would like to use as few bits for SNs as possible.

## Slide 19: Sequence Number Modulus
Worst case: all acks lost, whole Tx window resent
Receiver expects “new” SNs, gets “old” ones
Resent (“old”) SNs
Expected (“new”) SNs
Duplicate detection => intersection is empty
 need at least max TX window + max RX window SNs
Rx window = 1 => m  w+1
Rx window = Tx window => m  2w
Notes: Receiver detects duplicates because their SNs are not in the set it expects to receive next. We need enough SNs to ensure there is never any ambiguity. If the SNs wrapped round so that an expected new PDU had the same number as one which might legitimately be retransmitted then there will be ambiguity.
The slide shows the limit this imposes in two important cases. This is important information for protocol designers. For example, the original HDLC protocol used 3-bit sequence numbers so m = 23 = 8. HDLC used a receiver window of 1 so with m = 8 so the max Tx window size was 7. This proved not to be enough as transmission bit-rates increased and the protocol had to be modified.

## Slide 20: SN Modulus – Delayed Duplicate
We assumed l.h. set contained only PDUs in current Tx window. I.e, we assumed:
  Tx behaved correctly
  PDU order was preserved
Sometimes (e.g. Internet) a long-delayed PDU may be delivered out-of-order
  l.h. set potentially much bigger
  PDUs must time-out before SNs wrap
Resent (“old”) SNs
Expected (“new”) SNs
Notes: Unfortunately, the analysis in the previous slide is only valid if the underlying service preserves transmission sequence. If it does not, then a DATA PDU might be delayed for a long period before reaching Rx. Tx would timeout and retransmit and, probably, the retransmission would arrive in good time and the protocol would move on. A problem arises when the delayed PDU finally arrives.
P.T.O

## Slide 21: SN Modulus – Delayed Duplicate [2]
Suppose Tx win = Rx win = 3, m = 8, PDU 2 long delayed
  Rx may be expecting (say) 7, 1, and 2
  Tx window might be 4, 5, 6 (all acks for these lost)
4, 5, 6
7, 1, 2
If a long-delayed PDU 2 arrives …
2
Solution – make m huge so that “wrap time” > max. delay
E.g. TCP, m = 231 bytes. @ 10Mbps wrap time = 1718 sec
@10Gbps -> 1.718 sec …
Notes: The solution is to make m so big that there is no possibility of the SNs wrapping round within the longest possible delay time. Long delays are possible in the Internet and TCP uses a large value of m in the hope of avoiding the problem. TCP uses a 32-bit SN so m is 232 (= 4,294,967,296) which is pretty big. However, TCP is unusual in that the SN counts bytes rather than PDUs. At 10Mbps, a TCP PE will see the TCP SNs wrap round
This is sufficient. Note, though, that at 10Gbps this falls to 1.718 sec which may well be less than the maximum packet delay. TCP has an option to add timestamps to packets to to allow Rx to eliminate ancient PDUs.

## Slide 22: Bandwidth.Delay Product [1]
How big should Tx window be?
Time ab is the “Round Trip Time” (RTT) or “Round Trip Delay (RTD)
  Normally varies!
We want to transmit throughout interval ab
b/w = b bits/sec, RTT = d secs
  Can transmit b.d bits
  Tx window must allow this
  “Continuous Request”
Tx
Rx
Time
DATA
ACK
a
b
Notes: “Bandwidth” here should really be “capacity” but the former term is normally used.
The bandwidth.delay product is an important quantity for protocol performance. On something simple like a terrestrial data link (e.g. 256Kbit/sec ADSL line 1 Km long) it is fairly easy to estimate and will be fairly constant. On an Internet link across half the globe it may be highly variable and difficult to estimate. See section on TCP.

## Slide 23: Bandwidth.Delay Product [2]
Propagation time 105/(2x108)=5x10-4 sec
Data time (206x8)/4x106 = 4.12x10-4 sec
Ack time (6x8)/4x106 =1.2x10-5 sec
RTT = 2x 5x10-4 + 4.12x10-4 + 1.2x10-5 = 1.42x10-3 sec
B/w.delay = 4x106x 1.42x10-3 = 5680 bits = 3.44 data PDUs
Tx window  4
Tx
Rx
Time
DATA
ACK
Example: 4Mbit/sec line 100 Km long. 4 byte headers, 2 byte checksum, mean payload 200 bytes. Propagation speed 2x108 m/sec
Notes: Note that this is estimation! We have ignored processing times. Not all data PDUs will carry 200 bytes, ack PDUs may contain data. We probably use a window of at least 6 to be on the safe side.
Also, see next two slides.

## Slide 24: Timeout values
Clearly, Retransmit TimeOut (RTO) (ac) must be greater that RTT (ab)
Set very long RTO?
Tx window must span RTO
Big RTO means
  Need bigger Tx window
  Need more buffering at Tx
  Longer error recovery?
Tx
Rx
Time
DATA
ACK
a
b
Retransmission
c
Notes: We need to set RTO so that it is bigger than RTT – but, ideally, only just. This is difficult to achieve in environments like the Internet where RTT is variable and difficult to predict.
Note that for efficient operation we need Tx to continue between a and c (see also the next slide).

## Slide 25: Tx Window (Finally)
ACK
Consider selective retransmission and acknowledgement
Ack should have arrived at (c)
Timeout occurs at (d)
Ack finally arrives at (e)
Any data PDUs send in be will be buffered at Rx
Tx window must span RTO+RTT
Tx
Rx
Time
DATA
a
c
Retransmission
d
ACK
e
b
Notes: With the go-back-n strategy, once retransmission begins we simply repeat PDUs already sent (and possibly discarded by Rx).
With selective retransmission only the affected PDU is retransmitted and this may be followed by new PDUs. A bigger Tx window is needed to allow for these extra transmissions.

## Slide 26: Protocol Performance [1]
What are we trying to optimise? What does “utilisation” mean?
Single link – optimise use of link
  Make sure it is always in use
  Greedy strategy
Shared medium
  Optimise use for all users?
  Optimise one connection?
  Friendly strategy
PE
PE
PE
PE
PE
PE
PE
Notes: On a point-to-point link the aim will be to keep the link busy at all times. Errors should be recovered as soon as possible so we should set aggressive timeouts and not worry too much about unnecessary retransmissions. Utilisation measures the proportion of the time the link is doing useful work.
On a shared link there is a conflict between the network operator who wants to offer service to as many users as possible and individual users who want to optimise their own use. Aggressive timeouts, which may sometimes result in unnecessary retransmissions, suit individual users but at the expense of other users. For the operator, utilisation is a measure of the proportion of total network capacity that is being used.

## Slide 27: Protocol Performance [2]
If there are no errors and Tx window is big enough
  Transmission will be continuous
  Utilisation = 100%
If there is an error, time will be lost
How much time? Depends on:
  RTO (which depends on RTT)
  Strategy used (Go Back N, SACK etc.)
Effect on utilisation? Depends on:
  Frequency of errors
  Error distribution (burstiness)

## Slide 28: Error Rates
P(bit in error) = b, mean PDU size = s
P(PDU not in error) = (1-b)s, P(PDU in error) = 1- (1-b)s
But, errors are bursty
Small PDU size => large header overhead
Notes: Graph shows how increased error rate demands a smaller PDU size for a given PDU error rate (10-3 in this case). However, the calculation assumes bit errors are independent. In practice, errors tend to occur in bursts. This means that if a PDU has one bit in error it probably has several bits in error. Therefore the PDU error rate is lower than the graph suggests.

## Slide 29: Error Recovery Time
Go Back N, Rx window 1
  a d is lost (RTO)
Go Back N, Rx win = Tx win
  a c repeated in d e
  c d buffered and acked at e
  a c is lost (RTT)
Selective Retrans. + SACK
  Just one retransmission
  a b is lost
N.B. High capacity means more PDUs lost per unit time.
ACK
Tx
Rx
Time
DATA
a
c
Retransmission
d
ACK
e
b
Notes: For GBN, Rx window 1 all the time between the end of a failed transmission and the start of its retransmission is lost. I.e cost is 1 RTO.
For GBN, Rx window = Tx window retransmissions cease as soon as the ACK for the first retransmitted PDU is received. I.e cost is 1 RTT.
For selective retransmission + SACK only one PDU must be retransmitted.
This suggests we should always use selective retransmission + SACK. However, this is the most complex strategy with a greater chance of bugged or incompatible implementations. It also has the greatest buffer requirements at Tx and Rx. Consequently, it is not always the best choice.
Although transmission bit-rates increase, propagation delays remain much the same - hence the bandwidth.delay product increases. This means that, for Go Back N, more data is retransmitted each time an error occurs.
[N.B. The analysis above is greatly simplified and ignores a number of complications. However, it does capture the essence of the differences between the strategies.]

## Slide 30: Error Recovery Strategy
If error rate low, RTT low, capacity low
  Not too much data lost and doesn’t happen often
  Go Back N is reasonable
  If var(RTT) low
    RTO can be set close to RTT
    Rx window of 1 is OK
  If var(RTT) high
    RTO >> RTT
    Rx window = Tx window is better
  If Sequence not maintained
    Should use Rx window = Tx window
Otherwise sel. retrans. and SACK may be best
“Normal” TCP strategy
TCP option
Possible wired data-link strategy
Notes: Slide shows some considerations for the designers of real protocols. Note that sometimes combinations or variants of these strategies may be employed. Note also that some protocols may allow several strategies with the actual one used being negotiated at run-time according to the prevailing conditions.

## Slide 31: Internet Future
p = 25ms, c = 1Gbps, e=10-8
Notes: In future we may expect to see Gigabit speeds on the Internet accompanied by enhanced reliability – both brought about by the introduction of optical fibre.
The graphs show the utilisation achieved by three strategies:
  GBN-T: Go Back N with Tx window = Rx window
  GBN-1: Go Back N with Rx window = 1
  SR: Selective retransmission + selective acknowledgement
“Utilisation” means the proportion of the capacity used that is doing useful work – i.e. carrying payload. We assume fixed-size headers.
In the graphs p is the propagation time. To a first approximation RTT = 2p. c is the capacity available and e is the bit error rate.
Note that all three strategies initially give increased utilisation. This reflects the fact that the header overhead diminishes as the payload size increases. Eventually, however, the increased payload size leads to an increased PDU error rate and utilisation diminishes. The effect is much more dramatic for the two GBN strategies. This is because high capacity + relatively high RTT gives a high bandwidth.delay product so that retransmissions of complete windows are costly.

## Slide 32: Idle Request
Tx window = Rx window = 1
Also called “Stop and Wait”
Very simple strategy
Not “continuous request”
Utilisation OK provided b/w.delay product is low
E.g. 1Km, 1Mbps wireless link, 200 bytes data, 40 bytes ack
p = 103/(2x108) sec = 5s, d = 200x8/106 sec = 1600 s, a = 40x8/106 sec = 320 s
Utilisation = 1600/(2x5 + 1600 + 320) = 83%
Tx
Rx
Time
DATA
ACK
DATA
ACK
Notes: A reminder that simplicity is sometimes best!

## Slide 33: Sliding Window Flow Control
Suppose there are no errors
If window is big enough, transmission is continuous
  Utilisation = 100%
If window spans p% of RTT, utilisation is p%
Throughput is p% of capacity
Tx
Rx
Time
Window span
RTT
Reduce Tx window => flow control
Add delay at Rx to increase RTT => flow control
Notes: We may want artificially to restrict the throughput because:
The receiver may not be able to deal with incoming data quickly enough
We want to restrict the proportion of network resources used by a connection (congestion control)
By manipulating the Tx window we can artificially reduce throughput – i.e. we get flow control. TCP does this; Rx tells Tx what window to use.
We can also achieve flow control by artificially increasing RTT by delaying the transmission of acks. The danger here is that Tx will time out and retransmit.

## Slide 34: Rx Controls Tx window (e.g. TCP)
Initially Tx window = 4
(a) Tx window used - stops
(b) Rx wants 4 more – puts w=4, a=4 in PDU
(c) 4 is acked and w=4
  New window is 5678
  567 already sent
(d) Rx wants 3 more – puts w=3, a=7 in PDU
(e) Rx “opens the window” to increase the flow
Tx
Rx
Time
4
5
6
7
4
7
Tx Window
w=4
8
w=3
9
0
4567
4567
4567
4567
4567
~
5678
890
890
890
(a)
(b)
(c)
(d)
8
(e)
w=8
90123456
Notes: Ack PDUs now contain window sizes as well as ack numbers.
[Note that, in practice, TCP numbers bytes and not PDUs].
Also, TCP, like most protocols provides a duplex service. Thus the ack PDUs sent by Rx may contain data passing in the other direction. In such cases all PDUs carry both data and ack SNs as well as window sizes.

## Slide 35: Stop/go Flow control
8
Fixed Tx window (say 4)
RR and RNR flags
(a) Tx window used - stops
(b) Rx happy to continue – puts RR in ack 4
(c) Rx wants flow to stop – puts RNR in ack 7
(d) Although 901 are valid, Tx must stop
(e) Rx sends a “keep-alive”
(f) Tx re-enables the flow
Tx
Rx
Time
4
5
6
7
4
7
Tx Window
RR
8
RNR
4567
4567
4567
4567
4567
5678
5678
(a)
(b)
(c)
7
(e)
8901
RNR
8901
RR
9012
(d)
(f)
Notes: RR: Receiver Ready => transmissions can continue
RNR: Receiver Not Ready => transmissions must cease
The Tx window also provides flow control as at (a)
Whilst flow is stopped, Rx may repeat the last ack so that Tx knows it is still alive.
Clearly there is a delay between Rx issuing an RR or RNR and Tx receiving it. This causes some implementation problems, for example, Rx may need to issue RNR before it’s buffers are full since it knows some data PDUs may already be “in flight”.

## Slide 36: Possible API for a service using ARQ
Generally (not always!) a CO service
API example – class ARQService
// Open connection to a destination
public ARQService(address a);
// Wait for incoming connection (may block)
public ARQService();public void listen();
// Send len bytes of data (may block)
public void send(byte[] data, int len);
// Receive maxln bytes (may block)
public int receive(byte[] data, int maxln);
// Close the connection
public void close();
Notes: Warning. This is a toy example – not really comprehensive.
A key point is that this API would suit all the protocols; go-back-n, selective retransmission or whatever. I.e. the service is independent of the protocol.
The first constructor initiates a connection, the second one, in conjunction with the listen() method waits for an incoming connection request. This is a synchronous interface.
The type of address in the active connect would be specific to the service. For example, for TCP it could be an IP address + port.
Additional parameters might be needed at connect time in order to negotiate features of the service; maximum data sizes, optional facilities etc.
The criteria for return from receive() need some thought. One possibility is to return as soon as any data is available, up to a maximum of maxln bytes. Another is to return only when maxln bytes have been received. This may be more efficient but there is a danger of an indefinite block if the remote sends less data than expected. Some APIs include a push() method which allows the sender to force the receiver’s blocking receive to complete. However, for this to work there needs to be a flag in the PDU header to convey the “push”. TCP has this. In our example we return as soon as data is available. The return value indicates the number of bytes actually delivered.
The data parameter in receive() is a reference to an empty byte array that will be filled with incoming data.

## Slide 37: Summary
Sequence numbers and acknowledgements
Tx window limits number “outstanding”
Tx window size affects performance
  Optimum affected by RTT and RTO
Continuous request, idle request
Recovery strategies – Go Back N, Rx win = 1, Rx win = Tx win, SR, SACK
Performance affected by strategy, error rate, RTT, capacity etc.
Flow control