## Slide 1: Routing
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Calculating routes: where and when?
Where?
  Distributed:
    Each node calculates next hops to all destinations
  Centralised:
    NCC: decides all routes
    Single point of failure
  Source:
    Originating host decides routes
    Needs a lot of information
When?
  Continual
    New calculation for each packet
  Periodic
    Every few seconds
  Load change
    When congestion occurs
  Topology change
    Initiated by management
Notes: There are three possible models for locating the routing decision:
1) Distributed: each node makes decisions about the next hop ‑ i.e. on which link should the packet be forwarded. This is robust but can lead to consistency problems.
2) Centralised: a Network Control Centre (NCC) plots routes between pairs of hosts or exterior nodes and informs the relevant nodes. This is most useful in networks using VCs internally. The NCC constitutes a single point of failure and so must be very robust.
3) Source: the originating host or exterior node chooses the route and this choice is recorded in the packet.
Models 2) and 3) require knowledge of the whole network all in one place. Model 1) can adapt easily to topology change but is generally harder to manage.
Generally, one can say that the more frequently routes are changed the more optimal they are likely to be. However, there will be increased costs involved in moving routing information around, updating tables, etc. Also, strategies that change routes frequently are more prone to problems resulting from inconsistent routing information. This may cause a packet to loop around the network without ever reaching its destination.
Four strategies can be identified:
a) Continual updates: these must be based on purely local information such as queue lengths. Essentially a new route is calculated for each packet.
b) Periodic updates: these are based on the periodic exchange of state information with other nodes. Generally the intention is to provide adaptive routing where routes are altered to reflect real-time circumstances. This implies updates occur every few seconds.
c) Response to major load change: routes may be re-organised after congestion is detected for example.
d) Response to topology change: change routes when a new node, host or link is added.

## Slide 3: Information–free Routing
Inefficient but simple
Flooding
  send all packets on all links
  robust
  used to bootstrap other mechanisms
Random
  send packets on link chosen at random
  good load distribution
Almost information free - Hot-potato algorithm
  Queue packets on link with shortest queue
Notes: It is worth noting that there do exist routing strategies which require no external information:
Flooding: this is a simple strategy; all nodes send all packets out on all links. Packets are numbered so that nodes can destroy packets they have already forwarded. If you are really keen that all your packets reach their destinations then this is the strategy for you; in fact, probably several copies of each will be delivered. This is, of course, very wasteful of network capacity but it is extremely robust. Consequently it is favoured in some military networks. It is also used for some special purposes associated with routing - for example discovering the initial network topology. Some kind of mechanism is needed to prevent packets circulating forever. This can be done with a hop-count in the packets. When the count reaches a pre-determined maximum, the packet is discarded. Alternatively, packets can be numbered and nodes can discard packets already encountered.
Random: one link is selected at random and the packet is forwarded on that. Eventually it will (may) reach its destination. This is perhaps more interesting from a theoretical than a practical point-of-view.
The hot potato algorithm is a somewhat more plausible variant of the random algorithm. Here, the packet is always forwarded on the link with the shortest queue (this is observed to be the strategy adopted by taxi drivers in Rome).

## Slide 4: Backward learning
A
C
B
D
x
y
z
destination next hop hops
A C 2
E
Simple:
  often used as bootstrap for other routing protocols
Algorithm:
  look for source address
  forwarding table entry in reverse direction
  destination unknown: flood
  data packets refresh forwarding table entries
Problems:
  looping
  node failures
destination next hop hops
A C 2
destination next hop hops
A E 3
A
C
B
D
x
y
z
E
Notes: The key feature of backward learning is that it distributes routing information without imposing any additional load on the network. The method exploits the fact that datagram packets invariably contain source and destination addresses. Node B which receives a packet from node A (to node D, say) on link x can conclude that node A is accessible via x and can place that fact in its forwarding table. In effect each incoming packet contains routing information and engenders a continual updating of the distributed routing information
The algorithm bootstraps by flooding; if the forwarding table contains no route to a destination the packet is sent on all outgoing links. This ensures that the packet will eventually get through to the destination and also teaches many nodes about routes back to the source. Clearly, this can replicate packets.
Flooding can result in several copies of a packet arriving at a node on different links. A rule is needed to enable the node to chose the “best” backward path. Placing a hop count in the packets, (to be incremented by each node along the route), helps with this. Thus node B will know that the route to host A via link x is 2 hops. If it then receives a packet from A on link y with a hop count of 3 it can ignore it. A tie-breaking rule is still needed when hop-counts are equal – choosing the link with the lowest id is a possibility.
A problem arises if a route goes bad due to some component along it breaking. For example (see slide), if the link between node C breaks, B will continue to forward packets for A along link x. Although packets may now arrive at B from A via link y, this route will be ignored as the hop count is greater than that stored in B’s current table. This means that B will never learn the new route. The solution is to have nodes delete entries from their routing tables if these are not refreshed by an incoming packet within a certain time interval. This forces the node to learn a new route.
Backward learning is not often employed as a routing method within packet switched networks. In fact, it finds its main application in the MAC bridges which are used to interconnect LANs. Note that MAC frames do not include hop-counts so that topologies with loops must be avoided.

## Slide 5: Sources of Routing Information
Local sources
  Queue lengths
  Measured delays
  Configured link “costs”
Central source – “Network Control Centre”
All nodes
  Metrics received via flooding
Adjacent nodes
Notes: Generally one can say that the more information available when a routing decision is made, the better that decision will be. Unfortunately, the more information used, the more computationally expensive will be the decision, and also the more information that will have to be exchanged between routers. Sources of information depend on where the decision is being made and what type of information is required. Some possibilities are:
from a local source: queue lengths, link capacities etc.
from a central source
from all nodes
from adjacent nodes

## Slide 6: Routing Policies and Constraints
Administrative
  Commercial agreements to carry traffic from certain sources
  Priority routes for some traffic
Security
  Avoid “untrusted” networks
QoS
  Route certain traffic types via “suitable” links
Real cost (financial)
  Only use high-cost links when all else fails
Notes: All sorts of policies may be applied. Certain types of traffic may be excluded from some routes perhaps because it is low priority. Sometimes there are legal factors; private networks are not allowed to carry third-party traffic, US companies may not like their traffic being routed through Iraq etc. some factors that may be part of a routing policy include:
administrative-related information (e.g. for managing resources)
security-related issues for sensitive traffic
QoS factors for certain real-time applications
cost of sending data
Of course, some of these factors will be in conflict with others, e.g. QoS and real financial cost

## Slide 7: Problems with the ARPANET algorithm
Distance-vector – inherent problems
Use queue length as metric – diverts traffic away from congestion
High capacity links not specially favoured
Queue lengths are not stable
Oscillations:
  route flapping
So, replace it!
Notes: The ARPANET problem suffered all the inherent distance-vector problems. There were additional problems related to the choice of metric.
One strength of the algorithm lay in the fact that the distance measure is queue length, the metric is related to congestion. Thus, the algorithm tended to direct traffic away from congested areas. However, several problems were found:
  high capacity links are not given favoured status
  queue length varies rapidly in time. Therefore the algorithm tended to respond to statistical fluctuations rather than real changes in load.
  the algorithm proved very prone to oscillation. Once load has been moved to an un-congested area, this tends to become congested and so on.

## Slide 8: Internet - Large-scale structure
Traffic types:
  local: intra-AS
  transit: inter-AS
AS:
  stub AS: e.g. site network
  multi-homed AS: e.g. ISP
  transit AS: e.g. backbone provider
Internet:
  collection of interconnected stub, multi-homed and transit ASs
transit
transit
transit
multi-homed
stub
transit
transit
transit
backbone
networks
ISPs
site networks
or ISP dial-up users
Notes: Autonomous systems (ASs) are typically networks that are run by a single administration, and internally, a single routing protocol will be used, e.g. RIPv2 or OSPFv2. ASs are characterised but the kind of traffic they carry. IP traffic is local or transit traffic:
local: traffic with source or destination addresses within the AS
transit traffic: anything other than local traffic
and an AS is either a sub AS, multi-homed AS or transit AS:
stub AS: carries only local traffic and connects to only one other AS
multi-homed AS: connects to more than one other AS, but carries only local traffic
transit AS: carries local and transit traffic, and is connected to more than one other AS
These characterisations are in the context of routing, but in the context of service provision and consumption, a stub AS or multi-homed AS is typically a site network, though it is possible that this is also an Internet Service Provider (ISP). (Note that ISP dial-up users are effectively part of the ISP site network.) Transit networks could be ISPs (those that perhaps do not have dial-up users just corporate users with their own site networks), or backbone service providers. Connectivity between ASs is by mutual arrangement between AS administrators.
So, one way of defining the Internet is as an ad hoc collection of stub, multi-homed and transit ASs, all using IP.

## Slide 9: Autonomous Systems
The Internet is partitioned along administrative boundaries
  “Autonomous systems”
Within an autonomous system
  Single routing protocol
    “Interior gateway protocol” – e.g. RIP, OSPF
  Single administration
Between autonomous systems
  Exterior gateways
  “Exterior gateway protocol” – e.g. BGP