## Slide 1: Spectra and Modulation
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Spectra, Modulation and Multiplexing
Fourier Transforms and spectra
Analysis of signals
Frequency Shifting
Modulation
Frequency-Division Multiplexing

## Slide 3: Questions
I have looked at the next slides and have seen an integral sign. How do I change to another course?
How do we make our data suitable for transmission?
What are the capabilities and performance of such transmission techniques?:
  What are the problems?
How can we sub-divide a single physical channel into several sub-channels?
Notes: Data can be transmitted through wires, fibres or through space using microwaves etc. Each of these media has its own characteristics in terms if capacity, noise immunity etc. When we transmit data we have to represent it by “signals” which are suitable for the medium in question. The theory presented here gives a very brief introduction to the mathematical modelling that may be used by the designers of transmission systems in order to optimise their use.

## Slide 4: The Approach
Start with a “signal” that represents our data
  Physical quantity (e.g voltage) varying with time
Apply a “Fourier Transformation”
  Analyses the signal into component frequencies
  A “complex” function
Compare signal frequencies with channel frequencies
Understand effect of modifying signal on component frequencies

## Slide 5: Recollection – Periodic Functions
Fourier Theorem:
  sinusoidal components
0
0.2
0.4
0.6
0.8
1
1.2
0
2
4
6
8
10
12
time
square wave
0
frequency [Hz]
square wave
1
2
3
2
5
2
7
2
9
2
Notes: Fourier’s Theorem states that any periodic signal can be represented as a sum of sinusoidal components of varying amplitude and frequency. For example, a square wave can be represented by the expression:
The period of the square wave is 2 secs so the frequency is 1/ 2 Hz. This is also the frequency of the first component in the Fourier series – sin(t). However, the next component – sin(3t) has a frequency 3 times as much and the next – sin(5t) 5 times as much.
The diagram on the right shows the spectrum of the square wave. For a periodic function this will be discrete.

## Slide 6: Now – aperiodic functions
0.5
1
1.5
E.g. Digital signals consist of a sequence of square “pulses”
For a given bit-rate what frequencies will be generated?
  How much of each?
Frequency (MHz)
-1
1
Time (s)
Fourier Transform
“Spectrum”
Notes: Often a digital signal can be thought of as a sequence of square pulses.
Fourier transforms allow us to analyse such pulses. The slide shows an idealised square pulse of duration 2 s. We can think of this as representative of a single bit in a 0.5 Mbps bit stream. (Note that we are no longer considering a periodic function so we need something more than a Fourier Series.)
On the right we see the spectrum produced by the Fourier transform which shows that the bulk of the power of the square pulse is in the range 0– 0.5 MHz. There are also frequencies above 0.5 MHz but these are of decreasing significance.
We now have two views of the same signal; one in the “time domain” and one in the “frequency domain”.
Real transmission systems only pass a limited range of frequencies. We might know that a particular one effectively limits frequencies to the range 0-1 MHz. We could throw away the right-hand part of the spectrum and apply an inverse Fourier transform to see what effect this would have on the “squareness” of the pulse.

## Slide 7: Complex Numbers – Quick Revision
a = r(cos + isin) = rei

r
R
I
i2 = -1
 is the “argument”
arg(a) = 
r is the “modulus”
|a| = r

## Slide 8: Fourier Transforms [1]
Fourier Theorem
  Periodic function with freq. f may be represented as a sum of sinusoidal waves with freq. f, 2f, 3f ,4f …
For a non-periodic (“Aperiodic”) function it turns out that
  I.e. s(t) is a sort of infinite sum of sinusoidal waves
Notes: The slide shows the similarity between the discrete sum of the Fourier theorem (which applies to periodic functions) and the “infinite sum” implicit in the integration which must be used for aperiodic functions. (Note that we do not prove either of these results here).
Note that cos(2ft + ) is a sinusoidal wave with frequency f and phase . I.e. the wave is shifted /2f to the left.

## Slide 9: Fourier Transforms [2]
The formulae for s(t) and S(f) enable us to switch between the time and frequency domains
Notes: In this course it is not necessary to understand fully the mathematical justification behind Fourier theory (neither is it necessary to remember the formulae!).
Note that the expression for s(t) implies the existence of negative frequencies. These have no practical meaning for us and can be ignored.

## Slide 10: Example – Square Pulse Signal
-T/2
T/2
Time
Notes: Notice that S(f) incorporates the amplitude and phase components of the signal into one complex function. The value of the technique for us is that it enables us to take a “signal” s(t) and analyse it in terms of the energies associated with each of its frequency components.
A real signal, i.e. one which is carrying information for us, is very complex. It would be hard for us to compute the Fourier transform for such a signal analytically. However, many signals of interest to us consist of a train of roughly square pulses. It is quite simple to analyse a single, isolated square pulse and, in fact, this reveals some important characteristics of more complex pulse trains.

## Slide 11: Example – Square Pulse Signal [2]
Effective bandwidth
Frequency (Hz)
-3/T
-2/T
-1/T
1/T
2/T
3/T
T
Main-lobe: effective bandwidth
  (Approx 90% of total energy)
Faster signal changes require greater bandwidth
Notes: We obtained the Fourier Transform
This is an unusual case in that the F.T. is real – there are no is left. The modulus of S(f) – which gives the signal magnitude spectrum – is plotted on the slide. (Note that the left-hand part of the graph shows negative frequencies and can be ignored). Clearly the range of frequencies – hence the bandwidth – is infinite. However, the bulk of the energy is concentrated in the main lobe between 0 and 1/T. We would say that the “effective bandwidth” is 1/T. (Often this is loosely referred to as the “bandwidth” of the signal). The definition of effective bandwidth is a arbitrary. However, it reflects the fact that provided a communications channel successfully carries at least the effective bandwidth then most of the information in the signal will be preserved (see also the next slide).
Note that the quicker the change in the signal (the smaller the value of T and so the shorter the pulse), the greater width of the main-lobe, i.e. faster changing signals require more effective bandwidth.

## Slide 12: Channel Bandwidth
Real channels do not carry all frequencies equally effectively
Channels are often modelled as carrying some frequencies almost perfectly, others not at all
The graph shows the effect of eliminating all frequencies greater than 4/T from the square pulse
The graph shows how a square pulse would emerge from the channel
-T/2
3T/2
-T
-3T/2
0
T/2
T
Notes: Recall the two Fourier relationships:
These describe the same signal in the time and frequency domains respectively. Passing a signal through a bandwidth-restricted channel can be modelled by multiplying S(f) by a function which represents the restriction. A simple form might be:
Which eliminates all frequencies greater than 4/T. (In reality, the function might be more complex but we like to keep the maths simple!) The Fourier transform for the output signal from this channel will be:
This can be solved numerically and gives the graph shown on the slide.
Note that one effect of the bandwidth restriction is to spread the pulse over a longer time-interval.

## Slide 13: Inter-symbol interference (ISI)
Signal pulses “spread”:
Inter-symbol interference
Need greater separation
Reduced bit-rate
Notes: In reality, all channels are bandwidth limited. As the previous slide showed, this results in pulses spreading. This can lead to inter-symbol interference (ISI) which results in a reduction of bit-rate.
ISI is the name given to the mistaken identification of one bit due to the presence of a neighbouring bit. The importance of ISI varies according to the system. The data-rate of optical fibres is usually determined by the need to separate bit-intervals sufficiently to avoid ISI.

## Slide 14: Interactions between signals [1]
1
-1
1
-1
Signal a
Signal b
time
time
1
-1
2
-2
Signal a + signal b
time
Notes: It is often useful to have two (or more) signals share a channel. For example, when a broadband Internet connection is provided over a telephone cable then both the broadband and telephone signals must co-exist. This can only work if we can successfully disentangle the signals at the receiver.
When two signals share a channel their combined effect can be modeled as an addition. Sometimes they reinforce, sometimes they conflict.

## Slide 15: Interactions between signals [2]
Suppose we transmit two signals u(t) and v(t)
It is easy to show that
  The Fourier transform is linear
For a particular component (f1 say), can add the FTs
V(f1)
U(f1)
V(f)=(v(t)), U(f)=(u(t))
W(f)=(u(t)+v(t))=(u(t))+(v(t))
Note |W(f1)||U(f1)|+|V(f1)| and
|(u(t)+v(t))|  |(u(t))|+|(v(t))|
W(f1)
Notes: What happens to the Fourier Transforms (hence spectra) when two signals are added?
First we see that the FT is linear since
However, note that the FT is a complex function so that addition of two FTs must follow the rules for complex addition as shown in the diagram. This means that for any particular frequency, the power of the combined signal is generally less than the sum of the powers of the original signals – i.e. the signals interfere.

## Slide 16: Interactions between signals [3]
S(f1)
r

r = |S(f1)| = R(f1) (amplitude of f1 component)
 = arg S(f1) = (f1) (phase of f1 component)
For a particular value f1 we can show S(f1) on an Argand diagram.
Notes: Recall that Fourier analysis interprets a signal as an infinite sum of sinusoidal waves. If we take a particular component frequency, f1 say, then S(f1) tells us the amplitude and phase of the component sinusoidal wave which has frequency f1. The slide shows this on an Argand diagram,

## Slide 17: Interactions between signals [4]
Consider two signals u(t) and v(t) and their components at a particular frequency f1.
U(f1)
V(f1)
U(f1)+ V(f1)
In phase. Amplitudes add.
U(f1)
V(f1)
1800 out of phase, equal amplitudes. Components cancel.
U(f1)+ V(f1)
U(f1)
V(f1)
U(f1)+ V(f1)
In general. Components interfere.
Notes: The slide shows several ways in which two components might interact at a particular frequency. In general the components will interfere in an arbitrary way. Normally, this is a problem since it mean that both signals will be damaged in the frequencies in which they overlap. Sometimes though, the interference can be useful. For example some noise reduction techniques rely on using cancellation.

## Slide 18: Interactions between signals [5]
|{u(t)}|
|{v(t)}|
|{u(t)+v(t)}|
Often a signal is concentrated in a limited frequency range.
Suppose two signals u(t) and v(t) use different ranges so that
U(f) <>0 => V(f) = 0 and vice versa.
There will then be no interference
Can we shift signals so they do not interfere?
Notes: Signals using overlapping frequency ranges would normally interfere destructively.
However, if the two signals do not have overlapping frequencies (U(f) <> 0 => V(f) = 0 and vice versa) there will be no interference and no information need be lost.
We could exploit this if we could alter the frequency range used by one or both signals so that there is no overlap. We could then send two or more signals through the same medium. This is the principle behind frequency-division multiplexing used in radio and TV transmission as well as in data communication through a wire (e.g. ADSL separates voice and data channels in this way).
Frequency shifting can also be of use if the medium suppresses the most important frequencies in our signal – we can simply shift the frequency range to one compatible with the medium.
There is a range of techniques for achieving a shift – known as “modulation”. Fourier analysis is important in designing and understanding modulation techniques.

## Slide 19: Modulation example - OOK
On-Off Keying
Binary stream switches carrier on and off
Simple, cheap
Not particularly efficient
Used for optical fibre transmission
Mathematically the signal is multiplied by the carrier
Next slides show the maths!
0
0
0
1
1
1
fC

## Slide 20: Carrier Wave [1]

## Slide 21: Carrier Wave [2]
New spectrum is
  Shifted to fc
  Half the original power
  Requires twice the effective bandwidth
Notes: The resulting spectrum is two duplicates of the original spectrum each of half the original height. Taking the effective bandwidth as being the width of the main lobe as before, we see the effective bandwidth is doubled. (As before we can ignore the negative frequencies.) The implication of this is that a channel which carries the modulated signal will need more bandwidth than one to carry the original signal. The transmitter may also need more power to compensate for the lower energy.
However – we have achieved something very useful in that the signal spectrum has been shifted. By choosing fc we can shift the spectrum anywhere we want it.
Note that the effect:
  Shift spectrum by fc;
  Halve the power;
  Double the bandwidth,
is independent of the nature of the original signal.

## Slide 22: OOK again
not to scale
fC
fC
Transmitter
Notes: Mathematically, the original signal, s(t) is multiplied with the carrier, c(t), which is is simple sinusoidal wave of frequency fc. We saw earlier that the resulting spectrum will consist of two “sidebands” which are copies of the original signal translated in frequency by fc. The slide shows this – this time with the negative frequencies eliminated.
Sometimes, the lower sideband may be removed before transmission by use of an appropriate filter (e.g. a “bandpass” filter that only allows the upper sideband to pass through) before transmission. This restores the bandwidth to that of the original signal. (Remember: bandwidth costs money!)
Note that the sidebands have a lower amplitude than the original signal. Typically, the final signal, m(t), is amplified before being transmitted, however this is not important in this context.

## Slide 23: OOK again [2]
not to scale
low-pass
filter
fC
Receiver
2fC
Notes: At the receiver, the signal is once more multiplied with a copy of the carrier wave that is generated locally. This results in the original signal, s(t), in it’s original frequency range, plus another signal at 2fc. A “lowpass” filter is used to recover the original signal.

## Slide 24: Other Modulation Techniques
OOK uses amplitudes to represent bit values.
Can also use
  Frequencies (FSK), Phase shifts (PSK)
Usually possible to analyse as signal × carrier
Therefore
  Frequency Shift to carrier frequency
  Half the power
  Twice the bandwidth
Practical techniques combine several modulation techniques

## Slide 25: Modulation Example
The example shows two phase shifts and one amplitude change
  4 phase shifts 450, 1350, 2250, 3150
  2 amplitudes
  4 x 2 = 8 symbols => 3 bits per symbol
450
2250
Notes: The example shows Quadratue Amplitude Modulation (QAM) 4 phase shifts and 2 amplitudes giving 8 symbols hence 3 bits per symbol.

## Slide 26: Constellation Diagrams
Used to summarise a modulation scheme
E.g. The QAM scheme in the previous slide might be
0
+90
+180
+270
QAM
000
001
010
011
100
101
110
111
Notes: The diagram shows, for example, that 001 will be transmitted by phase shifting by 450 and adopting the higher amplitude.

## Slide 27: Frequency-Division Multiplexing [1]
If channel bandwidth >> signal bandwidth
  Multiplex several sub-channels
We can modulate each sub-channel with a different carrier
How can we ensure the sub-channels do not interfere?
Notes: FDM is used extensively in wireless communication where the use of different carrier frequencies serves to prevent different activities from interfering. It is also used in wired communication – for example to separate the voice and data channels in ADSL. Further, it is not possible, currently, to use the full capacity of optical fibre as a single channel since the interfaces between electrical and optical systems cannot go fast enough. The solution is to divide the capacity of the fibre into several smaller portions by FDM. This is known as “Wavelength-Division Multiplexing” (WDM) – see later.
FDM relies on some principles we discovered earlier.
  Multiplying a signal by a sinusoidal carrier shifts the signal spectrum so that it is centred on the carrier frequency. By using a different carrier for each sub-channel we can ensure that their resulting spectra are well-separated. (See next slide)
  The Fourier Transform is linear. This means that, assuming the spectra do not overlap, the spectrum of the multiplexed signal is simply the sum of the spectra of the sub-channels. One consequence of this is that if two signals we are adding have widely separated spectra they will not interfere significantly.

## Slide 28: Frequency-Division Multiplexing [2]
Filter signals to remove frequencies outside “effective bandwidth”
Choose carrier frequencies so that overlap is minimal
Bandpass filters to recover signals
f2
f4
f5
Original signal
f1
f3
f1
f3
Notes: We have seen that any signal has an “effective bandwidth”. In general there will be frequency components outside the effective bandwidth range. We lose nothing important if these components are discarded. In fact, in the context of FDM, it makes good sense to filter out these components so that they cannot interfere with adjacent channels.
We must then choose carrier frequencies which are far enough apart to prevent interference. Ideally we might aim to separate the channels by no more than the band-width of the sub-channels. However, in practice, somewhat more separation is needed – called “guard bands” - to ensure inter-channel interference is acceptably low. The slide shows a typical; example with five sub-channels centred on five different carrier frequencies.
The receiver can pass the multiplexed signal through a series of bandpass filters – circuits which allow a range of frequencies to pass but which suppress all others. This enables the sub-channels to be recovered. This is exactly what you do when you tune a radio to a particular frequency.
A classic example of FDM is the scheme used on old analogue telephone trunks. 12 voice channels are multiplied by carriers at 62kHz, 66kHz, … , 106hHz. Thus, each sub-channel is allocated 4kHz. In fact each sub channel is filtered to 3kHz so there is a 500Hz guard band either side of each sub-channel.

## Slide 29: Wavelength-Division Multiplexing
Like FDM but applied to light
Each channel is assigned a different wavelength - a colour
Up to 100 sub-channels on one fibre
Notes: <header>
Slide <number>
It is possible to apply the FDM technique to optical transmission - in which case it is called “Wavelength-Division Multiplexing” (WDM). Light frequencies or wavelengths correspond to different colours. Each input channel is assigned a different colour and all colours are transmitted simultaneously down the common channel. Optics at the far end separate the colours and restore the original sub-channels. Optical switches can also be built to switch sub-channels between fibres in arbitrary ways.
The nice thing about WDM is that it can easily be applied to existing fibres. Around 100 sub-channels can be multiplexed each of which has the same capacity as the original fibre channel - quite close to a free lunch.
Note that this really is exactly like other forms of FDM. All the normal considerations about choice of carrier frequencies, guard bands and so on still apply.

## Slide 30: Summary
Fourier Transforms to analyse spectra
  Effect of adding and multiplying waves
  “Effective bandwidth”
Frequency Shifting
Modulation
  ASK, FSK, PSK, BPSK, QAM etc.
Frequency-Division Multiplexing
  Wavelength-Division Multiplexing