## Slide 1: Internet Convergence (Supporting material)
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: ICMP – a little management
Internet Control Message Protocol
Messages for reporting problems
Messages to probe the network
All sent as datagrams
Not all routers and hosts support all messages
Notes: ICMP is the Internet Control Message Protocol. Strictly speaking, ICMP is a separate protocol from IP. However, it shares IP's header format and its messages are routed in just the same way as IP datagrams. It is at the same level as IP in the protocol hierarchy and can be thought of as a sideways extension of IP. The IPv4 version of ICMP is RFC 792. The IPv6 version is actually part of IPv6.
ICMP messages are used mainly to convey information about errors or conditions that require attention. There are many message types, most of which have sub-types indicated by a code field. As an aid to diagnosis, all ICMP error messages include the first 8 bytes of the IP datagram which triggered the error.

## Slide 3: ICMP - echo request
All hosts and routers are supposed to respond to echo requests
Used to implement the “ping” program
Notes: All IP interfaces are supposed to implement the ICMP “echo request” and “echo response” services. These are used by the ping program to probe the network.

## Slide 4: ICMP - time exceeded
  % traceroute knabe.syswiz.it
  traceroute to knabe.syswiz.it (192.92.105.11) 30 hops max, 40 byte packets
  1 cisco (128.16.6.150) 2 ms 2 ms 3 ms
  2 cisco-pb (128.40.14.245) 4 ms 3 ms 2 ms
  3 128.40.20.254 (128.40.20.254) 3 ms 9 ms 6 ms
  4 194.83.100.62 (194.83.100.62) 3 ms 4 ms 3 ms
  5 146.97.250.5 (146.97.250.5) 4 ms 556 ms 4 ms
  6 ten34-gw.ja.net (128.86.1.250) 4 ms 7 ms 5 ms
  7 janet.UK.ten-34.net (193.203.228.9) 5 ms 7 ms 7 ms
  8 london6.att-unisource.net (195.206.64.69) 6 ms 7 ms 6 ms
  9 london5.att-unisource.net (195.206.64.49) 6 ms 7 ms 7 ms
  10 amsterdam9.att-unisource.net (195.206.65.29) 211 ms 26 ms 27 ms
  11 amsterdam5.att-unisource.net (195.206.65.89) 14 ms 14 ms 16 ms
  12 geneva5.att-unisource.net (195.206.65.242) 32 ms 32 ms 30 ms
  13 milan1.att-unisource.net (195.206.64.98) 45 ms 52 ms 48 ms
  14 195.206.66.190 (195.206.66.190) 47 ms 563 ms 278 ms
  15 194.20.7.6 (194.20.7.6) 41 ms 69 ms 66 ms
  16 194.185.4.14 (194.185.4.14) 47 ms 46 ms 70 ms
  17 gw1-to-ser1.inet.it (194.185.221.106) 52 ms 50 ms 67 ms
  18 cs1-to-eth0.inet.it (194.185.129.226) 72 ms 51 ms 51 ms
  19 gw-syswiz.inet.it (194.185.134.182) 85 ms 102 ms 212 ms
  20 knabe.syswiz.it (192.92.105.11) 81 ms 81 ms 80 ms
Notes: Most often, the ICMP “time exceeded” message is sent back to a host because a datagram's TTL field has reached zero and it has been discarded by a router. This is exploited by an interesting program called "traceroute" which is available on many systems. Effectively, TTL is a hop counter. Traceroute begins by launching a datagram towards its destination with TTL set to 1. The first router on the path decrements the counter, finds it is now zero and discards the datagram. At the same time it sends an ICMP "time exceeded" message back to the source. Traceroute receives this and prints the source IP address from the ICMP datagram - which will be that of the first router. Traceroute now repeats the procedure with TTL equal to 2 and so discovers the IP address of the second router. By this means traceroute discovers the addresses of all the routers on the path to the destination.
Note, however, that the route may change between one transmission and the next. Thus traceroute does not give quite the snapshot of an IP route that the print-out suggests. In particular, a the RTD for a distant router may sometimes be longer than that for a nearby router. This is probably due to network congestion reducing between the early and late probes.

## Slide 5: Some other ICMP messages
Source quench
  May be sent from a router to a host asking the host to slow down
  Which process should the host hit?
Redirect
  Sent by a router to indicate that another router on the same IP network would be a better choice
Destination unreachable
  Sent back to host together with a reason