## Slide 1: Dynamic Routing
Context – within an autonomous system
Metric – some measure of the “cost” of a route
  Hop count
  Delay
  Sum of link costs
  Proportion of bandwidth in use
  Queue lengths
Two basic approaches
  Distance vector – report global view to neighbours
  Report local view to whole network
Issues
  Speed of convergence
  Consistency
Notes: “Dynamic Routing” means a mechanism whereby routers (or switches) exchange information enabling new forwarding tables to be calculated.
The Internet pioneered the use of dynamic routing and there are standards specifying how it should be done. It is up to the management of an AS to decide which, if any, scheme should be used.
Many networks are managed via static routing. The managers prefer the control and stabilitythis offers over the resilience of dynamic routing.

## Slide 2: Distance vector algorithms [1]
Distance:
  hop count, queue length, …
Each node:
  evaluates distance to all other nodes
  distributes information to adjacent nodes
  finds shortest (lowest distance) route to to all other nodes
Distances are always estimates
  Different nodes may make different estimates
Notes: The distance vector in the name is a table, computed by each node in the network, which indicates the “distances” between the node and all other nodes in the network. (In practice this table will probably also include the preferred “next-hop” to each destination. Thus it doubles as a forwarding table). These vectors are transmitted to all adjacent nodes at frequent intervals. “Distance” (the routing metric) can mean a variety of things; hop count, delay, number of packets queued up along the route etc. Once a node has received distance vectors from all its neighbours it can begin to compute a new routing table. In order to do this, the node must also have an estimate of its distance from each of its neighbours. The computation is according to the “distributed Bellman-Ford algorithm” illustrated on the next slide.
The most famous example of this class of algorithm was that used in the original ARPANET. This used the lengths of the queues on the different links as the measure of “distance” and sent out distance vectors every 128 ms.
An example of a distance vector protocol is the Routing Information Protocol (RIP) (RFC2453) used in IP networks.

## Slide 3: Bellman-Ford
1
A
C
B
F
E
D
2
2
1
1
1
3
3
5
5
Notes: In the network shown, the numbers on the links are the metrics observed by the nodes. (In practice all nodes would probably not see quite the same picture but, for simplicity, we will assume that they do). We will consider routing table calculations for node A.
A begins with the metrics it can observe on its local links. Periodically it receives distance vectors from its neighbours. These show each neighbours estimates of the distance to all other nodes. The calculation for routes to node E is shown. Essentially A makes new estimates by adding its local observations to the estimates of its neighbours and chooses the smallest. It can be seen that the route via D is best with a distance of 2. This calculation is repeated for all nodes leading to the new forwarding table. This also provides the information needed to construct the distance vector that must be sent to the neighbours at the next routing update.

## Slide 4: Distance vector problems
A
B
C
D
1
1
1
“Counting to infinity” – bad news travels slowly
Routing tables inconsistent during changes
  Routing loops possible
Solutions possible to ameliorate problems (RIP etc.)
Notes: A number of problems are inherent to distance-vector algorithms
  When the network is large the distance vectors are large and may not fit into one packet. If two or more packets must be sent then there is the danger that one will be lost leading to inconsistency.
  News of changes spreads by one hop at each routing update. Thus there will be times when only a portion of network nodes is aware of the change. There will be an inconsistent view of the “best” route to a destination and this can lead to routing loops
  News of link failure spreads rather slowly. (“Bad news travels slowly”)
This last point is illustrated by considering what happens when the link between A and B fails. Initially, the link between A and B is fine and the forwarding table entries for B, C and D will show delays to A of 1, 2 and 3 respectively. Suppose the link to A from B is now cut. At the next routing update, B will announce the 1 unit delay to A from its current table. B will hear nothing from A but will hear that C has a route to A with delay 2. Assuming that B has by now twigged that its delay along the B-A link is effectively infinite it will be happy to use the path that C apparently has. Since C is one unit away, B now thinks it can get to A with delay 3 via C – etc.
The algorithm can be modified to ameliorate these problems as in the Internet “Routing Information Protocol” (RIP) which is used within small ASs.

## Slide 5: Link-state algorithms
Each node:
  Assesses metric on local links
  Distributes information to all nodes
    Multicast or flooding
  Receives information from all nodes
  Finds lowest cost path to all other nodes
Dijkstra’s Algorithm:
  shortest-path (SP) tree to all other nodes
All nodes shares same information, perform same calculation
  Hence no routing loops
Notes: In distance vector algorithms, nodes send information to their neighbours about their distances from all other nodes. In link-state algorithms, nodes send information to all other nodes about their distances from their neighbours.
The distribution of routing updates is done by flooding. Every node forwards routing updates on all links except those on which the updates arrived. Hop counters or sequence numbers are used to ensure that the process eventually terminates. Although flooding sounds an expensive process when compared with the distance vector method, in practice, this is not the case. Routing updates in distance vector algorithms must be done frequently in order that information about changes can reach all nodes in the network reasonably quickly. Routing updates in link-state algorithms reach all nodes in the network very quickly and so need be much less frequent – say about once every few minutes. A further advantage of the link-state algorithm is that the size of routing update packets is independent of network size – so the algorithm scales well.
Once the routing updates have been received each node possesses complete knowledge of the state of the network and can begin to calculate its forwarding table. If every node has the same information and performs the same calculation then forwarding tables will be consistent.

## Slide 6: Dijkstra’s Algorithm [1]
A
B
C
D
E
5
2
1
1
3
4
A
D
2
A
B
C
D
1
5
3
1
3
More candidates
A
B
C
D
1
5
3
2
Add C to SP tree
A
D
2
B
C
1
A
5
D
3
1
4
Prune and add D to SP tree
A
B
C
D
1
5
3
1
Add candidates
Notes: A semi-formal description of Dijkstra’s Algorithm is as follows:
At the start of each iteration there will be:
  A set of nodes already added to the SP tree. One of these nodes will be the “most recently added node”. The tree represents the shortest paths discovered so far.
  A set of candidate nodes. These might represent shortest paths but we may discover a shorter path as the algorithm proceeds.
  The remaining nodes that the algorithm has not yet encountered.
Each iteration involves two steps:
1) Update the set of candidate nodes. To do this:
  Add all the neighbours of the “most recently added node” to the candidate set and calculate their path lengths
  Prune the candidates. I.e., if any node appears more than once, retain only the one with the shortest path
2) Update the SP tree.
PTO

## Slide 7: Dijkstra’s Algorithm [2]
A
B
C
D
E
5
2
1
1
3
4
E
A
D
2
B
C
1
1
4
5
More candidates
E
A
D
2
B
C
1
1
4
6
Add A
E
A
D
2
B
C
1
1
4
7
No more candidates
E
A
D
2
B
C
1
1
4
8
Add E
Notes: At this point, the candidate nodes represent shortest paths encountered so far. However, one candidate – the one with the shortest path cost amongst all candidates – is special. It will certainly be impossible to reach this node via one of the others at lower cost. Therefore:
Select the candidate node with the shortest path and add it to the SP tree
Iterations continue until all nodes have been added.
In the example, the resulting shortest path tree is used to update the routing table for node B.
The Internet “Open Shortest Path First” routing protocol (OSPF) is a link state algorithm which is suitable for large, complex ASs.