## Slide 1: Wireless Technologies
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Wireless Operation
Point-to-point links
  Wave and satellite links
  4G/WIMAX
Shared medium
  Wireless LANs
  Cellular
We will concentrate on Shared Medium
Notes: Wireless technology has become increasingly important since:
  It costs a lot to install wires
  It allows mobility
Much of the original impetus for wireless technologies came from telecomms. The original aim was to emulate wired links over satellite, microwave links etc. The results are circuit-switched services and are not considered in detail here.
New technologies such as WIMAX also provide point-to-point connections and are aimed at replacing the existing copper wire connections to homes and offices and support telephony and broadband data.
Other work is focused on shared-media packet switching. These techniques allow multiple transmitters to share a frequency band in a flexible way – there are no fixed capacity allocations as there would be in a circuit-switched technology. They are used in wireless LANs and PANs (Personal Area Networks) and in packet-switched extensions to cellular networks (GPRS and 3G for example). In order to allow this sharing some sort of Medium Access Algorithm (MAC) is needed.
LANs and PANs and cellular networks offer mobility (note that “wireless” does not necessarily imply “mobile”). This introduces issues like registration and “hand-off” when a station moves between networks, routing and tracking problems etc.

## Slide 3: Wireless Capacity Available
Licenced Frequency bands
  E.g. 1.90-2.025 GHz and 2.11-2.20 GHz – 3G Mob
  Allocated internationally -> national providers
Unlicenced Band
  Industrial/Scientific/Medical (ISM) - 2.40-3.0GHz
  Used by
    IEEE 802.11b, Bluetooth, Microwave ovens
Capacity
  E.g. IEEE802.11b - 2.4-2.485 GHz
  Bandwidth 85MHz, SNR=30dB => ~850Mbps (Shannon)
Notes: The ISM bands are operated in an unlicensed way. Anyone can use them provided power is kept low. Clearly there can be interference from neighbouring users.
Frequencies are regulated, so the useable range is restricted. Nevertheless there is quite a lot of useable bandwidth, especially if transmissions are low power and hence short range. “Short range” enables frequencies to be re-used in geographically distant networks. (This is what makes cellular networks possible).
Generally, fixed allocation per station (e.g. FDM or TDM) is inefficient – stations are not always transmitting (may be switched off) in which case the allocated bandwidth is wasted.
Better to have a flexible scheme which can allocate bandwidth to stations as needed.
Some schemes, e.g. IEEE 802.11, use both. A slice of bandwidth, called a channel, is allocated to each network. For example, IEEE 802.11b specifies 13 (in the UK) partially overlapping FDM channels. Two wireless LANs will not interfere provided their channel numbers differ by 5 or more. Thus we use FDM to separate networks. However, each network will have many stations and a flexible MAC algorithm is used to share channel bandwidth between them.

## Slide 4: Problems to Solve
How to combat noise?
How can two networks co-exist in same area?
MAC algorithm needed
Network set-up
  Ad hoc networks
  Registration
Your network
My network
Notes: Traditionally, the spectrum has been divided into different frequency bands each of which was more-or-less permanently allocated to a task – e.g. to a particular radio station. This would be difficult with wireless LANs where networks may be set up on an ad hoc basis in an area which contains many such networks.

## Slide 5: Dealing with Noise
Wireless channel: plenty of bandwidth but lots of noise
Shannon
Suppose we want C=1Mbps but SNR is –10 dB
VERY noisy!
Notes: The slide shows that, in principle, we can defeat the noise if we throw enough bandwidth at the problem – but we need lots!
We need a way to spread our signal over a huge range of frequencies. Note that conventional modulation techniques do not do this. For example the simplest form of ASK about doubles the effective bandwidth of the signal. We need something that increases the signal bandwidth by several orders of magnitude.

## Slide 6: Spread-spectrum and Noise
Direct-Sequence Spread-Spectrum
  Send multiple symbols per bit
  High symbol rate => high bandwidth (spreading)
  Noise immunity since we only require “most” symbols to get through
Frequency-Hopping Spread-Spectrum
  Use multiple carrier frequencies
  Hop between several frequencies during transmission of a single bit
  More frequencies used => high bandwidth (spreading)
  Noise immunity since only some frequencies will be affected by noise
Notes: The term “spread-spectrum” covers a range of techniques. Here, we are interested in its use mainly to combat noise. The essential idea is that each bit is encoded in a way which spreads it over a wide range of frequencies. As long as noise only corrupts a minority of the frequencies used the bit can still be correctly received with high probability.

## Slide 7: Direct sequence spread spectrum
spreading sequence 10110111000
1
1
0
bit sequence 110
chip sequence
Xor bits with pseudorandom “spreading sequence”
  -> Sequence of “chips”
Chipping rate normally >> bit rate
E.g. bit rate 1Mbps and 11 bits/chip
Chipping rate = 11 Mchips/sec, “spreading factor” = 11
Modulate chip sequence and transmit
Notes: Before the bit-stream is modulated, it is xored with a high bit rate pseudorandom binary sequence (sometimes called the chip sequence). Each bit in the sequence is a called a chip and the rate of the chip bits is called the chipping rate. The chip sequence is “pseudorandom” because, while the individual chips in the sequence look as if they have a randomly occurring value, the whole bit stream does repeat itself.
The chipping rate is typically (at least) an order of magnitude higher than the bit rate. Therefore, after modulation (using BPSK or PSK for example) a higher bandwidth signal will result. If the chipping rate is n times the bit rate then we expect to use n times as much bandwidth – a “spreading factor” of n.
[N.B some implementations modulate before combining]

## Slide 8: DSSS - Synchronisation
b  p  p = b - so receiver must xor with same spreading sequence as Tx
  Must synchronise to Tx chip rate
  Tx prepends sequence of 1s
  Rx timeshifts spreading sequence until 1s recovered
1
Rx mis-aligned
1
Rx aligned
Tx
Notes: In principle Rx has only to xor with the same chipping sequence to recover the original bits. However, this will only work if the receiver has it’s chipping sequence synchronised with that of the transmitter.
In frame-based communication this can be achieved by prepending a known bit pattern (a “preamble”) to each frame. This could be a sequence of 1s. As Rx receives the preamble it time-shifts it’s chipping sequence until a sequence of 1 bits emerges. After initial synchronisation, the data bits will follow. Synchronisation bits might be used only at the beginning of a transmission, or at predetermined times during a transmission, .e.g. every 10ms.

## Slide 9: DSSS - Noise
Suppose noise affects (say) 2 chips
  Must synchronise to the spreading sequence
1
Tx
2 chip errors
Received bit could be:
  1 with 2 chip errors
  0 with 9 chip errors
Bit can still be decoded as a 1 with high probability
Notes: It is important to realise that the code sequence will be subject to noise so that many chips will be in error. If, in the scheme in the slide, two chips in a ‘1’ bit were in error then decoding would yield 9 ‘1’ values and 2 ‘0’ values. Nevertheless we would be happy to decode this as a 1.
DSSS may be used as the basis of a channel allocation algorithm called “Code-Division Multiple Access” (CDMA). Here stations may transmit concurrently but each uses a different chip sequence. An individual station’s transmission can be extracted by performing chip-by-chip logical operations on the combined signal. (See later)

## Slide 10: Frequency hopping spread spectrum
Bandwidth split into several channels
Hopping sequence:
  Tx hops between channels
  pseudorandom hop code
Hopping rate
  > bit rate => Fast FHSS
  < bit rate => Slow FHSS
Good Tx/Rx sync required
0
1
2
3
5
4
6
channel
(frequency)
time
A
A
A
A
bit
A
A
A
A
bit
A
A
A
A
bit
A
A
A
A
bit
A 0236
Notes: In frequency hopping spread spectrum, the available bandwidth is split into equal-sized sub-bands called channels. During transmission, separate carriers that are located at the centre frequency of each channel are modulated with the transmission (e.g. using BPSK or QPSK). The transmitter transmits on one channel then hops to another, i.e. a single transmission takes place across several (perhaps all) of the channels. The hopping rate (sometimes called the chipping rate) is the rate at which the signal switches channels.
For noise suppression it is usual to use Fast FHSS where the hopping rate is > bit rate. Thus the transmission hops between several carrier frequencies during the transmission of a single bit. Each of these several transmissions is sometimes termed a “chip”.
The hopping sequence (sometimes called the hop set) is not arbitrary but determined by a pseudorandom sequence called the hop code. The receiver can reproduce the identical hopping sequence and so decode the signal. Good synchronisation is required between sender and receiver.
Noise will cause some chips to be received incorrectly. However, as long as most are received correctly the bit can correctly be recovered.
FHSS may be used as a channel allocation mechanism – two transmissions may take place simultaneously with each using a different hopping sequence – see later.

## Slide 11: Spread Spectrum and Security
Who invented FHSS?
  Heddy Lamarr (voted most beautiful women in the world 1940)
  George Antheil (avant-guard composer)
Frequency-hopping control of torpedo
88 frequencies (number of keys on a piano!)
Frequency shifts controlled by piano roll
  Same roll in ship and torpedo
  Impossible to jam without knowing sequence
Notes: Both DSSS and FHSS involve a shared pseudo-random sequence. If this is produced by a pseudorandom number generator then the seed to that generator is effectively a key decoding the transmitted message, and so this technique has obvious security applications, for instance military use (anti-jamming devices or secure transmission), or (a more domestic but certainly useful example) in mobile phone systems.
Surprisingly, Hollywood actress Hedy Lamarr, who died on January 18, 2000, turns out to have invented FHSS. Having been married (briefly) to Fritz Mandl, an Austrian industrialist and supplier to wartime Germany, Lamarr learned that accurate torpedo and missile guidance was a vital wartime issue and that radio control signals for torpedoes were easily jammed. She and her friend, composer George Antheil, conceived the idea of having the radio signals which guided the torpedoes shift frequencies to a rapid, pre-determined sequence. Such a signal would be difficult to jam without knowledge of the hopping sequence. They produced not only the idea but also a design for an implementation based on “piano rolls “ that were used to control automatic pianos.
They were awarded U.S. Patent Number 2,292,387 for a "Secret Communications System“ but were unable to exploit it due to security restrictions imposed by the US Navy. Lamarr finally received a reward for her efforts 1998, when Wi-LAN Inc. acquired a 49 percent claim to Patent 2,292,387 for an undisclosed amount of Wi-LAN stock.

## Slide 12: Problems to Solve
How to combat noise? 
How can two networks exist in same area?
MAC algorithm needed
Network set-up
Your network
My network

## Slide 13: Sharing
We start with a slice of bandwidth
Need several networks to co-exist in an area
Need several stations to share a network
FDM
Spread spectrum
CSMA
TDMA
CDMA
FDMA
Notes: Lots of techniques are available for sharing bandwidth – some are listed on the slide. Some techniques are best suited for making fixed, long-term allocations and these tend to be used to allocate bandwidth to whole networks. Other techniques are more dynamic and attempt to allocate bandwidth to individual stations as needed – these can form the basis of MAC algorithms. Some of these, CSMA for example, are distributed algorithms others rely on some sort of central control in a “base station” or “access point”.
Not only are there lots of different techniques there are also many variants of each and different technologies use them in different ways. A particular technique, FHSS for example, might be used to partition a channel between networks in one technology, for noise suppression in another and as the basis of a MAC algorithm in a third.
There are two main contexts for our discussion; Local Area Networks (including Personal Area Networks like Bluetooth) and cellular mobile networks like GPRS and 3G.
We begin by looking at ways of sharing bandwidth between networks. FDM is dealt with elsewhere in the course. Here we will briefly look at the use of spread-spectrum techniques to implement sharing.

## Slide 14: Spread Spectrum and Network Separation
0
1
2
3
5
4
6
channel (frequency)
time
If two adjacent networks use different hop codes …
FHSS – no (or little) interference
  Works with fast and slow FHSS
A
A
A
A
bit
A 0236
B 2205
C 6512
A
A
A
A
bit
A
A
A
A
bit
A
A
A
A
bit
C
C
C
C
B
B
B
B
B
B
B
B
Notes: Spread spectrum techniques also allow several networks using similar technologies to co-exist in the same geographical area. The slide shows a FHSS scheme in which each network uses a different hop code. These might be chosen at random. If the codes are long enough they are likely to coincide in only a few places which means that most chips still arrive successfully. In the slide the codes for A and B coincide in one place, the code for C clashes with neither A nor B. Essentially, co-existing networks appear as noise to each other. Bluetooth uses this method to allow many “piconets” to exist in the same area.
DSSS could be used to provide a similar channel separation with codes chosen to be orthogonal. Such codes are described in the CDMA MAC section.

## Slide 15: Problems to Solve
How to combat noise? 
How can two networks exist in same area? 
MAC algorithm needed
Network set-up
Your network
My network

## Slide 16: Wireless LANs
Infrastructure wireless:
  wireless connectivity to a fixed network
  fixed-wire replacement, e.g. laptops
  Portable devices
  Access Point (AP)
Ad hoc wireless:
  totally wireless network
  communication only between portable devices
portable
devices
AP
fixed wire
replacement
AP
ad hoc
Notes: With wired LANs, a major cost is the installation of the wiring for network connectivity. This wiring must be maintained and changed as the network configuration changes. Additionally, as more and more people use portable computing devices such as laptops, it becomes impractical to have completely wired access. This brings requirements for an infrastructure wireless arrangement that allows:
mobile users to have access to resources that are connected to an existing fixed (wired) network
replacement of some of the wired network access points to the infrastructure with wireless access for fixed or mobile users
Typically, this kind of access will be within the confines of a single room or office, but in some cases the distance to the network access point may be around 100m. The wireless part of a cellular network also may be classified as infrastructure wireless. An “Access Point” (= “Portable Access Unit” or “Base Station”) provides a wireless relay point that allows connectivity to the infrastructure network. The presence of an Access Point can simplify MAC algorithms since the AP can perform a controlling role in allocating capacity to individual stations.
Another situation is where portable/mobile devices wish to communicate directly between themselves without the use of an infrastructure network. This arrangement forms an ad hoc network of wireless communicating devices.

## Slide 17: Hidden terminal and Exposed terminal
A  B: OK
A  C: OK
B  C: not OK
If C transmits to A, B could also transmit
A  B: OK
C  D: OK
C can “overhear” B:
  C will not transmit when B transmits
A
B
C
D
Network 1
Network 2
A
B
C
Notes: When wireless networks are set-up, two common physical pathological cases can be observed:
With hidden terminal, some obstruction may prevent two terminals (“terminal” = “station” in this context) that should be able to communicate from being able to communicate directly. Therefore they do not “hear” each other’s transmissions. This causes two difficulties:
  Obviously, they cannot communicate directly!
  Since they are not aware of each other they may both try to use the channel at the same time – i.e. their transmissions could collide. This defeats some MAC algorithms.
If two nearby networks use the same channel there may be partial interference – i.e. it may only affect a few terminals in each. Those affected are called exposed terminals and “hear” each other’s transmissions. With some MAC algorithms this will prevent them from transmitting even though such transmission would, in fact, be received successfully by other terminals in their own networks..
Both of these problems can be solved by using a handshake before sending data in order to establish connectivity. A suitable handshake protocol is distributed foundation wireless MAC (DFWMAC) also known as RTS-CTS (request-to-send – clear-to-send). These are discussed later.

## Slide 18: MAC algorithms for Wireless LANs
Within a LAN we have multiple stations sharing the medium
  Need a MAC algorithm
Distributed algorithms
  CSMA/CA, CSMA/CD, CDMA
Centralised algorithms
  AP manages allocations
  R-ALOHA, FDMA, TDMA
Notes: Several MAC methods could be used for wireless networks in order to deal with contention at the medium-access level.
Varieties of CSMA can be used as can the DSSS-like CDMA
Where an Access Point is present in an infrastructure mobile network, this can act as the controller allocating resources to individual stations. This makes techniques such as TDMA and FDMA possible.

## Slide 19: CSMA
“Listen before speaking”
If “busy” then defer transmission
“Collisions” may still occur
time
A
B
bit 1
p
bit 1
p
Deferral strategies: persistent, non-persistent
Collision detection and transmission abortion
  Takes 2 x p
  Difficult with wireless?
Notes: Carrier-Sense Multiple Access systems have been widely studied (see DCNDS pre-reading and support notes for example). Performance may not degrade gracefully on a congested net. The “listen” aspect may be problematic if there are hidden terminals. Main advantage is simplicity and the fact that no base-station is required – hence suitable for ad hoc networks.

## Slide 20: Throughput Comparison
Notes: The graph shows the theoretical throughput curves for two varieties of CSMA and ALOHA (which does not listen before speaking!).
We can see that CSMA is always better than Aloha.
When the normalised load is low, persistent CSMA wins. This is because non-persistent is wasting time by deferring packets for a random time when these could, most likely, be transmitted immediately. However, as the load increases, persistent CSMA performance collapses as the network becomes dominated by collisions.
[The non-persistent graph is actually misleading. At high loads the probability of collisions becomes significant thus invalidating one of the assumptions made in the analysis. In reality the throughput would start to collapse as a result.]
CSMA-CD is persistent but reduces the effect of congestion collapse by aborting transmission as soon as a collision is detected and waiting a random time before listening again. Thus, when the network becomes congested, it behaves more like non-persistent CSMA.

## Slide 21: CSMA/CD: comb
C, in: A, B out
C can transmit
Wireless systems cannot “listen whilst speaking”
Pseudo-random bit pattern - comb
A 1 0 0 0
B 1 1 0 0
C 1 1 1 0
1
0 (listening)
time
A, B, C in
B, C in: A out
Station(s) to transmit:
  first transmits comb
  for a 1 transmit, for a 0 listen
If station hears another transmitting it drops out.
Notes: Although CSMA-CD can be significantly more efficient than non-persistent CSMA it is difficult to implement in a wireless network since:
  It is costly to make a device which can detect a relatively weak incoming signal whilst it is itself transmitting
  The “hidden terminal” problem means that some collisions may be missed.
The first problem can solved by a rapid alternation between transmitting and listening at the start of a frame. In order to avoid two stations synchronising their transmits and listens – hence missing each others’ transmissions a pseudo-random sequence called a “comb” is used.
A station first checks to see if the medium is idle, and if it is, starts to transmit the comb. During transmission of the comb, when the comb contains a 1 a signal is transmitted, but when the comb contains a 0, the station listens to the medium rather than transmitting. If, during the listening phase, the medium is not idle, then there is another station transmitting a comb, i.e. there is a collision and this station should “drop out” of its transmission. If a station completes transmitting its comb, then it transmits its frame. A collision could still occur if two stations have the same comb value, and this will have to be spotted by CRC checks at the receiver.

## Slide 22: TDMA
time-frame with fixed number of time-slots
  signalling time-slot (slot 0)
  source requests a time-slot using slot 0 (N.B contention!)
AP listens on signalling time-slot for requests
  assigns channel to source
  source uses time-slot for a single data frame
0
1
2
3
4
0
1
3
2
…
Time
A: “Want slot”
AP: “Use 3”
A
A
Notes: Strictly-speaking the term time division multiple access (TDMA) applies to any system which allocates the whole of a channel’s capacity to individual sub-channels for some time period. Hence pure TDM (which allocates fixed time-slots in strict rotation) qualifies as TDMA. So do distributed MAC algorithms such as CSMA-CD and token passing. However, the term TDMA is most often applied to systems which employ a central arbiter (typically in an AP) to allocate timeslots to sub-channels in an arbitrary way.
In a typical time division multiple access (TDMA) system, the channel is split into time-frames which are further sub-divided into time-slots (in the slide there are 5 time-slots per time-frame). This mechanism is used with an AP which provides synchronisation pulses for the time-frames and/or time-slots. The AP acts as an arbiter, allocating time-slots by listening for requests on the single signalling channel. The time-slot may be allocated for one or many time-frames depending on the QoS required. Once the allocation has lapsed, the transmitter must signal the AP for another time-slot allocation to send more data.
It is clear that contention can occur in the signalling channel. Therefore a distributed MAC is needed in this channel, for example CSMA/CA. Note that the time required for a booking message is generally much shorter than one time-slot. Therefore, several booking messages may be sent during one booking slot whilst still keeping the utilisation of the booking slot low.

## Slide 23: Code Division Multiple Access
Division of capacity through use of codes
Similar techniques to DSSS
Good performance – efficient use of bandwidth
Good noise immunity
Bits divided into “chips”
  64 or 128 chips per bit
Each station has a unique (carefully allocated) “chip sequence”
Notes: CDMA has similarities to DSSS. Essentially each station uses a different pseudo-random code (or “chip sequence”). If these are carefully chosen, it is possible for a receiver to filter out a single station’s transmission.
In the examples here we will assume there are 8 chips per bit. It turns out that the demonstration is simpler if we represent a 1 chip as +1 and a zero chip as –1.

## Slide 24: CDMA Example
Assume 8 chips per bit, 4 stations A-D
  A 00011011 (-1 –1 –1 +1 +1 –1 +1 +1)
  B 00101110 (-1 –1 +1 –1 +1 +1 +1 -1)
  C 01011100 (-1 +1 –1 +1 +1 +1 –1 -1)
  D 01000010 (-1 +1 –1 –1 –1 –1 +1 -1)
CDMA codes are “orthogonal” e.g.
  A.C = (-1.-1 + -1.+1 + -1.-1 + +1.+1 +
  +1.+1 + -1.+1 + +1.-1 + +1.-1)/8
  = (+1 + -1 + +1 + +1 +
  +1 + -1 + -1 + -1)/8 = 0
To transmit a ‘1’ send the CDMA code. To transmit a ‘0’ send the complement.
Notes: CDMA chip sequences are carefully chosen to be orthogonal. i.e. the normalised inner product of any pair is zero. This means that when we compare two CDMA codes we find as many pairs the same as we find different.
To send a ‘1’ a station sends its chip set; so A sends
(-1 –1 –1 +1 +1 –1 +1 +1)
To send a ‘0’ a station sends the complement; so A sends
(+1 +1 +1 -1 -1 +1 -1 -1)
Note that,

## Slide 25: CDMA Example [2]
Suppose A sends ‘1’, C ‘0’ and D ‘1’
Combined signal will be:
  A 1: -1 –1 –1 +1 +1 –1 +1 +1
  C 0: +1 -1 +1 -1 -1 -1 +1 +1
  D 1: -1 +1 –1 –1 –1 –1 +1 –1
  S : -1 –1 –1 –1 –1 –3 +3 +1
  S : -1 –1 –1 –1 –1 –3 +3 +1
  D : -1 +1 –1 –1 –1 –1 +1 –1
  (+1+-1++1++1++1++3++3+-1)/8 = 1
To retrieve D’s transmission, compute S.D
Note that
Notes: We make two simplifying assumptions; that the stations are in bit synchrony and that the signals are of equal power so they add in a simple arithmetic way. The slide shows three bits being added. We can then extract whichever station we want simply by forming the inner product with its chip sequence.
In practice neither of our assumptions would be true. We would also have to contend with noise. However, it turns out that, provided the chip sequences are long enough, it is possible for the receiver to synchronise with the bits from an individual station. We can also cope with unequal power provided this is constrained to some limit. In effect we would find that the result of a calculation would not come to exactly 1 (or –1) but would be close enough for us to decide, at high probability whether a 0 or 1 was encoded.

## Slide 26: Problems to Solve
How to combat noise? 
How can two networks exist in same area? 
MAC algorithm needed 
Network set-up
Your network
My network

## Slide 27: Network Set-up
“Mobility”, “Roaming” =>
  Autoconfiguration
  Security Issues
Station must discover AP
  Beacon frames – transmitted by AP
  Probe frames – transmitted by station
  How to choose between APs?
  How to find a network?
Authentication
  … of station, … of AP
Association
Notes: A principal appeal of wireless communication is that it should be available wherever you are with a minimum of human intervention. Ideally we would like to be able to “roam” “seamlessly” between networks whilst having applications continue to operate. This requires “autoconfiguration” whereby the station and AP discover each other and establish communication. Unfortunately such ease of movement between networks introduces potential security issues.
The first problem is for the station to discover a wireless network. Typically the AP will periodically transmit “beacon” frames. The station must listen for these. Since FDM of FHSS may be used to partition bandwidth between networks, the station will have to scan all possible channel frequencies. Alternatively (or additionally) the station may transmit “probe” frames in the hope of eliciting a response from an AP. Again, probes must be transmitted on all channels.
Having discovered each other, AP and station must then authenticate each other in order to determine whether an “association” is desirable for both. Clearly networks want to protect against undesirable intruders. Equally, users may not want their lap-tops to associate with unsecure networks.
Finally, the station must “associate” with the AP and operation can begin.

## Slide 28: Roaming
Cooperating APs
  Cellular networks
  IEEE “Extended Service Set”
S1 associates with AP1
AP1 informs other APs of S1
S1 moves close to AP2
S1 “reassociates” with AP2
AP2 informs other APs of S1
AP
S
S
S
S
AP1
AP2
AP3
S
S
S
S
S1
S1
Notes: Many wireless systems allow several APs to cooperate to provide a service. E.g. in IEEE 802.11 several APs may provide an “Extended Service Set”. In this case the APs are probably connected by wired LANs and must cooperate in maintaining knowledge of all the currently associated stations and to which AP each is associated. Obviously this knowledge is needed in order that frames can be correctly routed. If a station moves physically it may determine that a different AP is a “better” choice. It may now send a “reassociation” frame to the new AP. The new AP must now inform the others of the station’s new location.
Such re-association is fundamental to the operation of cellular networks where mobile devices can easily move between “base stations” (= AP). Base stations are interconnected via point-to-point links and a database of device locations is maintained centrally.
[Note that this kind of roaming is handled entirely by the wireless network and is not visible from outside. I.e an IEEE ESS can be identified as a single IP subnet. IP packets send to a station in this subnet can be routed identically even though the station might move between APs. The situation is different if a station moves to another ESS with a different subnet address. This problem has to be solved at the IP level – see “mobile IP”].

## Slide 29: Examples
IEEE 802.11b uses:
  FDM to separate networks
  DSSS to provide noise immunity
  non-persistent CSMA as a MAC algorithm
Bluetooth uses:
  FHSS to provide noise immunity and separation from adjacent networks
  TDMA as a MAC algorithm
GSM (the European mobile phone standard) uses a TDMA MAC
Third generation mobile phone systems use a CDMA MAC

## Slide 30: IEEE 802.11x
Originally … IEEE 802.11
  2.4-2.5 gigahertz (GHz) ISM
  1Mbps, 2Mbps, radio and IR, not widely used
Then … IEEE 802.11b
  2.4-2.5 gigahertz (GHz) ISM
  Max. 11 Mbps, widely used
Then … IEEE 802.11a
  frequencies in the 5 GHz range
  Max. 54 Mbps, not common in Europe
Then … IEEE 802.11g
  2.4-2.5 gigahertz (GHz) ISM
  Max. 54 Mbps, widely used
Notes: Most versions use the 2.4-2.5 gigahertz (GHz) S-Band Industrial, Scientific, and Medical (ISM) frequency band shared with Bluetooth, microwave ovens etc.
Note that ranges vary and that the maximum bit rates are only available if range and noise are low. All versions will use a lower bit rate to combat noise.

## Slide 31: IEEE 802.11b/g
2.4-2.485 GHz => 85MHz b/w
14 overlapping channels 5 MHz separation
  Interference between adjacent channels
  Not all channels available everywhere
AP + set of stations = “Basic Service Set”
  All use same channel
2 or more connected BSS = “Extended Service Set”
BSS or ESS is named by a “Service Set Id”
Notes: We concentrate on IEEE 802.11 b and g. These share the same frequency range and partition it in the same way so as to allow co-located networks separated by FDM.
A simple network – termed a Basic Service Set (BSS) consists of an AP plus a collection of wireless stations. The operator of the AP decides which channel to use. Typical choice would be channel 1, 6 or 11 which are well enough separated to make inter-channel interference acceptable.
A collection of interconnected BSSs may cooperate to form an Extended Service Set (ESS). This is necessary to allow a LAN to operate over a large geographical area. A stand-alone BSS or an ESS is given a name by the operator – termed a Service System Id (SSID)

## Slide 32: Frame format
Frame Contr.
Dur. or Id
Address 1
Address 2
Address 3
Seq. Control
Address 4
Data
CRC
2
2
6
6
6
2
6
4
0-2312
Version
Type
Subtype
To DS
From DS
More Frag.
Retry
Power
More
2
2
4
1
1
1
1
1
1
1
1
W
O
Fragmentation
MAC Protocol
Power Management
Notes: Protocol Version - indicates the version of IEEE 802.11 standard.
Type - Frame type: Management, Control, Data
Management Subtype - Authentication, Deauthentication, Association req/resp, Reassociation req/resp, Disassociation, Beacon, Probe req/resp etc.
Control Subtype - RTS, CTS, ACK, PS-Poll etc.
To DS - 1 => frame sent to Distribution System (DS) (i.e the AP)
From DS - 1 => frame received from the Distribution System (DS)
More Frag. - set to 1 when there are more fragments of this frame
Retry - retransmission of a previously transmitted fragment.
Power – switch Power Management on/off
More - more frames buffered to this station.
W - frame body is encrypted according to the WEP algorithm.
O - Order frame is being sent using the Strictly-Ordered service class.
Duration – used in the MAC algorithm
ID – Association ID (used in Power-Save poll messages).
Address fields (1-4) – used in MAC algorithm
Sequence Control - consists of fragment number and sequence number
Data - is information that is transmitted or received.
CRC - contains a 32-bit Cyclic Redundancy Check (CRC).

## Slide 33: Getting Started
AP may send beacon frames at intervals, station scans all channels
Station sends probe frames, AP may respond
S
AP
?
OK or Reject
Open Authentication
S
AP
?
OK or Reject
Challenge
Response
Shared Key Authentication
Association request (SSID + station information)
Association response (Association ID)
Notes: AP may keep quiet (no beacons) and need not respond to probes from unknown MAC addresses which provides some protection against intruders. However, it is fairly easy for a station to monitor for network activity.
With Open Authentication the two parties simply learn each other’s MAC addresses. With Shared Key Authentication the station demonstrates its knowledge of a (previously agreed) shared key. It does this by using the key to encrypt a number (the challenge) sent by the AP and returning the encrypted version. Unfortunately the key used is the same one that is used in WEP (Wired Equivalent Privacy) encryption which may subsequently be used to provide confidentiality of data transfer. The challenge/response exchange provides an attacker with vital information – a plain-text/encrypted-text pair – that can assist discovery of the key. For this reason it is actually safer to use Open Authentication.
Finally, the station sends an Association Request which includes the SSID of the network it want to join together with information about itself – supported data rates for example. The AP may then accept the association allocating a numeric ID to it.

## Slide 34: IEEE 802.11 - Typical Operation
AP, Router and ADSL modem may be in one box
  Router does NAT + Firewall + DHCP server
Manager chooses SSID and channel number
S/w on station host initiates scans and probes
  User selects network and association is attempted
Host uses DHCP to get Internet parameters
Internet
Router
AP
BSS
Notes: The slide shows a typical home system in which IEEE 802.11 is used in conjunction with ADSL to provide broadband internet to a small wireless LAN.
Note that the association steps described in the previous slide only affect the MAC layer. If it succeeds software in the host will begin establishing IP-level connectivity. It will probably do this by broadcasting a DHCP (Dynamic Host Configuration Protocol) request. The DHCP server will respond with an IP address, router address etc.
Note that a box sold as a “wireless broadband router” implements several distinct functions:
ADSL modem to implement a high-bit-rate stream
Framing mechanism
IP router
NAT
IEEE 802.11 AP
… plus, possibly several others …

## Slide 35: Basic MAC [1]
CSMA/CA (non-persistent)
Stop and Wait ARQ – assists error recovery
Tx senses for period DIFS
  If still free, begins DATA
Other stations defer transmission
Rx senses for period SIFS
  If still free, begins ACK
SIFS < DIFS => ACK has priority over DATA
ACK
DATA
sense
DIFS
Tx
Rx
time
SIFS
sense
A
Notes: The MAC algorithm is built on CSMA/CA (CA = “Collision Avoidance – it is a non-persistent CSMA). (In IEEE 802.11 terminology this is the “Distributed Coordination Function (DCF)). Unlike CSMA/CD, which is used on the Ethernet, this does not detect collisions and arrange retransmissions. Therefore a stop and wait ARQ protocol has been added. If no ACK is received the frame will be retransmitted (note use of “Retry” field in frame format).
DIFS and SIFS are chosen so that if there is contention with another station trying to transmit DATA at A, the ACK will win.

## Slide 36: Basic MAC [2]
Hidden terminal problem; hosts “hear” AP but not each other
  CSMA/CA will fail
RTS requests reservation for time t
CTS grants reservation for time t
All stations hear CTS and defer for time t
ACK
DATA
sense
SIFS
Tx
AP
time
sense
SIFS
A
RTS
CTS
SIFS
sense
DIFS
sense
CTS
Other
defer
Notes: For an infrastructure network (i.e one with an AP) the protocol includes an optional “Point Coordination Function” (PCF) based on two frames:
RTS: Request to send, CTS: Clear to send
RTS includes an estimate of the time needed to send DATA and ACK (See “Duration” field in the frame format). CTS grants exclusive access to the channel for this time. All other stations, including the hidden one, hear the CTS and defer.
The PCF also has an impact on the “exposed terminal” problem where a station may “hear” the transmission of nearby a station on an adjacent network and defer unnecessarily. With PCF it will hear the RTS but not the CTS from the AP which is (presumably) further away. At this point it can conclude that its network is free and will transmit. Although time is lost waiting for the CTS this will generally be a shorter time than would be needed for a data frame.

## Slide 37: Other things
Need to support (at least) Ethernet frame size
  .. but noise => small frames
  hence fragmentation and re-assembly
Low power mode
  Station announces low power mode
  AP buffers frames
  Beacons include list of stations that should wake
  Stations must wake at beacon intervals
Encryption
  Wired Equivalent Privacy
Notes: All but the last fragment of a frame have the “More Fragments” bit set. The station gives a 12-bit frame ID to each frame (frames are numbered consecutively) + a 4-bit fragment number. These are combined in the Sequence Control field. Each fragment has a complete MAC header and is transmitted according to the MAC protocol rules described earlier.
Wireless devices are often battery powered so saving power is desirable. “Listening” uses power (about 700mW). To avoid this a station may set low power mode (“Power” bit in frame format) and cease listening (reducing power consumption to about 60mW). The AP must now buffer any frames that are transmitted to this station. The station must then wake up and listen at the time AP sends beacon frames – careful synchronisation is needed. Beacon frames include a list of stations for which data is buffered. Stations notified in this way send “PS-Poll” frames requesting that the buffered frames be sent. The AP uses the “More” bit to indicate if still more frames are buffered.
The Wired Equivalent Privacy (WEP) system is a shared key system designed to provide the sort of defence against eavesdropping that would be expected in a wired LAN. All stations in a BSS or ESS share the same key. Without knowledge of the key a station is effectively excluded so the use of WEP in effect provides access control as well as privacy.

## Slide 38: Address Usage
“Distribution System” – network used to inter-connect APs
Address 1 – Wireless receiver
  Not necessarily final destination
  All wireless stations filter on this
Address 2 – Wireless transmitter
  Not necessarily the originating source
Address 3 – final destination or originating source
Address 4 – Used in “wireless links”
Notes: Wired or wireless networks may be used to interconnect APs in an ESS. A network which performs this role is called a “Distribution System”.
When a frame passes (say) from a wireless LAN to an Ethernet-based DS there are three MAC addresses involved; the wireless transmitter, the AP’s wireless interface, and the destination LAN host. The IEEE architecture handles this by having 4 address fields in the header.
Note that addresses 1 and 2 always refer to wireless interfaces on the wireless network the frame is currently traversing.

## Slide 39: Address Examples
WHa
WHb
APx
APy
B
Y
A
-
1
0
1
2
3
4
F
T
X
A
B
-
0
1
1
2
3
4
F
T
A
B
S
D
2
WHa
WHb
APx
APy
B
Y
A
-
1
0
1
2
3
4
F
T
X
A
B
-
0
1
1
2
3
4
F
T
3
Y
X
B
A
1
1
1
2
3
4
F
T
WHa
WHb
APx
B
X
A
-
1
0
1
2
3
4
F
T
X
A
B
-
0
1
1
2
3
4
F
T
1
Notes: T = the “To DS” bit
F = the “From DS” bit
Example 1 shows a frame being relayed between hosts on the the same wireless LAN by an AP.
Example 2 shows a frame passing between wireless hosts via an Ethernet. Ethernet operation is normal with the Ethernet hardware associated with the APs behaving as transparent bridges – it is up to the APs to do the correct address mappings.
Example 3 replaces the Ethernet by a wireless link. On this link Addresses 1 and 2 identify the relevant wireless transmitter and receiver whilst 3 and 4 identify the original source and final destination.

## Slide 40: A Possible API
All IEEE 802 MACs provide the same service
  => Nothing specifically “wireless” in the API
CL service
class MACService
// Initialise the adaptor
public MACService(param p);
// Send len bytes of data
public void send(address a, byte[] data, int len);
// Receive a max of maxlen bytes (may block)
public int receive(address a, byte[] data, int maxlen);
Notes: Warning. This is a toy example – not really comprehensive.
A key aim of the IEEE LAN design is that all LANs provide essentially the same service. Therefore, we would expect the APIs for different LANs to differ only in some detailed initialisation parameters.
The constructor would be called once at the beginning. The parameters passed might specify filter criteria to select or reject incoming frames. There might also be some technology-specific information such as a WEP key, SSID etc. The initialisation activities performed by the service implementation will be technology-dependent. For example, a wireless adaptor may be caused to associate with an AP.
The addresses used here will be IEEE MAC addresses. For compatibility with other IEEE MACs these will be the originator (receive) and final destination addresses (send) (A and B in slide 33). It is up to the firmware in the wireless Network Interface Card (NIC) to fill in all the addresses and other fields in the frames.
We would not expect complex buffering strategies here; send and receive will be 1-1 with MAC frame transmission.
The data and address parameters in receive() are references to empty structures to be filled in when data is received. Thus the receiver can discover the source address.
There would also be several get/set methods which could be used to discover/set operational parameters.

## Slide 41: Summary
Dealing with noise
  DSSS, FHSS
Channel separation
  FDM, FHSS
MAC algorithms
  CSMA variants, TDMA, CDMA
  Stop and wait
Hidden/exposed terminal
  CTS/RTS
Association, Roaming
  Beacons etc.
  Authentication
IEEE 802.11
  Association
  MAC algorithms,
  Fragmentation
  Power saving
  Encryption
  Address usage