## Slide 1: Local Interconnection
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: How do you communicate?
Post
Telephone (land line)
Telephone (mobile)
Email
Internal post
Local Address
Global Address
CO
CL
Notes: Five possible methods of person-to-person communication are shown. Suppose we want to inter-work between them? For example, to make a phone call that results in an email message being delivered. Almost anything is possible but some are much easier to implement than others. We must consider:
Service compatibility:
Telephone services are CO – we make a call and then use it to exchange a stream of short messages. The other services are CL – each message is a separate event separately addressed.
Address (number) compatibility:
Although email and the postal service are both CL, if you put a letter in the post addressed to g.knight@cs.ucl.ac.uk it will not arrive.
Note that addressing schemes must be organised so as to avoid duplicate addresses. This implies an “authority” to allocate addresses – probably through some sort of hierarchical devolution. Some schemes have global scope (e.g. international telephone numbers). Some have local scope (e.g. internal post – “G Knight, Computer Science” is not globally unique).
The two telephone services provide compatible services and share a global addressing scheme, so inter-working is easy. Email and the post provide compatible services but use different addressing schemes. Interworking requires a mapping service between the schemes – “address resolution.”

## Slide 3: How do computers communicate?
Ethernet (IEEE 802.3)
WiFi (IEEE 802.11)
ATM
Internet
LANE
Local Address
Global Address
CO
CL
Notes: Many “network” technologies are available for communication between computers. A few are shown in the slide (LANE see below). We can classify them as CO/CL and we can look at their addressing schemes. All the technologies in the slide use globally unique addresses but they do not all use the same scheme.
All the IEEE LANs (plus LANE) use 48-bit MAC addresses which are guaranteed to be globally unique. Each address consists of a manufacturer number (allocated by the IEEE) and a serial number (allocated by the manufacturer). All these technologies provide a similar CL service. Because of these compatibilities we would expect to be able to inter-work easily between them. E.g. we would hope that an Ethernet station could transmit a frame with an address belonging to a WiFi station and expect it to be delivered.
ATM is a very different from the IEEE LAN technologies; CO service and a different addressing scheme. This makes it much more difficult to inter-work. Imagine trying to design a system to interface a telephone conversation to a series of letters. One solution is to wrap up ATM so that it looks like a LAN to its users – this is the approach with LANE.
“Internet” is quite different from the others. By itself it can do nothing. It must exploit the other technologies to carry it’s datagrams between hosts. Like LANE it “wraps up” other technologies. Unlike LANE it does not try to emulate anything. It is a pure internetworking technology.

## Slide 4: Internetworking Approaches
Similar service, global addresses
Incompatible services.
Emulate
E
E
Incompatible services.
I
I
I
I
I
I
Internet layer
- easy to relay
B
B
- easy to relay
B
- easy to relay
R
R
Notes: The first diagram shows the IEEE approach; you can have lots of different technologies but all share a common, global addressing scheme (which guarantees no address conflicts) and provide a closely similar service. In fact the service – called the MAC service is a simple CL one. It is quite easy to design a device which can receive an item from one network and transmit it on the next. The IEEE terms such devices “bridges”. Nowadays the bridge function is most often incorporated in a box that can inter-connect several networks and is called a “switch”.
IEEE LANs have been so successful that non-IEEE technologies, such as ATM, can be provided with interface software which emulates an IEEE LAN. Once this has been done a standard IEEE bridge function can be used for inter-connection.
The Internet approach is much more general. An abstract internetwork service is defined which can then be implemented (usually by software) on any network technology. Devices can then be designed to relay between these abstract networks (called IP subnets). These are called “routers” in Internet terminology. There does not have to be a 1-1 relation between real networks and IP subnets. The three networks in the top diagram could be incorporated as a single IP subnet with the internet service being implemented solely at the extreme ends.
Note that interfaces may now have two addresses; a real “physical” address plus an emulated or abstract one.

## Slide 5: Addresses and Routing
Must ensure data delivered to correct host on correct network.
Devices must map destination address -> next hop
  “Forwarding table”
  One entry for every host? Big??
  One entry for every “network”? Smaller
Latter requires “structured” addresses
  E.g. IP Address = Net Id + Host Id (128.16.5.2/16)
  E.g. Phone no. = Area Code + Local No. (020 7679 7214)
Notes: The approaches in the previous slide solve the basic incompatibility problems. In each case we end up with an internet (small ‘i’) consisting of many, similar “networks” – even if some “networks” are emulated or abstract. There may be dozens, perhaps hundreds of such networks connected by “bridges” or “routers”. The two services we have considered – the IEEE MAC service and the Internet (big ‘i’) service - both send data units which normally contain two addresses; source and destination. How can the hosts and relay devices combine to use this address information to deliver the data to the correct place? The relay devices must have forwarding tables in which they look up destination addresses in order to determine the “next hop”? A large internet may possess tens of thousands of hosts. We would like to avoid having a separate table entry for each of these. Internet addresses (and telephone numbers and postal addresses) have a structure which makes the identity of the destination network explicit. This means that forwarding tables just need one entry per network – a much more manageable number (this is termed “address aggregation”). The down side of this is that addresses must be allocated accurately and that moving a host to a new network means changing it’s address.
IEEE MAC addresses do not have a useful structure, which is one reason to limit the size of a bridged network. However, it does make it simple to move devices between networks without changing addresses.

## Slide 6: Address Structure
Hierarchical addresses guarantee global uniqueness
www.ucl.com is globally unique
  it doesn’t tell you what its is, where it is, or how to get there.
  tells you who it belongs to
CS Dept., UCL, WC1E 6BT, UK is globally unique
  tells you country, sorting office, delivery round, department
128.16.5.2 is globally unique
  may tell where it is (128.16 => UCL-CS)
  but suppose host is nomadic ….
Notes: A major reason for using hierarchical addresses is to assist with the management of global uniqueness. A “top level” authority delegates to a number of uniquely named “next level” authorities and this process then recurses. E.g. the Internet naming authority delegates to “country code” authorities such as “uk”. “uk” then delegates to authorities such as “ac” etc. As long as each authority issues names which are unique within its scope then global uniqueness is assured.
Such a scheme may assist with routing and this is the case with postal addresses. However, this need not be the case.
Hosts that move cause particular problems. IPv4 addresses used to tell you where (in the networking sense) a host could be found. Now that hosts may move and attach to different subnets this is no longer the case. (Consider also mobile phone numbers – especially when travelling abroad.)

## Slide 7: The IEEE Transparent Bridge
“MAC Bridge” role – relay MAC frames between LANs
“Transparent”
  Hosts/bridges do not need to know network topology
  Hosts do not need to know location of destination
  Bridges “learn” forwarding tables
Intended to work between any pair of IEEE LANs
B
B
IEEE 802.x
IEEE 802.y
IEEE 802.z
Notes: The MAC bridge “role” is very simple, it just copies a frame from one LAN onto another. Nowadays it is not common to find a box sold as a “bridge”. Instead the bridge role may be found incorporated into devices such as Ethernet switches, wireless ADSL routers etc.
The “transparent” version of the IEEE bridge was designed to work without human intervention; no re-configuration of hosts or addresses, no human input to forwarding tables etc.

## Slide 8: MAC bridge - problems
Interconnection between different LAN types?
  Maximum frame lengths may differ
  Data rates different
  Technology-specific features
Latency
  Store and forward delay
  Different bit-rates prevents “cut-through” between segments
Filtering
  Only relay frames when necessary
  Security – restrict access to LANs
Notes: LAN differences:
  maximum frame lengths are different e.g. Ethernet has a maximum frame size ~1500 bytes, token ring uses a maximum of ~4000 bytes. Generally there is no provision for fragmentation in the MAC layer so there is a tendency to go for lowest common frame size.
  the data rates are different, e.g. Ethernet is 10Mb/s or 100Mb/s, token ring is 4Mb/s or 16Mb/s.
  some LANs have special features which have no equivalents on other LANs, e.g. token ring has priorities and acknowledgements, Ethernet does not.
All this may cause difficulty for bridging.
Bridges also impose a store-and-forward delay. This may be minimised by using “cut-through” – i.e. begin to forward frame on next hop as soon as destination address has been recognised. Cut-through is impossible if LANs operate at different bit rates.

## Slide 9: Why not one big LAN?
Shared medium - traffic increases => contention
Solution – partition into separate LANs
Ultimately – “switched LAN”
  One host per segment
A
B
C
D
A
B
C
D
Br
D
C
A
B
Sw
AB, CD
AB, CD
AB, CD
AC, BD
Notes: As load increases on a shared-medium LAN, contention increases and performance drops.
Often, traffic is localised – however, two transmissions between physically distant pairs of hosts still cause a collision.
Solution: partition the LAN via bridges. Each partition is more lightly loaded than the original LAN.
Ultimately a LAN switch can be employed. This is a multiport bridge – usually with a non-blocking architecture. If there is just one host on each segment then contention is completely eliminated.
Sometimes the motivation is that two geographically separated LANs exist and it is desired to link these. A bridge, or a pair of “half-bridges” linked by a serial line, can achieve this.

## Slide 10: Transparent bridge
Backward learning:
  look for source address
  forwarding table entry in reverse direction
  destination unknown: flood
  frames refresh table entries
X 1
Y 3
X 1
Y 2
BA
BB
1
2
3
2
1
X
Q
P
R
S
Y
BA Forwarding Table
Address Interface
BB Forwarding Table
Address Interface
3. BB learns X reached via 1
2. BA floods the frame on LANs P and R
4. BB floods the frame on LAN S
1. XY, BA learns X reached via 1
7. BA learns Y is accessible through 3
5. YX, BB learns Y reached via 2
6. BB forwards the frame on LAN R
8. BA forwards the frame on LAN Q
Notes: The bridge achieves transparency by operating in promiscuous mode; i.e. it processes all frames whether or not they were addressed to it. (Note that all stations “see” all frames but, normally, they ignore those not addressed to themselves). The bridge can then build up a forwarding table by backward learning. If bridge BB receives a frame with source address X on interface 1 then it knows that interface 1 would be a good place to send any subsequent frames that have X as their destination address. This information is stored as a forwarding table entry. Of course, if it receives a frame with destination address X through interface 1 it can ignore it as the frame is already on the right LAN. If a frame is received for which no forwarding table entry exists it will be flooded on all interfaces except the one it arrived on. [N.B. “flood” is not the same as “broadcast”. A broadcast frame is addressed to all hosts. A flooded frame is addressed to a single host but is flooded because the location of that host is unknown.]
If routes are not refreshed frequently by the receipt of an incoming frame they are timed-out and re-learnt. This allows the bridge to adapt to topology changes and host re-locations.
A certain amount of intelligent filtering is both desirable and possible. Hence it is generally possible for a manager to instruct a bridge to restrict forwarding to a list of known MAC addresses. Note that this is more clumsy than with a router due to the flat MAC address space.

## Slide 11: Loop problem
Problem with flooding strategy
Frame from X arrives at BB via two route
BC
1
2
BA
BB
1
2
3
2
1
X
Q
P
R
S
Confusion!!
Spanning tree algorithm
  Blocks ports to eliminate loops
Notes: The flooding algorithm causes problems if the topology contains loops as a bridge will eventually receive a flooded frame on two of its interfaces with resultant confusion. For example, a frame from host X for an unknown destination will be flooded by both bridges BA and BC. Two copies will eventually appear on LAN R. Bridges BA and BB will see this as a frame for an unknown destination and will forward the frame and so on.
An algorithm which allows bridges to negotiate a spanning-tree has been devised to cope with this problem. The spanning-tree algorithm overlays a spanning-tree on the network and so prevents loops forming. It does this by effectively disabling some bridge interfaces. For example, we might disable interface 3 on bridge A. This fixes the problem but at the expense of introducing sub-optimal forwarding paths, and makes load-sharing impossible.

## Slide 12: Ethernet Switches
Switch = multiport bridge
  Non-blocking architecture
  Simultaneous transmission between any pair of ports
Different speeds on different ports
Single host per port allows:
  full duplex operation
  no collisions
  flexible-length frames
Can build hierarchy of switches
Gigabit Ethernet on “backbone links
Cut-through operation
  Same speed on entry and exit ports
  Begin transmission before reception completes
Sw
Sw
Sw
Sw
Notes: Nowadays only very lightly loaded LANs rely on a single, shared Ethernet segment and CSMA-CD.
For heavier loads Ethernet switches are used – effectively these are multi-port MAC bridges. Ultimately the network can be arranged with one host per port. Since the links are “duplex” (i.e. they allow simultaneous transmission in each direction) there is no contention on these links.
A “non-blocking” switch will allow simultaneous relaying between any pair of ports. I.e there will be no contention within the switch.
Typical office networks these days consist of a hierarchy of switches perhaps arranged one per room each one connected to a port on a master switch via Gigabit Ethernet links.
Switches can accommodate different speeds on different ports so 10 Mbps, 100Mbps and 1000Mbps versions may inter-work.When relaying between ports which use the same speeds the switch will “cut through” – i.e. it will begin transmission as soon as the header has been processed and before reception is complete. This greatly reduces switch latency.
With one host per port CSMA-CD is no longer needed so that the restriction it applies to minimum frame sizes can be ignored.

## Slide 13: VLANS - Virtual LANS
Associate LAN stations according to logical criteria (rather than physical)
  E.g. separate LAN for accounts department
Restrict scope of broadcast and multicast
Ethernet switches can do selective forwarding
  Some LAN stations physically connected but logically disconnected
Flexible configuration to achieve what is desired
Notes: <header>
Slide <number>
The most convenient configuration of switches, backbones etc. may not be the best logical configuration. For example, it might make sense to place all the accounts department’s computers on one LAN and restrict access to it from outside. However, the members of the accounts department may occupy several offices widely distributed throughout an office building making a physically separate LAN costly to install. A VLAN would allow the members of the accounts department to be physically connected to several separate LAN segments but logically connected to a single “virtual” LAN.
This might be done for security reasons. It also serves to restrict the scope of broadcast and multicast frames which would otherwise appear on all connected LAN segments.
Ethernet switches can be configured to implement VLANs by deliberately restricting their forwarding capabilities so that some LAN segments may not communicate with others. Typically this is done by labelling ports as belonging to a particular VLAN. Switches will only forward frames between ports with identical labels.

## Slide 14: Level 2 VLANS - Example
VLAN A  VLAN A 
VLAN A  VLAN B 
Servers are on both VLANs
Could install a router to allow IP-level connectivity
VLAN A
VLAN B
S
S
Router?
Y
X
Switch C
Switch A
Switch B
Backbone LAN with servers
Notes: <header>
Slide <number>
The network above has two VLANs.
LAN segments belonging to VLAN A are distributed between ports on three switches as are those of VLAN B. The switches will refuse to output VLAN A traffic on a VLAN B segment and vice versa. However, traffic belonging to either VLAN may pass through the backbone LAN and switch C so that all hosts may access the servers.
If desired, a router could be installed to provide IP connectivity between the two VLANs. Such a router would not pass LAN broadcast or multicast traffic. In addition, it is generally possible to configure routers to disallow traffic to/from certain hosts or carrying certain kinds of traffic. These features allow a good measure of management control of traffic passing between the two VLANs.
Paths via the router shown on the slide can be quite tortuous. For example when X sends to Y, the packet must pass through switches A, C and B a in order to reach the VLAN B half of the router. It then traces a similar route from the VLAN A half of the router on to host Y. Presumably the network designers were more concerned with a proper separation of the VLANs than with efficiency. If the latter consideration were more important, a different configuration would be needed.

## Slide 15: The Internet Approach
Link, MAC, Physical – Technology dependent, unaltered
Convergence – encapsulation, address resolution
Common – datagrams, forwarding, fragmentation (maybe)
Transport – end-to-end
Convergence
Link/MAC
Physical
Internet
Common
Transport
I
I
I
I
I
I
R
R
XXX
YYY
ZZZ
IP Subnet
R
R
IP Subnet
IP Subnet
Notes: As noted earlier, the Internet service is an abstract one which can be implemented on any network technology. The Layers shown in the slide are abstractions of the functions involved.
The two lowest layers are technology dependent. All that is required of them is that they provide some means of carrying IP datagrams between stations. A set of stations that may communicate in this way constitutes an IP subnet. IP subnets may then be connected by IP routers. In fact an IP subnet may not correspond to a single, physical network – a collection of bridged LANs could be viewed as a single IP subnet.
The convergence layer implements a mechanism for exploiting a specific network technology to carry IP datagrams. Depending on the nature of the technology this may be simple or quite complex – perhaps involving the setting up and taking down of connections. It will always involve address resolution (where IP addresses are mapped to technology dependent addresses) and encapsulation (where IP datagrams are inserted into technology dependent frames).
Finally there is a common layer which deals with ensuring that IP datagrams are correctly forwarded towards their final destinations. Transport protocols such as TCP then use the resulting Internet service to carry their PDUs end-to-end between hosts.
Further information on specific address resolution and encapsulation mechanisms is given later in the course.

## Slide 16: Encapsulation
Data
IP datagram = Header + Data
Header includes destination address + other stuff
Most protocols use similar design (but with different headers)
One protocol can carry another - encapsulation
Address etc.
Data
Header
Data
Header
Header
Can be 11, 1many, many1
Many involve other issues, setting up connections etc.
Notes: Most communication protocols employ a unit of transmission (a protocol data unit (PDU) consisting of control information (addresses, sequence numbers and so on) followed by data (sometimes referred to as the payload). The data part is usually of arbitrary length. In the lower layers the header is usually of fixed length and format, which makes for efficient processing. Sometimes there is also a trailer which might include a checksum. The distinction between data and header is analogous to that between a letter and an envelope. The Post Office should only look at the information on the envelope. Similarly the protocol should only look at the information in the header.
When (say) and IP datagram is carried in an Ethernet frame the Ethernet protocol treats it as data and prepends its own header. This is an example of encapsulation.
Protocols may impose constraints on the size of the data they carry. This means that data may have to be fragmented and carried in multiple PDUs. On the other hand it might be possible to fit several pieces of data into one PDU (provided they are all going to the same destination of course!).
Encapsulation may involve other issues. For example some protocols need to set up a connection before they can carry any data.

## Slide 17: Complicated? – Take the IP View
HA
AP
WiFi
Br
AR
IP
IP
IP
DS
Sw
ATM
IR
ADSL
IP View
HA
IP
IR
AR
IP
IP
IP subnet
IP subnet
Notes: The slide combines a number of concepts from this section.
HA is a desk-top PC in someone’s home with a wireless connection to an access point (AP) which incorporates an IEEE transparent bridge function. On the other side of the bridge an Ethernet connects to an ADSL router (AR). (Of course WiFi and Ethernet provide very similar services hence bridging is easy)
This router connects to the ADSL link. IP datagrams are carried on this link encapsulated in PPP and ATM cells which are switched at the DSLAM (DS) across an ATM network to router at the ISP (IR). (The ATM network might itself contain several more ATM switches.)
Along the way the path involves (at least):
IP, IEEE 802.11 (WiFi). IEEE 802.3 (Ethernet), PPP, AAL-5, ATM, ADSL
Three different ways of encapsulating IP (as it crosses the four technologies)
Three addressing schemes (IP, IEEE MAC, ATM)
However, from the IP point of view the system consists simply of one host and two routers connected by two IP subnets.
The moral of the story is that when thinking about IP you should concentrate on IP issues and ignore the underlying complications.

## Slide 18: Summary
“Easy” to interconnect similar networks
  MAC bridge does this for IEEE LANs
Dissimilar networks must be wrapped up so they look similar
IEEE Transparent bridge
  Backward learning, loop problem
LAN switching
  Reduced (or no) contention
Internet – wrap up anything to look like an IP subnet
  Join up with routers