## Slide 1: WAN Technologies
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: PDH
Frame – 32 time slots:
  repeats every 125s
  slot 0: synchronisation
  slot 16: signalling
  30 data channels
  2.048Mb/s
  E1 channel
Higher aggregation possible
Legacy:
  multiple clock signals
  justification bits
Plesiochronous digital hierarchy (PDH)
Need to demultiplex whole signal to retrieve lower level multiplexing
Add-drop multiplexer (ADM):
  complex
  hard to detect faults
PDH now being replaced by SDH
Notes: Recall that TDM uses timeslots, each of which represents a 64Kb/s channel. In fact, there is additional structure to the use of TDM in real life. 32 TDM slots are arranged as a frame which repeats every 125s. Within the frame, slot 0 is used for frame synchronisation and slot 16 is used for common channel signalling for the data channels. This yields a total data rate of 2.048Mb/s and is called an E1 circuit (this is for Europe – North America uses 24 slots giving 1.544Mb/s and is called DS1 or T1). Higher aggregation is possible by combining E1 circuits. In fact, the development of these digital channels is based on the use of older analogue capability, and many different TDM systems were built in relative isolation. This led to slight differences in the timing/clocks of these systems. To allow aggregation and combining of various multiplexes, “padding” bits called justification bits have to be inserted into the bit stream to provide proper synchronisation. Hence this family of multiplexes is called the plesiochronous digital hierarchy (PDH) (plesiochronous means “almost synchronous”). While this solution allows the multiple systems to be combined, in order to extract a particular lower level multiplex/circuit requires that the whole bitstream must be completely demultiplexed. This is function is performed by an add-drop multiplexer (ADM). The hierarchy for PDH appears below, but is now being replaced by a much more scaleable transmission technology – synchronous digital hierarchy (SDH).
PTO

## Slide 3: The Demultiplexing problem
E1 frame
Slot 25
E2 frames
E3 frames
125 s
125 s?
In principle, “slot 25s” are always 125 s apart
Inserting a “justification bit” destroys this relation
Justification bit
Notes: The slide shows the position of slot 25 in the first three PDH multiplexes. If things were truly synchronous consecutive instances of slot 25 will always be 125s apart. However, the insertion of a justification bit disrupts this sequence. This makes it impossible to demultiplex slot 25, or any other slot, simply based on synchronous timing. With PDH the only solution is to demultiplex the whole structure to determine whether justification bits are present. The whole structure must then be re-multiplexed ready for the next link.
With SDH there are “pointers” in the frame headers which indicate precisely where the sub-multiplex frames begin. Thus a single slot can easily be picked out without having to dismantle the whole structure.

## Slide 4: Add-Drop Multiplexors
We have an E4 (= 64 x E1) circuit A  B
We need an E1 circuit A  C
Divert every 64th bit?
  No! because of justification bits
Must demultiplex E44xE316xE264xE1
  Then re-multiplex!
A
B
C
Add-drop multiplexor
E4
E1
Notes: <header>
Slide <number>
Telecommunications providers install very high capacity lines between major centres. PDH is used to provide lower capacity circuits to customers. Some customers may be at an intermediate point (e.g. at C in the slide). We may want to provide circuits to customers at C.
In the slide an E4 circuit (= 64 x E1) goes from A to B and we want to provide an E1 circuit from A to C. Ideally this would be simple; the bits of the E1 circuit would arrive at regular intervals and these could be diverted to C. Unfortunately the presence of justification bits means that the bits of the E1 circuit are not quite evenly spaced. In order to find them accurately we need to demultiplex the whole E4 stream (-> 4xE3 ->16xE2 -> 64xE1). We can then extract the appropriate E1 channel – but we must then re-multiplex to re-build the E4 circuit.
This is the task of the “Add-drop multiplexor” (ADM). The presence of the PDH justification bits means that the task of the ADM is complex; so PDH ADMs are expensive.

## Slide 5: Synchronous Digital Hierarchy- SDH
Multiplexing standards for fibre
Raw bit-rate | SDH (Europe) | SONET (US)
51.84 Mbps | - | STS/OC1
155.52 Mbps | STM1 | STS/OC3
622.08 Mbps | STM4 | STS/OC12
1,244.16 Mbps | STM8 | STS/OC24
2,488.32 Mbps | STM24 | STS/OC48
Overhead reduces bit-rates:
155.52 Mbps = 150.336 Mbps data + 5.184 Mbps overhead
Notes: <header>
Slide <number>
SDH/SONET provides higher capacity circuits than PDH which are suitable for optical fibre. It also adds more management and maintenance capabilities and allows much more efficient ADMs.
The systems are complex (!) only a very brief introduction is included here.
History
SONET was proposed by Bell Communications Research (Bellcore) in 1984 on behalf of the regional Bell operating companies (RBOCs). The standard was ratified by ANSI in 1984 (drafted by the Exchange Carriers Association). It was based upon Synchronous Transport Signal level 1 (STS-1) a 51.84 Mbit/s transmission system incorporating a 90 byte repeating frame transmitted 8000 times a second.
ITU-T adopted the idea and widened the scope somewhat. The ITU-T version is referred to as Synchronous Digital Hierarchy (SDH). It is based upon Synchronous Transport Mode level 1 (STM-1) which is 155.52 Mbit/s. Although the two systems are not completely compatible STM-1 is compatible with STS-3 and all levels thereafter. The ITU-T has issued a whole series of SDH related standards but they were later amalgamated as G.707. This contains the definition of the bit rates, the network node interface and the multiplexing structure for SDH.

## Slide 6: SDH Example – STM1
Repeating frame (8000 frames per second)
Frame is a “Synchronous Transport Module” (STM)
Frame consists of “overhead” + “payload”
Payload consists of several “virtual containers” VC
  Each VC is (typically) a PDH circuit + overhead
9 bytes
261 bytes payload
9 segments
VCs
Notes: <header>
Slide <number>
The slide shows an STM1 frame. This is conventionally drawn as 9 segments each of which consists of 9 overhead bytes and 261 bytes of payload. Segments are transmitted left-to right, top to bottom.
N.B. we have a total of 9 x (9 + 261) = 2430 bytes in a frame. 2430 bytes 8000 times a second means 2430 x 8000 x 8 = 155.52 Mbps.
The payload can be partitioned into an arbitrary number of VCs. Each VC occupies an integral number of columns. Various sizes of VCs are allowed. For example, a VC12 occupies 4 columns so it uses 4x9 = 36 bytes of each frame. Thus we have 36 bytes 8000 times a second which means 36 x 8000 x 8 = 2.304 Mbps. This is enough for one E1 channel + overhead.
The situation is slightly more complicated than described since VCs may contain other VCs and so on.

## Slide 7: SDH and Pointers
Payloads may cross frame boundaries
Payloads may shift to compensate for timing variations
Pointers keep track of things
STM1 Frame
Admin. Unit
AU pointer
VC pointer
Virtual container
Notes: <header>
Slide <number>
SDH separates logical payload boundaries from physical frame boundaries. The slide shows the top-level payload; termed an “administrative unit” (AU). This occupies 9 segments but need not start and end on a frame boundary. The AU is divided into VCs – but again, a VC need not start on an AU boundary.
“Pointers” are used to keep track of things; the AU pointer indicates where the AU starts within the frame, a VC pointer indicates where a VC points within the AU.
Pointers may change from frame to frame. This happens when the system has to accommodate sub-channels that are slightly slow or fast. For example VC12 carrying a “slow” E1 channel will gradually drift through the AU to accommodate its extra delay.
However, the system of pointers means it is always possible to locate a sub-channel no matter how deeply multiplexed it may be. Thus, in contrast to PDH, it is possible to pull out a sub-channel without demultiplexing the whole structure. This means that SDH ADMs can be much more efficient than PDH ones with consequent cost savings.

## Slide 8: SDH and Data Communication
Data communication is based on packet-switching
We need links to connect switches and hosts
SDH can provide the links
SDH provides
  Robustness
  Bandwidth management
  Easy configuration via ADMs
Notes: <header>
Slide <number>
A data communications provider may wish to use fibre to connect two switches. If the fibre is managed using SDH it is easy for the SDH provider to reconfigure their network to provide the capacity where it is needed. SDH also includes redundant paths to provide resilience in the face of fibre breaks etc.