## Slide 1: LANs and Bridges
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Example – IEEE LANs and MANs
IEEE 802 LANs and MANs
  IEEE 802.1 Overview and Network Management
  IEEE 802.2 Logical Link Control
  IEEE 802.3 CSMA‑CD LAN (Ethernet)
  IEEE 802.5 Token Ring
  IEEE 802.6 DQDB MAN
  IEEE 802.11 Wireless LAN
  Etc. Etc.
Notes: The Institute of Electrical and Electronic Engineers (IEEE) in the US has taken on the role of standardising LAN technologies. Their committee 802 does the work with various numbered sub-committees looking after individual technologies.

## Slide 3: IEEE Layers
The Physical layer
  Defines the electrical characteristics, bit encodings, connector types etc.
The Medium Access Control (MAC) layer
  Defines the channel allocation strategy and framing
  Datagram operation
The Logical Link Control Layer
  Common to all the technologies
  Specifies protocols to enhance the MAC layer so as to provide a full OSI Layer 2 service
  Protocol discrimination
Notes: The model was described in an earlier slide. The key idea is that, whilst the technologies may differ wildly, the service provided by the MAC layer remains (broadly) the same – i.e. a simple connectionless service.

## Slide 4: Spanning-tree algorithm
Find a tree connecting all bridges
Assign costs to LANs
Bridges send BPDUs to each other
  Bridge ID
  Root ID
  Cost to root (CB)
Establish root bridge:
  Initially, all assume they are root
  lowest bridge ID wins
Bridges keep state
  Root port
  Local cost to root (CL)
Receive BPDU on non-root port:
  Calculate CN = CB + LAN cost
  If CN < CL, adopt new root port
  If CB < CL, set port as “blocking”
Adapts to topology changes
Notes: Each bridge has a unique ID (which is administratively assigned, and unique within the context of the LAN). Optionally, system administration may allocate costs to paths based on bit-rate to control the way that the spanning-tree algorithm will work. (This is not an essential step).
Initially each bridge assumes that it is root and sends a bridge PDU (BPDU) on each of its attached LANs. The root acts as a reference point which allows overall path costs to be compared. A BPDU contains:
  Currently assumed root id (self initially)
  Path cost to root – CB (zero initially)
  Bridge ID (self)
  Port ID (through which BPDU is transmitted)
On receipt of a BPDU, a bridge determines whether the source of the BPDU should be root (if it has a lower ID than its current ID for root). If the bridge which sent this BPDU should be the root, then:
  Calculate new path cost CN = CB + cost of LAN over which BPDU has travelled
  Update path cost, bridge ID and port ID and forward BPDU on other ports
  Note path cost to root on port through which this BPDU was received
  The port with lowest cost path to root is the root port

## Slide 5: BC – Root Port
CN = CB + 2 < CL
At BC:
Root ID: BA
Root port: 1
CL: 4
2
1
1
1
2
3
2
2
2
X
3
2
BA
BC
BB
BD
BE
3
2
BPDU from BA to BC on port 3:
Bridge ID: BA Root ID: BA
CB: 0
Cost
Interface no.
Notes: We assume that all bridges have already agreed that BA is the root. BC currently believes its best path to the root is via port 1 of length 4.
On receipt of a BPDU on a non-root port, compute new cost of path to root on that port (CN) based on the path cost in the BPDU (CB) and the cost of the segment on which it arrived. Compare this with the current cost through root port (CL):
If (CN < CL) then the port on which the BPDU was received becomes the new root port and the cost to root is updated.
In the slide, BC receives a BPDU through port 3 and calculates the cost to the root through that port:
CN = CB + 2 = 0 + 2 = 2 < CL
So there is a cheaper path to the root through port 3 than through port 1. Therefore Bc chooses port 3 as root port with CL = 2.

## Slide 6: BC – Blocking
CN = CB + 3 > CL
CB < CL => block 1
At BC:
Root ID: BA
Root port: 3
CL: 2
2
1
1
1
2
3
2
2
2
X
3
2
BA
BC
BB
BD
BE
3
2
BPDU from BB to BC on port 1:
Bridge ID: BB Root ID: BA
CB: 1
Notes: On receipt of a BPDU on a non-root port, compute new cost of path to root on that port (CN) based on the path cost in the BPDU (CB) and the cost of the segment on which it arrived. Compare this with the current cost through root port (CL):
If (CB < CL < CN) mark port as blocking – no data frame will be forwarded on this port but BPDU frames can still be received and transmitted.
In the slide, BB advertises a cost to root of 1 to BC. BC calculates:
CN = 1 + 3 = 4 > CL.
This means there is no need to change the root port. However, CB < CL. This means that BB has a cheaper path to the root than BC. Therefore, BC should set its port 1 to blocking.

## Slide 7: BE – Root Port
At BE:
Root ID: BA
Root port: 1
CL: 5
2
1
1
1
2
3
2
2
2
X
3
2
BA
BC
BB
BD
BE
CN = CB + 2 < CL
2
4
BPDU from BC to BE on port 2:
Bridge ID: BC Root ID: BA
CB: 2

Notes: In the slide, BE calculates the cost to the root (BA ) through its port 2:
CN = CB + 2 = 2 + 2 = 4 < CL
Therefore BE chooses port 2 as root port with CL = 4.

## Slide 8: BE – Blocking
CN = CB + 2 > CL
CB < CL => block 1
At BE:
Root ID: BA
Root port: 2
CL: 4
2
1
1
1
2
3
2
2
2
X
3
2
BA
BC
BB
BD
BE
2
4
BPDU from BD to BE on port 1:
Bridge ID: BD Root ID: BA
CB: 3

Notes: In the slide, BD advertises a cost to root of 3 – so CN = 3 + 2 = 5 > CL. This means there is no need to change the root port. However, CB < CL. This means that BD has a cheaper path to the root than BE. From the point of view of host X, BD is the better bet. Therefore, BE should set its port 1 to blocking.
This algorithm runs periodically, and can cope with topology changes dynamically. When ports are set to blocking, no data frames are forwarded on these ports until they are switched to forwarding by a subsequent execution of the spanning-tree algorithm. This redundancy helps the spanning-tree algorithm to make a network robust to failures (given enough extra – redundant – paths between network segments).

## Slide 9: Spanning Tree – Complete
2
1
1
1
2
3
2
2
2
X
3
2
BA
BC
BB
BD
BE


No loops
Fully connected
No load sharing
Sub-optimal routes
Notes: The algorithm achieves its aim but at some cost:
  It is impossible to use two bridges to share the load of traffic between networks. T
  The routes between LANs are clearly sub-optimal.
Given this, why would one ever bother to introduce loops? The answer is redundancy. If bridge BD should fail, the algorithm will unblock BE’s port 1 and connectivity will be restored.

## Slide 10: Source-routing bridge
For use on token ring
Route is:
  bridge ID, LAN ID, bridge ID, LAN ID, …
  must be carried in every frame - inserted by source
Route set-up:
  discovery frames
  optimal routes possible
  load distribution possible
  many hosts generate a lot of discovery frame traffic
X
B2
B3
B1
B4
L1
L2
L3
L4
Y
XY: B3, L4, B4, L2, B2, L3
or: B1, L2, B2, L3
Notes: The source-routing bridge is the bridging technology usually used with token ring. It requires bridges and hosts to learn the complete route to all possible destinations. This is in contrast to the transparent bridge which only learns the first hop of each route. It also requires host participation. Hosts must at least know whether the remote destination is or is not on their LAN segment. If it is not, the high order bit of the destination address – the remote bit – in a transmitted frame is set to 1 so that the bridge will recognise it as special.
It is relatively simple to learn whether a destination is on the local LAN because token ring addresses are structured so that 12 bits are regarded as a LAN identifier. Each bridge has a 4-bit identifier which must be unique in the context of its LANs. Thus there may be two bridges with identifier 6 but these cannot have any LANs in common. Allocating bridge identifiers is the job of a human administrator. Source routes consist of a sequence of bridge ID, LAN ID, bridge ID, LAN ID … So, a route from X to Y might be B3, L4, B4, L2, B2, L3.
Bridges operate in promiscuous mode. On receipt of a frame they look for the remote bit in the header and, if this is set, they look at the source route. If they see they are on this route they will forward the frame on to the next LAN, otherwise the frame will be dropped. For example, if B4 receives a frame from LAN4 with a source route as in the example above, it will forward it on LAN2.
Routes are learnt through the use of discovery frames. Bridges flood these if they do not know a route to a destination. The destination floods them back towards the source and each bridge records its identity in the frame as it passes. The source of the discovery frame can then work out the “best” route based on whatever criteria seem appropriate. In principle optimal routes can be chosen and it should even be possible to distribute traffic between alternative routes. (Thus, not all traffic will follow the same route from X to Y). The disadvantages are that human intervention is needed to configure bridges and the high cost of flooding discovery frames in large networks.