## Slide 1: Sharing Resources
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Sharing
Link sharing
Network sharing
Notes: The key to efficient data communications is the efficient sharing of physical resources. This results from the fact that almost nothing, computers nor people, need to communicate all the time. Therefore dedicating communications resources exclusively almost always wastes resources during idle periods.
The resource might be a single “link” – piece of cable or fibre for example. This is termed “sharing the medium” and is covered mainly in Z03.
The resource may be a network involving many wires with specialised computers called “switches” to connect them together. The traditional telephone network has this form but so do several dedicated computer network technologies including the Internet itself. We look at different ways of achieving this sort of sharing in the next few slides.

## Slide 3: A little history
1837 The telegraph (Cooke and Wheatstone)
1838 Morse code (Samuel Morse)
  Electronic digital communication
1843 Facsimile transmission
  Data communication
1865 Commercial facsimile transmission
1876 The telephone (Alexander Graham Bell)
  Analogue voice
1878 First commercial telephone exchange
Analogue telephone network grew and grew …
Notes: Long-distance electronic communication began in 1837 when William Cooke and Charles Wheatstone invented the telegraph. This grew into a large, successful, international network mainly carrying text encoded in "Morse Code" (invented by Samuel Morse in 1838). In 1876, Alexander Graham Bell invented the telephone to carry voice over wires and, in 1878, installed the first telephone exchange in New Haven, Connecticut. From this grew an enormous world-wide communications network and a new engineering discipline - "telecommunications". Telecommunications engineers deal with the all aspects of the design, construction and operation of telecommunications networks. This includes the exchanges or "switches", and the basic physics of propagating information via waves carried in wires or some other medium. Until quite recently, in most countries, the telecommunication network was an effective monopoly, usually owned by the Government. It deployed some large, high-cost equipment, was tightly managed and carefully planned Whilst the network was complex, the equipment connected to it was usually very simple - a basic analogue telephone. Only today, has the dominance of voice traffic on world-wide telecommunications networks begun to be challenged by data traffic. However, there has always been some data traffic. Fax, for example, pre-dates the telephone having been invented in 1843 with the first commercial usage in 1865. More recently, Telex provided a simple text-based service on the telecommunications network.

## Slide 4: A little more history
1960s communication between computers
  Used analogue telephone infrastructure
  MODEMs
  Low capacity, noisy, error-prone
1961 Packet-switching
  Kleinrock and Baran (US)
  Davies and Scantlebury (UK)
  Pouzin (France)
1970s Mini-computers, 1980s Micro-computers
1972 Ethernet LAN - Metcalfe
Notes: During the 1960s, computers began to proliferate and communication between them became an issue. Proliferation is relative, though - computers were still quite thin on the ground. Therefore, the communication of interest was generally over quite long distances. Convenience, and in many cases government regulation, meant that computer to computer communication had to be built on the existing telecommunications network. This network, as employed a technique called "circuit-switching" which turns out to be less than ideal for computer to computer communication. Consequently, in several countries, work began on developing networks specifically for data communications. In 1961, Leonard Kleinrock published a paper which introduced the concept of "packet switching" of digital data. Kleinrock and Paul Baran in the US, Donald Davies and Roger Scantlebury in the UK, and Louis Pouzin in France all worked on experimental packet-switching networks. Eventually, packet-switching became the basis of a new breed of data communications networks. As noted above, most of the early deployment of data communications networks was over relatively large distances - anything from a few tens of kilometers to a few thousands. Today we would call these "Wide Area Networks" (WANs).
The 1970s saw the emergence of mini-computers, followed, in the 1980s, by desk-top work-stations and PCs. It was now common to find many computers on one site all of which needed to communicate. This resulted in the development of the "Local Area Network" (LAN). Since LANs did not cross public land, they were freed from the constraint of having to build on the public telecommunications networks. Several LAN technologies competed in the early days, mostly based on the idea of a "shared media" network. Here, all the computers are connected to a single wire rather than being connected together in pairs. Although the technologies were quite different from those used on WANs, the packet-switching idea remained. One of the earliest LAN designs, proposed in Bob Metcalfe's 1972 Harvard PhD Thesis, eventually became the Ethernet, which is the dominant LAN technology today.
LANs developed both in performance and in range. The result was the "Metropolitan Area Network" (MAN) designed to provide a high-speed backbone around, say, a university campus or a business park. As for with the LAN, the MAN used specially installed wiring usually independent of the public telecommunications network.

## Slide 5: Circuits and Circuit-switching
Notes: At a) we can see Bell’s original set-up. An electrical circuit joins two phones enabling analogue voice signals to pass between them
At b) we see an early realisation of a “switched” telephone service. The switches consist of plug boards operated by a human operator. By setting plugs appropriately at the two switches (more normally known as “exchanges”) any telephone can be connected to any other. This arrangement still sets up an electrical circuit end-to-end for the duration of the call.
At c) we see an automated version of b). Switches Xs and Xt were originally warehouse-sized electro-mechanical devices which set up electrical circuits end-to-end. More recently the internals of the network have become digital and the switches are direct streams of bits along the appropriate wires. From the point-of-view of users the service looks the same. Thus, although there is no longer an end-to-end electrical circuit the term “circuit” is still used and the switching technique employed is called “circuit-switching”.

## Slide 6: Telephone Service Characteristics
Any telephone can communicate with any other telephone;
A telephone can only communicate with one other telephone at a time;
Other telephones may be "blocked" - unable to communicate because the wire they need is in use;
Communication between two telephones (once established) is unaffected by activity elsewhere in the network.
Whilst they are communicating, the two telephones have exclusive use of the wires that link them;
Words are delivered in the same order in which they are spoken.
Time intervals between words are preserved
We can distinguish three phases in the life of a circuit; setting it up, using it and tearing it down
Notes: Many thousand telephones will be connected to each local exchange. We would like several of these to be able to make long-distance calls concurrently. We could achieve this by running multiple wires between each pair of exchanges. However, copper is expensive and a cheaper alternative is available - this is to "multiplex" several calls down one piece of wire. For the first half of this century, (and still today in some cases) the technique used to achieve this was "Frequency-division multiplexing" (FDM) which is explained below. FDM was used to partition the capacity of a link into (usually) equal portions; each portion being sufficient for one telephone call. The effect is that a single high-capacity wire behaves, in all important respects, like a collection of low-capacity wires. Once we introduce multiplexing, there is no longer a dedicated physical path between two telephones. Instead, there is a dedicated logical path which is, to all intents and purposes, indistinguishable from a dedicated physical path. This means that the eight characteristics of circuit-switching, set out above, are, effectively, maintained. The only change is that we must now replace the word "wire" with "capacity".
In a modern telephone system, voice traffic is carried digitally - i.e. it is converted to a stream of bits by a "CODEC“. The bits may still travel along wires, though they may also be transmitted using microwaves through the atmosphere, light in optical fibres etc. The electro-mechanical exchanges have been replaced by electronic "switches" - in US terminology, the local exchange function is performed by a "central office switch" whilst the trunk exchange function is performed by a "toll switch". The multiplexing technique used is now "Time-division multiplexing" (TDM) - see below. TDM effectively partitions the capacity between a pair of exchanges into 64 Kbps "sub-channels" - each sub-channel being enough for one telephone call. However, the circuit-switched service is preserved - complete with all its eight characteristics.
The switches now deal in streams of bits. If bits are arriving from a sub-channel at 64Kbps they must depart at precisely the same rate - otherwise bits will either accumulate in the switch or we will have gaps in the stream. Of course, this applies to every switch and every sub-channel in the network. Ideally, the whole network should be synchronised to a common clock and this is the practice in the most modern systems. If the synchronisation is not precise, it must, at least, be very close. Consider what happens if bits arrive at 64.1 Kbps rather than 64 Kbps. By the time 641 bits have arrived only 640 will have departed so one bit would have to be dropped. 640 bits take 10ms to transmit, so we would be dropping 100 bits every second!

## Slide 7: Frequency Division Multiplexing
12 carrier frequencies at 4KHz intervals
  60 KHz to 108 KHz
Voice waves filtered to approx. 3KHz bandwidth
Voice modulated on carrier
  Carrier spreads ± 1.5 KHz
Notes: FDM is like radio on a wire. Different radio stations transmit on different frequencies. A radio receiver “tunes in” to a frequency an can extract the signal that has been modulated on it. Exactly the same technique can be used to provide sub-channels over a single piece of wire.
The slide shows the arrangement that was common on telephone trunks. Note that the actual frequency transmitted is a combination of the “carrier” and the voice signal that is modulated upon it – which means there will be some variation. This means there must be adequate separation between the carriers used in each of the sub-channels. This ultimately imposes a limit on the number of sub-channels that can be carried.

## Slide 8: High “speed”
Higher speed vehicles travel faster …
12 kph, ~ 36 vehicles/min
24 kph, ~ 144 vehicles/min
Bits always go at the same speed
  ~ 2x108 m/s in copper, ~ 3x108 in fibre
1 Mbps
2 Mbps
High “capacity”!
Notes: The terms “high-speed network” and high-speed link” are misleading. Bits, in a given medium, always travel at the same speed – the limit is really the speed of light.
However, bits may be packed more or less densely – i.e. the rate at which bits are injected into the channel may vary. A high transmission rate means more bits are injected, hence delivered, in a given interval - we should really call this a “high-capacity” channel. A file transfer through such a channel will complete in a shorter time than it would through a low-capacity channel. However, the propagation time for each individual bit will be the same in each case (assuming equal lengths and media).
[Note that a road densely packed with cyclists moving at 20 kph may actually have more capacity than a road carrying bloated single occupancy BMWs travelling at 100 kph! All that is required is that you can fit more than 5 bicycles in the space occupied by a BMW (which you can).]

## Slide 9: Time Division Multiplexing
Voice digitised by a CODEC
  64 Kbps PCM
64 Kbps per channnels
256 Kbps channnel
8
8
8
8
8 bits
8 bits
8 bits
8 bits
125 s
125 s
X
X
X
X
8 bits
8 bits
8 bits
8 bits
Notes: TDM works with streams of bits transmitted at a constant bit-rate. If n sub-channels each of b bps are to be multiplexed then the output channel must be able to carry exactly nb bps.
The multiplexor works by taking small fixed-size groups of bits from each input channel in rotation. A complete set of bits from all the input channels is called a “frame”. Frames are transmitted on the output channel. A similar arrangement at the far end dismantles the frame and restores the individual sub-channels.
In the slide bits are taken 8 at a time so in 125s 32 bits will have arrived in parallel from the 4 64 Kbps sub-channels. The resulting 32-bit frame can be transmitted in 125s on the 256 Kbps output channel. Note that the multiplexor inevitably introduces a delay pf approximately 125s.

## Slide 10: Time-division Multiplexing
TDM interleaves bits (sometimes bytes) from several streams onto a higher bit-rate stream
Timings between bits of a stream are preserved
The effect is as if there are two separate “bit-pipes
Notes: The slide shows bits from a pair of digital circuits interleaved on a single link. (In some systems the interleaving may be in terms of bytes rather than bits). Recall that bits always travel at the same rate, therefore the bits on the multiplexed link must be packed twice as tightly requiring twice the capacity of an input link. Once demultiplexed the original bit timings are restored – so bits are delivered at exactly the rate they were originally transmitted. In fact the multiplexing is invisible to the transmitter and receiver which have the illusion of a dedicated link.
Of course, more than 2 incoming links may be multiplexed but the arithmetic must be exact; the bit-rate on the multiplexed link must be equal the the sum of the bit-rates on the incoming links.
A simple timing change in the demultiplexor would cause the upper bit stream to be switched to the lower link and vice-versa. Thus it is easy to turn a TDM system into a “circuit-switch” which can connect arbitrary inputs and outputs.

## Slide 11: Statistical Multiplexing
Packet Switch
Data sent in “lumps” called “frames”, “packets” etc.
Lumps may vary in size
Inter-arrival times are random
Usually processing is FIFO
Notes: Packets arrive at random intervals. They are queued on the correct output link (generally, links may be both inputs and outputs). If a lot of traffic arrives for a particular output link in a short interval a long queue may develop.
Statistical multiplexors (i.e. packet-switches, routers etc.) must provide buffering (memory) for queued packets. Queuing implies additional delay which some applications cannot tolerate easily. Often the best strategy is to discard packets rather than deliver them with long delays in the hope that the application will handle the problem intelligently.
Internet routers act as statistical multiplexors. In a sense the whole of the Internet can be thought of as an enormous statistical multiplexor.
Packets may be treated on a first-come, first served basis. However, this is increasingly seen as inadequate. We would like to be able to give priority to certain types of traffic. For example, interactive voice (Internet phones etc.) needs very low delay - so there is a case for pushing this type of traffic to the front of queues. Other types of traffic may be very sensitive to packet loss and so on. These sorts of issues are all concerned with meeting a particular “quality of service” contract for a particular type of traffic. In order to make sense of these issues in a network such as the Internet there needs to be a way of signalling to the network what kind of treatment should be given to a particular packet or sequence of packets. There must also be a means of charging extra for high-priority traffic. This is a very active area of research.

## Slide 12: Statistical Multiplexing
Data communication – not all bits are useful
  TDM does not exploit this
  Statistical multiplexing does
Notes: TDM works at the bit level; all bits of the original streams are delivered to the final destination. A few applications (e.g. PCM voice) generate a stream of bits at a constant rate all of which must be delivered – TDM suits such applications well. Most applications (including more modern compressed voice applications) generate data in bursts interspersed with periods of idleness. Most serial links still generate bits during such idle periods, (it is in the nature of the technology used to do this). Framing techniques, such as bit-oriented synchronous framing described earlier, enable data bits to be distinguished from idle bits. Statistical multiplexing treats the data bits and ignores the idle bits.
The slide shows two 1Mbps input streams in which about half the bits are in data frames the rest being idle bits (i.e. utilisation is about 50%). The statistical multiplexor exploits this by using a multiplexed link with a capacity < 2Mbps. The utilisation on this link is about 67%. (Of course the scheme is not restricted to just two input channels.)
Statistical multiplexors operate in “store-and-forward” mode – a complete frame must be received before transmission begins on the output link. This introduces a store and forward delay equal to the transmission time on the output link. E.g. if a frame has 15,000 bits the delay will be 10ms.
There can also be contention for the output link when two frames arrive simultaneously on the two input links. This contention is normally resolved by queuing – another source of delay. Queuing times, hence delays, can be highly variable – thus a statistical multiplexor introduced jitter as well as delay.
In the worst case there may be insufficient space for the queue so a frame must be discarded. So statistical multiplexing may cause data loss.
The demultiplexor cannot assume that frames will neatly interleaved – some information must be included in the frames to indicate to which channels they belong. Thus some bits in the frames must carry control information rather than data; an additional overhead due to statistical multiplexing.
Despite the disadvantages of statistical multiplexing the enhanced utilisation it brings for bursty data makes it the best choice for most current data communications.

## Slide 13: Circuit-switched Data Networks
Any host can communicate with any other host;
A host can only communicate with a small, fixed number of hosts at a time (E.g. N-ISDN 2 B-Channels);
Other hosts may be "blocked" - unable to communicate because the wire they need is in use;
Communication between two hosts (once established) is unaffected by activity elsewhere in the network.
Whilst they are communicating, the two hosts have exclusive use of the sub-channel which links them;
Bits are delivered in the same order in which they are sent.
Time intervals between bits are preserved
We can distinguish three phases in the life of a circuit; setting it up, using it and tearing it down
Notes: Now that the telephone network is digital internally it is tempting to try to use it for data. However, the service provided is still circuit-switched and has the characteristics shown in the slide. Several of these do not suit data communications well:
  A host can only communicate with a small, fixed number of hosts at a time (E.g. N-ISDN 2 B-Channels);
We would like one computer to be able to communicate with multiple computers concurrently.
  Other hosts may be "blocked" - unable to communicate because the wire they need is in use;
Generally we would prefer congestion to lead to reduced performance rather than no service.
  Whilst they are communicating, the two hosts have exclusive use of the sub-channel which links them;
This is OK but the cost of providing this is too high. The problem is that computer communication is “bursty”. Therefore, for much of the time an open circuit will be idle. It would be much better if this idle capacity could be re-allocated, not held exclusively.
  Time intervals between bits are preserved
We would like to be able to communicate between dissimilar devices. For example, I would like to be able to communicate with you even though my modem goes at 19,200 bps and your goes at 38,400 bps.
All of this means that data communications needs a different approach.

## Slide 14: Circuit-switching
“Circuit” – constant bit-rate pipe across network
“Switched” – path established dynamically
Typically based on TDM
PSTN
ISDN
Notes: In modern digital communication a “circuit” is a constant-rate bit-pipe. Typically circuits are implemented using TDM channels passing through “circuit-switches”. A circuit-switch is capable of connecting input and output channels in an arbitrary way. Large switches may be able to handle many thousand such channels.
In some cases circuits are set up “administratively”. A customer will order a circuit of a particular capacity between two locations. An operator will use management software to configure switches to provide the circuit. Such circuits are called “leased circuits” or “leased lines”. Usually a monthly charge will be made.
In other cases circuits are set up “dynamically”. A “signalling” protocol between the customer’s equipment and an external network switch specifies the destination of the circuit which is then set up dynamically. Further signalling is used to disconnect the circuit. Such circuits are called “switched circuits”. Call charges will be based on the duration of the circuit – ISDN and PSTN provide switched circuits.

## Slide 15: Packet-switching
Circuit-switching is inefficient for data
Data is “bursty”
  We must open a circuit big enough for the peaks
  Capacity will be wasted during the troughs
Fixed allocations
  If we want 65Kbps we must ask for 128 Kbps
Packet – a collection of bits
  53 bytes, 1500 bytes …
Packets from different sources are mixed on a link
  Statistical multiplexing
Notes: The archetypal circuit-switching application is the voice telephone call. The technology used to digitise calls inside a modern telecommunications network results in a continuous stream of bits at 64Kbps. Data sources rarely generate a continuous stream of bits. Instead, they emit bursts of bits separated by arbitrary-length periods of idleness. Packet-switching exploits these periods of idleness by allowing the unused capacity to be used by other data sources. Essentially it is a multiplexing technique which aims to allocate network capacity on-demand with a very fine time granularity. This is in contrast to FDM and TDM which allocates fixed slices of capacity for extended periods.
A packet is a small collection of bits and is the basic unit of transfer. Packet lengths vary; at present, they are mostly 1500-bytes or less but some emerging technologies presage much larger sizes (and others, much smaller!). In general, though, packets are smaller than user-level objects such as the files or WWW-pages that we wish to transmit. Consequently, such objects must be split up and sent in a succession of packets.

## Slide 16: Packet-switching
Based on statistical multiplexing
“Packet-switches” – store and forward
Packets multiplexed to many destinations
X.25
Frame relay
ATM
Ethernet
Notes: Note that the two forms of multiplexing often co-exist. For example the 1.5Mbps link in the previous slide could actually be one TDM sub-channel in a higher capacity link. This is very often the case in the wide area. A company might lease (say) a 10Mbps link from a provider in order to connect two statistical multiplexors at two company sites. The provider’s network will likely consist on fibre running at several Gbps. Only a fraction of this will be needed to satisfy the company’s requirement and this will be apportioned using TDM.
The slide shows a network of “packet-switches” connected by “links”. Each link is a bit-pipe at some bit-rate. Packet-switches are usually store-and-forward, in which case the bit-rates may vary from link to link. Packet-switches can receive packets on any link and forward them on any other. They base their forwarding decisions on information contained in the packets. By setting this information appropriately a source may mix packets to a variety of destinations – something that is not possible with circuit-switching.
In a “virtual-circuit” network all packets to a particular destination follow the same pre-arranged route. If these routes are set up administratively we have “Permanent Virtual Circuits”, if they are set up dynamically via signalling we have “Switched Virtual Circuits”.
In a datagram network a separate routing decision is made for each packet. Thus packets belonging to a sequence will not necessarily all follow the same route and may be delivered out of order.
X.25, ATM and Frame Relay are examples of Virtual-Circuit packet networks.
Ethernet (though its structure is quite different from that shown in the diagram) is a datagram network.
The Internet is a datagram network constructed by interconnecting thousands of individual packet-switching networks of various types.
Since an idle host uses no (or almost no) network resources packet-switching tariffs are based on the volume of data sent.

## Slide 17: Mesh-type Packet Networks
Topology similar to circuit-switched network
  “Packet-switch”, “router”
  Store and forward operation
A
D
C
B
S
T
U
V
Notes: The slide shows a typical mesh-type network. Many wide-area computer networks are of this type – examples are X.25, ATM and Frame Relay.
The slide shows two flows of packets: from A to C via packet-switches T, S and V; from B to D via S, T and U.
The Internet has a similar structure except that the “links” are actually themselves networks. The switches are then called “routers”.
Each switch is a statistical multiplexor. There may be congestion and queuing delays.

## Slide 18: Packet-switching advantages
Hosts with nothing to send send nothing
Links are statistically multiplexed
Easy for hosts to multiplex packets to many destinations
Source and destination can operate at different bit-rates
t
p
128Kbps
384Kbps
192Kbps
Time
Ha
Hb
Sa
Sb
Notes: Packet-switching tends to be much more efficient for data transmission. Data transmission id “bursty” so there are often lengthy idle periods. Statistical multiplexing exploits the fact that a large enough collection of computers will almost never all be busy or all idle at the same time. Effectively, idle periods are filled by traffic from other sources. Circuit-switching cannot ddo this.
The store-and-forward operation allows there to be different speeds on each link. This means. For example, that a PC with a 34 Kbps modem can still retrieve a web page from a server with a 10 Gbit connection to the Internet.

## Slide 19: Packet-switching disadvantages
Store and forward delay
  Minimised by small packets
Time
b)
Time
a)
Notes: Store-and-forward operation has the disadvantage that the whole of a packet must be received on the input link before transmission on the output link can begin. These store-and-forward delays accumulate as a packet travels through a network and can become excessive. Small packets minimise the effect. However, small packets means more packets which may be harder for a switch to process. There is always a fixed per-packet overhead and this is proportionately greater for small packets.
It should also be noted that high bit-rate links reduce transmission time and hence reduce store-and-forward delay.

## Slide 20: Packet-switching disadvantages
Switches may become congested
  Queues form
  Delays
  Discard packets
End-to-end delay is unpredictable
  Jitter
Packet header overhead
  Sequence numbers
  Addresses
  Connection identifiers
Notes: There is always a chance that all sources will generate traffic concurrently, which may exceed a link's capacity. Packet-switches try to handle this by forcing some packets to wait in a queue until the congested link clears. This adds "queuing delay" to the store-and-forward delay. If congestion is really bad the packet-switch may run out of queuing space and begin discarding packets. Packet-switching is a form of "statistical multiplexing"; enough capacity is provided to carry the average combined load (plus some extra) but not enough to carry the peak combined load. The method works most of the time because it is statistically unlikely that all sources will peak at the same time.
We need some way of distinguishing packets so we can ensure they are delivered to the right place. In practice, this means we must add some sort of label to each packet - so there is a packetisation overhead.

## Slide 21: Packet variants
Cell-switching
  Small, fixed-size packets
  Asynchronous Transfer Mode (ATM), 53 bytes
Frame Relay, Frame-switching
  Data-Link layer switching
  Variable-size frames
Message-switching
  Email messages, files
  Very large store and forward delay
Notes: Cells and cell-switching
Cells are a specialised form of packet which are a) fixed size and b) small (normally 53-bytes). They are used in so-called "Asynchronous Transfer Mode" networks.
Frames, frame-relay and frame-switching
"Frame" is the usual name for the unit of data transfer in the Datalink layer. Frame-relay and frame-switching are particular technologies which transfer what they call "frames" through a sequence of "frame-switches". For the purpose of our discussions here, these frames are exactly like packets.
Messages and message switching
In this context, a message is a collection of data that is meaningful to an application; for example, a file, a WWW page or an email message. Message switching operates in the same store-and-forward mode as packet-switching but messages are switched as units rather than being split into packets. It is clear that store-and-forward operation with large data units such as files will result in long end-to-end delays. Thus, message-switching makes no sense for any kind of interactive data communication. It does find a use within electronic mail systems, however - but not on its own. In practice the “links” between message switches are provided by packet-switched networks.

## Slide 22: Packets or Circuits?
Any host can communicate with any other host;
A host can only communicate with a small, fixed number of hosts at a time (E.g. N-ISDN 2 B-Channels);
Other hosts may be "blocked" - unable to communicate because the wire they need is in use;
Communication between two hosts (once established) is unaffected by activity elsewhere in the network.
Whilst they are communicating, the two hosts have exclusive use of the sub-channel which links them;
Bits are delivered in the same order in which they are sent.
Time intervals between bits are preserved
We can distinguish three phases in the life of a circuit; setting it up, using it and tearing it down




?


?
Notes: Comparing packet-switching with circuit-switching we see many changes. 2 and 3 are clear advantages. 4, 5 and 7 are potential disadvantages. They arise as a consequence of statistical multiplexing which, of course, leads to much better utilisation of transmission capacity. One of the challenges of packet-switching is to maintain the statistical gain whilst keeping the effects of 4, 5 and 7 within acceptable bounds.
6 and 8 may or may not be true depending on whether we use “virtual circuits” or “datagrams”. This is discussed in the next few slides.

## Slide 23: Virtual Circuits or Datagrams?
Bits are delivered in the same order in which they are sent.
We can distinguish three phases in the life of a circuit; setting it up, using it and tearing it down
Answer “yes
  Virtual circuits
    Set up route and reserve resources
    Use it
    Tear it down
Answer “no”
  Datagrams
    Each packet is an independent event
?
?
Notes: We can distinguish two ways of implementing pack-switched networks – Virtual Circuits and Datagrams. Virtual Circuits lend to predominate in WANs whilst datagrams hold sway in LANs. However, the biggest network of all – the Internet – uses datagrams as a technology to interconnect other networks.

## Slide 24: Addresses and Identifiers
Hosts must have addresses (like ‘phone numbers)
  Millions of hosts
    Millions of addresses
    Long addresses (128 bits => ~1038 addresses)
Addresses are needed when a connection is set up
VCs must have unique VCIs on a link
  Thousands of VCs per link
    Thousands of VCIs per link
    Short VCIs (24 bits => ~107 VCs)
VCIs are also called… Logical Channel Numbers (X.25), Data-Link Channel Identifiers (Frame Relay), Virtual Channel Numbers, Virtual Path Numbers (ATM) …
Notes: When a circuit is set up across a circuit-switched network two things happen:
  A route is chosen through the circuit-switches. This route will not change during the life of the circuit.
  A slice of the capacity on each link is reserved..
The VC approach applies a closely similar style within a packet-switched network:
  A route is chosen through the packet-switches. This route will not change during the life of the VC.
  Resources are reserved. The packet-switches must be able to distinguish between incoming packets belonging to different VCs so that they can be forwarded on the correct links. Therefore, packet-switches must store some information about the VCs which currently pass through them. Packet-switches must also ensure they have sufficient buffer space for any of the new VC's packets that may need to be queued.
The first issue - that of route selection - is common to many technologies, there is not time to cover it in detail here. We concentrate here on the second issue - distinguishing between packets belonging to different VCs. When a VC is set up, we have to tell the network where we want it set up to. For this to be possible, all the "end-points" of the network (to which the "end systems" or "hosts" are attached) must have identifiers analogous to telephone numbers. In data communications these are referred to as "addresses" - though, in practice, they are nearly always numbers. We cannot use these addresses to distinguish between VCs because there may be several VCs terminating at the same destination. Ideally, we would like to allocate a distinct number to each extant VC. However, this is impossible to manage for the thousands of VCs which might exist throughout the whole network. Instead, we settle for ensuring that all the VCs extant on any particular link have distinct numbers - called Virtual-Circuit Identifiers (VCI).

## Slide 25: Virtual Circuits
1
5
7
2
8
1
7
5
A
D
C
B
S
T
U
V
Forwarding table for switch S
Notes: VCIs cannot have global significance - it would not be practical to find a value that was not already in use for another VC somewhere in the network. Instead, we allocate different VCIs on each link. Thus the VC on the slide indicated by the broken line has VCI 5 between B and S, 8 between S and T and so on. Switches must keep a record of the links being used by each VC and the VCIs being used on each link. The table in the slide shows this information for the switch S.
When a packet arrives at S from T, S will look at the VCI in the packet’s header (it should be either 7 or 8). If it was (say) 7, S would queue the packet on the link to V and would change the VCI in the packet header to 5.

## Slide 26: VCs – Advantages
Small headers
  Minimises packet overhead
Efficient forwarding
  Simple table look-up
Easy to ensure sequenced delivery
  All packets follow the same route
Admission control
  Host specifies requirements when asking for a connection
  Network only accepts if it has resources
Traffic Policing
  “Contract” for each VC
  Can police on a per-VC basis
Notes: There may be hundreds of thousands or even millions of end-points in a network so end-point addresses must be quite big numbers - for example, current Internet thinking is that they need to be 128-bits long. The number of VCIs on a link at any one time will be very much fewer than the number of end-points. Therefore, we can allocate far fewer bits to a VCI - 24 in one popular current technology. Since every packet must carry a VCI it is an advantage that they can be quite short.
Because we set up the route in advance and all the packets belonging to a particular VC follow the same path, it is easy to ensure there is no mis-ordering of packets.
A network can refuse to set up a connection if there are insufficient resources – e.g. there are already too many connections. Arguably this is more sensible than the Internet approach where all traffic is accepted and everyone suffers when the network is overloaded.
A network can “police” connections. For example a user may have a contract specifying that s/he will transmit no more than 500 packets per second. If more are transmitted the network may discard the excess.

## Slide 27: VCs - Disadvantages
VCI field in packet header must change at each switch
  May need to re-calculate checksum
  Processing overhead?
VC set-up overhead
  At least two PDUs to setup VC
  At least two PDUs to disconnect VC
  Suppose you only want to send one Data PDU?
  No problem if we use “Permanent Virtual Circuits” (PVCs)
Suppose a switch breaks?
  Adjacent switches cannot repair (they do not retain end-point addresses
  Hosts must request new VCs
Notes: If a switch breaks down, there is no way that the adjacent nodes can repair the VC. In the earlier example, if S breaks, T will know two of its VCs are affected but it does not know where they go to on the other side of S. The VC has been destroyed and will probably have to be set up again from scratch.
Time is taken to set up the VC before any data can be sent and the impossibility of repairing a VC if a link or a switch breaks.

## Slide 28: Datagram Networks
Datagram – a self-contained unit of transmission
  Independent
  Global addresses
Each datagram is routed separately
  No route set-up phase
Switch processing
  Choose “next-hop” on basis of destination address
Bits are delivered in the same order in which they are sent.
We can distinguish three phases in the life of a circuit; setting it up, using it and tearing it down


Notes: When we considered the different characteristics of circuit and packet switching we left two questions undecided. Answering “yes” to these led to the virtual-circuit approach. Answering “no” leads to datagrams. Datagrams are packets which flow through networks rather as letters flow through the postal service. Each datagram carries the full address of its destination. Each is treated by the network as a separate event and is dealt with without reference to any other datagrams which may have preceded it.
Most LANs operate on the datagram principle. In LANs, operation is very simple since datagrams can usually be delivered to their final destination in one “hop”.
In mesh-type networks using the datagram principle datagrams travel along several “hops” between packet-switches. In datagram networks these packet-switches are usually called “routers or “bridges”. Routers/bridges are the “sorting offices” of datagram networks. They examine the addresses of incoming datagrams and forward them to the most likely neighbouring router/bridge. If all goes well the datagram eventually reaches its destination. Note that there is no concept of “setting up a route” or “reserving resources for a connection”.

## Slide 29: Datagram forwarding - example
Internet router
  Destination address 128.16.5.2
  Several entries may match …
  Table look-up is complex …
Address | Mask | Link
128.16.0.0 | 255.255.0.0 | 1
128.16.5.2 | 255.255.255.255 | 2
128.16.5.0 | 255.255.255.0 | 1
… | … | …
Routing table
Notes: We will look at Internet router operation in more detail later in the course. Briefly, each “Internet Protocol” (IP) datagram includes a destination “IP address” in the header. IP addresses are 32 bits long and are generally written at 4 decimal bytes, e.g. 128.16.5.2. Each host on the Internet has an IP address. The Internet is partitioned into “networks”. All the hosts on a network have IP addresses which start with the same bits. For example, all the computers in the UCL CS department have addresses which start 128.16. This can be regarded as our network address. Organisations like UCL-CS can partition their network into “subnets”. For example, we might have a subnet on which all the addresses begin 128.16.5.
Internet routers include “forwarding tables” which say on which link a datagram should be forwarded. Generally the entries in this table match networks or subnets. This is useful as one table entry can do the job for a whole set of hosts - for example, an entry for 128.16 would cover all the computers at UCL-CS. When trying to match an address to an entry in a routing table we must know how many bits in the address are relevant. In the table in the slide this is indicated by the “mask”. For example, 255.255.0.0 (ie. 16 1s followed by 16 0s in binary) means just the first 16 bits are relevant, 255.255.240.0 means just the first 20 bits etc. Some addresses may match multiple entries. For example, the address 128.16.5.2 matches all the addresses in the table in the slide. In such cases the rule is to take the longest match. Therefore, 128.16.5.2 selects the second entry, 128.16.5.8 would select the third and 128.16.6.2 would select the first.
This business of masking and multiple matches means that IP forwarding is quite complex computationally. Clever algorithms exist to accomplish the task in the shortest possible time. However, this remains an issue for large routers at the heart of the Internet which may need to forward millings of datagrams per second.

## Slide 30: Datagrams – disadvantages
Heavier processing in switches (see previous)
  BUT – clever look-up algorithms exist
Global addresses are big – large per-packet overhead
  No good for cells (2 128-bit addresses in 53 bytes for ATM!)
Admission control and policing must be per-host, not per-connection
  BUT - addressed by Internet QoS work
Independent routing cannot guarantee sequenced delivery
Notes: The datagram style of working is strongly favoured by the Internet community. Naturally, it has strengths and weaknesses:
The datagram equivalent of the VCI mapping table in is the "routing table". Since a packet-switch has no idea what will be the destination address of the next datagram it receives, it must know which link to use for each and every end-point in the network. If we are not careful, the routing table will end up being very big. Furthermore, it will have to be searched for every incoming datagram. Worse still, it turns out that an incoming datagram may match several entries in the routing table so significant computation must be done to decide where to send the datagram next. Fortunately, there are some tricks we can play to make this “forwarding decision” decently efficient.
End-point addresses are much larger than VCIs. Since every datagram must carry a destination end-point address, we have a larger per-packet overhead that we would for a packet in a VC network. If the packets are big, this is not an issue. If they are small, 53-byte cells for example, then the overhead will be prohibitive. Cell-based technologies are virtually obliged to use VCs.
The inability of datagram networks to guarantee sequenced delivery is a problem for the sort of applications which require it. The solution is to use software in the computers at the end-points which marks datagrams with sequence numbers and re-orders them when they are delivered out-of-order. This is one of the services provided by the Internet TCP protocol.

## Slide 31: Datagrams - advantages
Datagram networks often use “dynamic routing”
  Routing table continually updated by information from other switches
  New routes are learnt when switches break or become congested
  Robust!
No connection set-up overhead
  Good for short transactions
Datagram service is very simple
  Cheap to implement
  No unwanted “features”
Notes: Datagram networks often use "dynamic routing". This means that there is a background process which continually updates the routing table in accordance with information received from other packet-switches. Therefore, a new table will be learned if a packet-switch breaks or becomes congested. Once dynamic routing is in place, datagram networks become very robust; if a switch breaks, a few datagrams may be lost whilst a new route is learnt. Thereafter, communication continues - there is no need for the end-points to act to recover the situation, as there would be if a new VC had to be established.
Since there are no VCs there is no time lost in setting up connections.

## Slide 32: Summary
Fixed allocations – FDM, TDM
Sharing networks
Circuit-switching, packet-switching
  Statistical multiplexing
Global Addresses
Virtual Circuits
  VCIs
Datagrams