## Slide 1: Sharing the Medium
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Introduction
Sharing a link
  TDM, FDM - fixed allocations
  Statistical multiplexing - variable allocations
Sharing a network
  Circuit switching
  Packet switching
  Queuing strategies in routers
What about sharing the medium?
Notes: We have looked at sharing links either by FDM or TDM. Both of these divide the capacity of a link into fixed capacity sub-channels each of which may be used by a separate activity. We have looked at statistical multiplexing where a link carries packets each of which belongs to a separate activity but which may be mixed on the link in an arbitrary order.
We have looked at sharing a network. The networks we have considered have looked roughly like the telephone network with switches connected by link. We have seen that we can share the network by switching circuits or packets. Packet switching is the preferred choice as it is a form of statistical multiplexing which is favoured by the bursty nature of computer traffic,
We now ask whether it is possible to eliminate the switches and share the medium directly. If we are to succeed we need a way of controlling access to the medium since it is dear that only one computer can be using it at any one time. Techniques for doing this are called "Medium Access Control" (MAC) algorithms.

## Slide 3: Approaches
Bad ideas
  TDM - stations take turns to transmit
  FDM - each station transmits on a different frequency
Good ideas ?
  Contention
  Token passing
  Reserving timeslots
  Anything else?
Notes: Using pure TDM and FDM would be a bad idea. These give fixed allocations to stations. Idle stations would waste their allocations. In fact there are other problems:
For TDM we would nee done timeslot for each station. What happens when we add another station?
For FDM we could allow each station to transmit on its own frequency. Receivers would now have to listen on all frequencies.
Several ideas have been made to work:
Contention. More-or-less like a conversation between a group of people. If one person is speaking, everyone else keeps quiet. We must decided what to do if two people start talking “simultaneously”.
Token passing. There is one token which is passed around. Only the station with the token is allowed to transmit.
Reserving timeslots. A bit like TDM but timeslots are not allocated to stations in rotation. Instead, there is a reservation protocol allowing stations to book timeslots as needed.
There are several others including one interesting idea based on encryption.

## Slide 4: Aloha - simple contention
Packet radio - University of Hawaii - 1970s
"Contention-based" system - transmitters uncoordinated => collisions
Collision recovery - wait a random time and try again
How well will this work?
host
host
host
Notes: The ALOHA protocol was devised at the University of Hawaii in the 1970s. The protocol was first used on a packet radio network which was built to connect the various campuses of the University which were distributed amongst several islands, The transmitters were uncoordinated so it was quite possible for two or more to transmit simultaneously causing collisions. The ALOHA protocol attempts nothing to prevent this. It merely says "if a collision occurs wait a random time and try again". The random factor is necessary in order to prevent collisions occurring systematically on the re-transmissions. It is easy for a station to detect a collision; it just listens to the channel and detects whether the signal it transmitted has been altered in any way. Note that on a satellite network, as opposed to a packet radio network, there will be a considerable (propagation) delay before collisions can be detected. Geostationary satellites are 35,784 Km above the equator. At the speed of light the round-trip delay is about 240 ms - more if you are not on the equator. Protocols which allow these sort of conflicts between stations in order to solve the channel allocation problem are called "contention" systems. There are many variants.

## Slide 5: Aloha Throughput
Notes: The graph shows the theoretical throughput curve for Aloha. This is based on the assumption that all packets are of the same length and that the intervals between transmission attempts have a negative exponential distribution.
In the graph:
  S is the “throughput” – the combined rate for all stations at which packets are successfully delivered.
  G is the “offered load” – the combined rate for all stations at which packets are transmitted. G will be bigger than S since it includes colliding transmissions.
  Both S and G are “normalised” – they are measured in units of packets per packet time. Thus a perfectly utilised network would have athroughput of 1
When G=1, i.e. the offered load exactly matches the network capacity, the throughput then is about 0.14. Thus 86% of our transmissions are actually retransmissions.
Trying to go faster than 18.4% utilisation just makes matters worse. Eventually very little is happening except retransmissions colliding with each other and throughput approaches zero.
Does this mean that Aloha is hopeless? Not really but you have to ensure that the network has enough raw capacity so that G can be kept below 0.5.

## Slide 6: Slotted Aloha
Upper diagram – A and B both collide
  Vulnerability period 2T
Lower diagram – transmissions start on “timeslot boundaries”
  A collides but B is deferred - vulnerability period T
Utilisation is now 36.8%
  … but there is an extra ½T delay on average …
Time
t0
t0+T
t0-T
Time
t0
t0+T
t0-T
A
A
B
B
Notes: The upper diagram shows that, with standard ALOHA, a packet transmission beginning at t0 will be destroyed by another transmission beginning in the interval (t0 -T, t0+T) – a vulnerability period of 2T
If we constrain transmissions to start on timeslot boundaries (so-called “slotted ALOHA”) then any transmission becoming available during the interval (t0, t0+T) will be deferred and will not collide. This reduces the vulnerable period to T.
The analysis can be done as before and results in a doubling of the maximum utilisation. The down-side is that packets must wait for a timeslot – an average of T/2 sec. additional delay.
There must be some mechanism for ensuring that all stations are synchronised to the same slot boundaries. In a satellite network this can be done by having the satellite transmit regular pulses indicating timeslot boundaries.

## Slide 7: Carrier Sense Multiple Access
“Listen before speaking”
Avoids collisions?
Time
t0
t0+T
bit 1
bit F
time
A
B
D
p
t
bit 1
No!
  (but it helps)
Notes: If a station continuously monitors the network it can discover when another station is transmitting and can defer its own transmission until the network is silent. This avoids many collisions. The buzz phrase for this is "carrier sense".
Carrier sense does not avoid all collisions. The problem is that propagation delay ensures that another station's transmission may already have begun (legitimately) but has not yet reached us (see slide). The longer the propagation delay, the more likely this is to happen. In the extreme case of a satellite network, the propagation delay is about 240ms. Listening to the network may tell us that the network was silent 240ms ago but it does not help us to know what is happening now. Carrier sense cannot be used in such networks.
However, provided the propagation delay is low, CSMA. gains a lot over. x .Aloha as we will see. This is the situation for most LANs (both wired and wireless) where the maximum distance between stations is nearly always less than a few Km. For example, the propagation delay on a 2Km optical fibre is 20003x108 = 6.7s. At 10Mbps only 67 bits can be transmitted in this time - a very small portion of the size of the average packet. However, note that at 1Gbps, a speed that is available commercially, 6700 bits or 837 bytes can be transmitted in 6.7s - a sizeable portion of a packet.

## Slide 8: Non-persistent CSMA
If stations transmit immediately the medium goes quiet there will be many collisions
Non persistent – “if medium is busy wait a random time and retry”
Packet arrives
Transmit here
Persistent
Packet arrives
Non-Persistent
Transmit here
Random time
Notes: As indicated in the previous slide, the naive CSMA strategy is for a station to wait until the medium is silent then begin transmission immediately. This is called "persistent CSMA". The problem with this strategy is that if two or more stations are waiting, they will almost certainly collide when they begin transmission. (Here we should note that the diagram above omits a potentially important detail; namely that it takes some time for the fact that the network is silent to propagate to all stations. Thus there must always be an interval between the end of one transmission and the beginning of the next. For the purpose of this discussion we assume a very small propagation delay so that this interval may be neglected). It should be clear that, when network load is heavy, persistent CSMA will generate very many collisions so that throughput will drop.
Several solutions to this problem have been studied. One approach is "non-persistent CSMA". Here a station which finds the network busy "backs off' i.e. it waits a random time before listening again. The effectiveness of this strategy is examined in the next slide. Another approach is "p-persistent CSMA". Here a station continues to listen to a busy network waiting for it to become silent. When it does so, the station transmits with a probability p, defers (i.e. waits a random time) with a probability (1-p). If p is 1 we have persistent CSMA, If p is (say) 0.5, then two stations both waiting for silence will collide with probability 0.25. The downside is that they will both defer with probability 0.25 leading to an unnecessary delay.
Note. We are considering here the strategy to be adopted when a station finds that the network is busy and defers its transmission. Do not confuse this with the strategy to be adopted when, despite our efforts, a collision does occur. In particular, note that CSMA-CD (see later) handles collisions in a way which resembles that used by non-persistent CSMA to handle deferrals.

## Slide 9: Throughput Comparison
Notes: The graph shows the theoretical throughput curves for two varieties of CSMA and ALOHA.
We can see that CSMA is always better than Aloha.
When the normalised load is low, persistent CSMA wins. This is because non-persistent is wasting time by deferring packets for a random time when these could, most likely, be transmitted immediately. However, as the load increases, persistent CSMA performance collapses as the network becomes dominated by collisions.
[The non-persistent graph is actually misleading. At high loads the probability of collisions becomes significant thus invalidating one of the assumptions made in the analysis. In reality the throughput would start to collapse as a result.]

## Slide 10: Collision detection
In CSMA, collisions last one packet time
  Why not stop once a collision is detected?
  How long does it take to detect a collision?
time
A
B
bit 1
p
bit 1
p
bit F
t
Answer: 2p
  E.g. 10Mbps Ethernet: tmax = 1.2ms, p = 10s
Notes: With both persistent and non-persistent CSMA a collision costs us one packet time. If we were to detect collisions as soon as we could and immediately stop transmission we would waste less time. Is this complication worthwhile?
The diagram shows the worst case in which B starts to transmit just before the first bit of A's transmission arrives. This takes one propagation delay p. However, at this point A is unaware of the collision and will not become aware until the first bit of B's transmission reaches A. This takes another time p. Thus, in the worst case it takes 2p to detect a collision where p is the maximum propagation delay between two stations. So, if we add collision detection, the time wasted in a collision reduces from t to 2p.
The original Ethernet (10Mbps) MAC protocol is CSMA with collision detection - CSMA-CD. The maximum size Ethernet packet is 1500 bytes and the transmission rate is 10Mbps. This means tmax = 1.2ms. The maximum distance between two stations is 2Km which means that p is 10s. So the saving certainly appears to be worthwhile.

## Slide 11: CSMA-CD Performance
CSMA-CD is a persistent strategy
When load is low,
  Negligible collisions
  Performs like persistent CSMA
When load is high,
Many collisions
  Collisions handled by “binary exponential back-off”
  Effectively a deferral
  Performs like non-persistent CSMA
Best of both worlds!
But …
  There is a cost (see next slide)
  CD is difficult in wireless networks
Notes: CSMA-CD is an effective protocol and is used on the most widespread LAN - Ethernet Since it takes 2p (worst case) to detect a collision all transmissions must last at least 2p.
CSMA-CD is a persistent strategy and, when load is low and there are few collisions, its performance is like that of p-CSMA. When the load increases, collision occur – and are detected. Collisions are handled by “binary exponential back-off”. Stations involved defer transmission by a random time with mean t. If collisions recur the strategy is repeated but with means 2t, 4t, 8t etc. This means that CSMA-CD behaves much like np-CSMA at high loads.
The down-side is the minimum frame-size requirement (see next slide) and the fact that collision detection is difficult in wireless systems – if is difficult to construct equipment that can transmit and receive the same frequency simultaneously.

## Slide 12: CSMA-CD
Protocol used on the Ethernet
time
A
B
bit 1
p
bit 1
p
bit F
t
Must have t > 2p or collisions may be missed
For a given p there is a minimum frame-size
10Mbps Ethernet, min. frame is 64bytes
Notes: The original commercial Ethernet ran at 10Mbps and had a maximum cable length of 2.5Km hence p = 25002x108sec = 12.5s. Thus t > 25s. At 10Mbps we can transmit 10 bits per s so the minimum frame size should be 250 bits - about 32 bytes, In fact we have to allow a bit for the electronics to react and then add on a little bit more just to be safe. Hence the 10Mbps Ethernet standard specifies a minimum frame size of 64 bytes.
This is unfortunate if we only want to send one byte but maybe not too bad. However the situation changes as the bit-rate increases. Fast Ethernet uses 100Mbps and reduced the maximum cable length to 200m to compensate. Gigabit Ethernet (1000Mbps) increases the minimum frame size to 512 bytes. However, gigabit Ethernet is often used as a duplex point-to-point link in which case there is no contention and the restriction can be dropped.

## Slide 13: Ethernet
Originally on coax cable, now mainly on “twisted pair”
Faster versions often use optical fibre
Binary exponential back-off
Bus
Bus with spurs
Hub
Notes: Ethernet comes in a host of varieties using various different media at three bit rates. 10Mbps is widespread. The original topology was a bus using coax cable. "Spurs" could be added so one might have a main cable running round a building with spurs into each office. Now 10Mbps Ethernet is mainly on twisted pair using a hub - effectively the bus is put in a box.
100Mbps ("Fast Ethernet") is a fairly straightforward speed-up. The network span (and hence the propagation delay) has had to be reduced in order to keep t > 2p. Fortunately the trend is towards small LANs connected by devices called Ethernet switches so the 200m span is not too much of a problem. Each mini LAN has only a few hosts which reduces contention and hence collisions. Note that a switch is not the same as a hub.
1000Mbps ("Gigabit Ethernet") is beginning to appear. Making transmission work economically and reliably at such speeds is a challenge. Most versions use optical fibre though a standard for copper wire does exist. Reducing the span still further was not an option. Therefore the minimum frame size has been increased to 512 bytes (frame is just the LAN word for a packet). This could be very wasteful if many small frames are to be transmitted as these must be padded.
A variety of bit encodings are used. The original version used Manchester encoding but some variants use NRZ1.
"Binary exponential backoff” is the strategy used after a collision is detected. If all colliding stations tried again immediately a further collision would be almost certain. Instead, stations wait a random time with mean 2p before trying again. If there is another collision the process is repeated this time with a mean of 4p then 8p etc.

## Slide 14: Token passing [1]
Token:
  is passed around a ring
  token holder transmits
  token is then released
Topology:
  physical ring
  logical ring
Bits stored on ring:
  1Km ring holds 50 bits
  some bits at receiver, some at transmitter, some on ring
concentrator
token ring
(physical ring)
token bus
(logical ring)
Notes: The idea of token passing is very simple. A small, special bit pattern called the token is passed around all stations connected to the media and only a station holding the token can transmit. After transmission it releases the token, passing it to the next station in the ring. All messages transmitted on a ring circulate through all stations in a known order and can potentially return to their source. Note that the number of bits on a ring at any one time can be quite small. For example, at 10Mb/s one bit is transmitted every 0.1s. If the propagation speed is 2x108 m/s (= 200m/s) then each bit occupies 20m. If a ring has a circumference of 1Km it will only have 50 bits "stored" on the cable. In addition to these bits there will probably be at least one bit stored at each station as these act as repeaters (regenerating the input signal on the output). Thus, one can expect the total number of bits on the ring to be of the order of 100 - so an average size data frame (say 512 bytes) does not fit on the ring. During the transmission of such a frame, part of it will have been received, part will be on the medium and part will still be waiting at the transmitter.
The token may pass along a physical ring topology, or a logical ring topology.
On an idle ring, the token circulates continuously and each of the participating stations merely relays the bit-stream (and hence the token) around the ring. Once it has the token, a station can use the full bandwidth of the medium for its transmission. On the IBM token ring, the transmitted bits travel around the ring and back to the transmitter - which then removes them. The receiving station may set some bits at the end of a data frame to indicate correct reception. Once transmission is complete the transmitting station re-generates the token followed by "idle fill' data until the token (or a data frame) returns. When the ring is idle, with the token circulating, each station acts as a simple bit-repeater. For this to work the token must be small enough to fit on the ring in its entirety. The token contains some bits which specify a priority, and stations may then grab a high-priority token only if they themselves are configured as high priority stations.

## Slide 15: Token passing [2]
length of a bit
number of bits on ring
token transmission time
round trip delay on ring
maximum frame transmission time
maximum latency
Maximum latency when each station has a maximum size frame to transmit
Notes: Some mechanism must be introduced to ensure that the station holding the token does not hog the network. There is a maximum transmission length and a requirement that a station always releases the token after transmission. At start-up, or if the token is corrupted and lost, no station can transmit, a protocol is required to generate a new token. The possible solution of having a specialised "monitor" station to perform this task is not favoured, as it would introduce a single point of failure. All stations monitor the ring to check that a token is circulating. If a station finds no token it will generate a new token, if two stations do so simultaneously they will back-off and re-transmit the token in a fashion similar to that used for CSMA/CD.
One important characteristic of token passing MAC algorithms is that it is possible to determine the maximum delay before a transmission succeeds (the maximum latency). This deterministic property of the token ring distinguishes it from the CSMA/CD LAN and is important in some time-critical applications such as process control. What is the longest time a station must wait before grabbing a free token? In the worst case, all stations have maximum length frames ready to transmit. Suppose a station has the token, it transmits a frame, followed by a free token. As soon as the last bit of the free token reaches the next station this next station can begin its own transmission. Typical token ring values are shown below.
NS: number of stations (20) TT: token transmission time LR: length of ring (1000m) TF: maximum tSume transmission time LB: length of bit TR: round trip delay on ring ST: token size (24 bits) SF: frame size (4096 bits) R: data rate (16Mb/s) NR: number of bits on ring V: propagation speed (2x 10Sm/s) TMAX: maximum latency/delay
Note that N is chosen here as 20, but token ring/bus can handle 100s of stations per ring/bus.

## Slide 16: Token Passing - Performance
If only one station is trying to transmit then the time for each transmission is TMIN=TF + TT + 2xTR
  E.g. TMIN = 2.56x10-4 + 1.5x10-6 + 2x6.25x10-6 = 2.70x10-4 sec
  Utilisation is 2.56x10-4  2.70x10-4 = 95%
  … but diminishes when ring length increases
If all stations are trying to transmit the system behaves like TDM
At light loads, CSMA-CD tends to be more efficient
At heavy loads, token passing wins
Notes: At light loads the time for the token to circulate back to a transmitting station becomes significant; it imposes an unnecessary gap between transmissions.
At heavy loads, when every station has something to transmit, token passing allocates the network to each station in turn and so behaves like TDM. Arguably, this is fair. It also allows the utilisation to remain high and there is no throughput collapse as seen with CSMA techniques when the network becomes dominated by collisions.

## Slide 17: Code Division Multiple Access
Division of capacity through use of codes
Complex, difficult to engineer
Good performance – efficient use of bandwidth
Used in wireless networks
Good noise immunity
Bits divided into “chips”
  64 or 128 chips per bit
Each station has a unique (carefully allocated) “chip sequence”
Notes: In the examples here we will assume there are 8 bits per chip. It turns out that the demonstration is simpler if we represent a 1 chip as +1 and a zero chip as –1.
Note that we are now sending 8 signals per bit so we need 8 times the bandwidth we would need with a more conventional encoding. However, things turn out not to be as bad as they seem. Suppose we have a 2Mbps channel and divide this between 20 stations using TDM. Each station will get 100Kbps. Using CDMA the channel delivers 2 Megachips per sec. However, the coding scheme allows each station to transmit at that rate. Assuming 8 chips per bit this gives 250Kbps to each station.

## Slide 18: CDMA Example
Assume 8 chips per bit, 4 stations A-D
  A 00011011 (-1 –1 –1 +1 +1 –1 +1 +1)
  B 00101110 (-1 –1 +1 –1 +1 +1 +1 -1)
  C 01011100 (-1 +1 –1 +1 +1 +1 –1 -1)
  D 01000010 (-1 +1 –1 –1 –1 –1 +1 -1)
Chip sets are “orthogonal” e.g.
  A.C = (-1.-1 + -1.+1 + -1.-1 + +1.+1 +
  +1.+1 + -1.+1 + +1.-1 + +1.-1)/8
  = (+1 + -1 + +1 + +1 + +1 + -1 + -1 + -1)/8 = 0
To transmit a ‘1’ send the chip set. To transmit a ‘0’ send the complement.
Notes: Chip sets are carefully chosen to be orthogonal. I.e. the normalised inner product of any pair is zero. This means that when we compare two chip sets we find as many pairs the same as we find different.
To send a ‘1’ a station sends its chip set; so A sends (-1 –1 –1 +1 +1 –1 +1 +1)
To send a ‘0’ a station sends the complement; so A sends (+1 +1 +1 -1 -1 +1 -1 -1)
Note that,

## Slide 19: CDMA Example [2]
Suppose A sends ‘1’, C ‘0’ and D ‘1’
Combined signal will be:
  A 1: -1 –1 –1 +1 +1 –1 +1 +1
  C 0: +1 -1 +1 -1 -1 -1 +1 +1
  D 1: -1 +1 –1 –1 –1 –1 +1 –1
  S : -1 –1 –1 –1 –1 –3 +3 +1
  S : -1 –1 –1 –1 –1 –3 +3 +1
  D : -1 +1 –1 –1 –1 –1 +1 –1
  (+1+-1++1++1++1++3++3+-1)/8 = 1
To retrieve D’s transmission, compute S.D
Note that
Notes: We make two simplifying assumptions; the stations are in bit synchrony and the signals are of equal power so they add in a simple arithmetic way. The slide shows three bits being added. We can then extract whichever station we want simply by forming the inner product with its chip sequence.
In practice neither of our assumptions would be true. We would also have to contend with noise. However, it turns out that, provided the chip sequences are long enough, it is possible for the receiver to synchronise with the bits from an individual station. We can also cope with unequal power provided this is constrained to some limit.