## Slide 1: Internet Transport Protocols
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Transport Ports
Interface on host – identified by IP address
Processes on hosts – identified by “ports”
  16 bit number
Process D
Etc.
UDP Module
IP Module
TCP Module
Process A
Process B
Process C
IP “protocol” field
May be several processes using the same destination port.
Transport protocol destination ports + IP addresses
Notes: Consider an incoming IP datagram. Conceptually the, processing is as follows.
Initial handling is by the IP module in the host OS which will deal with issues concerning fragmentation and addressing – should the frame be forwarded elsewhere for example. If all is in order, the IP module must decide which transport module should handle the datagram contents. This is determined by the protocol field in the IP header (TCP. UDP, etc.). The transport module will then do whatever protocol processing is necessary and will determine which OS process should handle the data part of the transport PDU. This is the purpose of the “source and destination port” fields in the Transport PDU header.
There may be several processes handling the same port. This would happen, for example, where a web server spawns a new process to handle each incoming HTTP request. This could lead to several concurrent processes handling port 80, each one handling an individual TCP connection. In such cases the source port and IP address fields will be relevant in selecting the process.

## Slide 3: Port Processing
S1234, D59
D1234, S59
Source/destination ports swapped on reply
S1234, D59
D1234, S59
S1238, D59
D1238, S59
A
X
B
Client must choose new source port for each process
Server must also check source IP address
… and destination IP address
Notes: The slide shows the most common cases. In principle a client can use the same source port when sending to two different destinations. However, it is possible that the the two destinations, whilst they have different IP addresses, are both interfaces to the same host. Therefore the destination IP address also must be checked on receipt of a packet.

## Slide 4: Port Processing
Well-known ports
  Allocated by IANA (see /etc/services on Unix)
  Servers “listen” on these ports
  Clients use these as destination ports.
Ephemeral ports
  Chosen as source ports by clients for life-time of “session”
  Locally unique
Source – destination swapped in replies
Source/dest. IP + source/dest. port globally unique
Notes: “Session” here could mean a TCP connection but it could also mean a stream of UDP packets all belonging to the same application instance.
Note the last point; within the Internet architecture four pieces of information are needed to identify a “session”.

## Slide 5: UDP
Connectionless, unreliable, unordered, datagram service
  No error control, no flow control, no congestion control
Port numbers
Header checksum
0
8
16
24
(31)
Source Port
Destination Port
Checksum
Length
Data
Notes: UDP provides an unreliable, connectionless datagram service. It does not guarantee delivery or ordering, and individual packets may be duplicated within the network. Exactly how “unreliable” the service is depends very much on the network environment. In a lightly loaded LAN, it is unlikely that you will observe much packet loss. Across a wide area backbone, however, there may be significant packet loss, especially over paths involving large numbers of routers or heavily loaded routes.
UDP is used as a transport protocol for many “streaming” type applications in which the jitter that would be introduced by TCP’s ARQ protocol would be unacceptable.

## Slide 6: TCP PDU Format
urg check urgent ptr field
ack check ack num. field
psh push
rst reset
syn synchronise seq num.
fin no more data
0
8
16
24
(31)
Source Port
Destination Port
Sequence Number
Acknowledgement Number
Flags
Reserved
Offset
Window
Urgent Pointer
Checksum
Options
…
Data
…
Notes: The sequence number field carries a 32-bit unsigned number indicating the number of the first byte in the data. The acknowledgement number field also contains a sequence number and indicates the next byte that the sender expects. It is only significant if the ACK flag is set. In this way, TCP ACKs can be piggy-backed on data segments. The window field indicates the number of bytes (starting at acknowledgement number) that the sender of this header is willing to accept currently.
The data offset indicates the number of 32-bit words in the TCP header (i.e. the start of the data). This is normally 20 but will be more if any options are used.
The window field is used in the variable window flow control.
The SYN flag effectively asks for a synchronisation of sequence numbers and is used at connection establishment. The FIN flag indicates that there will be no more data transmitted by from the sender (but some may be in transit). The PSH flag indicates that the data should not be buffered but delivered immediately (pushed) to the TCP user. The RST flag indicates that the connection should be reset. This is normally an abnormal termination.
Various options are available, the most popular being maximum segment size negotiation (4 bytes required), timestamp (10 bytes required), use of selective acknowledgement (SACK), and window size scale factor (requires 3 bytes).

## Slide 7: Three-way handshake
PE A sends a SYN which is delayed for a long time
PE A repeats the SYN
PE B responds with a SYN + ACK 101
PE A responds with an ACK
  The connection is now used
The original SYN arrives at PE B
PE B responds with a SYN + ACK 101
PE A recognises the old ACK no. and does not send an ACK
No connection is set up!
Notes: The slide shows a TCP connection being set up. A TCP PDU with the SYN flag set is sent by PE A (with Initial Sequence Number (ISN) 100). This is long-delayed finally to be delivered at c. Meanwhile, a second attempt to establish the connection succeeds and, we suppose, the connection is used and terminates successfully. Note that PE B responds to the SYN at a by sending a SYN PDU containing its own ISN (200) and acknowledging PE B’s (ACK 101; TCP insists that the value is incremented by 1 in the ACK). PE A then responds at b with the third part of the so-called “three-way handshake”. This simply acknowledges PE B’s choice of ISN (ACK 201).
To see why this third PDU is necessary, consider what happens when the original SYN PDU finishes its wanderings and arrives at PE B, what should PE B do? In fact, there is no way that PE B can appreciate that this is an ancient PDU – it is not practicable for it to keep track of all the ISNs used by every remote PE. In any case, it is possible that PE A is behaving badly and re-using an ISN in a genuinely new connection request. Therefore, PE B must assume that the event at c is a request for a new connection and must respond (SYN 300, ACK 101). Fortunately, PE A does appreciate that ACK 101 is no longer valid – i.e. it does keep track of its own ISNs. Therefore, PE A does not send an ACK 301 back to PE B at d. PE B will consider that the connection is not correctly established and will drop it. Thus, the three-way handshake prevents the establishment of spurious connections as a consequence of delayed SYN PDUs.

## Slide 8: TCP ARQ operation
Sequence and ack numbers measure bytes, not PDUs
Initial SN chosen to be different from any used in the recent past
Transmitter normally uses go-back-N strategy
  Selective retransmission option
Receiver buffers all PDUs that are “in the window”
  Acks normally cumulative but there is a SACK option
Receiver may vary the receive window in order to control the flow
  “Variable-window flow control”

## Slide 9: TCP retransmission strategy
Retransmission after a timeout – how long should the retransmit timeout (RTO) be?
  Difficult to estimate – RTT may vary greatly
Originally
Where R is the RTT estimate and M is the measured RTT. =0.9, =2.
Improved (Jacobson)
D is a smoothed estimate of the mean deviation from the mean. R and M are as before. =0.875, h=0.25
Notes: Jacobson (1988) showed original approach could not follow wide variations in RTT leading to overlong timeouts (hence delays) or short timeouts and unnecessary retransmissions.
Jacobson’s improved method calculates a smoothed estimate of the variance (in fact the mean deviation from the mean which is a good estimator for the variance and is easy to calculate) and uses this to adjust the RTO with respect to the estimated RTT. When the variance is high, RTO moves away from the estimated RTT. The algorithm and constants used are carefully designed to enable implementation by integer arithmetic.
These formulae make use of “Exponentially Weighted Moving Averages”.
It can be seen that successive multiplication by  reduces the weight given to older measurements. Note that:
which has the same form as the formulae above.

## Slide 10: TCP congestion control
No congestion control in IP
  No reliable way for router to report congestion
Layers above IP must have congestion control
  Detect congestion through lost or delayed ACKs
  Slow down!
TCP has built-in congestion control:
  all TCP implementations have (roughly) the same congestion control algorithm
Real-time applications (e.g. using RTP):
  congestion control must be part of application
Notes: IP provides a simple datagram delivery service. Packets may be lost when the network is heavily loaded due to congestion. This is when more packets are arriving at an IP router than it can process and/or buffer, so it drops packets. However, IP does not include any reliable mechanism of explicitly reporting such congestion occurrences. So, the layers above IP must devise their own methods of spotting such occurrences and react accordingly (e.g. reduce the transmission rate), otherwise the network will undergo congestion collapse.
TCP uses a congestion control mechanism based on lost or delayed ACKs. The assumption is that a lost or delayed ACK is due to congestion in the network. As all TCP implementations should implement the same congestion control algorithm, and the user has no control over the way in which the algorithm works, it should result in fair-share of the network resources. Indeed, it has been observed that today’s TCP congestion control does a reasonable job.
The congestion control mechanism in TCP that has evolved over the years. We will consider the very basic operation, but the full mechanism is more sophisticated and complex (see RFC2581 for more details).
Note that real-time applications – that do not use TCP – must have their own congestion control mechanisms.

## Slide 11: How to fill a router’s buffers
HB
HA starts with a w=8
  Has to stop at a
8 packets buffered at R
Packet 1 acked at b
  One further transmission
HA sends 1 packet per RTT
Always 8 packets at R!
…
w = 8
HA
R
1 Gbps
100 Mbps
a
b
Notes: The slide shows a simple scenario involving two hosts a router and links which differ in capacity by a factor of 10. We would refer to the right-hand link as the “bottle-neck” link.
We can see that HA’s initial burst of 8 packets is pointless, all it does is to fill up buffers at R. The protocol will settle into a mode in which the HA receives acks at a rate determined by the packet transmission time on the bottle-neck link. Each ack triggers the transmission of 1 packet. There will always be 8 packets buffered at R.
Such behaviour is likely to lead to congestion at R – i.e. it will run out of buffers and will begin to discard packets. Ideally HA should detect this as soon as it begins and should slow down – i.e. it should adopt a smaller window. This is the purpose of the TCP “slow-start” algorithm.

## Slide 12: TCP slow start
Two windows
  wnd – the normal receive window (in segments)
  cwnd – initially 1 segment, increase by 1 for each ACK received
  Transmit window min(cwnd, wnd)
0
100
200
300
400
500
600
700
800
900
1
1
2
2
3
3
4
4
5
5
6
6
7
7
8
Time s
cwnd
RTT 150 s
Tx time on slow link 100 s
Notes: Although TCP windows are measured in bytes it is more convenient in this context to imagine them measured in “segments” – a segment being the amount of data TCP puts into one packet.
The slide illustrates the progression of cwnd in the scenario on the previous slide. We assume a minimum RTT of 150 s and a transmit time on the slow link of 100 s. The diagram shows the approximate interval between a segment transmission and receipt of the corresponding ack. Note that this can never be less than 150 s. Also, as we observed previously, the interval between two acks cannot be less than 100 s. Thus segment 2 takes 150 s whilst 3 takes 250 s. To illustrate what happens, consider the receipt of the ack for 2 at 300 s. cwnd increases to 3 so that 3, 4 and 5 are now in the window. 3 has already been sent but we can now send 4 and 5.
Note that:
  ack 1 triggers the transmission of segments 2,3
  acks 2,3 trigger the transmission of 4, 5, 6, 7
  acks 4, 5, 6, 7 will trigger the transmission of 8 – 15
Thus cwnd increases roughly exponentially.
Eventually cwnd  wnd at which point cwnd is no longer relevant. Further, in this particular example, the queue at the router will fill causing packets to be dropped. See next slide for what happens then.

## Slide 13: TCP congestion avoidance
Maintain an estimate of RTD
A delayed or duplicated ACK is taken to imply congestion
On congestion: sthresh = wnd/2, cwnd = 1
on ACK: if cwnd  sthresh cwnd = cwnd+1
else cwnd = cwnd + 1/cwnd
Thus we do slow start until a threshold, thereafter a more conservative strategy
cwnd grows exponentially
cwnd grows linearly (cwnd ACKs increases cwnd by 1)
Notes: Congestion avoidance is triggered by detection of an increased RTT. This will be seen either as a delayed ACK or as a duplicate ACK (the latter implying an unnecessary retransmission). When this happens, the transmitter begins to slow start.
The slow start strategy of increasing cwnd by 1 segment each time an ACK is received has the effect of roughly doubling cwnd each round-trip time. (See previous slide). This rapid increase in cwnd continues until a threshold at which point a more conservative strategy is adopted. This adds 1/cwnd to cwnd each time an ACK is received. Thus n ACKs result in an increase to cwnd of n * 1/n = 1 each RTD. So, we switch from an exponential to a linear increase in time.
The expectation is that if all TCP connections through the congested node adopt this strategy then the reduction in traffic will cure the congestion.

## Slide 14: TCP congestion avoidance [2]
Resulting flow is far from steady
  Saw-tooth pattern
Non-TCP traffic should be “TCP friendly”
  Try to emulate TCP behaviour
wnd
sthresh
Slow start
“Normal”
C
C
C
time
Progression of effective tx window
Notes: The slide shows how the effective transmitter window, min(cwnd, wnd), might vary. Note that we are keeping wnd constant – i.e. the receiver is not varying it for flow-control purposes.
Non-TCP traffic like voice should try to behave in a similar way – for example, drop to a lower quality encoding when congestion is experienced.