## Slide 1: Wireless Technologies (Support Material)
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Carrier Sense Multiple Access
“Listen before speaking”
Avoids collisions?
Time
t0
t0+T
bit 1
bit F
time
A
B
D
p
t
bit 1
No!
  (but it helps)
Notes: If a station continuously monitors the network it can discover when another station is transmitting and can defer its own transmission until the network is silent. This avoids many collisions. The buzz phrase for this is "carrier sense".
Carrier sense does not avoid all collisions. The problem is that propagation delay ensures that another station's transmission may already have begun (legitimately) but has not yet reached us (see slide). The longer the propagation delay, the more likely this is to happen. In the extreme case of a satellite network, the propagation delay is about 240ms. Listening to the network may tell us that the network was silent 240ms ago but it does not help us to know what is happening now. Carrier sense cannot be used in such networks.
However, provided the propagation delay is low, CSMA. gains a lot over. x .Aloha as we will see. This is the situation for most LANs (both wired and wireless) where the maximum distance between stations is nearly always less than a few Km. For example, the propagation delay on a 2Km optical fibre is 20003x108 = 6.7s. At 10Mbps only 67 bits can be transmitted in this time - a very small portion of the size of the average packet. However, note that at 1Gbps, a speed that is available commercially, 6700 bits or 837 bytes can be transmitted in 6.7s - a sizeable portion of a packet.

## Slide 3: Non-persistent CSMA (CSMA/CA)
If stations transmit immediately the medium goes quiet there will be many collisions
Non persistent – “if medium is busy wait a random time and retry”
Transmit here
Persistent
Frame available
Non-Persistent
Listen and transmit here
Random time
Frame available
Notes: The naive CSMA strategy is for a station to wait until the medium is silent then begin transmission immediately. This is called "persistent CSMA". The problem with this strategy is that if two or more stations are waiting, they will almost certainly collide when they begin transmission. (Here we should note that the diagram above omits a potentially important detail; namely that it takes some time for the fact that the network is silent to propagate to all stations. Thus there must always be an interval between the end of one transmission and the beginning of the next. For the purpose of this discussion we assume a very small propagation delay so that this interval may be neglected). It should be clear that, when network load is heavy, persistent CSMA will generate very many collisions so that throughput will drop.
Several solutions to this problem have been studied. One approach is "non-persistent CSMA". Here a station which finds the network busy "backs off' i.e. it waits a random time before listening again which should avoid the type of collisions mentioned above. For this reason non-presistent CSMA is an example of CSMA with collision avoidance (CSMA/CA). The effectiveness of this strategy is examined in the next slide.
Another approach is "p-persistent CSMA". Here a station continues to listen to a busy network waiting for it to become silent. When it does so, the station transmits with a probability p, defers (i.e. waits a random time) with
PTO

## Slide 4: Collision detection
In CSMA, collisions last one frame time
  Why not stop once a collision is detected?
  How long does it take to detect a collision?
time
A
B
bit 1
p
bit 1
p
bit F
t
Answer: 2p
Provided t >> 2p and collisions are frequent, CD is worthwhile
Notes: a probability (1-p). If p is 1 we have persistent CSMA, If p is (say) 0.5, then two stations both waiting for silence will collide with probability 0.25. The downside is that they will both defer with probability 0.25 leading to an unnecessary delay.
Note. We are considering here the strategy to be adopted when a station finds that the network is busy and defers its transmission. Do not confuse this with the strategy to be adopted when, despite our efforts, a collision does occur. In particular, note that CSMA-CD (see later) handles collisions in a way which resembles that used by non-persistent CSMA to handle deferrals.
With both persistent and non-persistent CSMA a collision costs us one frame time. If we were to detect collisions as soon as we could and immediately stop transmission we would waste less time. Is this complication worthwhile?
The diagram shows the worst case in which B starts to transmit just before the first bit of A's transmission arrives. This takes one propagation delay p. However, at this point A is unaware of the collision and will not become aware until the first bit of B's transmission reaches A. This takes another time p. Thus, in the worst case it takes 2p to detect a collision where p is the maximum propagation delay between two stations. So, if we add collision detection, the time wasted in a collision reduces from t to 2p.

## Slide 5: Reservation ALOHA
Pure ALOHA 18.4% utilisation, slotted 36.8%
  Can we do better?
R-ALOHA – start as TDM, one slot per channel
A
B
C
D
A
B
C
A
D
…
Time
A
A
C
D
A
A
C
A
D
…
A
A/B
C
D
A
B
C
A
D
…
B is not using its slot – other stations may contend. A reserves B’s slot
B regains its slot by contending with A
Notes: Reservation ALOHA builds on the likelihood that since traffic is bursty; a channel which is currently free will probably remain so for a while, one that is busy will probably remain busy.
Each channel owns a slot and if all are busy the system works exactly like TDM with timeslots allocated to stations in strict rotation. The rule though, is that if a channel does not use its slot this time round then the slot is available to all the other channels next time round on a contention basis. If this results in a collision, then all stations except the owner must desist in the next round. This means that an owner can always grab its slot back simply by transmitting in it. At worst, there will be one slot lost to a collision before ownership is resumed. In the slide, channel B looses its slot to A then claims it back.
Obviously the stations must be closely synchronised for this to work. However this can easily be achieved by having the PAU transmit timing pulses.
The main defects of R-ALOHA are:
  The number of stations must be known in advance
  Collisions are still relatively expensive, destroying complete slots when they occur.

## Slide 6: Non-persistent CSMA throughput (1)
The arrows show instances of attempted transmissions
  Long arrows show “network busy” and result in deferrals
  Normalised load rate G = D + S
Assume all frames are the same length
Ideally, at full load, deliver 1 frame/frame time (U=1)
Suppose successful delivery rate S frame /frame time (U=S<1)
Not all transmission attempts succeed:
  Some are deferred at the rate D frame /frame time
  Some collide – we can ignore these at light loads
time
Rate D
Rate S
Notes: In this analysis we assume that the collision rate is negligible. This is reasonable provided we have a low propagation delay. (N.B. remember to distinguish between "network busy" and "collision". The former certainly occur, it is the latter we claim are negligible.)
We assume all frames are the same length and so take the same time to transmit. It is convenient to take this time as the unit of time in the calculation.
The load is G frames per frame time. “Arrivals” (i.e. attempts by some station to transmit) are represented by the arrows in the diagram. A portion of arrivals encounter a free network and are delivered at rate S / frame time. The remaining frames encounter a busy network and are deferred at a rate D / frame time. Clearly G = D + S.

## Slide 7: Non-persistent CSMA throughput (2)
time
Rate D
Rate S
Network is busy for a fraction S of the time
P(arrival encounters a busy network) = S
Rate of “busy” arrivals = GS = D
Notes: The fact that we deliver S packets in unit time means the network is busy for a fraction S of the total time. It follows that a fraction S of the offered packets will encounter a busy network. Thus D = GS.
Combining these two results we have:
Actually, there is a possible flaw in this argument. If deferred transmissions were very likely to be retried after a very short interval we would get many more "busy" events than the proportion S would suggest since the retry would find the same transmission still in progress. However, it turns out that, if we assume that both the process generating packets and the process governing the random deferral times are both negative exponential, then their combined distribution will also be negative exponential. In this case, the proportionality argument is valid and the result stands.

## Slide 8: FDMA
0
1
2
3
5
4
6
time
frequency channel number
Channel allocation:
  fixed number of frequency channels
  signalling channel
  source requests a channel
PAU:
  listens on signalling channel (0) for requests
  assigns channel to source
  source uses channel for a single frame
Notes: As with TDMA, the term frequency division multiple access (FDMA) can be applied to any channel allocation scheme which uses a broadband channel sub-divided into several frequency bands – including classical FDM. However, the term is most often applied to schemes which allocate frequency bands for short periods in arbitrary ways.
The frequency division multiple access (FDMA) scheme is used only with radio systems. (In principle, it could be used with infra-red, but this is not currently practical for low cost LAN transceivers.) A PAU is required to control operation of the scheme. In FDMA, the available RF spectrum is split into separate RF channels with a separate, single channel used for signalling.
When a station wants to transmit, it makes a request for a channel by use of the signalling channel. A channel for the data transmission is then allocated to the station by the PAU. The channel is allocated for the duration of the transmission of one data frame, after which it becomes available for use by another station. The transmitter must signal the PAU for another channel allocation to send more data.
Multiple transmissions can occur simultaneously, but each transmission does not get use of the whole RF bandwidth. In the slide there are there separate channel requests, with the first and third request from the same station.

## Slide 9: IEEE 802.11b power management
Two modes:
  active
  power save (PS)
Station can tell AP it is entering PS mode:
  power mode message sent when changing power modes
AP actions:
  AP tracks station power mode
  AP can buffer packets
  AP can send beacon to indicate which stations have data waiting
Wireless devices may be mobile
Batteries => limited power
Notes: Again, CSMA/CA or ALOHA can be used for the signalling channel.
Notice that this scheme actually combines FDMA and TDMA since each RF channel operates as a TDMA channel. Stations using this scheme must be “frequency agile” so that they can send and receive on any of the frequencies in use.
AP: access point
PS: power save

## Slide 10: Bluetooth - Rationale
Standard, convenient device interconnectivity
Mobile phones,headsets, PDAs, laptops:
  coffee machines, utility meters, hi-fi equipment, etc.
Simple, low-cost, radio-based system:
  simple, “wire-replacement” system, re-use existing standards
  aiming for cost of ~US$5 to build into a device
  uses ISM radio band (2.4000-2.4835GHz)
http://www.bluetooth.com/
Named after a Viking called Harald Bluetooth
Notes: Bluetooth was initially developed by Ericsson as an always-on short-range radio link that could be implemented on a chip.

## Slide 11: Bluetooth usage examples
from http://www.bluetooth.com/bluetoothguide/models/two_in_one.asp

## Slide 12: Relationships
Master/slave
Slave can only talk to master
Slave can only talk with permission
M/S
M
S
S
S
S
S
Piconet
Scatternet
Master + up to 7 active slaves = “piconet”
Devices can be member of several piconets
  “scatternet”
Notes: The master:
  Initiates the formation of a piconet
  Determines the hopping sequence to be used within the piconet (FHSS)
  Provides synchronisation for TDM
  Initiates all communication (polling)
  May be a member of other piconets either as slave or master
A slave:
  Speaks only when spoken to
  Speaks only to the master
  May be a member of other piconets either as slave or master

## Slide 13: Relationships [2]
BD_ADDR: 48 bit – globally unique
AM_ADDR: 3 bit – identifies active slave
PM_ADDR:8-bit – identifies inactive slave
At power on:
  in standby (sniff mode)
  listen every 1.28s
  check one of 32 hop frequencies for other devices
If address of another device known:
  send PAGE message
If address not known:
  send INQUIRY message
SDP is used to discover device capabilities
Notes: BD_ADDR Bluetooth Device Address
AM_ADDR Active Member Address
PM_ADDR Parked Member Address
SDP service discovery protocol

## Slide 14: Physical layer
2.402-2.480GHz (Unlicensed)
  minor change in ES, FR, JP)
FHSS
  79 channels (23 channels, ES, FR, JP)
  1MHz spacing
  Hop rate – 1600 hops/s
Possible interference:
  2.4GHz band used by IEEE802.11 wireless LANs
Hopping sequence derived from master’s unique address
FHSS ameliorates interference from adjacent piconets

## Slide 15: Baseband Protocol
FHSS hop rate (1600 hops/s) defines timeslots
  625s timeslot
  Slots used in TDM scheme
Time Division Duplex (TDD)
  Master/slave take turns
  Master uses even slots, slave uses odd slots
Most frames fit into one slot
  3 and 5 slot frames allowed
fk
fk
fk
fk+3
fk+4
fk
fk+1
fk+2
fk+3
fk+4
Notes: The diagram show slot usage by one device. The empty slots would normally be used by the correspondent.
fk, fk+1 etc. are the frequencies used within the hopping sequence. Note that, although a multi-slot frame spans several slots and uses the same frequency throughout, the original hopping sequence is subsequently restored.

## Slide 16: Baseband Protocol[2]
General packet format
Header:
  AM_ADDR (3)
  type (4)
  flow control (1)
  ARQN (1)
  SEQN (1)
  HEC (8)
Access code:
  provides receiver sync
Payload:
  indicates length and number of timeslots that will be used
  contains CRC
  if FEC used used, 5 parity bits added after each 10 bits, including CRC bits
  padding may be required for FEC usage
access code
header
payload
72bits
54bits
0-2745 bits
Notes: AM_ADDR active member address
ARQN automatic repeat request number
HEC header error correction
SEQN sequence number

## Slide 17: Baseband Protocol[2]
SCO
Packet-based
Mainly for voice
Upto 3 simultaneous channels supported (64Kb/s each)
Can be used in parallel with an ACL channel
ACL
For data
Asymmetric:
  721Kb/s (either direction) + 57.6Kb/s reverse direction
Symmetric:
  432.6Kb/s
“Links” are built on the basic timeslot structure
Two types:
Notes: ACL asynchronous connectionless
SCO synchronous connection oriented
SCO links allocate a fixed capacity between master and a single slave. Pairs of slots are reserved at regular intervals in order to provide constant bit-rate. There is no error control.
There is just one ACL link between master and all slaves. In general, there is error control.

## Slide 18: Error correction and Flow Control
3 options:
  1/3 rate FEC
  2/3 rate FEC
  CRC + ARQ
Packet header:
  always uses 1/3 rate FEC
Data:
  2/3 rate FEC
  (15,10) shortened Hamming code
  Corrects all 1-bit errors in 10 bits and detects all 2-bit errors
  may need 0-9 bits of padding
CRC + ARQ:
  (not always used)
  ACK or NAK for each pkt
  Un-numbered scheme, i.e. stop-wait scheme
Stop/Go Flow control
Notes: ARQ automatic repeat request
CRC cyclic redundancy check
FEC forward error correction
Baseband layer provides error correction and flow control. Several techniques are combined different techniques are applied to different frame types and to different fields within frames.
1/3 rate FEC means sending each bit in triplicate – majority wins
So-called “Fast ARQ”. ACK or NACK must be transmitted in timeslot following DATA. If ACK not received in following timeslot, DATA is retransmitted.

## Slide 19: Protocol architecture [1]
L2CAP
BASEBAND
Bluetooth Radio
LMP
Audio
RFCOMM
PPP
IP
TCP + UDP
AT commands
TCS binary
SDP
Bluetooth core protocol
host
controller
interface
adopted protocol
Notes: LMP link manager protocol
L2CAP logical link and control adaptation protocol
PPP point-to-point protocol
RFCOMM serial cable replacement protocol
SDP service discovery protocol
TCS telephony control protocol

## Slide 20: Protocol architecture [2]
LMP:
  link setup
  authentication
  power mode control
  connection states in piconet (master or slave)
SDP:
  selects usage model or profile
  exchange of device capability information
RFCOMM
  Emulates serial ports over L2CAP
  RS232 Emulation
  Multiple emulations per device
Notes: LMP link manager protocol
SDP service discovery protocol
RFCOMM serial line replacement protocol

## Slide 21: L2CAP Functions
Protocol discrimination
  “Type field”
Segmentation and re-assembly
QoS
  Flowspec based on RFC 1363
Groups
  Provides broadcast within a piconet
Channels
  CO – full duplex
  CL – used for group communication
  Signalling
Built on ACL link
No error or flow control
  Rely on baseband
Notes: Similar aims to LLC in IEEE 802 – hides technology-specific features of baseband behind “standard” link-layer interface.
Many applications set up CO channels between master and slave. These provide full-duplex, QoS controlled channels.
CO channel is used for group communication (multicast). It allows higher levels to address packets to the whole piconet.

## Slide 22: Power modes
Different power modes:
  conserve battery life
Active mode:
  normal operation
Sniff mode:
  less power than active mode
  listen to network
  e.g. standby
Hold mode:
  less power than sniff mode
  clock remains sync’d
  e.g. inactive slave, retains 8-bit piconet address
Park mode:
  less power than hold mode
  no contact with master
  does not retain piconet addr

## Slide 23: Interface support
Can emulate different interface protocols, e.g.:
  USB
  RS232
  PC card (for laptops)
Uses a serial cable emulation protocol:
  allows use of PPP etc.
Allows use of telephony protocols:
  TCS binary
  Hayes AT commands
Notes: PPP point-to-point protocol
TCS telephony control protocol
USB universal serial bus

## Slide 24: Example usage models
Dial-up networking:
  serial line emulation
  e.g. wireless modem for access
LAN access:
  dial-up server emulation
  e.g. wireless access point for multiple users
L2CAP
RFCOMM
PPP
AT commands
SDP
L2CAP
RFCOMM
PPP
SDP
IP
modem emulator or driver
LAN access application