## Slide 1: A Brief Introduction to Queuing Theory
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Queuing Systems
A number of “servers”
A number of “queues”
Traffic patterns
The simplest system has
  Single server
  Single queue
  Negative Exponential process
Notes: In many situations in computer communications and networks, there is competition for some resource. The competitors are usually frames or packets, of varying sizes, which arrive at unpredictable moments and compete for access to a transmission channel. These situations can be analysed mathematically using a branch of statistics called “queuing theory”. The results obtained play an extremely important rôle in the correct design of computer networks and components. This section considers only the simplest cases, however, even these are often of practical use.
The simplest system (on which we shall concentrate) has a single “server” and a single “queue” (think of a small sub-Post Office on pensions day). More complicated systems involve multiple servers with a single queue and multiple servers with multiple queues.

## Slide 3: Example – a sub-post-office
Average arrival rate might be 12 customers/hour (0.2 cust./min)
  Reciprocal of the average arrival rate gives the average inter-arrival time -> 5 minutes
Server might be able to serve 15 customers/hour (0.25 cust./min) (Average Service Rate)
  Reciprocal of the average service rate gives the average service time -> 4 minutes
Actual inter-arrival and service times will vary - but how?
Notes: If customers arrive at intervals of exactly 5 minutes and each takes exactly 4 minutes to serve then we never get a queue and the situation is extremely uninteresting. In practice, customers do not behave in this convenient way. Although the average inter-arrival time might be 5 minutes, there will be considerable fluctuations around this value and the same is true for service times. Generally speaking, the more these times vary from the mean the more we would expect the queue length to fluctuate.
Note that the average service rate must be more than the average arrival rate or the queue will eventually grow without limit.

## Slide 4: (Rough) Analysis
Customer (packet) being served
Customers (packets) “in the system”
System in state S5
Customer (packet) being served
Customers (packets) “in the system”
Event A5
Customer (packet) service completed
Customers (packets) “in the system”
Event C5
Notes: The state of the system is characterised by the number of “customers” in the system – n. Note that this includes the customer currently being served.
In our case the customers will often be packets queued up in memory awaiting transmission. The “service” consists of transmitting a packet and the service time will be proportional to the length of the packet.
Two types of event are of interest; the arrival of a new customer and the completion of the service of a customer. These correspond to state transitions Sn->Sn+1 and Sn-> Sn-1 respectively and we denote them by An and Cn.

## Slide 5: (Rough) Analysis [2]
Denote mean arrival rate by λ, mean service rate by μ
Denote “utilisation” by ρ where ρ = λ/μ
Assume λ and μ are constant – i.e. arrival and service rates are not affected by number in the system
Assume inter-arrival and service times are independent – i.e. a long inter-arrival time does not make it more likely that the next one will be short
Would like to know
  P(n customers in the system), mean time in system, etc.
Notes: In this context “utilisation” is a measure of the proportion of the time the server is busy. For the post-office example ρ = 0.2/0.25 = 0.8 = 80%
The assumptions in the third and fourth bullet points are vital for the simplicity of the analysis though they may often be unrealistic in practice. For example, a short queue of packets at a switch may have been caused by packets being held up elsewhere. In such a case we may expect a burst of packets once the hold-up clears – i.e. we expect λ to be higher (and inter-arrival times to be shorter) than normal for a while.

## Slide 6: (Rough) Analysis [3]
Probability there are n in the system is denoted by Pn
Example: post office (λ=12 per hour) and suppose P2=0.128
  I.e. 2 people in the post office 12.8% of the time
  I.e. 12.8% of arrivals will find 2 people in the post office
  State “2” arrivals occur at rate 12.8% of 12 = 1.536 per hour
SO … At what rate does event An occur?
  An occurs at the rate Pn.λ
At what rate does event Cn occur?
  Note that C0 never occurs!
  For n>0 (i.e. there is a customer waiting to be served) Cn occurs at the rate Pn.μ
Assume we reach a “steady state” – i.e. over a long period mean queue length remains constant
Notes: Analysis proceeds by considering the rates at which the different events occur.
As an example of the reasoning above, consider the post office with  = 0.2 and suppose P2 = 0.128. We expect to be in state S2 for 12.8% of the time so that 12.8% of the arrivals will occur when we are in state S2 – these are our C2 events. Therefore, C2 events a occur at the rate 12.8% of  - i.e. at P2. .

## Slide 7: (Rough) Analysis [4]
We must have balance, Sn  Sn+1 must occur as often as Sn+1  Sn
Notes: The state transitions up and down must occur at the same rate so that the queue remains stable when viewed over a long enough period.
We end up summing an infinite geometric series. Not that we assume here that the queue can approach infinity – not realistic.

## Slide 8: M/M/1 - Number in the system
“Number in system” includes customer being served
Mean number in system is
Post Office, N = 4
Notes: To calculate the mean number in the system.

## Slide 9: M/M/1 – Time in the system
Mean time in the system is given by
For the post office this is:
Notes: To calculate the mean time in the system first note that  is the rate at which customers are served as long as there are customers to serve – which sometimes there are not. The rate at which customers leave the system must be  - i.e. everything that enters the system leaves it. From this we see that the mean time between customer departures will be 1/ . We can now calculate the mean time in the system as (mean number in system)x(mean time between departures). This is “Little’s Theorem” which we do not prove – but it is intuitively true.
Delays are very important to us especially in interactive applications. We can see that if  (i.e. the utilisation is high) then the delay will be large.

## Slide 10: M/M/1 – Finite queue
Previous results assumed queue could grow forever
  In practice we have a limit – N say
Probability of n in system is now:
Notes: In practice our queuing systems will have space limitations – e.g. there will be a maximum number of packets we can buffer (max. no. of people in the PO). Any excess will likely be discarded (PO customers will go away). It is important to be able to calculate this probability for a given buffer capacity.
Note that introducing a limit N on the size of the queue means that the probabilities of queue-lengths > N are all zero. This means that the probabilities of queue sizes  N will be greater than those for an infinite queue. (Remember that probabilities must sum to 1).
The analysis proceeds in the same way as for the infinite queue except that we sum over N, thus:

## Slide 11: M/M/1 Queue - Blocking
If customer arrives when there are N in system it will be “blocked”
Probability of blocking is:
We found for a finite queue of size N probability of n in system is:
If post office can only hold 5 customers:
Notes: The “blocking probability” follows naturally from the finite queue result. This is an important statistic for data networks as it tells us the proportion of packets that will be discarded at a router or switch for a given buffer size. (However, remember that the M/M/1 assumptions are not necessarily realistic!)
Formulae for the mean number and time in the system for a finite queue can be derived. However, if we are just interested in a qualitative view of how the system behaves then it is often good enough to assume an infinite queue.

## Slide 12: Throughput
Important concept in data communications:
  Volume passing through system in unit time
Not all bits are the same …
  Some bits are used for addresses, checksums etc.
  Some packets used for management
  Some packets discarded because of congestion
  Some packets lost due to transmission errors
  Some packets are retransmissions
Not part of useful data volume
Not part of throughput
Notes: We often want to maximise “throughput”. Essentially we want to get the maximum useful work from a channel.
The slide shows that the word “useful” is important since the channel also carries other information that, whilst essential, is not part of the useful data from the point of view of the user.
In the next slides we look at the effect on throughput of congestion – i.e. when blocking occurs and packets are discarded.

## Slide 13: Throughput and retransmissions [1]
Must have (throughput)  = (1-PB)
Suppose Tx retransmits discarded packets (e.g. TCP)
If protocol is efficient, Rx receives each packet exactly once, then:
   is the rate at which Tx generates new packets
  - = PB is the rate at which Tx generates retransmitted packets
Tx
Rx
QS
 pps
 pps
PB pps
Notes: When considering a queuing system we regard the throughput as the rate at which customers leave the system. In data communications, the customers are “packets” of data – for example IP datagrams. For an infinite queue no packets are lost hence the throughput equals the arrival rate ( = ). In practice the queue size will be limited by the amount of memory available for storing (= “buffering”) packets. This means that the blocking probability is non zero so that a proportion of arriving packets will be discarded.
The slide shows a very simple system with a transmitting system (Tx - which might be a web server), a queuing system (QS - which might be a router) and a receiving system (Rx - which might be s desk-top computer). Because packets may be discarded Tx and Rx will likely employ a protocol such as TCP to ensure dropped packets are retransmitted. This means that the input to QS consists both of newly generated packets from Tx together with retransmissions of discarded packets.I.E  is the rate of new packets + rate of retransmitted packets.

## Slide 14: Throughput and Retransmissions [2]
The chart shows throughput with  = 1000 pps, N = 5 packets
  As  increases so does PB and hence the discard rate  PB
  When  >> buffer is almost always full so 
   =   onset of congestion (roughly speaking!)
  Retransmissions dominate when  is large
Notes: The chart shows what happens when packets are forced through the system on the previous slide at an increasing rate.
Eventually the buffer is almost always full (e.g. with  = 1500 pps, P0 = 0.048 so buffer is full 95.2% of the time). This means that the server (i.e. the channel between QS and Rx) is almost always busy so  approaches . However, this high utilisation of the output channel comes at the expense of a high retransmission rate which may have a cost on Tx (which has to do more work) and on the channel between Tx and QS (which carries much more traffic). For example we need to send a total of 1500 pps in order to achieve a useful through put of just less than 1000 pps. This may not matter if we have exclusive use of the Tx-QS channel. However, if it is shared then this would be considered wasteful since we could cut back  to (say) 1000 pps with only a small reduction to .

## Slide 15: Throughput and retransmissions [3]
Real networks consist of chains of queuing systems
If QS2 is congested (>) then the retransmission rate (PB) will be high
  So there will be more load on QS1 which may become congested
Tx should slow down (e.g. <) so that PB is small
  Big reduction in  small reduction in 
  N.B. TCP congestion control algorithm
Tx
Rx
QS1
 pps
 pps
PB pps
QS2
Notes: Congestion feeds back through a queuing network as congestion causes discards which causes retransmissions which increases  and causes more congestion. The solution is for the traffic sources (like Tx) to slow down so that the discard rate is low. This is inherent in the TCP protocol (see later in the course) which monitors discards and deliberately slows down its transmission rate when congestion seems to be occurring.
[Warning. It is not really correct to pretend that chains of queuing systems can be modelled as M/M/1 queues since the presence of a queue alters the arrival time distribution invalidating the M/M/1 assumption at succeeding QSs. However, the qualitative aspects of the argument above remain true.]

## Slide 16: Example – Statistical Multiplexing
Frames mean length 150 bytes (= 1200 bits)
10 frames/sec on each input channel
Single FIFO queue,  = 40 f/s (Additive property)
Transmission rate =  = 64000/1200 = 53.33 f/s
64Kbps
Queue
Utilisation =
Mean time in system
Mean number in system
Notes: We assume that a frame arriving on the input channel is immediately queued to the output channel. We expect a queue to form occasionally. This will generally consist of a mixture of frames from the four input channels.
For simple systems we can treat the 4 input processes as one process with λ = 4 x 10 f/s (the so-called additive property).
[N.B. we are assuming an infinite queue.]
Note that this analysis is in terms of frames since this is the unit with which the queuing system deals. Measuring in terms of bits/sec rather than frames/sec will; lead to confusion!

## Slide 17: Example – TDM
As before but output channel divided into four sub-channels by TDM
  Four separate queuing systems  = 10 fr/sec on each
Transmission rate =  = 16000/1200 = 13.33 fr/sec
4x16Kbps
Queues
Utilisation =
Mean time in system
Mean number in system
Notes: If we operate the system as 4 equal-sized sub-channels, one for each input channel, we have 4 separate queuing systems. We see that the average delay will be 4 times greater. Further, we now have 4 queues each as big as the one for the statistical multiplexing case, so we would need 4 times as much memory.
Comparing these results with those of the the previous slide we can see the efficiency of statistical multiplexing – i.e. there is a “statistical gain”. Put another way, we could increase the arrival rate of the statistically multiplexed system (thus improving the utilisation of the output channel) whilst still getting better performance that we got from TDM.

## Slide 18: How much memory?
Table shows blocking probabilities for the statistical multiplexor
20 buffers gives probability of 7.947x10-4 of discard
  Once every 1258 frames.
  at 40 frames per second, once every 31 secs.
Notes: If we run the system as a statistical multiplexor we must decide how much memory to allocate to the queue which may form. The table shows the blocking probabilities for various buffer sizes. Basically we trade-off buffer size against discard probability.
Clearly the more buffers we have, the lower the probability of discarding packets but the longer will be the maximum delay. 20 packets takes 0.37 secs to transmit at 64 Kbps. This may be longer than applications can tolerate or it may trigger a re-transmission timeout somewhere. In short, we may be better off discarding than queuing for this time.

## Slide 19: Statistical Functions
For mathematical completeness …
We assumed inter-arrival and service times were constant and independent.
Can be shown events have a Poisson distribution,
  P(n events in time t)
Can be shown times have Neg. Exponential dist.
  PDF
Single Q, single server, -ve exponential arrival and service times => M/M/1 queuing system
Notes: Many queuing systems have been modelled analytically. We have looked only at the simplest denoted by M/M/1. The bottom bullet point in the slide gives the formal conditions for an M/M/1 system.
The slide states, without derivation, the statistical distributions that apply to the arrival process and the service times.

## Slide 20: Warning!
Very few situations are really M/M/1 queues
  Packet size distributions are not -ve exponential
  Inter-arrival times often very bursty
M/M/1 results just give a rough indication of characteristics
  Time   as    (Slide 9)
  Throughput  0 as    (Slide 14)
When doing calculations work in packets/sec not bits/sec

## Slide 21: Summary
Notes: Note that you are not expected to learn these formulae!