## Slide 1: Sharing Network Resources
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Sharing
Link sharing
Network sharing
Notes: The key to efficient data communications is the efficient sharing of physical resources such as wires or the “spectrum”. It is rarely the case that a resource should be dedicated to a single activity. For example: a single optical fibre has the capacity to carry literally millions of simultaneous telephone conversations; a WiFi network can carry data from dozens of computers.
In this context “sharing” is often termed “multiplexing” and there is a host of techniques available to achieve it. In this section we look at a few of the techniques that are used within so-called “switched” networks – i.e. those that are built from “switches” connected by “links”.

## Slide 3: A little history
1837 The telegraph (Cooke and Wheatstone)
1838 Morse code (Samuel Morse)
  Electronic digital communication
1843 Facsimile transmission
  Data communication
1865 Commercial facsimile transmission
1876 The telephone (Alexander Graham Bell)
  Analogue voice
1878 First commercial telephone exchange
Analogue telephone network grew and grew …
Notes: Long-distance electronic communication began in 1837 when William Cooke and Charles Wheatstone invented the telegraph. This grew into a large, successful, international network mainly carrying text encoded in "Morse Code" (invented by Samuel Morse in 1838). In 1876, Alexander Graham Bell invented the telephone to carry voice over wires and, in 1878, installed the first telephone exchange in New Haven, Connecticut. From this grew an enormous world-wide communications network and a new engineering discipline - "telecommunications". Telecommunications engineers deal with the all aspects of the design, construction and operation of telecommunications networks. This includes the exchanges or "switches", and the basic physics of propagating information via waves carried in wires or some other medium. Until quite recently, in most countries, the telecommunication network was an effective monopoly, usually owned by the Government. It deployed some large, high-cost equipment, was tightly managed and carefully planned Whilst the network was complex, the equipment connected to it was usually very simple - a basic analogue telephone. Only today, has the dominance of voice traffic on world-wide telecommunications networks begun to be challenged by data traffic. However, there has always been some data traffic. Fax, for example, pre-dates the telephone having been invented in 1843 with the first commercial usage in 1865. More recently, Telex provided a simple text-based service on the telecommunications network.

## Slide 4: A little more history
1960s communication between computers
  Used analogue telephone infrastructure
  MODEMs
  Low capacity, noisy, error-prone
1961 Packet-switching
  Kleinrock and Baran (US)
  Davies and Scantlebury (UK)
  Pouzin (France)
1970s Mini-computers, 1980s Micro-computers
1972 Ethernet LAN - Metcalfe
Notes: During the 1960s, computers began to proliferate and communication between them became an issue. Proliferation is relative, though - computers were still quite thin on the ground. Therefore, the communication of interest was generally over quite long distances. Convenience, and in many cases government regulation, meant that computer to computer communication had to be built on the existing telecommunications network. This network employed a technique called "circuit-switching" which turns out to be less than ideal for computer to computer communication. Consequently, in several countries, work began on developing networks specifically for data communications. In 1961, Leonard Kleinrock published a paper which introduced the concept of "packet switching" of digital data. Kleinrock and Paul Baran in the US, Donald Davies and Roger Scantlebury in the UK, and Louis Pouzin in France all worked on experimental packet-switching networks. Eventually, packet-switching became the basis of a new breed of data communications networks.
The 1970s saw the emergence of mini-computers, followed, in the 1980s, by desk-top work-stations and PCs. It was now common to find many computers on one site all of which needed to communicate. This resulted in the development of the "Local Area Network" (LAN). Since LANs did not cross public land, they were freed from the constraint of having to build on the public telecommunications networks.

## Slide 5: Circuits and Circuit-switching
“Circuit”: Fixed capacity allocated between end-points for the duration of a “call” or “connection”
E.g. telephone call: 64kbps full-duplex circuit
“Switched Circuits”: set up as needed
Resource wasted if end-points do not use it
Dedicated Circuit
Switched Circuits
Automatically Switched Circuits
Notes: At a) we can see Bell’s original set-up. An electrical circuit joins two phones enabling analogue voice signals to pass between them
At b) we see an early realisation of a “switched” telephone service. The switches consist of plug boards operated by a human operator. By setting plugs appropriately at the two switches (more normally known as “exchanges”) any telephone can be connected to any other. This arrangement still sets up an electrical circuit end-to-end for the duration of the call.
At c) we see an automated version of b). Switches Xs and Xt were originally warehouse-sized electro-mechanical devices which set up electrical circuits end-to-end. More recently the internals of the network have become digital and the switches are direct streams of bits along the appropriate wires.
Note the rather abstract definition of a “circuit” on the slide: Fixed capacity allocated between end-points for the duration of a “call” or “connection”. So we still talk about a “circuit” even though there may be no longer be an electrical circuit. The important thing is that the capacity allocated is fixed for the duration of the circuit. If the traffic on the circuit does not use all this capacity, for example if the traffic is intermittent, then some of this capacity is wasted. For this reason circuit-switching is no longer widely used for data communications (which tends to produce highly irregular traffic loads). This does not mean that it may not make a return in the future!

## Slide 6: Multiplexing Links
Physical links (fibres, wires) cost a lot to install
  Cheaper to install one 1Gbps link than 1000 1Mbps links
May then wish to allocate portions of link capacity to different activities
  E.g. treat a 1Gbps link as 1000 virtual 1Mbps links
  or as 1 0.5Gbps link and 50 10Mbps links etc.
Two basic techniques
  Frequency Division Multiplexing
    Analogue technique – divide frequency range into sub-bands
  Time division Multiplexing
    Digital technique – allocate bits to sub-channels in rotation

## Slide 7: Frequency Division Multiplexing
Example from analogue telephone network
12 carrier frequencies at 4KHz intervals
  60 KHz to 108 KHz
Voice waves filtered to approx. 3KHz bandwidth
Voice modulated on carrier
  Carrier spreads ± 1.5 KHz
Notes: FDM is like radio on a wire. Different radio stations transmit on different frequencies. A radio receiver “tunes in” to a frequency an can extract the signal that has been modulated on it. Exactly the same technique can be used to provide sub-channels over a single piece of wire.
The slide shows the arrangement that was common on telephone trunks. Note that the actual frequency transmitted is a combination of the “carrier” and the voice signal that is modulated upon it – which means there will be some variation. This means there must be adequate separation between the carriers used in each of the sub-channels. This ultimately imposes a limit on the number of sub-channels that can be carried.

## Slide 8: High “speed”
Higher speed vehicles travel faster …
12 kph, ~ 36 vehicles/min
24 kph, ~ 144 vehicles/min
Bits always go at the same speed
  ~ 2x108 m/s in copper, ~ 3x108 in fibre
1 Mbps
2 Mbps
High “capacity”!
Notes: The terms “high-speed network” and high-speed link” are misleading. Bits, in a given medium, always travel at the same speed – the limit is really the speed of light.
However, bits may be packed more or less densely – i.e. the rate at which bits are injected into the channel may vary. A high transmission rate means more bits are injected, hence delivered, in a given interval - we should really call this a “high-capacity” channel. A file transfer through such a channel will complete in a shorter time than it would through a low-capacity channel. However, the propagation time for each individual bit will be the same in each case (assuming equal lengths and media).
[Note that a road densely packed with cyclists moving at 20 kph may actually have more capacity than a road carrying bloated single occupancy BMWs travelling at 100 kph! All that is required is that you can fit more than 5 bicycles in the space occupied by a BMW (which you can).]

## Slide 9: Time-division Multiplexing
TDM interleaves bits (sometimes bytes) from several streams onto a higher bit-rate stream
Timings between bits of a stream are preserved
The effect is as if there are two separate “bit-pipes
Notes: The slide shows bits from a pair of digital circuits interleaved on a single link. (In some systems the interleaving may be in terms of bytes rather than bits). Recall that bits always travel at the same rate, therefore the bits on the multiplexed link must be packed twice as tightly requiring twice the capacity of an input link. Once demultiplexed the original bit timings are restored – so bits are delivered at exactly the rate they were originally transmitted. In fact the multiplexing is invisible to the transmitter and receiver which have the illusion of a dedicated link.
Of course, more than 2 incoming links may be multiplexed but the arithmetic must be exact; the bit-rate on the multiplexed link must be equal the the sum of the bit-rates on the incoming links.
A simple timing change in the demultiplexor would cause the upper bit stream to be switched to the lower link and vice-versa. Thus it is easy to turn a TDM system into a “circuit-switch” which can connect arbitrary inputs and outputs.

## Slide 10: Statistical Multiplexing
Data communication – not all bits are useful
  TDM does not exploit this
  Statistical multiplexing does
Notes: TDM works at the bit level; all bits of the original streams are delivered to the final destination. A few applications (e.g. PCM voice) generate a stream of bits at a constant rate all of which must be delivered – TDM suits such applications well. Most applications (including more modern compressed voice applications) generate data in bursts interspersed with periods of idleness. Most serial links still generate bits during such idle periods, (it is in the nature of the technology used to do this). Framing techniques, such as bit-oriented synchronous framing described earlier, enable data bits to be distinguished from idle bits. Statistical multiplexing treats the data bits and ignores the idle bits.
The slide shows two 1Mbps input streams in which about half the bits are in data frames the rest being idle bits (i.e. utilisation is about 50%). The statistical multiplexor exploits this by using a multiplexed link with a capacity < 2Mbps. The utilisation on this link is about 67%. (Many variants on the scheme are possible).
There can be contention for the output link when two frames arrive simultaneously. This is normally resolved by queuing or, in extremis, by discarding a frame.
We cannot assume that multiplexed frames will neatly interleaved – some information must be included in the frames to indicate to which channels they belong.
Nearly all today’s data networks use some form of statistical muliplexing

## Slide 11: Packet-switching
Based on statistical multiplexing
“Packets”, “frames”, “cells” – all basically the same idea
“Packet-switches” – store and forward
Packets multiplexed to many destinations
Notes: The slide shows a network of “packet-switches” connected by “links”. Each link is a bit-pipe at some bit-rate. Packet-switches can receive packets on any link and forward them on any other. They base their forwarding decisions on information contained in the packets. By setting this information appropriately a source may mix packets to a variety of destinations – something that is not possible with circuit-switching.
The Internet is a packet-switched network constructed by interconnecting thousands of individual packet-switching networks of various types.

## Slide 12: Packet-switching advantages
Hosts with nothing to send send nothing
Links are statistically multiplexed
Easy for hosts to multiplex packets to many destinations
Source and destination can operate at different bit-rates
t
p
128Kbps
384Kbps
192Kbps
Time
Ha
Hb
Sa
Sb
Notes: Packet-switching tends to be much more efficient for data transmission. Data transmission id “bursty” so there are often lengthy idle periods. Statistical multiplexing exploits the fact that a large enough collection of computers will almost never all be busy or all idle at the same time. Effectively, idle periods are filled by traffic from other sources. Circuit-switching cannot ddo this.
The store-and-forward operation allows there to be different speeds on each link. This means. For example, that a PC with a 34 Kbps modem can still retrieve a web page from a server with a 10 Gbit connection to the Internet.

## Slide 13: Packet-switching disadvantages
Store and forward delay
  Minimised by small packets
Time
b)
Time
a)
Notes: Store-and-forward operation has the disadvantage that the whole of a packet must be received on the input link before transmission on the output link can begin. These store-and-forward delays accumulate as a packet travels through a network and can become excessive. Small packets minimise the effect. However, small packets means more packets which may be harder for a switch to process. There is always a fixed per-packet overhead and this is proportionately greater for small packets.
It should also be noted that high bit-rate links reduce transmission time and hence reduce store-and-forward delay.

## Slide 14: Packet-switching disadvantages (2)
Switches may become congested
  Queues form
  Delays
  Discard packets
End-to-end delay is unpredictable
  Jitter
Packet header overhead
  Sequence numbers
  Addresses
  Connection identifiers
Notes: There is always a chance that all sources will generate traffic concurrently, which may exceed an exit link's capacity. Packet-switches try to handle this by forcing some packets to wait in a queue until the congested link clears. This adds "queuing delay" to the store-and-forward delay. If congestion is really bad the packet-switch may run out of queuing space and begin discarding packets. Packet-switching is a form of "statistical multiplexing"; enough capacity is provided to carry the average combined load (plus some extra) but not enough to carry the peak combined load. The method works most of the time because it is statistically unlikely that all sources will peak at the same time.
We need some way of distinguishing packets so we can ensure they are delivered to the right place. In practice, this means we must add some sort of label to each packet - so there is a packetisation overhead.

## Slide 15: How to organise a switched network?
“Virtual circuits” method
  Make a packet-switched network look a bit like a circuit switched one
    Set up route and reserve resources
    Use it
    Tear it down
  All packets on VC follow same route
“Datagram” method
  Each packet is an independent event
  Each packet routed separately
  No analogue of a “circuit”
Notes: We can distinguish two ways of implementing packet-switched networks – Virtual Circuits and Datagrams. Virtual Circuits tend to predominate in WANs whilst datagrams hold sway in LANs. However, the biggest network of all – the Internet – uses datagrams as a technology to interconnect other networks.
Note that we are focusing here on the mechanisms used inside switched, packet networks.

## Slide 16: Addresses and Identifiers
Hosts must have addresses (like ‘phone numbers)
  Millions of hosts
    Millions of addresses
    Long addresses (e.g. 48 bits => ~1016 addresses)
Addresses are needed:
  When a VC is set up
  When each datagram is sent
Every datagram needs to carry a destination address
VC packets only need carry destination address during VC set-up
Notes: Every network technology must adopt an addressing scheme which allows each participating host (more accurately the host’s network interface) to be allocated a unique address. We could allow to hosts to use the same address provided they are on discrete networks. In practice, though, it is normal to devise a scheme which guarantees every host in the world will have a different address. A simple example is the IEEE MAC address scheme which is used on nearly all LANs. This allocates a different 48-bit MAC address to every host interface. The requirement that addresses be globally unique means we need lots of addresses which, in turn, means we must allocate lots of bits to the addresses.
Every datagram must carry the full destination address – which occupies quite a few header bits.
It turns out that for VCs we only need include the full destination address in the packets we use to set up the connection at the start.

## Slide 17: Identifying Virtual Circuits
1
5
7
2
8
1
7
5
A
B
S
T
U
V
T
7
V
5
V
5
T
7
B
5
T
8
T
8
B
5
From
VCI
To
VCI
Forwarding table for switch S
C
D
Notes: Packets in a VC network have to carry identifiers so that switches can tell to which VC a packet belongs and can route it accordingly. These identifiers are called, generically, virtual circuit identifiers (VCI). (Unfortunately some VC network technologies adopt different names).
Conceptually each switch has a forwarding table which records the mapping between incoming VCIs and outgoing link + VCI. Note that incoming and outgoing VCIs are generally different. This avoids having to allocate VCIs that are unique within the scope of the whole network. Instead a VCI just has to be unique within the scope of a single link. VCIs are recorded in the headers of packets and thus have to be modified by the switches they pass through.
The slide shows an example in which VCIs identify full-duplex VCs.
Note that since VCIs have only to be unique within the scope of a link they can be much shorter than global addresses. For example, one technology, ATM, can be operated using 8-bit identifiers which allows 256 VCs per link.

## Slide 18: Datagram Forwarding
A
B
S
T
U
V
A
B
C
D
Destination
T
B
V
T
Next Hop
Forwarding table for switch S
C
D
Notes: In principle the forwarding table must have an entry for each possible destination address. (In practice we may be able to do better than this – for example we could have a default entry which covers all addresses not explicitly in the table).
Each datagram must include the full, global destination address in its header. This address is matched in the forwarding table and the datagram is routed accordingly.
Note that a VC network must also have a table like this which is used when the VC is set up. In neither the VC nor the datagram case have we discussed how these tables are built. They may be installed “by hand” or the may be an automated process which calculates them dynamically.

## Slide 19: VCs vs Datagrams
Datagrams
  Less state in switches
  More header overhead
  No connection set-up
VCs
  Less header overhead
  Smaller forwarding table (faster switching?)
  VC set-up takes time
  If switch or link breaks whole route must be re-learned
  Possible to negotiate special QoS on a VC

## Slide 20: Summary
Fixed allocations – FDM, TDM
Sharing networks
Circuit-switching, packet-switching
  Statistical multiplexing
Global Addresses
Virtual Circuits
  VCIs
Datagrams