## Slide 1: Transmitting Digital Information
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Introduction
Channels have limited capacity (bits/sec)
  Nyquist, Shannon …
How much “information” can a channel carry?
  One thousand paperback novels per day?
  One full-motion video per hour?
  How do we quantify information?
Is there an optimal way of encoding information?
How do we represent bits physically?
  Baseband encoding
  Modulation
  Spread-spectrum
How do we group bits into larger blocks?

## Slide 3: Quantifying “Information”
Question: How much information is there in an 80 character line of text?
Possible answer: There are 96 printable characters so there are 9680 different possible lines. Hence we need log2(9680) = 80log2(96)  527 bits to specify a line.
But: If we know line is English text then there are far fewer possible lines - so we should need fewer bits.
Or: If we know the line lists 5 students from a class of 32. 25 = 32 so we need 5 bits per student => 25 bits to specify a line.
Conclusion: Fewer possibilities => less “information”
Notes: Claude Shannon wanted to understand how fast “information” could be transmitted along a wire. In 1948 he proposed a way of quantifying the information in a particular situation. Lots of possibilities mean you needed lots of information to specify a single instance.
Thus (see slide) if a line of 80 characters can be chosen at random we need about 527 bits to specify a single line.
However, if we know the line must be valid English text there are fewer possible lines, so we should need fewer bits to specify a line. (Generally about half as many)
As an extreme example, suppose we know the line lists the names of 5 students from a class of 32. In principle, we need only 25 bits to specify the line.

## Slide 4: Information, encoding, compression
How much information is there in a photograph?
Image is 2.65”x4.78”, scanned at 300 pixels/inch, 24-bits per pixel
“Bit-map” will be 2.65x300x4.78x300x3=3420090 bytes (3,340 KB)
But: photos are not random pixels.
ZIP reduces this to 2856KB
GIF version is 833KB
JPEG version is 176KB
Notes: The photo shown is an object in the real world photographed using a camera. In order to store it on a computer or send it across a network it must be encoded. The simplest encoding is constructed by treating the image as a series of dots – in this case 300 dots per inch horizontally and vertically. Each dot(or pixel) has a colour which must be encoded. In this case we record the intensity of red, green and blue, allocating 8 bits to each intensity. This means each pixel requires three bytes of information so we can calculate the size in bytes for the image using this encoding – about 3,340KB.
Does this mean that a photo of this size contains 3,340KB of “information”?
Not really – because if we choose our pixel values at random, very few will correspond to real-world objects. The number of real-world photos is much less than the number of random bit-maps. How much less? We don’t really know but we can get an idea by looking at the way images may be compressed.
PTO

## Slide 5: Symbol probabilities
Earlier we said: “If we know the line lists 5 students from a class of 32. 25 = 32 so we need 5 bits per student => 25 bits”
This is only true if each student is equally likely to appear in the list.
For example
  If student A appears in every list,we only need specify 4 students from 31 which needs about 20 bits
  Any symbol we use to represent student A carries zero information
  Is there an optimal encoding for given probabilities?
Notes: The photo can be reduced to 2856KB using the zip programme. This is a general-purpose compression program which uses the “Lempel-Ziv” algorithm (Ziv, J. and Lempel, A. : "A Universal Algorithm for Sequential Data Compression", IEEE Transactions on Information Theory, May 1977). This works by detecting repeated patterns in the data and allocating short codes to these. Thus, if a pattern appears 10 times we can keep one copy plus nine short codes.
The GIF format also uses Lempel-Ziv. However, it is able to use it more intelligently since it knows that the data being compressed is a photo bit-map. This makes its search for patterns much more successful. (It also reduces the range of available colours).
Lempel-Ziv is a “lossless” compression algorithm – the pre-compression version can be restored exactly. JPEG is a “lossy” algorithm. It makes assumptions about the nature of images and human perceptions of them and aims at storing a version which will appear to be identical to a human viewer even though some fine details have been lost.

## Slide 6: Information and Entropy[1]
In a certain country the weather each day is either “hot” or “cold” with probabilities 0.95 and 0.05
Here is some historic weather data…
HHHHHHHHHHHHHHHHHHHHHH…
The symbol H tells us very little – we already guessed it would be probably be hot
The symbol C, when it appears, is surprising – it carries more “information”.
Shannon: Information – “that which reduces uncertainty”
If H and C were equi-probably the weather would be more uncertain
  A symbol would then carry more information
Notes: Shannon noted that, in many cases, the symbols used to represent information are not all equally likely. If a symbol is very likely to appear we learn little when it does appear. We say it carries little “information”.
In Shannon’s information theory we define “information” as “that which reduces uncertainty”.
If you have perfect information no uncertainly remains.
If you are “almost certain” of something then having your opinion confirmed carries very little information.
On the other hand, having your opinion contradicted is surprising and carries a lot of information.
The statement “tomorrow it will be hot” carries less information than the statement “tomorrow it will be cold” – i.e. H carries more information than C
If, in another country the weather was scorchio or rigido
[Note that in the above we are always using the word “information” in the technical sense defined by Shannon.].

## Slide 7: Information and Entropy[2]
We need to quantify the information carried by a symbol
  Lower the probability the higher the information
Take reciprocal of probability then convert to bits
The average information per symbol (the entropy) is
Notes: Sources produce symbols with certain probabilities. For example, an English text source produces the letter “E” with probability 0.1305 and “Z” with probability 0.0009. Zs carry more information than Es. To quantify this Shannon took the reciprocal of the probability and then took log base 2 to convert to bits.
For the hot/cold example this gives:
Which has the right properties since IC >> IH.
We can also calculate the average information per symbol for this source. This is simply the weighted average of the information for the individual symbols. It is generally called the entropy.
For the hot/cold source this works out as:
Contrast this with a country where H and C each have a probability 0.5. The entropy will be:
It is generally true that the entropy will be highest when the symbols are equi-probable. There is maximal “uncertainty” in such situations so the symbols carry maximum information.

## Slide 8: Entropy and encoding
The entropy gives a target for the efficiency of our encoding
  We should aim at 0.286 bits/symbol in the hot/cold example
We may do this by encoding groups of symbols
Mean 0.43 bits/symbol
Symbol | Probability | Code
HHH | 0.857 | 0
HHC | 0.045 | 101
HCH | 0.045 | 110
HCC | 0.0024 | 11100
CHH | 0.045 | 100
CHC | 0.0024 | 11101
CCH | 0.0024 | 11110
CCC | 0.00013 | 11111
Notes: The entropy tells us the average information per symbol associated with a source – measured in bits/symbol. Ideally we should be able to find a code which approaches the entropy in the number of bits it uses.
In the hot/cold example we have two symbols H and C. A naïve encoding will allocate 1 bit per symbol (H=1, C=0). This is a long way from the ideal 0.286 bits per symbol.We can do better if we generate a new set of symbols by grouping the original ones. The slide shows the symbols grouped in threes. We can calculate the probabilities of these new symbols from the originals e.g. P( HCH)= P(H)xP(C)xP(H) = 0.95x0.05x0.95 = 0.45. (We are assuming that the probabilities are independent – for example the probability of H is unaffected by what happened the day before). We can then allocate codes ensuring that the longest codes go with the lowest probabilities. The code shown is a Huffman code. This is guaranteed to approach the ideal as close as possible for a given set of symbols and probabilities. We can calculate the average length of this code by computing the average of the code lengths weighted by the probabilities (1 x 0.857 + 3 x 0.45 + …). This gives 0.43 – not all that close to 0.286 but certainly better than 1. We could get closer still by grouping in fours or fives.
Bear in mind that the code must be instantaneously parseable. This means that no code can be the prefix for any other. For example, we cannot use the code 10 for HHC as there would then be ambiguity about the code 100 – is it HHC, HHH or is it CHH?

## Slide 9: Information - Summary
Information is measured in bits
Information sources generate symbols
  The average information per symbol is the entropy
To store or transmit information we must encode it
In principle we can devise a code whose average length per symbol approaches the entropy
In practice codes are often much less efficient
A compression algorithm may improve coding efficiency – but we can never do better than the entropy
Notes: Note that our definition of information is very technical and differs markedly from normal usage. This says nothing at all about the value or the quality of the information. However, the results are meaningful in data communication in that more information (in the Shannon sense) will take longer to transmit.

## Slide 10: Representing Bits Physically
We need to represent bits as electrical or optical signals
  Baseband – encode the bits directly
  Broadband – modulate a carrier wave
Receiver must be able to “see” where bits begin and end
  Synchronisation problem
We also need to be able to group bits into “frames”
  Receiver must be able to “see” where frames begin and end
  Another synchronisation problem

## Slide 11: Baseband Transmission
Receiver must sample signal at correct intervals
b) and c) have transitions for every bit
a) and d) minimise transitions
Notes: The signalling used in RS232-C carries no “clocking” information - a sequence of 0’s appears as a steady voltage. There is no way the receiver can tell how many 0’s are in the sequence from the signal alone. Instead, the receiver must have a clock which is synchronised with the transmitter’s. This is only reasonable if a small number of bits is transmitted – 8 say. Clocks that stay in sync. for longer than this cost too much. RS232-C is used in conjunction with asynchronous framing in where synchronisation is re-established for each 8-bit byte (see later).
Bipolar Encoding uses a “return to zero” (RTZ) waveform in which zero volts occurs between each pair of bits. The zero voltages enable the receiver to detect bit boundaries.
Manchester Encoding is an example of “phase encoding”. Here bits are encoded by voltage changes. The -+ transition encodes 1, +- encodes 0. This is used on the Ethernet LAN. There is always a transition between bits so the receiver can easily detect bit boundaries.
Non return to zero (NRTZ) encoding is a “differential” encoding; the change in voltage determines what is encoded. In the slide for a 1 the voltage is left unchanged, for a 0 it is changed; this is usually called “Non return to zero - inverted” (NRTZ-I). It is clear that a long sequence of 1’s will result in a continuous voltage and therefore carries no clocking information. However, NRTZ-I is used with an encoding scheme which ensures that the longest sequence of 1’s is 6 (see later). PTO

## Slide 12: Baseband Problems
Simple baseband encodings
  Essentially a square wave – generates high frequencies
  e.g. RS232-C transmitting 10101010101….
  Suppose bit-rate is 1 Mbps
  frequency of square wave f = 0.5 MHz
  frequency of 5th harmonic (sin(5t)) = 2.5 MHz
  Channel bandwidth must be at least 2.5 MHz
Nyquist C = 2Flog2Q
  Q=2, F=2.5 MHz  C = 5 Mbps
  4 Mbps wasted
1 bit
1 cycle
Notes: One advantage of NRTZ-I is that, on average, it uses the same number of voltage transitions as the simple RS232-C encoding. Both of the other techniques introduce additional transitions - i.e. there are more transitions for a given bit-rate so more bandwidth is needed.
The baseband encodings in the previous slide are simple to implement and are good choices when there is plenty of bandwidth available and little noise – for example over high-quality copper wires in the local area. In other circumstances something else is required and modulation techniques are used – see next slide.

## Slide 13: Modulation – An Alternative
Start with a carrier wave – sinusoidal wave
Modify carrier wave to represent bits
  Change, amplitude, frequency, phase
Carrier frequency determines frequency range of signal
Multiple bits per symbol possible
f
0
W
Original signal
f
0
fC
fC-W
fC+W
Modulated signal
Notes: Modulation starts with a carrier wave at constant frequency. The amplitude, frequency or phase of the carrier are varied so as to represent bits (next slides). One advantage is that the modulated signal uses frequencies that are centred on the carrier frequency. This means we can choose a carrier frequency to suit the frequency range of the channel.
The diagrams show the spectra of a typical signal and a typical result of modulating that signal using a carrier wave of frequency fC. We see that the bandwidth used is doubled (W -> 2W) and that the frequency range is now centred on fC. We do not prove this result here but if follows simply from Fourier Transform theory.

## Slide 14: Modulation
0
0
1
0
0
0
1
0
45
135
45
11
10
11
a) Amplitude shift keying
b) Frequency shift keying
c) Phase shift keying
N.B. 4 phase shifts (450, 1350, 2250, 3150) => 2 bits per symbol
Notes: The slide shows the three main techniques:
Amplitude shift keying uses two amplitudes for 1 and 0 (this would be loud and soft for a sound wave). The main problem is attenuation – the gradual reduction in amplitude as a wave travels. This makes it difficult to differentiate the two amplitudes. In one version the 0 amplitude is zero so that the carrier is switched on for 1 and off for 0 – so-called on-off keying.
Frequency shift keying essentially uses two carriers, one for 1 and one for 0.
Phase shift keying relies in making the carrier wave “jump” – i.e. to miss out part of the wave. Recall that one complete cycle represents 3600. The scheme in the slide permits four different phase shifts (hence each represents two bits):
  450 -> 11
  1350 -> 10
  2250 -> 00
  3150 -> 01
The first phase shift in the slide misses out 1/8 of a complete cycle – 450 and so encodes 11. One advantage of phase shift keying is that boundaries between symbols are easily detected by the receiver.

## Slide 15: Modulation Example
The example shows two phase shifts and one amplitude change
  4 phase shifts 450, 1350, 2250, 3150
  2 amplitudes
  4 x 2 = 8 symbols => 3 bits per symbol
450
2250
Notes: The example shows Quadrature Amplitude Modulation (QAM) 4 phase shifts and 2 amplitudes giving 8 symbols hence 3 bits per symbol.

## Slide 16: Constellation Diagrams
Used to summarise a modulation scheme
E.g. The QAM scheme in the previous slide might be
0
+90
+180
+270
QAM
000
001
010
011
100
101
110
111
Notes: The diagram shows, for example, that 001 will be transmitted by phase shifting by 450 and adopting the higher amplitude.

## Slide 17: Frequency Division Multiplexing
Divide channels into independent sub-channels
Use different carrier frequencies on each sub-channel
Ensure sub-channel frequencies do not overlap
E.g. ADSL
N.B. relative bandwidths - Shannon
Notes: By carefully choosing carrier frequencies it is possible to implement several sub-channels over a single physical channel. (Of course, this is exactly what happens with radia and television transmissions). This is termed frequency division multiplexing (FDM)
The slide shows the spectra of the three channels used for ADSL. The horizontal axis represents frequencies and the vertical signal power. Three different carriers are allocated with gaps in between to prevent interference. The first band (labelled “POTS” for “Plain Old Telephone Service”) is used for ordinary voice traffic and uses the frequencies from 0 to 3.4kHz. This is needed so that the local loop can continue to provide a telephone service alongside the ADSL data services. The remaining bands are used for upstream and downstream data traffic. Notice that the downstream band has greater width – as one would expect from Shannon’s theorem due to its greater capacity.

## Slide 18: Spread-spectrum and Noise
From notes 1: If C=1Mbps, SNR is –10 dB then B=7Mhz
  How can we use this bandwidth to combat noise?
  Spread-Spectrum techniques
  Extensive use in wireless networks
Direct-Sequence Spread-Spectrum
  Send multiple symbols (“chips”) per bit
  High chipping rate => high bandwidth (spreading)
  Noise immunity since we only require “most” chips to get through
Frequency-Hopping Spread-Spectrum
  Use multiple carrier frequencies
  Hop between several frequencies during transmission of a single bit
  More frequencies used => high bandwidth (spreading)
  Noise immunity since (probably) only some frequencies will be affected by noise
Notes: The term “spread-spectrum” covers a range of techniques. Here, we are interested in their use mainly to combat noise (They are also used, for example as a means of sharing capacity between co-located networks). The essential idea is that each bit is encoded in a way which spreads it over a wide range of frequencies. As long as noise only corrupts a minority of the frequencies used the bit can still be correctly received with high probability.
In the next slides we look at the direct sequence scheme. Frequency hopping is not considered further.

## Slide 19: Direct sequence spread spectrum
spreading sequence 10110111000
1
1
0
bit sequence 110
chip sequence
Xor bits with a spreading sequence
  a sequence of “chips”
Chipping rate normally >> bit rate
E.g. bit rate 1Mbps and 11 bits/chip
Chipping rate = 11 Mchips/sec, “spreading factor” = 11
Modulate chip sequence and transmit
Notes: Before the bit-stream is modulated, it is xored with a high bit rate binary sequence called the spreading sequence. Each bit in the spreading sequence is a called a chip and the rate of the chip bits is called the chipping rate.
The chipping rate is typically (at least) an order of magnitude higher than the bit rate. Therefore, after modulation (using BPSK or PSK for example) a higher bandwidth signal will result. If the chipping rate is n times the bit rate then we expect to use n times as much bandwidth – a “spreading factor” of n.
[N.B some implementations modulate before combining]

## Slide 20: DSSS - Synchronisation
b  p  p = b - so receiver must xor with same spreading sequence as Tx
  Must synchronise to Tx chip rate
  Tx prepends sequence of 1s
  Rx timeshifts spreading sequence until 1s recovered
1
Rx mis-aligned
1
Rx aligned
Tx
Notes: In principle Rx has only to xor with the same spreading sequence to recover the original bits. However, this will only work if the receiver has it’s spreading sequence synchronised with that of the transmitter.
In frame-based communication this can be achieved by prepending a known bit pattern (a “preamble”) to each frame. This could be a sequence of 1s. As Rx receives the preamble it time-shifts its spreading sequence until a sequence of 1 bits emerges. After initial synchronisation, the data bits will follow. Synchronisation bits might be used only at the beginning of a transmission, or at predetermined times during a transmission, e.g. every 10ms.

## Slide 21: DSSS - Noise
Suppose noise affects (say) 2 chips
  (assume we have synchronised to the spreading sequence)
1
Tx
2 chip errors
Received bit could be:
  1 with 2 chip errors
  0 with 9 chip errors
Bit can still be decoded as a 1 with high probability
Notes: It is important to realise that the transmitted chips will be subject to noise so that some chips will be received in error. If, in the scheme in the slide, two chips in a ‘1’ bit were in error so that decoding yields 9 ‘1’ values and 2 ‘0’ values. Nevertheless we would be happy to decode this as a 1.
DSSS may be used as the basis of a channel allocation algorithm called “Code-Division Multiple Access” (CDMA). Here stations may transmit concurrently but each uses a different spreading sequence. With careful choice of spreading sequences transmissions to “other” stations appear as noise and can be excluded.

## Slide 22: Grouping Bits
So far we have looked at ways of transmitting bits
In data comms. we are interested in groups of bits (“frames”)
  8-bit ASCII characters typed on a keyboard
  53-byte cells in an ATM network
  arbitrary-length frames on an Ethernet or WiFi network
Bits are received by “reading” the input (e.g. measuring the voltage) in the “middle” of each bit.
Receiver must achieve bit synchronisation
  c.f. phase-shift keying, Manchester encoding
Must also achieve frame sychronisation
  start and end of frame
Notes: The final part of this note looks at two techniques which are used to group bits into the larger units which are used in data communications.

## Slide 23: Asynchronous Framing
Async. frames usually carry 8 bits
  Receiver must detect start then count in the bits
  Receiver must clock bits at the same rate as the transmitter
1
0
0
1
1
0
1
1
The data
Idle level (=1)
Receiver waits for “start bit” (=0) and starts clock
Receiver samples line to recover data
There must be at least one 1-bit before the next start bit – a “stop bit”
Notes: Asynchronous framing is used for slow irregular character transmissions – for example from a keyboard to a remote computer.
There are two signal levels; 1 and 0.
When the line is idle the 1 signal is transmitted
Each character is preceded by a 0-bit – called the start bit. The receiver monitors the line searching for this bit. Once a start bit has been detected the receiver starts its clock.
The receiver samples the line at the appropriate intervals and recovers the bits.
The transmitter must insert at least one 1-bit after the character to enable the next start bit to be detected.
Note that Tx and Rx must both be configured to use:
the same bit rate
the same number of bits per character
Also, the Tx and Rx clocks must be sufficiently accurate that they can remain in sync throughout the transmission. The technique is termed “asynchronous” because there is no synchronisation between characters.
Note that in the scheme illustrated we have to transmit 10 bits in order to convey 8 bits of information – a 25% overhead.
[N.B. 8-bit async. framing typically carried 7-bit ASCII codes plus a single “parity bit” used for error checking – see the notes on “Dealing with errors”.]

## Slide 24: Bit-oriented Synchronous Framing
Data may be arbitrary length
Special bit patterns:
  flag - 01111110
  idle - 01111111
One flag at start of data and one at end of data
flag or idle pattern in data:
  if 5 successive 1s, insert 0
  bit-stuffing to achieve data transparency
flag
flag
idle
idle
bit-stuffing
0
0
1
1
1
1
1
1
1
0
0
1
1
Data to be sent
0
1
1
1
1
1
1
0
0
1
1
1
1
1
1
0
0
1
1
1
1
1
1
1
0
0
1
1
0
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
0
Notes: Bit-oriented synchronous frames are delimited by the flag bit pattern 01111110 (zero, six ones, zero). Between frames, the receiver continuously searches for this pattern and, when found, begins immediately to read in the data part of the frame. The transmitter often sends several idle patterns before the flag so that the remote end can achieve bit-synchronisation. The data part may be any number of bits. Whilst reading the data bits, the receiver searches for the flag pattern which indicates the end of the frame.
A problem would arise were the data to contain the flag pattern as this would look like the end of the frame to the receiver. We need to hide such patterns and so achieve data transparency. The method is called bit-stuffing. Whenever the transmitter finds a sequence of five 1s in the data, it stuffs a 0 into the bit stream. When the receiver receives 5 successive 1s it examines the next bit:
If this is a 0 it must be the result of bit stuffing and so can be discarded.
Else (it’s a 1),
If it is followed by a 0, we have a flag,
Else, we have an idle.
(The bit streams shown above would be continuous but have been broken into 4-bit groups to make them easier to read.)
Bit stuffing is done in the transmission hardware so can be done “on the fly” as the bits are transmitted and received. This framing, or variants of it, is used in many digital networks; LANs, ISDN, Frame Relay etc.

## Slide 25: Data Transmission - Summary
Baseband transmission
  Some make bit transitions easy to spot
Modulation
  Amplitude, Frequency and Phase Shift keying
  Multiple bits per symbol
  Spectrum shift
  Frequency Division Multiplexing
Spread Spectrum
  DSSS – chips, use to combat noise
Framing - synchronous and asynchronous
  Transparency – bit-stuffing