## Slide 1: Dealing with Errors
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: How many errors are OK?
Bit Error Rate (BER): fraction of bits delivered wrongly
  e.g. high-quality optical fibre link BER might be 10-15
    i.e. 1 bit in error for every 1015 bits delivered
  e.g. wireless link BER might be 10-4
    i.e. 1 bit in error for every 104 bits delivered
We send packets and reject if there is even one error
Prob. a packet is in error |  | BER | 
 |  | 10-15 | 10-4
Packet size (bits) | 1000 | 10-12 | 0.095
 | 10000 | 10-11 | 0.632
Wireless, 1,000 bits: about 1 packet in 10 will be in error
Fibre, 10,000 bits: 1 packet in 1011 (=100,000,000,000)
Notes: The estimates for the packet error rate are calculated as follows
P(bit in error) = b, mean packet size = s
P(bit not in error) = (1-b)
P(packet not in error) = (1-b)s so P(packet in error) = 1- (1-b)s
In this calculation we assume that bit errors occur independently. In practice this is not true and errors tend to occur in bunches. This tends to concentrate errors in a smaller number of packets meaning that the true packet error rates will be somewhat less than those shown in the slide.
However, an important conclusion is that high BER mandates smaller packet size.

## Slide 3: What can we do?
Improve the BER
  Discover which bits are in error and correct them
  Must send extra (redundant) bits to achieve this
  Therefore reduced effective bit-rate
  An example of “Forward Error Correction” (FEC)
Detect packets with errors and re-transmit them
  Must send extra bits to achieve this (fewer than FEC)
  Accept a delay while retransmission occurs
We cannot achieve perfection
  Can neither detect nor correct ALL errors
  Aim to improve the “residual” error rate so it is “acceptable”
Notes: What is an “acceptable” residual error rate?
For an audio broadcast each packet may contain about 125ms of sound. Losing a packet might cause a short “click” to be heard. If one packet in 1000 is in error we get about one click every 125 x 1000 ms = 125 sec. We might consider this acceptable.
On the other hand we would not be happy with one error in every 1000 packets carrying information on money transfers between banks.

## Slide 4: Redundancy
Here is a srelling mistake
Not all combinations of letters make legal words:
  if they did how would we detect error?
Redundancy:
  information that is not essential
  helps in detecting errors
To detect/correct errors, we need redundancy:
  how much do we need?
  what is the cost?
Notes: It is obvious that there is a srelling mistake in this sentence. It is obvious because the set of all possible words that can be made from English letters can be partitioned into two sets; English words and non-English words. Srelling belongs to the latter set as do dfede, msndasad, and qjykfda. In fact, vastly more “illegal” words can be made than “legal” ones. Suppose we somehow re-organised English spelling so that all combinations of letters spelled legal words. We would not now be able to tell whether a word had been mangled by a transmission service; the result would always be another legal word. We may still be able to detect the error from the context. However, this is really equivalent to saying the set of all possible sentences that can be made from English words can be partitioned into two sets; English sentences and non-English sentences.

## Slide 5: Codewords
For simplicity assume we send m bits in each message
In addition we send r error control bits with each message
Thus we send codewords of c bits where c = m + r
Define Hamming Distance between two codewords as the number of bits that differ between them
10000011
01000010
01000001
HD=2
HD=3
HD=3
Code with 3 codewords
The Minimum Hamming Distance of the code is 2
To detect all h-bit errors requires Minimum Hamming Distance > h
Notes: The Hamming Distance (Richard Hamming 1915–1998) is the key concept in assessing the error control capabilities of a coding scheme. In particular the minimum Hamming distance (i.e. the lowest HD between any pair of codewords in the code) determines these capabilities.
If we are to detect all h-bit errors then changing h (or fewer) bits in a legal codeword must not generate another legal codeword. This means that all legal codewords must be more than h bits apart. I.e the minimum HD > h.

## Slide 6: Error Detection Example – Parity Bit
Example – ASCII (8-bit):
  7-bits data, 1-bit even parity
Even parity  choose parity bit so that there is an even number of 1 bits.
Minimum Hamming distance will be 2
  Since changing a single bit must give odd parity
A 0 100 0001
B 0 100 0010
C 1 100 0011
parity
bit
1-bit error: 0100 0101 
0000 0010 
1000 0011 
2-bit errors: 1100 0011 ?
0110 0011 ?
0100 0001 ?
Notes: One requirement for an error detection scheme is that we can distinguish between legal and illegal codewords. With English detecting an illegal codeword (i.e. a spelling mistake) is done mainly by exhaustive search. This is not efficient. A parity check is better in that there is an algorithmic way of determining legality; add up the 1-bits and check whether the total is even or odd.
We have m = 7, r = 1 and c = 8
There are thus 28 possible codewords. 27 of these will have even parity (the legal codewords and 27 will have odd parity (the illegal codewords).

## Slide 7: Error correction
Rule: correct an illegal codeword by changing to “nearest” legal codeword
To correct all h-bit errors:
  Consider all illegal codewords HD  h from a legal codeword
  We require all this set to be HD > h from any other legal codeword
  Thus we require minimum HD > 2h
legal codeword
Hamming space
h
h
1
illegal codeword
Min H.D. = 5
Codewords 2-bit error 3-bit error
00000 00000 00000 10001 00000 10001
00000 11111
11111 00000
11111 11111
Corrects all 2-bit errors
Notes: For example, to correct all 1-bit errors requires a minimum Hamming distance of 3. So 8-bit ASCII has no error correcting properties. Suppose we have a system with just four codewords:
0000000000 0000011111 1111100000 1111111111
This has a minimum Hamming distance of 5, so it should be able to correct all 2-bit errors. The nearest legal codeword is the result of seeing which are the fewest number of bits we need to alter to get to a legal codeword.

## Slide 8: How Much Redundancy to Correct 1 bit?
Suppose we want to correct all 1-bit errors
c = m + r
Each circle includes 1+c codewords
There are 2m circles
There are 2c codewords
(1+c)2m  2c => 1+m+r  2r
E.g. m = 7, r = 4
legal codeword
Hamming space
1
1
1
illegal codeword
Notes: Taking m = 7 (for ASCII) and using some values for r, we find the inequality is satisfied at r = 4.
This does not tell us how to construct a suitable code of course. All we know is that it must have 11 bits and that the minimum Hamming distance must be 3 or more. Fortunately Mr Hamming invented a way of doing the job …

## Slide 9: Hamming code
11 10 9 8 7 6 5 4 3 2 1
m m m r m m m r m r r
Check bit
Msg bit 08 04 02 01
11 1 0 1 1
10 1 0 1 0
09 1 0 0 1
07 0 1 1 1
06 0 1 1 0
05 0 1 0 1
03 0 0 1 1
A = 1 0 0 0 0 0 1
11 10 9 8 7 6 5 4 3 2 1
1 0 0 0 0 0 1 Tx
11 10 9 8 7 6 5 4 3 2 1
1 0 0 1 0 1 0 0 1 0 0 Rx
8 4 2 1
0 1 1 0 = 610
check
1 0 0 1
1
0 0 0 0
0
1 0 0 0 1 0
0
0
1 0 0 0 1 0
Notes: Let us look at a Hamming Code for 7-bit ASCII. This must have 4 check bits.
The trick is to ensure that each message bit will affect a unique set of check bits if it is in error. This is done by numbering the bits as in the slide and placing the check bits in the power-of-2 positions; 1, 2, 4 and 8. We then arrange that bit m is checked by the check bits for which there is a 1 in the binary representation of m. Thus bit 9 (= 10012) will be checked by bits 8 and 1. This means we can be sure that if just the checks for bits 8 and 1 fail then bit 9 must be in error and can be corrected.
Following this scheme we can see, for example, that check bit 2 must take part in the checks for bits 11, 10, 7, 6 and 3. In the slide we calculate the value of the check bits so as to give even parity.
To check a codeword we perform the 4 parity checks and write down a 1 for each one that fails. We can then read off the number of the bit that is in error.
This scheme is simple to implement in hardware. A version of it with 8 message bits and 4 check bits is used to provide 1-bit error correction for some types of computer memory.
Note we are talking here only of 1-bit errors.

## Slide 10: ARQ Protocols – Repeating Yourself
Many systems achieve reliability by detecting errors and retransmitting
Agreed rules are needed to manage this – a protocol
Terminology:
  Protocol Entity (PE) – h/w or s/w implementing protocol rules
  Protocol Data Unit (PDU) – a message sent between PEs
    Data PDU – one which includes data
    Acknowledgement PDU (Ack) – one confirming receipt of a data PDU
  Packet, frame, segment, cell – all (more-or-less) synonyms for PDU
  Transmit timeout – event signifying ack has not been received in time
Automatic Repeat reQuest protocols
  “Transmitter” (Tx) sends data PDUs to “Receiver” (Rx)
  Rx sends ack PDUs to Tx
  All data PDUs must be acked
  PDUs not acked within a timeout period must be retransmitted
Notes: The slide introduces some of the basic terminology and method of operation. Different protocols adopt their own terminology. For example, PDUs may be called packets, frames, cells, messages etc.

## Slide 11: ARQ Protocols
checksum
data
header
protocol control information (PCI
PDU
Many different versions:
  Some manage transmission on a link (Data Link protocols)
  Some work between hosts (“end-to-end” e.g. TCP)
Objective is normally to deliver an error-free stream of data in the correct order
May also provide flow control
  Rx tells Tx to slow or stop
Protocols specify the format of PDUs
  Typical structure:
Notes: Note that there are many different protocols which employ ARQ techniques. They are used, for example, between computers communicating across the Internet (e.g. TCP) and between mobile devices and base stations. They operate in highly varied environments in terms of data transmission rate, error rate, propagation delay etc. Consequently they vary a good deal at the detailed level. These notes attempt to establish general principles rather than considering the details of particular protocols.
ARQ protocols implement:
Flow control: Receiver can force transmitter to reduce or increase the rate of PDU flow.
Error control: Receiver can force retransmission of missing or damaged PDUs.

## Slide 12: Time-sequence Diagrams [1]
Useful to show the sequence of events in time
ab, data PDU transmission time
bc, Propagation time
cd, Processing time at Rx
de, ack PDU transmission time
ef, Propagation time
fg Processing time at Tx
We sometimes assume
  constant transmission times
  constant propagation times
  Negligible processing times
Tx
Rx
Time
DATA
ACK
a
b
c
d
e
f
DATA
g
Notes: Note that the relative values of transmission, propagation and processing times can vary hugely. Sometimes it may be valid to treat some values as negligible. E.g. if communicating between Earth and Mars then propagation time dominates everything.
These diagrams are a very useful aid to understanding event sequences but they must be drawn reasonable accurately and neatly!
You must be precise in the use of terms and distinguish correctly between:
Transmission time: depends on PDU size and bit-rate
Propagation time: depends on distance, propagation speed (normally a high fraction of the speed of light) plus any delays in intermediate systems (routers etc.)
Processing time: depends on processor speed, protocol complexity, operating system scheduling delays etc.

## Slide 13: Time-sequence Diagrams [2]
Tx and Rx are protocol entities
We assume there are users that:
  request Tx to send data
  receive data delivered by Rx
    “indication”
Rx must deliver data in sequence
  Buffering
Tx
Rx
Time
DATA
ACK
DATA
Request
Indication
Notes: An ARQ protocol is always providing a service on behalf of users. Tx will only send data PDUs if there is data to send. Rx only delivers data once it is sure (as sure as it can be!) that:
  There are no errors in the data
  No data has been lost or mis-ordered.
Sometimes Rx will buffer data until a missing data PDU arrives. It may also need to do this if the user is not currently willing to receive data.
For simplicity in these notes we normally assume:
  That Tx always has data to send
  That Rx is always willing to receive data
  That requests and indications are 1-1 with data PDUs. (In practise a PE might split a request into several data PDUs).

## Slide 14: Sequence Numbers [1]
Generally, PDUs include sequence numbers in their headers so we can tell which PDU is being acked
The second data PDU is a retransmission caused by the lost ack
  The “duplicate” PDU 3 must be detected
Rx PE must not deliver the duplicate to its user
  Data must not be delivered twice!
Rx must ack the retransmission otherwise Tx will time out again!
Tx
Rx
Time
DATA 3
ACK 3
ind 3
DATA 3
Notes: “ind 3” means that the data in that PDU is ready to be passed to the user (a so-called “indication”). Here “user” probably means another piece of hardware or software.
The data would not necessarily be passed straight away or in one lump. It is possible, for example that the Rx PE will buffer several PDUs and pass them to the user in one indication.

## Slide 15: Sequence Numbers [2]
Tx must match acks to data
What does receipt of ACK 4 mean?
  Just DATA 4 received OK?
  DATA 4, 3, 2, … received OK?
Protocols vary!
Note that Tx has (at least) 2 data PDUs outstanding here
  Tx window is at least 2
Tx
Rx
Time
DATA 3
ind 3
DATA 4
ACK 4
ind 4
Notes: There are many different ARQ protocols which differ in many details. How should “Ack n” be interpreted?
Data PDU n received (“selective acknowledgement”)?
Data PDUs n, n-1, n-2 … received (“cumulative acknowledgement”)?
Send Data PDU n next?
Anything else?
All of these are used in different ARQ protocols.

## Slide 16: Transmit Window [1]
Suppose Tx window size is 3 PDUs
At (a) PDUs 3, 4, 5 are “in the window”
At (b) PDUs 3, 4, 5 are “outstanding”
Receipt of ACK 3 means Tx window is {4, 5, 6} – DATA 6 can be sent
At (c) the window is full. Tx must stop and wait for another ACK.
Tx
Rx
Time
DATA 3
ind 3
DATA 4
ind 4
DATA 5
DATA 6
ACK 3
ind 5
ind 6
ACK 2
(a)
(b)
(c)
Terminology
  Outstanding PDU – one that has been transmitted but not yet acknowledged
  Transmit window – set of PDUs that are permitted to be outstanding
Notes: Note that, at the start (after Ack 2) the Tx window comprised DATA PDUs 3, 4 and 5. After receipt of ACK 3 the window “slides” forward to comprise 4, 5 and 6. For this reason such protocols are termed “sliding window” protocols.
We assume here that the TX window size remains fixed at 3. (Some protocols allow the Tx window to be varied)

## Slide 17: Transmit Window [2]
Suppose Tx window size is 2 PDUs
At (b) Tx window is full – Tx must stop
Time between (b) and (c) is wasted – poor performance
Tx window must be big enough!
(See later slide)
Tx
Rx
Time
DATA 3
ind 3
DATA 4
ind 4
DATA 5
ACK 3
ind 5
ACK 2
(a)
(b)
(c)
Notes: The slide shows the importance of setting the Tx window size correctly. If it is set too small then time will be wasted waiting for an ack (assuming Tx has further data to send).
Why not make the Tx window enormous?
a) Enormous windows imply enormous sequence numbers which waste space in the PDU headers.
b) Tx must keep copies of outstanding PDUs in case these need to be retransmitted so there are storage implications.
c) Some protocols retransmit the entire window when an error occurs so large windows can cause unnecessary transmissions.
Tx window must be big enough but not too big.

## Slide 18: Receive Window of 1
DATA 4
Terminology:
  Receive Window – the set of PDUs it is legal for Rx to receive
Rx window = 1 (Tx window = 3)
=> Rx processes data PDUs in strict sequence
(a) 5 is received 4 is expected
  5 is ignored!
(b) Tx window is {4, 5, 6} so 6 can be sent
  6 will be ignored at Rx
No ACK arrives, 4 retransmitted
(c) 4 passed to user and ACKed
Tx
Rx
Time
DATA 3
rdy 3
ind
ACK 2
DATA 4
DATA 5
ACK 3
(a)
rdy 4
(c)
DATA 5
(b)
DATA 6
DATA 6
ACK 4
rdy 5
rdy 6
Notes: Note that although Rx window is 1 here we are still using a Tx window of 3.
This is a simple strategy for the receiver which only accepts PDUs which arrive in sequence and discards all others. It is not necessarily efficient - note that DATA 5 and 6 are successfully received twice. “Ignored” means what it says - no record of these PDUs is kept at Rx.
Because Tx window is 3 PDUs Tx stops after transmitting DATA 6 for the first time.
Note that data is delivered to the user in the correct order and that acks are cumulative.
Because Rx will discard all out-of-sequence PDUs Tx must retransmit all of these.

## Slide 19: Rx Window = Tx window
DATA 6
DATA 5
DATA 4
Rx window = Tx window
=> Rx processes data PDUs in any order
(a) 5 is received but 4 expected
  DATA 5 is buffered!
(b) Tx window is {4, 5, 6} so 6 can be sent
  6 will be buffered at Rx
No ACK arrives, 4 retransmitted
(c) 4, 5 and 6 passed to the user, 6 ACKed
Tx
Rx
Time
DATA 3
ind
ACK 2
DATA 4
DATA 5
ACK 3
(a)
rdy 4, 5, 6
(c)
DATA 6
(b)
rdy 3
ACK 6
Notes: This strategy is more complicated for the receiver and requires it to buffer PDUs whilst waiting for gaps to be filled. It can be more efficient though - especially in situations where PDUs may suffer arbitrarily delays and be delivered out of sequence. This is possible on the Internet and, consequently, TCP receivers normally use this strategy.
Note, once more we assume a Tx window of 3 PDUs.
Note that in the example above we are assuming that ACKs are cumulative – so that ACK 6 implies receipt of DATA 6, 5 and 4. This is not the only possibility – see next slide.
[Comparing with the previous slide there is no reduction in the number of re-transmitted PDUs. However, this is not always the case and this strategy often results in a reduction in retransmissions.]

## Slide 20: Selective Acknowledgement
DATA 4
Rx window = Tx window
Rx uses “selective acknowledgement” (SACK)
(a) 5 received 4 expected
  5 is buffered and acked!
(b) Tx window is {4, 5, 6} 6 can be sent
  6 buffered and acked
(c) 5 is acked, 4 is missing so resend 4
(d) 4, 5 and 6 are passed to the user and 4 is ACKed
Tx
Rx
Time
DATA 3
ind
ACK 2
DATA 4
DATA 5
ACK 3
(a)
ACK 4
DATA 6
ACK 5
(b)
rdy 3
rdy 4, 5, 6
ACK 6
(d)
(c)
Notes: With selective acknowledgement each DATA PDU is acknowledged individually – i.e acks are not cumulative. This can mean more ACK PDUs are sent but can reduce the number of retransmissions. Compare with the previous slide and note that the earlier (selective) ACKs of DATA PDUs 5 and 6 mean these do not have to be transmitted.
Note that we are still using a Tx window size 3 and that this must be three consecutive PDUs. This means the Tx window does not slide forward at (c).
The strategies “Rx window = 1”, “Rx window = Tx window + cumulative Acks”, “Rx window = Tx window + selective Acks” represent increasing efficiency at the cost of increasing complexity. Which is “best” will depend on such things as propagation delay, transmission rate and error rate.

## Slide 21: Tx Strategy – “Go Back N”
DATA 6
DATA 5
DATA 4
Diagram is from slide 19
Rx uses cumulative acks
Tx must start a timer each time it sends data
  Retransmission TimeOut (RTO) > Round Trip Time (RTT)
After (b), Tx:
  knows DATA 3 received OK
  knows nothing about 4, 5, 6
At (c) Data 4 “times out”
All of 4, 5, 6 must be retransmitted
This is the Go Back N strategy
Tx
Rx
Time
DATA 3
ind
ACK 2
DATA 4
DATA 5
ACK 3
(a)
rdy 4, 5, 6
(c)
DATA 6
(b)
rdy 3
ACK 6
Notes: If Rx uses cumulative acks then:
If Tx does not receive an ack for a PDU n it knows n must be retransmitted
Also, Tx will not learn the fate of PDUs n+1, n+2 since these cannot be acked until n is received.
Therefore Tx must go back to PDU n and retransmit it plus all subsequent PDUs.
Note that this argument applies whether Rx window = 1 or Rx window = Tx window.

## Slide 22: Tx Strategy, Selective Retransmission
DATA 4
Diagram is from slide 20
Rx uses SACK
At (b) Tx knows 3, 5, 6 received OK, 4 might be lost
Only 4 need be retransmitted
This is the “Selective retransmission” strategy
Tx is idle until (c)
  Should use bigger window (=6)
  7, 8, 9 could then be transmitted
Tx
Rx
Time
DATA 3
ind
ACK 2
DATA 4
DATA 5
ACK 3
(a)
ACK 4
DATA 6
ACK 5
(b)
rdy 3
rdy 4, 5, 6
ACK 6
(c)
Notes: If Rx is using SACK, Tx has more precise information about which PDUs have been received and which (may) have been lost. (Note that Tx never knows whether it is the data PDU that is lost or its ack).
Tx can use “selective retransmission” and avoid unnecessary retransmissions.
Tx can use the time saved by moving on to the next data PDUs 7, 8, 9 etc. But it can only do this if its Tx window is bigger. In this example the window needs to be 6 data PDUs.

## Slide 23: Summary So Far [1]
Tx and Rx strategies are linked
If Rx demands data PDUs in strict sequence
  This means Rx window = 1
  If data n is missing then all subsequent data PDUs will be ignored
  Tx must retransmit all outstanding PDUs => Go Back N strategy
  Acks are implicitly cumulative

## Slide 24: Summary So Far [2]
If Rx can accept data PDUs in any sequence
  Rx window = Tx window
  If data n missing then all subsequent data PDUs are buffered
  2.1 If acks are cumulative
    Ack n => n, n-1, n-2 .. received OK
    Ack n missing means whole window may have been lost => Go Back N
  2.2 If Rx uses Selective Ack
    Ack n => just n received OK
    Ack n missing means data n is missing => Sel. Retran.
Notes: Note the point at 2.1. If the last ack Tx receives is for n-1 then data n may have gone missing and must be retransmitted. The fate of n +1, n +2 … n +w (which may already have been sent) is not clear to Tx. Tx could just retransmit n and hope that n +2, n +2 etc. were received, in which case it will eventually receive an ACK for n +w. However, if any of n +1, n +2 … n +w was lost then time will have been wasted. Go Back N avoids this waste of time at the expense of (probably) unnecessary retransmissions.

## Slide 25: Error Recovery Time
Go Back N, Rx window 1
  a d is lost - retransmission timeout (RTO)
Go Back N, Rx win = Tx win
  a c repeated in d e
  c d buffered and acked at e
  a c is lost – Round Trip Time (RTT)
Selective Retrans. + SACK
  Just one retransmission
  a b is lost
N.B. High capacity means more PDUs lost per unit time.
ACK
Tx
Rx
Time
DATA
a
c
Retransmission
d
ACK
e
b
Notes: For GBN, Rx window 1 all the time between the end of a failed transmission and the start of its retransmission is lost. I.e cost is 1 RTO.
For GBN, Rx window = Tx window retransmissions cease as soon as the ACK for the first retransmitted PDU is received. I.e cost is 1 RTT.
For selective retransmission + SACK only one PDU must be retransmitted.
This suggests we should always use selective retransmission + SACK. However, this is the most complex strategy with a greater chance of bugged or incompatible implementations. It also has the greatest buffer requirements at Tx and Rx. Consequently, it is not always the best choice.
Although transmission bit-rates increase, propagation delays remain much the same - hence the bandwidth.delay product increases. This means that, for Go Back N, more data is retransmitted each time an error occurs.
[N.B. The analysis above is greatly simplified and ignores a number of complications. However, it does capture the essence of the differences between the strategies.]

## Slide 26: Error Recovery Strategy
If error rate low, RTT low, capacity low
  Not too much data lost and doesn’t happen often
  Go Back N is reasonable
  If var(RTT) low
    RTO can be set close to RTT
    Rx window of 1 is OK
  If var(RTT) high
    RTO >> RTT
    Rx window = Tx window is better
  If Sequence not maintained
    Should use Rx window = Tx window
Otherwise sel. retrans. and SACK may be best
“Normal” TCP strategy
TCP option
Possible wired data-link strategy
Notes: The slide shows some considerations for the designers of real protocols. Note that sometimes combinations or variants of these strategies may be employed. Note also that some protocols may allow several strategies with the actual one used being negotiated at run-time according to the prevailing conditions.

## Slide 27: Idle Request
Tx window = Rx window = 1
Also called “Stop and Wait”
Very simple strategy
Not “continuous request”
Utilisation OK provided b/w.delay product is low
E.g. 1Km, 1Mbps wireless link, 200 bytes data, 40 bytes ack
p = 103/(2x108) sec = 5s, d = 200x8/106 sec = 1600 s, a = 40x8/106 sec = 320 s
Utilisation = 1600/(2x5 + 1600 + 320) = 83%
Tx
Rx
Time
DATA
ACK
DATA
ACK
Notes: A reminder that simplicity is sometimes best!
The bandwidth.delay product is important to ARQ protocol efficiency. Here “bandwidth” is really the capacity in bps and “delay” is the round-trip time (RTT). Thus bandwidth x delay is a measure of how many bits may be in transit between Tx and Rx and back to Tx. In general the transmit window size must be big enough to accommodate all these bits. For idle request is is never big enough but if the RTT is low it may not make too much difference.

## Slide 28: Flow control – Stop and Go
8
Fixed Tx window (say 4)
RR and RNR flags in PDUs
(a) Tx window used - stops
(b) Rx happy to continue – puts RR in ack 4
(c) Rx wants flow to stop – puts RNR in ack 7
(d) Although 9,0 and 1 are valid, Tx must stop
(e) Rx sends a “keep-alive”
(f) Rx re-enables the flow
Tx
Rx
Time
4
5
6
7
4
7
Tx Window
RR
8
RNR
4567
4567
4567
4567
4567
5678
5678
(a)
(b)
(c)
7
(e)
8901
RNR
8901
RR
9012
(d)
(f)
Notes: RR: Receiver Ready => transmissions can continue
RNR: Receiver Not Ready => transmissions must cease
The Tx window also provides flow control as at (a)
Whilst flow is stopped, Rx may repeat the last ack so that Tx knows it is still alive.
Clearly there is a delay between Rx issuing an RR or RNR and Tx receiving it. This causes some implementation problems, for example, Rx may need to issue RNR before it’s buffers are full since it knows some data PDUs may already be “in flight”.

## Slide 29: Flow Control – Variable Window (e.g. TCP)
Initially Tx window = 4
(a) Tx window used - stops
(b) Rx wants 4 more – puts w=4, a=4 in PDU
(c) 4 is acked and w=4
  New window is 5678
  567 already sent
(d) Rx wants 3 more – puts w=3, a=7 in PDU
(e) Rx “opens the window” to increase the flow
Tx
Rx
Time
4
5
6
7
4
7
Tx Window
w=4
8
w=3
9
0
4567
4567
4567
4567
4567
5678
890
890
890
(a)
(b)
(c)
(d)
8
(e)
w=8
90123456
Notes: Ack PDUs now contain window sizes as well as ack numbers.
[Note that, in practice, TCP numbers bytes and not PDUs].
Also, TCP, like most protocols provides a duplex service. Thus the ack PDUs sent by Rx may contain data passing in the other direction. In such cases all PDUs carry both data and ack SNs as well as window sizes.