## Slide 1: Properties of Physical Media
Graham Knight (G.Knight@cs.ucl.ac.uk)
Room 112

## Slide 2: Properties of different media
Copper:
  twisted pair, co-ax, parallel
Radio:
  lower frequencies, higher frequencies, microwave, satellite
Light:
  free space and optical fibre
Why do we use many different media?
What are their relative advantages and disadvantages?
Notes: There are many different media used for interconnecting communications equipment; wired connections made of various copper cabling to optical fibre based systems, as well as systems that use radio or light through the atmosphere. We look here at these various different forms of media and examine briefly their relative merits and failings.

## Slide 3: Copper cabling – twisted pair
Cheap – widely available
Versatile
Easy to connect
Subject to interference
Signal “leakage”
Relatively high attenuation
Widely used:
  smart Tx/Rx electronics at termination
  speeds upto 100Mb/s
telephone
wire
Ethernet
cable
(CAT5 UTP)
with plug
(RJ45)
Notes: A transmission line is a pair of conducting wires held apart by an insulator or dielectric. They come in a variety of constructions. The simplest and least expensive form is two-wire cable or copper-pair. Unshielded twisted-pair (UTP) cable consists of (often sets of) two wires sheathed in an insulator and twisted together. Shielded twisted pair (STP) cable contains (often sets of) two wires sheathed in a insulator as for UTP, but now surrounded by a conducting foil shield that provides some protection from external signals.
Twisted-pair is by far the most common form of datacomms in the LAN. CAT5 UTP (Category 5 unshielded twisted pair) with and RJ45 plug is the wiring/connection used in most LAN installations. This will support up to 100Mb/s quite easily. Recently, standards have emerged that may allow some installations to achieve 1000Mb/s over CAT5 UTP – Gigabit Ethernet or 1000baseT.
Twisted-pair is also the telephone wire that comes into your home. It has reasonable propagation characteristics, but is subject to interference and cross-talk. Recent developments in line termination equipment has enabled high data rates (several Mb/s) over distances of several hundred metres, i.e. using digital subscriber line (DSL) technology.
Twisted pair becomes impractical for use at high electrical bandwidths – above ~200MHz. At such high bandwidths, it is only usable for short cable lengths.

## Slide 4: Copper cabling – parallel cables
Multiple copper wires
Higher data rate:
  multiple signals
Cheap – widely available
Similar problems as TP
Short distances – skew
Widely used:
  computer bus
  peripheral devices and components
parallel
printer
interface
(IEEE1294)
ribbon cable
(SCSI interface)
Notes: Ribbon cable consists of individual copper wires held together by an insulator in such a way that the individual wires are insulated from each other but the insulator effectively forms a flat ribbon (e.g. cable used to connect components in PCs such as disc drives).
Parallel cables allow multiple bit transmissions simultaneously and is fairly cheap, but suffers from the same drawbacks as twisted-pair, namely interference and crosstalk. Another disadvantage of parallel cables is skew – simultaneous bit transmission travelling at different speeds on the individual wires.
Nevertheless, this type of cable is perfectly adequate for a computer backplane bus and connecting computer peripherals over small distances (a few metres or less). However, this type of cabling is rarely used for datacommunications between end-systems..

## Slide 5: Copper cabling – coaxial cable
Central conductor:
  outer braid (earth)
High data rates possible
Good immunity to interference
More expensive than TP
Physical breaks in line:
  termination of cable
Widely used in CATV networks:
  co-ax delivery to the home
coaxial
cable
T junction
connector
Notes: From the point of view of propagation characteristics, the preferred copper cabling is coaxial cable. This consists of a central conductor surrounded by an insulator. The insulator is itself contained within a copper braid that shields the conductor from external noise sources. The entire construction is housed in a flexible, waterproof cover. While having much better propagation characteristics and is usable with signal of bandwidth up to around 900MHz.
Coax is relatively expensive when compared to twisted-pair, a consequence of its physical geometry. Another disadvantage is that great care is needed when connecting coax cable, as aloose connection, or cable that has not been properly terminated can lead to transmission loss.
Coax is widely used where high electrical bandwidth is required, e.g. CATV networks.

## Slide 6: Radio [1]
Easy to set-up network:
  wiring
High data rates possible
Mature technology:
  mobile still maturing
Local and nationwide
Global – satellites
Interference
Security
Spectrum regulation
Safety
Notes: Propagation of waves in free-space is different from that in cable. With respect to signal propagation, cables are one-dimensional systems, and the signal is attenuated relatively little as travels along the cable. With radio, in three-dimensions, waves radiate spherically. For each doubling of the distance between the source and receiver, a 6dB loss is experienced. For all frequencies up to millimetre-wave frequencies, this free-space loss is the most important source of loss. Free-space systems usually require much more power than cable or fibre systems.
However, radio systems generally are relatively easy to set-up and there is much mature technology to support radio transmission and reception. The only exception here is mobile systems – both terrestrial and satellite – which are relatively new and so the technology is still evolving and maturing.
Radio spectrum is subject to international regulatory control, so it is not possible to use just any part of the spectrum at will – you have to obtain a licence. (There are some frequency bands set aside for industrial, scientific and medical (ISM) use, however.) The regulations govern not only which parts of the spectrum are used but also give rules about the power output of transmitters in order to minimise interference with other parties who may be using the same frequencies in another geographical area. Radio transmission is also subject to interference from other radio sources.
Also, by their very nature, one must be concerned about security as the radio broadcast is receivable by anyone within range of the transmitter and having suitable equipment.

## Slide 7: Radio [2]
Different propagation characteristics
Effects:
  reflection
  refraction
  diffraction
  (scattering)
Interference – multi-path effects:
  e.g. TV “ghosting”
refraction
diffraction
medium 1
medium 2
interface
reflection
Notes: Different radio frequency bands have different propagation characteristics within the atmosphere. When waves travelling in free-space are obstructed, new waves result from the interaction. There are four types of interaction:
reflection: this occurs when a wave meets a plane object. The wave is reflected back without distortion.
refraction: this occurs when a wave encounters a medium with a different wave speed. The direction and speed of the wave is altered.
diffraction: this occurs when the wave encounters an edge. The wave has the ability to turn the corner of the edge. This ability of waves to turn corners is called diffraction. It is markedly dependent on frequency – the higher the frequency, the less diffraction. Very high frequencies (light) hardly diffract at all; “light travels in straight lines”.
scattering: catch-all description of wave interactions that are too complex to be described as reflection, refraction or diffraction. Typically the result of scattering is to remove radiation of the wave, and re-radiate it over a wide range of directions. Scattering too is strongly frequency dependent. Usually it will increase with frequency.
When a signal arrives at a receiver along with several scattered version of the same signal – multi-path reception – fading can result due to the destructive interference because of the multi-path signals.

## Slide 8: Radio – ISM
Existing spectrum allocation:
  e.g. radio and TV, (mobile) telecommunications, satellite
ISM:
  industrial, scientific and medical (ISM)
  3 bands
  some frequencies already occupied
  uses include military and culinary
Bands available
  902 – 928MHz (26MHz)
  2.4 – 2.483GHz (83.5Mhz)
  5.725 – 5.850GHz (125MHz)
Notes: Some frequency bands have better characteristics than others and they are usually already allocated for use for existing applications! These include commercial radio and TV, as well as national and international telecommunications (microwave and satellite). Recently, allocation has also been made for mobile phone systems. Allocation is controlled by the ITU. National bodies (e.g. the FCC in the US and he DTI in the UK) monitor national usage.
For general purpose unallocated use, there are several band allocated for industrial, scientific and medical (ISM) use. these bands may have licensed users, but unlicensed use is also possible, governed by certain rules. Uses of the ISM band include military and culinary (microwave ovens), as well as datacomms applications.

## Slide 9: HF (3 – 30MHz)
Atmosphere:
  troposphere – weather
  ionosphere
HF:
  ground wave
  sky-wave – uses ionosphere
Diffraction:
  OK for tunnels!
Ionosphere:
  effect varies through day
Uses: AM radio (LW and MW)
not to scale
ionosphere
Earth
Notes: The propagation of electromagnetic waves through the atmosphere is strongly influenced by the atmosphere. From the point of view of wave propagation, there are two layers. The troposphere is the lowest layer of the atmosphere. It extends (typically) from the surface to a height of 50Km. It contains all the Earth’s weather, all the liquid water, most of the water vapour, most of the gaseous atmosphere, and most of the pollution. The ionosphere extends from the top of the troposphere into outer space. The ionosphere plays a crucial historical role in radio communication. It consists of oxygen molecules that are ionised by the action of the sun. During the day, the quantity of ions rises. At night, the ions recombine to form uncharged oxygen molecules. The ionisation of the atmosphere converts the ionosphere into a plasma: an electrically neutral “gas” of positive and negative charges.
A plasma has a wave-speed that is a strong function of frequency. The consequence of this is that, to a low frequency wave, the ionosphere behaves as a mirror. Waves are simply reflected. This permits a mode of propagation in which the wave bounces forwards and backwards between the ionosphere and the Earth. It was this mode of propagation that permitted Marconi, against the experts’ advice, to achieve cross-Atlantic radio communication, and, in the process, discover the ionosphere. The Earth itself also acts as a mirror for electromagnetic waves. As the frequency increases to around 50MHz, the ionospheric effect reduces, and at higher frequencies the ionosphere becomes invisible – the signals pass right through.
HF wave propagation generally consists of two waves1. The sky-wave, that bounces from the ionosphere, and the ground-wave, that propagates along the ground. Due to the long wavelengths, HF communications are not effected by the troposhpere, and can usually bend around even large objects such as hills. The ionosphere permits communication over great distances: these are the frequencies of the radio ham. The ionosphere is not dependable, however, and signal strengths can vary considerably – effect is maximum in early evening, explaining the overcrowding of the medium wave-band in Britain with European transmissions in the evening.
1. Remember that HF is actually at the low end of the electromagnetic spectrum – see slide 8.

## Slide 10: VHF and UHF (50MHz – 1GHz)
Can not use ionosphere:
  frequency is too high
Diffraction effects are low:
  poor reception in tunnels
Susceptible to fading effects
Uses:
  VHF: FM radio
  UHF: television
Notes: Very high frequency (VHF) and ultra high frequency (UHF) are not affected by the troposphere, but are too high in frequency to exploit the ionosphere. In addition their decreased wavelength makes them increasingly less able to diffract around obstacles. At UHF in particular, areas in deep radio shadow can experience very poor reception, for example TV signal reception when surrounded by large buildings. In urban areas, most reception is due to scattered arrivals.
Experiments have shown that the free-space loss is increased in urban areas, to the extent of following a fourth power law (rather than a second power law). These effects are noticeable under motorway bridges: medium wavelength (MW as used for AM) transmission is usually better than VHF. VHF is used for FM radio stations and UHF for TV transmissions.
When the received signal consists of a number of scattered arrivals, an effect called fading occurs due to multi-path effects. According to the location, the many arrivals may interfere constructively or destructively. The phase relationship between the arrivals changes as the location of receiver changes. This causes a moving receiver (e.g. a mobile radio system) to experience fluctuations between strong and weak signals – fading.

## Slide 11: Microwave and millimetre wave [1]
Line of sight
Water and oxygen absorption
Usable frequencies:
  ~38GHz
  ~98GHz
Noise:
  atmospheric (e.g. lightning) in HF, VHF, UHF
  receiver noise in mm-wave and -wave
High receiver noise:
  thermal noise
  due to high bandwidth
Thermal noise, NT:
  related to bandwidth
NT thermal noise power [W]
k Boltzman’s constant [1.3810-23 Joules/Kelvin]
T absolute temperature [Kelvins, K]
B bandwidth [Hz]
Notes: Microwave and millimetre wave frequencies are usually completely blocked by obstructions. They need line-of-sight topologies. In addition, the wavelengths are small enough to become effected by water vapour and rain. Above 10GHz these effects become important. Above 25GHz, the effects of individual molecules become important. Water and oxygen are the most important gases. These have resonant absorption lines at 23GHz, 69GHz and 120GHz. Above these frequencies, absorption is increasingly effected by the Earth’s black-body spectrum. These peaks leave windows that may be used for communication, notably at 38GHz and 98GHz.
The use of the atmosphere as a transmission medium means that control over the noise environment is not possible. There are a number of sources of noise.
Natural noise is classified by its source. Atmospheric noise dominates the low frequencies, up to 2MHz. The primary cause of this noise is electrical discharges in the atmosphere: lightning. So-called galactic noise is radio noise from outside the solar system. It is important up to 200GHz. The sun also generates a small noise contribution at these frequencies.
In urban environments these natural sources of noise are dominated by man-made noise. In the HF and VHF bands these are mostly other signals, although the very high power early warning radars can generate noise in these bands. At higher frequencies car ignition systems generate high noise levels.
In comparison, receiver noise typically is small in the HF, UHF and VHF. At microwave frequencies, however, the thermal noise generated by the receiver is usually the dominant source of noise in the system.

## Slide 12: Microwave and millimetre wave [2]
Mature technology
Land acquisition
Difficult terrain
Bandwidth allocation
Atmospheric effects
Clear transmission path
Radio interference
Restrictive costs
mm-wave frequencies hard to utilise in practise
Notes: The maturity of radio frequency (RF) technology has permitted the use of microwave links as the major trunk channel for long distance communication. The use of microwave links has major advantages over cabling systems:
  freedom from land acquisition rights: the acquisition of rights to lay cabling, repair cabling, and have permanent access to repeater stations is a major cost in the provision of cable communications. The use of radio links, that require only the acquisition of the transmitter/receiver station, removes this requirement. It also simplifies the maintenance and repair of the link.
  ease of communication over difficult terrain: some terrains make cable laying extremely difficult and expensive, even if the land acquisition cost is negligible.
The use of microwave links has a number of disadvantages:
  bandwidth allocation is extremely limited: the competition for RF bandwidth from various competing users leads to very strict allocations of bandwidth. Unlike cabling systems, that can increase bandwidth by laying more cables, the radio frequency bandwidth allocation is finite and limited. In practise, allocations of 50MHz in the range 300MHz to 1GHz are typical.
  atmospheric effects: the use of free-space communication results in susceptibility to weather effects, particularly rain.
  transmission path needs to be clear: microwave communication requires line-of-sight, point-to-point communication. The frequency of repeater stations is determined by the terrain. Care must be taken in the system design to ensure freedom from obstacles. In addition, links must be kept free of future constructions that could obstruct the link.
  interference: the microwave system is open to RF interference.
  restrictive costs: the cost of design, implementation and maintenance of microwave links is high. Many countries are not well equipped with good technical resources to provide efficient and continuous operation.

## Slide 13: Microwave and millimetre wave [3]
Often used for inter-city links:
  e.g. towers in city centres
Higher bandwidth demands:
  -wave RF allocations fixed
  powerful mm-wave transmitters hard to produce
Gradually being replaced by optical fibre:
  much higher bandwidth and data rates
  more bandwidth by laying more fibre
Existing installations will remain in use
Notes: The modern urban environment presents a particular challenge, in that bandwidth allocation, RF interference, link obstruction and atmospheric pollution place maximum constraints on the system simultaneously. However, urban environments also have the highest land acquisition values too. Many modern cities have found it cost effective to build a single, very high tower to house an entire city’s trunk communication microwave dishes. These towers are now a common feature of the modern urban landscape.
As the demand for bandwidth increases, microwave links will become increasingly unable to deliver. The use of increased carrier frequencies in the millimetre wave region would be advantageous. However, for technical reasons, no efficient method of producing large quantities of millimetre power have been found. This is a necessity, given the increase in atmospheric attenuation at millimetre wave frequencies.
The tremendous growth of optical fibre technology and its bandwidth capacity has led to a gradual replacement of microwave links with optical fibre cable for point-to-point communication. The rate of growth has depended on the communication policy of various nations.
Within the national network in Britain, the replacement of microwave systems by optical fibre is well advanced, especially in heavily populated areas of the country. Microwave systems will continue for some time to come, however, if only because they are already paid for. In addition, microwave links retain a considerable cost advantage in sparsely populated areas.

## Slide 14: GEO Satellites
Geo-stationary orbit:
  36,000Km equatorial orbit
  Kepler’s Law
  3 satellites: total Earth coverage
No long cables
Trunk links: heavy load
Fast network set-up: sparsely populated areas
Power on satellite platform
Bandwidth overcrowding
High cost
Loss above 30GHz
Earth
not to scale
Notes: Satellite communication became a possibility when it was realised (by the science fiction writer, Arthur C. Clarke) that a satellite orbiting at a distance of 36,000Km from the Earth would be geo-stationary (or geo-synchronous), i.e. would have an orbital period equal to the Earth's own rotational period. It would thus appear to remain stationary relative to the Earth if placed in an equatorial orbit. Kepler’s Law states that the orbital period T of a satellite around the Earth is a function of the orbit radius, r, the Earth’s radius, R, and the acceleration due to gravity at the Earth’s surface, gS. As the orbit increases in radius, the angular velocity reduces, until it is coincident with the Earth’s at a radius of 36,000Km (above the earth). In principle, three geo-stationary satellites correctly placed can provide complete coverage of the Earth’s surface. In practice, GEO satellites typically have a coverage of 80 around the equator.
For intercontinental communication, satellite radio links become a commercially attractive proposition. Space communication showed phenomenal growth in the 1970s, and will continue to grow for many years to come. The growth has been so rapid that there is now danger of overcrowding the geo-stationary orbit. Satellite communication has a number of advantages:
  the laying and maintenance of intercontinental cable is difficult and expensive
  the heavy usage of intercontinental traffic makes the satellite commercially attractive
  satellites can cover large areas of the Earth quickly, useful for sparsely populated areas
Satellite communication is limited by four factors:
  technological limitations preventing the deployment of large, high gain antennas on the satellite platform.
  over-crowding of available bandwidths
  the high investment and insurance cost associated with significant probability of failure
  high atmospheric losses above 30GHz limit the use of carrier frequencies

## Slide 15: LEO and MEO Satellites
GEO:
  expensive to use
  large delay (~250ms)
Lower orbits:
  MEO (~10,000Km)
  LEO (~2,000Km)
MEO:
  delay ~100ms
LEOs:
  lots of commercial activity
  Big LEO and Small LEO
  Broadband LEO
Voice – examples:
  Iridium (Big LEO)
  Globalstar (Big LEO)
Data – example:
  Teledesic (Broadband LEO)
Notes: Satellites that have medium Earth orbit (MEO) or low Earth orbit (LEO) are an attempt to try and address some of the issues that affect GEO satellite usage. In particular, the need for large, expensive receiver terminals and the relatively high propagation delay due to large orbit radius.
LEO system orbit at around 2,000Km and MEOs at around 10,000Km. LEOs have footprints of about 2,000-3,000Km diameter and so to get large area coverage, many satellites would be required. The delay for LEOs and MEOs is around 40ms and 100ms respectively.
There are several LEO systems currently in the process of being deployed. The satellites will be arranged in constellations with inter-satellite links, forming a satellite network to carry data. Such constellations are also called Big LEO systems, as opposed to Small/Little LEO systems that have perhaps a single satellite. Small LEOs are intended for store-and-forward messaging, positioning and tracking. Big LEOs are aimed at voice and data applications. Small LEOs orbit the Earth and typical applications include spy satellites.
Examples of commercial Big LEO systems expected to offer services in the near future are Globalstar, Iridium and Teledesic. Not all constellations have inter-satellite links (e.g. Globalstar) and some (e.g. Iridium and Globalstar) are aimed more at the mobile-voice market (with faxing and paging) rather than the data market. Some of these systems intend to offer multi-megabits per second data to the subscriber and are called Broadband LEOs (e.g. Teledesic, 2Mb/s symmetric).
LEO satellites require power sources to keep them in a well-defined orbit. Satellites in LEO constellations will eventually (after 10-12 years) need replacing. The old satellites will fall out of their orbit (under control) and burn up in the atmosphere.
In a constellation, as the satellites are in constant motion, there is a need for sophisticated signalling protocols to allow one satellite to hand-off all its active channels to another satellite in the constellation as its footprint moves from one geographical area to another.

## Slide 16: Light and Infra-red – free space
High data rates possible
No interference:
  from radio/electrical signals
No regulations
Safety:
  laser sources need care
Line-of-sight:
  clear path
  may need to use diffusers/reflectors
Mainly infra-red
Uses:
  (remote control handsets)
  connections between laptops and peripherals
  small mobile systems, e.g. PDAs
  floor-floor communication (e.g. within lift-shafts)
Notes: As with any light-based system, the transmission path is immune to electromagnetic interference. However, use of light in free space is restricted to clear line of sight paths (or approximately line of sight paths). In some scenarios, e.g. connectivity between peripheral devices and a computer, personal digital assistants (PDAs), and remote control hand-sets, the signal can be propagated by reflections from walls and ceilings within a room.
Unlike radio communication, there are no regulations that govern the use of light for free-space transmission systems. High power lasers are often a good source of light for transmission but care must be taken that they do not damage human sight.

## Slide 17: Optical fibre [1]
Fibre construction:
  core
  cladding
Waveguide action:
  total internal reflection
Acceptance angle
Many ray paths – modes:
  signal dispersion
Multi-mode and mono-mode fibre
not to scale
core
cladding
cladding
cladding
core
A
B
C
acceptance angle
acceptance
cone
Notes: For many years it has been appreciated that the use of optical (light) waves as a carrier wave provides an enormous potential bandwidth. Optical carriers are in the region of 1013Hz to 1016Hz, i.e. three to six orders of magnitude higher than microwave frequencies. However, the atmosphere is a poor transmission medium for light waves. Optical communication only became a widespread option with the development of low-loss dielectric materials for fibre production.
Optical fibre is a waveguide. The fibre (in its simplest form) consists of a core of glass of one refractive index, and a cladding of a slightly lower refractive index. The fibre is then surrounded by a refractive sheath. Typical fibre dimensions are 100m to 500m diameter.
In simple terms, the action of a waveguide can be partially understood by considering the rays down the fibre. A light-wave entering the fibre is either refracted into the cladding, and attenuated, or is totally internally reflected at the core/cladding boundary. In this manner it travels along the length of the fibre. The maximum angle at which it may enter the guide and travel by total internal reflection is termed the acceptance angle. In summary, a light-beam suitably injected into the end of the core propagates along the core by total internal reflection. Not forgetting that the core is a three dimensional object, it is also possible for the wave to follow a helical path down the guide. These rays are called skew-rays.
In fact, it is not possible for the wave to take an arbitrary ray down the guide - only certain rays can be taken. These rays are called modes. For any particular frequency, there is a different ray. The modal action of a waveguide is a consequence of the wave nature of the radiation. A mono-mode fibre is a fibre that only has one acceptable ray-path per frequency. A multi-mode fibre has a number of possible rays that light of a particular frequency may take.

## Slide 18: Optical fibre [2]
Light source
0.8m – 1.8m (IR):
  1.3m
  1.5m
LED:
  cheap
  low power
  general purpose
Laser diode:
  expensive
  high power
  high data rates, long distances
Loss
Rayleigh scattering
Material absorption
Fibre bending
Dispersion
Multi-modal effects
Material dispersion:
  light source components
  laser diode is better
Notes: The attenuation of light in the guide has a number of sources. Absorption of light occurs in the glass and this decreases with frequency. Scattering of light from internal imperfections within the glass – Rayleigh scattering – increases with frequency. Waveguide imperfections account for low-level loss that is approximately constant with wavelength. Bending the waveguide changes the local angle of total internal reflection and loss increases through the walls. A combination of these effects results in a minimum absorption of about 2dB/Km to 5dB/Km in the 0.8m to 1.8m wavelength region, the infra-red (IR) region. It is these wavelengths that are used for transmission. In particular, there are two windows at ~1.3m (~1300nm) and ~1.5m (~1500nm).
In addition to attenuation, optical waveguides also suffer from dispersion. The dispersion has two sources. Due to the modal behaviour, a waveguide is an intrinsically dispersive device. Put simply, rays of different frequency travel on different paths having different lengths. As the different frequencies travel different lengths they take different times. In addition to the waveguide dispersion, however, is the material dispersion. Glass is an intrinsically dispersive media. In mono-mode fibres, the material dispersion dominates the waveguide dispersion.
The bandwidth of optical fibres is dominated by the dispersion. In fact, the bandwidth of individual fibres is actually much the same as high quality co-axial cable. It is ironic that the principle justification for optical communication, very large bandwidth, has not in practise been realised. However, it is possible to lay many hundreds of optical fibres in the same cable cross-section as a single co-axial cable.
Another factor that affects data rate is the light source used. A light emitting diode (LED) is a relatively cheap component suitable for low power, general purpose use. The light it produces consists of a large number of frequencies and so is more susceptible to material dispersion effects. A laser diode provides a relatively high power, coherent source of light which is much more suitable for use over long distances and higher data rates. However, it is much more expensive than a LED.

## Slide 19: Optical fibre [3]
not to scale
stepped
index
n
graded
index
n
mono
mode
n
mono-mode fibre
typical data
cladding
core
buffer
jacket
primary
coating
core diameter 3-10m
cladding diameter 50-125m
buffer jacket diameter 50-175m
acceptance angle 8-10
Notes: Fibre optic cable is available in three basic forms:
  stepped-index fibre. In this type of fibre, the core has a uniform refractive index throughout. This generally has a core diameter of 100m to 500m. This is a multi-mode fibre.
  graded-index fibre. In this type of fibre, the core has a refractive index that gradually decreases as the distance from the centre of the fibre increases. This generally has a core diameter of 50m. This is also a multi-mode fibre.
  mono-mode fibre. As the name suggests, the distinguishing characteristic of this fibre is that allows only a single ray path. The radius of the core of this type of fibre is much less than that of the other two, however it does have a uniform refractive index.
The refractive index, n, of a medium is a measure of the relative speed of light in that medium, and has no units. The refractive index of free space is 1.
From step-index to graded-index to mono-mode fibres, we find that the cost of production increases, the complexity of transmitter and receiver increases, while the dispersion decreases. This latter property change means that the mono-mode fibre also has the potential to provide greater data rates. As it becomes cheaper to produce mono-mode fibre technology (fibres and transceivers), we will see an increased use of this type of optical fibre.

## Slide 20: Optical fibre [4]
Very high data rates (Gb/s and Tb/s)
No RF interference
Secure
Low signal loss
Small cable dimensions
Relatively expensive
Hard to connect cabling
Technology still maturing
Multi-mode + LED:
  most common
  LAN, a few Km
  need repeaters for long runs
Mono-mode + laser diode:
  higher data rates
  longer cable lengths possible
  more expensive
  harder to connect
Costs ~25% more than quality copper:
  connections still more expensive
Notes: In addition to the potential bandwidth, optical fibre communication offers a number of benefits:
   size, weight, flexibility: optical fibres have very small diameters. A very large number of fibres can be carried in a cable the thickness of a coaxial cable.
  electrical isolation: optical fibres are almost completely immune from external fields. They do not suffer from cross-talk, radio interference, etc.
   security: it is difficult to tap into an optical line. It is extremely difficult to tap into an optical line unnoticed.
   low transmission loss: Modern optical fibre now has better loss characteristics than coaxial cable. Fibres have been fabricated with losses as low as 0.2dB/Km and less.
The primary disadvantage of optical fibre are the technical difficulties associated with reliable and cheap connections, and the development of an optical circuit technology that can match the potential data-rates of the cables. The speed of these circuits, which are electronically controlled, is usually the limiting factor on the bit-rate. The difficulty of connection and high-cost of associated circuitry result in optical fibres being used only in very high bit-rate communication. There is considerable current debate as to whether optics will ever completely replace electronic technology, indeed there is current research into optical mechanisms for processing and switching to complement the existing optical transmission systems.

## Slide 21: Access technologies
The TP local-loop:
  V.90 “analogue” modem:
    56Kb/s downstream, 28.8Kb/s (33.6Kb/s) upstream
  BR-ISDN:
    128Kb/s (264Kb/s)
  xDSL:
    several hundred Kb/s to several Mb/s
CATV HFC networks:
  co-ax cable to the home
  RF modems: several Mb/s
Wireless access:
  analogue and digital
  ISM – LANs
  near microwave – WANs
Leased lines:
  copper (TP and coax)
  fibre – high data rates, (10s Mb/s) long cable lengths (several Km)
LAN:
  co-ax: old
  CAT5 UTP, e.g. Ethernet
  optical fibre – special apps
Notes: Many WAN access technologies use the existing telephony local-loop: twisted-pair (TP).
Currently, the “traditional” (analogue) modem access technology has an ITU Recommendation that specifies 56Kb/s downstream and 28.8Kb/s to 33.6Kb/s upstream (V.90). This requires a digital termination at the ISP, however, so is not analogue end-to-end.
BR-ISDN (Basic Rate Integrated Service Digital Network) also works over the standard local-loop, offering up to 128Kb/s over 2 B-Channels, each offering 64Kb/s.
The established telcos are very keen to try and exploit the installed base of equipment and wiring that is based on the copper-pair used for telephony. The xDSL (Digital Subscriber Line) technologies offer various capabilities with data-rates from several hundreds Kb/s to several Mb/s. xDSL can have asymmetric data-rates, with greater rates downstream (to the subscriber) than upstream (from the subscriber). (See the ADSL Forum web-site at http://www.adsl.com/)
CATV network operators are trying to exploit the potentially greater capability of their co-ax or HFC (Hybrid Fibre Co-ax) networks for similar high-speed access. At the moment, these networks are mainly analogue, so an RF modem is required, but CATV operators are keen to move to digital full service networks (FSNs). CATV networks also may suffer from poor quality installation and noise. (In the UK, however, as the CATV networks are relatively new, this may not be a problem.) (See the US CableLabs web-site at http://www.cablelabs.com/).
Many of these technologies (except BR-ISDN) may have difficulty achieving their highest data rates due to factors such as cable quality and noise.
Many wireless access technologies are also being introduced, including satellite (around 256Kb/s) as well as radio-based local loops (hundreds of Kb/s to several Mb/s).
For all these technologies, the general trend is away from analogue networks towards digital channels.
In the LAN, CAT5 UTP is almost ubiquitous, though some remaining older installations may use co-ax cable, and some specialist networks may use optical fibre.

## Slide 22: Summary
Many technologies: wired and wireless
TP widely used:
  LANs – CAT5 UTP
  residential access
Radio:
  regulated usage of spectrum
Optical fibre:
  not widely used in LAN – costs
  very high data rates