## Slide 1: CS 352 Queue management
Rutgers University

## Slide 2: Queues and Traffic shaping
Big Ideas:
  Traffic shaping:
    Modify traffic at entrance points in the network
    Can reason about states of the interior and link properties, loads.
    Modify traffic in the routers
      Enforce policies on “flows”

## Slide 3: Congestion Control
Too many packets in some part of the system
Congestion
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Simplified Network Model
Input Arrivals
“System”
Output Departures
Goal:
Move packets across the system from the inputs to output
System could be a single switch, or entire network

## Slide 5: Problems with Congestion
Performance
  Low Throughput
  Long Latency
  High Variability (jitter)
  Lost data
Policy enforcement:
  User X pays more than user Y, X should get more bandwidth than Y.
  Fairness
    One user/flow getting much more throughput or better latency than the other flows

## Slide 6: Congestion Control
Causes of congestion
Types of congestion control schemes
Solving congestion

## Slide 7: Causes of Congestion
Many ultimate causes:
    New applications, new users, bugs, faults, viruses, spam, stochastic (time based) variations, unknown randomness.
Congestion can be long-lived or transient
  Timescale of the congestion is important
    Microseconds vs seconds vs hours vs days
    Different solutions to all the above!

## Slide 8: Exhaustion of Buffer Space (cont’d)
50 Mbps
50 Mbps
50 Mbps
50 Mbps
Router
Buffer

## Slide 9: Types of Congestion Control Strategies
Terminate existing resources
  Drop packets
  Drop circuits
Limit entry into the system
  Packet level (layer 3)
    Leaky Bucket, token bucket, WFQ
  Flow/conversation level (layer 4)
    Resource reservation
    TCP backoff/reduce window
  Application level (layer 7)
    Limit types/kinds of applications

## Slide 10: Leaky Bucket
Across a single link, only allow packets across at a constant rate
Packets may be generated in a bursty manner, but after they pass through the leaky bucket, they enter the network evenly spaced
If all inputs enforce a leaky bucket, its easy to reason about the total resource demand on the rest of the system

## Slide 11: Leaky Bucket: Analogy
Leaky
Bucket
Output
Packets from input

## Slide 12: Leaky Bucket (cont’d)
The leaky bucket is a “traffic shaper”: It changes the characteristics of a packet stream
Traffic shaping makes the network more manageable and predictable
Usually the network tells the leaky bucket the rate at which it may send packets when a connection is established

## Slide 13: Leaky Bucket: Doesn’t allow bursty transmissions
In some cases, we may want to allow short bursts of packets to enter the network without smoothing them out
For this purpose we use a token bucket, which is a modified leaky bucket

## Slide 14: Token Bucket
The bucket holds logical tokens instead of packets
Tokens are generated and placed into the token bucket at a constant rate
When a packet arrives at the token bucket, it is transmitted if there is a token available. Otherwise it is buffered until a token becomes available.
The token bucket holds a fixed number of tokens, so when it becomes full, subsequently generated tokens are discarded
Can still reason about total possible demand

## Slide 15: Token Bucket
output
Packets from input
Token Generator
(Generates a token
once every T seconds)

## Slide 16: Token Bucket vs. Leaky Bucket
Case 1: Short burst arrivals
6
5
4
3
2
1
0
Arrival time at bucket
Departure time from a leaky bucket
Leaky bucket rate = 1 packet / 2 time units
Leaky bucket size = 4 packets
6
5
4
3
2
1
0
6
5
4
3
2
1
0
Departure time from a token bucket
Token bucket rate = 1 tokens / 2 time units
Token bucket size = 2 tokens

## Slide 17: Token Bucket vs. Leaky Bucket
Case 2: Large burst arrivals
6
5
4
3
2
1
0
Arrival time at bucket
Departure time from a leaky bucket
Leaky bucket rate = 1 packet / 2 time units
Leaky bucket size = 2 packets
6
5
4
3
2
1
0
6
5
4
3
2
1
0
Departure time from a token bucket
Token bucket rate = 1 token / 2 time units
Token bucket size = 2 tokens

## Slide 18: Multi-link congestion management
Token bucket and leaky bucket manage traffic across a single link.
But what if we do not trust the incoming traffic to behave?
Must manage across multiple links
  Round Robin
  Fair Queuing

## Slide 19: Multi-queue management
If one source is sending too many packets, can we allow other sources to continue and just drop the “bad” source?
First cut: round-robin
  Service input queues in round-robin order
What if one flow/link has all large packets, another all small packets?
  Larger packets get more link bandwidth

## Slide 20: Idealized flow model
For N sources, we would like to give each host or input source 1/N of the link bandwidth
Image we could squeeze factions of a bits on the link at once
  ->fluid model
  E.g. “fluid” would interleave the bits on the link
  But we must work with packets
Want to approximate fairness of the fluid flow model, but still have packets

## Slide 21: Fluid model vs. Packet Model
1
2
3
4
5
1
2
3
4
1
2
3
1
2
4
3
4
5
5
6
1
2
1
3
2
3
4
4
5
6
5
5
6
Flow 1
(arrivals)
Flow 2
(arrivals )
Service
in fluid
system
Service in
Packet
system
time
time
time
time

## Slide 22: Fair Queuing vs. Round Robin
Advantages: protection among flows
  Misbehaving flows will not affect the performance of well-behaving flows
    Misbehaving flow – a flow that does not implement congestion control
Disadvantages:
  More complex: must maintain a queue per flow per output instead of a single queue per output

## Slide 23: Virtual Time
How to keep track of service delivered on each queue?
Virtual Time is the number of rounds of queue service completed by a bit-by-bit Round Robin (RR) scheduler
  May not be an integer
  increases/decreases with # of active queues

## Slide 24: Approximate bit-bit RR
Virtual time is incremented each time a bit is transmitted for all flows
  If we have 3 active flows, and transmit 3 bits, we increment virtual time by 1.
  If we had 4 flows, and transmit 2 bits, increment Vt by 0.5.
At each packet arrival, compute time packet would have exited the router during virtual time.
This is the packet finish number

## Slide 25: Fair Queuing outline
Compute virtual time packet exits system (finish time)
Service in order of increasing Finish times I.e., F(t)’s
Scheduler maintains 2 variables:
  Current virtual time
  lowest per-queue finish number

## Slide 26: Active Queues
A queue is active if the largest finish number is greater than the current virtual time
Notice the length of a RR “round” (set of queue services) in real time is proportional to the number of active connections
  Allows WFQ to take advantage of idle connections

## Slide 27: Computing Finish Numbers
Finish # of an arriving packet is computed as the size of the packet in bits + the greater of:
  Finish # of previous packet in the same queue
  Current virtual time

## Slide 28: Finish Number
  Define
    - finish # of packet k of flow i (in virtual time)
    - length of packet k of flow I (bits)
    - Real to virtual time function
    Then: The finish # of packet k of flow i is

## Slide 29: Fair Queuing Summary
On packet arrival:
  Compute finish number of packet
  Re-compute virtual time
    Based on number of active queues at time of arrival
On packet completion
  Select packet with lowest finish number to be output
  Recompute virtual time

## Slide 30: A Fair Queuing Example
3 queues: A, B, and C
At real time =0, 3 packets:
  Of size 1 on A, size 2 on B and C
  A packet of size 2 shows up at Real time = 4 on queue A

## Slide 31: FQ Example
The finish #’s for queues A, B and C are set to 1, 2 and 2
Virtual time runs at 1/3 real time
Real | # of active | Virtual | Queue A |  | Queue B |  | Queue C | 
Time | queues | Time | Finish # | Remaining | Finish # | remaining | Finish # | Remaining
T=0 | 3 | 0 | 1 | 1 | 2 | 2 | 2 | 2

## Slide 32: FQ Example- cont.
After 1 unit of service, each connection has received 1*0.33 =0.33 units of service
Packet from queue A departed at R(t)=1
Packet from queue C is transmitting (break tie randomly)
Real | # of active | Virtual | Queue A |  | Queue B |  | Queue C | 
Time | queues | Time | Finish # | Remaining | Finish # | remaining | Finish # | Remaining
T=0 | 3 | 0 | 1 | 1 | 2 | 2 | 2 | 2
T=1 | 2 | 0.33 | 1 | 0 | 2 | 2 | 2 | 2

## Slide 33: FQ Example- cont.
Between T=[1,3] there are 2 connections; virtual time V(t) function increases by 0.5 per unit of real time
Real | # of active | Virtual | Queue A |  | Queue B |  | Queue C | 
Time | queues | Time | Finish # | Remaining | Finish # | remaining | Finish # | Remaining
T=0 | 3 | 0 | 1 | 1 | 2 | 2 | 2 | 2
T=1 | 2 | 0.33 | 1 | 0 | 2 | 2 | 2 | 2
T=3 | 2 | 1.33 | 1 | 0 | 2 | 2 | 2 | 0

## Slide 34: FQ Example- cont.
Between T=[3,4] only 1 connection; virtual time increases by 1.0 per unit of real time
Real | # of active | Virtual | Queue A |  | Queue B |  | Queue C | 
Time | queues | Time | Finish # | Remaining | Finish # | remaining | Finish # | Remaining
T=0 | 3 | 0 | 1 | 1 | 2 | 2 | 2 | 2
T=1 | 2 | 0.33 | 1 | 0 | 2 | 2 | 2 | 2
T=3 | 1 | 1.33 | 1 | 0 | 2 | 2 | 2 | 0
T=4 | 2 | 2.33 | 4.33 | 2 | 2 | 1 | 2 | 0

## Slide 35: Final Schedule
Real | # of active | Virtual | Queue A |  | Queue B |  | Queue C | 
Time | Queues | Time | Finish# | remaining | Finish# | remaining | Finish# | remaining
0 | 3 | 0 | 1 | 1 | 2 | 2 | 2 | 2
1 | 2 | 0.33 | 1 | 0 | 2 | 2 | 2 | 2
2 | 2 | 0.83 | 1 | 0 | 2 | 2 | 2 | 1
3 | 1 | 1.33 | 1 | 0 | 2 | 2 | 2 | 0
4 | 2 | 2.33 | 4.33 | 2 | 2 | 1 | 2 | 0
5 | 1 | 2.83 | 4.33 | 2 | 2 | 0 | 2 | 0
6 | 1 | 3.83 | 4.33 | 1 | 2 | 0 | 2 | 0
7 | 0 | 4.83 | 4.33 | 0 | 2 | 0 | 2 | 0

## Slide 36: Weight on the queues
  Define
    - finish time of packet k of flow i (in virtual time)
    - length of packet k of flow I (bits)
    - Real to virtual time function
    - Weight of flow i
  The finishing time of packet k of flow i is
Weight

## Slide 37: Weighted Fair Queuing
Increasing the weight gives more service to a given queue
  Lowers finish time
Service is proportional to the weights
  E.g. Weights of 1, 1 and 2 means one queue gets 50% of the service, other 2 queues get 25%.