## Slide 1: Transmitting Bits
Graham Knight (G.Knight@cs.ucl.ac.uk)

## Slide 2: Introduction
We need to represent bits as electrical or optical signals
Baseband – encode the bits directly
Broadband – modulate a carrier wave
Receiver must be able to “see” where bits begin and end
We also need to be able to group bits into “frames”
Receiver must be able to “see” where frames begin and end

## Slide 3: Baseband Transmission
Receiver must sample signal at correct intervals
b) and c) have transitions for every bit
a) and d) minimise transitions
Notes: The simple signalling used in RS232-C carries no “clocking” information. A sequence on 0’s appears as a steady voltage. There is no way the receiver can tell how many 0’s are in the sequence from the signal alone. Instead, the receiver must have a clock which is synchronised with the transmitter’s. This is only reasonable if a small number of bits is transmitted – 8 say. Clocks that stay in sync for longer than this cost too much.
“Bipolar Encoding”. This uses a “return to zero” (RTZ) waveform in which zero volts occurs between each pair of bits. The zero voltages enable the receiver to detect bit boundaries.
“Manchester Encoding”. This is an example of “phase encoding”. Here it is not the absolute voltages that encode the bits bit the voltage changes. The -ve -> +ve transition encodes a 1, +ve -> -ve encodes a 0. Manchester encoding is used on the Ethernet and other LANs. There is always a transition between bits so that the receiver can easily detect bit boundaries.
“Non return to zero” (NRTZ) encoding appears similar to the simple RS232-C encoding. The difference is that this is a “differential” encoding; it is the change in voltage from one bit to the next which determines what is encoded. In Figure 8c, for a 1 the voltage is left unchanged, for a 0 it is changed; this is usually called “Non return to zero - inverted” (NRTZ-I). It is clear that a long sequence of 1’s will result in a continuous voltage and therefore carries no clocking information. However, if NRTZ-I is used with an encoding scheme which ensures that the longest sequence of 1’s is 6 (see later). It is possible for the receiver to rely on its own clock during this period and subsequently to resynchronise with the transmitted clock.
One advantage of NRTZ-I is that, on average, it uses the same number of voltage transitions as the simple RS232-C encoding. Both of the other techniques introduce additional transitions - i.e. there are more transitions for a given bit-rate. This introduces higher frequencies which may exceed the limits for the channel in use.

## Slide 4: Modulation
Notes: The objective is to construct a signal that can pass through the channel. For the PSTN this means a signal in the range 300Hz-3400Hz.
Amplitude Modulation. Essentially, all that is required is to choose one amplitude for 1 and another for 0. Sometimes the amplitude corresponding to 0 is zero. The wave used is called the “carrier”. Unfortunately “amplitude modulation” (AM) is badly affected by attenuation and noise both of which disturb the received amplitudes. AM is rarely used on its own.
Frequency Shift Keying” (FSK) is a form of “frequency modulation” (FM) and uses different frequencies to represent the 1 and 0 values (Figure 7b). For duplex operation, four carrier frequencies are selected to represent 0 and 1 in each direction.
One of the simplest standards - ITU-T V.21 - uses the following frequencies:
1 0
Channel 1 80 Hz 1180 Hz
Channel 2 1650 Hz 1850 Hz
This was used to provide 300 bps connections.
Phase Shift Keying. A phase shift can be viewed as a jump to another point along the wave. Shifts are usually measured in degrees or radians. In “Phase Shift Keying” it is usual to employ four phase shifts each of which encodes 2 bits:
Shift (deg.) Encoding
45 11
135 10
225 01
315 00
Higher rates are possible by combining methods. For example “quadrature amplitude modulation” (QAM) uses AM and PSK employing two amplitude levels as well as 4 phase shifts giving 8 states each encoding 3 bits.

## Slide 5: Asynchronous Framing
Async. frames usually carry 8 bits
  Receiver must detect start then count in the bits
  Receiver must clock bits at the same rate as the transmitter
1
0
0
1
1
0
1
1
The data
Idle level (=1)
Receiver waits for “start bit” (=0) and starts clock
Receiver samples line to recover data
There must be at least one “1” bit before the next start bit – a “stop bit”
Notes: Asynchronous framing is used for slow irregular character transmissions – for example from a keyboard to a remote computer.
There are two signal levels 1 and 0.
When the line is idle the 1 signal is transmitted
Each character is preceded by a 0 – called the start bit. The receiver monitors the line searching for this bit. Once a start bit has been detected the receiver starts its clock.
The receiver samples the line at the appropriate intervals and recovers the bits.
Transmitter must insert at least one 1 bit after the character to enable the next start bit to be detected.
Note that we have to transmit 10 bits in order to convey 8 bits – a 25% overhead.

## Slide 6: Bit-oriented Synchronous Framing
Data may be arbitrary length
Special bit patterns:
  flag - 01111110
  idle - 01111111
0
1
1
1
1
1
1
1
0
0
1
1
One flag at start of data and one at end of data
flag or idle pattern in data:
  if 5 successive 1s, insert 0
  bit-stuffing
flag
flag
idle
idle
0
1
1
1
1
1
1
0
0
1
1
1
1
1
1
0
0
1
1
1
1
1
1
1
0
0
1
1
0
1
1
1
1
1
1
1
0
1
1
1
1
1
1
1
0
bit-stuffing
0
Notes: Bit-oriented synchronous frames are delimited by the flag bit pattern 01111110 (zero, six ones, zero). Between frames, the receiver continuously searches for this pattern and, when found, begins immediately to read in the data part of the frame. The transmitter often sends several idle patterns before the flag so that the remote end can achieve bit-synchronisation. The data part may be any number of bits. It does not have to be an integral number of bytes. Whilst reading the data bits, the receiver searches for the flag pattern once more in order to determine the end of the frame.
Transparency is achieved by bit-stuffing. Whenever the transmitter finds a sequence of five 1s in the data, it stuffs a 0 into the bit stream. When the receiver receives 5 successive 1s it examines the next bit.
If this is a 0 it must be the result of bit stuffing and so can be discarded.
Else (it’s a 1),
If it is followed by a 0, we have a flag,
Else, we have an idle.
(The bit streams shown above would be continuous but have been broken into 4-bit groups to make them easier to read.)
Bit stuffing is done in the transmission hardware so can be done “on the fly” as the bits are transmitted and received.
This framing, or variants of it, is used in most digital networks; LANs, ISDN, Frame Relay etc. It is supported by the serial ports on PCs.

## Slide 7: Serial or Parallel?
Digital data is usually stored in 8-bit, 16-bit or 32-bit chunks
Parallel transmission sends several bits in parallel – e.g. computer bus
  Problems with “skew”
Serial transmission sends bits successively
Notes: Parallel transmission merges several physical channels into a single logical channel. Bits are distributed between the physical channels. For example, a computer may have a 32-bit bus between the processor and memory. This enables transfers to take place 32 bits at a time for a 32x speed-up over a serial bus.
Unfortunately the problem of “skew” means that parallel transmission can only take place over short distances. Skew arises because of small differences between the physical channels which means that a set of bits transmitted simultaneously do not arrive simultaneously. This makes it impossible correctly to re-group bits at the receiver.
Parallel transmission can generally be employed only over distances of a few metres. Consequently, most data transmission is serial; the data consists of a sequence of bits flowing through a single channel.

## Slide 8: Summary
Baseband, broadband
Bit encodings
  Some make bit transitions easy to spot
Modulation
  Frequency and Phase shift keying
Framing - synchronous and asynchronous
  Transparency – bit-stuffing
Parallel and serial transmission