## Slide 1: High “speed”
Higher speed vehicles travel faster …
12 kph, ~ 36 vehicles/min
24 kph, ~ 144 vehicles/min
Bits always go at the same speed
  ~ 2x108 m/s in copper, ~ 3x108 in fibre
1 Mbps
2 Mbps
High “capacity”!
Notes: The terms “high-speed network” and high-speed link” are misleading. Bits, in a given medium, always travel at the same speed – the limit is really the speed of light.
However, bits may be packed more or less densely – i.e. the rate at which bits are injected into the channel may vary. A high transmission rate means more bits are injected, hence delivered, in a given interval - we should really call this a “high-capacity” channel. A file transfer through such a channel will complete in a shorter time than it would through a low-capacity channel. However, the propagation time for each individual bit will be the same in each case (assuming equal lengths and media).
[Note that a road densely packed with cyclists moving at 20 kph may actually have more capacity than a road carrying bloated single occupancy BMWs travelling at 100 kph! All that is required is that you can fit more than 5 bicycles in the space occupied by a BMW (which you can).]

## Slide 2: Time-division Multiplexing
TDM interleaves bits (sometimes bytes) from several streams onto a higher bit-rate stream
Timings between bits of a stream are preserved
The effect is as if there are two separate “bit-pipes
Notes: The slide shows bits from a pair of digital circuits interleaved on a single link. (In some systems the interleaving may be in terms of bytes rather than bits). Recall that bits always travel at the same rate, therefore the bits on the multiplexed link must be packed twice as tightly requiring twice the capacity of an input link. Once demultiplexed the original bit timings are restored – so bits are delivered at exactly the rate they were originally transmitted. In fact the multiplexing is invisible to the transmitter and receiver which have the illusion of a dedicated link.
Of course, more than 2 incoming links may be multiplexed but the arithmetic must be exact; the bit-rate on the multiplexed link must be equal the the sum of the bit-rates on the incoming links.
A simple timing change in the demultiplexor would cause the upper bit stream to be switched to the lower link and vice-versa. Thus it is easy to turn a TDM system into a “circuit-switch” which can connect arbitrary inputs and outputs.

## Slide 3: Circuit-switching
“Circuit” – constant bit-rate pipe across network
“Switched” – path established dynamically
Typically based on TDM
PSTN
ISDN
Notes: In modern digital communication a “circuit” is a constant-rate bit-pipe. Typically circuits are implemented using TDM channels passing through “circuit-switches”. A circuit-switch is capable of connecting input and output channels in an arbitrary way. Large switches may be able to handle many thousand such channels.
In some cases circuits are set up “administratively”. A customer will order a circuit of a particular capacity between two locations. An operator will use management software to configure switches to provide the circuit. Such circuits are called “leased circuits” or “leased lines”. Usually a monthly charge will be made.
In other cases circuits are set up “dynamically”. A “signalling” protocol between the customer’s equipment and an external network switch specifies the destination of the circuit which is then set up dynamically. Further signalling is used to disconnect the circuit. Such circuits are called “switched circuits”. Call charges will be based on the duration of the circuit – ISDN and PSTN provide switched circuits.

## Slide 4: Statistical Multiplexing
Data communication – not all bits are useful
  TDM does not exploit this
  Statistical multiplexing does
Notes: TDM works at the bit level; all bits of the original streams are delivered to the final destination. A few applications (e.g. PCM voice) generate a stream of bits at a constant rate all of which must be delivered – TDM suits such applications well. Most applications (including more modern compressed voice applications) generate data in bursts interspersed with periods of idleness. Most serial links still generate bits during such idle periods, (it is in the nature of the technology used to do this). Framing techniques, such as bit-oriented synchronous framing described earlier, enable data bits to be distinguished from idle bits. Statistical multiplexing treats the data bits and ignores the idle bits.
The slide shows two 1Mbps input streams in which about half the bits are in data frames the rest being idle bits (i.e. utilisation is about 50%). The statistical multiplexor exploits this by using a multiplexed link with a capacity < 2Mbps. The utilisation on this link is about 67%. (Of course the scheme is not restricted to just two input channels.)
Statistical multiplexors operate in “store-and-forward” mode – a complete frame must be received before transmission begins on the output link. This introduces a store and forward delay equal to the transmission time on the output link. E.g. if a frame has 15,000 bits the delay will be 10ms.
There can also be contention for the output link when two frames arrive simultaneously on the two input links. This contention is normally resolved by queuing – another source of delay. Queuing times, hence delays, can be highly variable – thus a statistical multiplexor introduced jitter as well as delay.
In the worst case there may be insufficient space for the queue so a frame must be discarded. So statistical multiplexing may cause data loss.
The demultiplexor cannot assume that frames will neatly interleaved – some information must be included in the frames to indicate to which channels they belong. Thus some bits in the frames must carry control information rather than data; an additional overhead due to statistical multiplexing.
Despite the disadvantages of statistical multiplexing the enhanced utilisation it brings for bursty data makes it the best choice for most current data communications.

## Slide 5: Packet-switching
Based on statistical multiplexing
“Packet-switches” – store and forward
Packets multiplexed to many destinations
X.25
Frame relay
ATM
Ethernet
Notes: Note that the two forms of multiplexing often co-exist. For example the 1.5Mbps link in the previous slide could actually be one TDM sub-channel in a higher capacity link. This is very often the case in the wide area. A company might lease (say) a 10Mbps link from a provider in order to connect two statistical multiplexors at two company sites. The provider’s network will likely consist on fibre running at several Gbps. Only a fraction of this will be needed to satisfy the company’s requirement and this will be apportioned using TDM.
The slide shows a network of “packet-switches” connected by “links”. Each link is a bit-pipe at some bit-rate. Packet-switches are usually store-and-forward, in which case the bit-rates may vary from link to link. Packet-switches can receive packets on any link and forward them on any other. They base their forwarding decisions on information contained in the packets. By setting this information appropriately a source may mix packets to a variety of destinations – something that is not possible with circuit-switching.
In a “virtual-circuit” network all packets to a particular destination follow the same pre-arranged route. If these routes are set up administratively we have “Permanent Virtual Circuits”, if they are set up dynamically via signalling we have “Switched Virtual Circuits”.
In a datagram network a separate routing decision is made for each packet. Thus packets belonging to a sequence will not necessarily all follow the same route and may be delivered out of order.
X.25, ATM and Frame Relay are examples of Virtual-Circuit packet networks.
Ethernet (though its structure is quite different from that shown in the diagram) is a datagram network.
The Internet is a datagram network constructed by interconnecting thousands of individual packet-switching networks of various types.
Since an idle host uses no (or almost no) network resources packet-switching tariffs are based on the volume of data sent.